## Slide 1
Your PCB partner

## Slide 2
Established year : 1982
Employees: approximately 100 people
Production area : 3000 Sqr meter
Company Type : Private owned

## Slide 3
Telecommunication
Automotive
Medical
Information Technologies
Security products
Consumer products
Industrial Automation
Military & Defense
Science
Products by sector

## Slide 4
ISO 9001-2008
UL 94V-0
IPC 600H,6011,6012.6013
ROHS-Compliant
Our Standards

## Slide 5
Print Electronics quality system is based on and conforms to the Requirements of ISO 9001. Regular audits are performed
by the Israeli Institute of standards.
Production is according to IPC-A-600 Acceptability of Printed Boards with class 2-3
Quality
Company policy:
customers are welcome to consult with our quality assurance staff both at the design review stage and after production.

## Slide 6
Print electronics has computerized engineering system, enabling data processing, design-criteria evaluation and fabrication of manufacturing tools
Net list is checked against Gerber files using IPC-356.
Engineering

## Slide 7
Standard rigid boards
Double-sided boards & Multilayer up to 20 layers.
Flexible and rigid-flex boards.
Controlled impedance circuits.
Blind and buried via hole
HDI including Blind and buried VIAS
Heat sink- nickel plated copper
or aluminum (3D heat sink)
Other products
Products

## Slide 8
FR-4 High TG
ROHS/ Lead-Free compatible FR-4
Polyimide Glass
Teflon ™
High speed materials : Rogers, Arlon, Taconic
Kapton - Polyimide
Other
Base Material:

## Slide 9
Electroless nickel/immersion gold (ENIG)
Electrolytic Ni / Hard Au
Immersion Silver
HASL
HASL for Lead free application
Immersion Tin
OSP - Entek-106 +
Electrolytic Ni / Soft Au
Carbon Printing
Via holes- capping
Surface Finish

## Slide 10
BOARD THICKNESS: 8~126 mil (0.2~6.0mm)
Copper foil :0.5oz, 1oz, 2oz, 3oz
working panel size: 500X600mm(STD), 1200x2300mm.
Line width/space : 4/4 mil for internal and external layers. (3/3 mil)
Minimum Drill size (Finish): 0.15 mm. (0.1 mm)
Hole location tolerance : 15 µ.
Routing tolerance: +/- 0.2mm. (+/- 0.1mm)
Final thickness tolerance: +/- 5%
Aspect ratio (hole-to-thickness) up to 1:12
Design Feature STANDARD

## Slide 11
Net list electrical testing is performed as standard test
The testing is performed using:
Emma- Test double sided flying probe tester- 4 Machines.
Test voltage up to 250v.
ELECTRICAL TESTING

## Slide 12
Full visual check
  Full dimension check
  Electrical test
  Solder-ability test
  Micro section
Final Inspection

## Slide 13
CERN-ATLAS 2009
Thin-Gap Wire Chambers (TGC) of Weizmann Inst.
PCB-cathodes made by Print electronics
Products: Science

## Slide 14: THGEM!
Producer:
Print Electronics

## Slide 15: 300x300 THGEM
THGEM geometry:
Hole dia.: 0.5 mm
Pitch: 1 mm
Thickness: 0.4 mm
Rim: 0.05 mm
Ni/Au plating
Producer:
Print Electronics www.print-e.co.il

## Slide 16
AOI
Hot air leveling
Inspecta
CNC ROUTING
Some of our machines & equipment

## Slide 17
CNC Drilling
Silk Printer
E-T
DI
Some of our machines & equipment

## Slide 18
Immersion Silver
Polar stack up & Impedance
Enig
Some of our machines & equipment

## Slide 19: Product By layer Count
Products by no’ of layers

## Slide 20: Sales by Region
Sales Region

## Slide 21
Some of our Main Customers
Notes: 21

## Slide 22
Address:
3 Eitan St. New Ind zone, Rishon Le-Zion 75650
ISRAEL
Tel: +972-3-9611168
Fax: 972-3-9612232
www.print-e.co.il
info@print-e.co.il