## Slide 1: Recent operation and outlook for the ISOLDE Resonance Ionization Laser Ion Source (RILIS)
Bruce Marsh - EN-STI-LP
LA3NET Topical Workshop: Laser based particle sources
20-22nd February 2013

## Slide 2: Outline of Talk
Introduction to ISOLDE and the RILIS installation
  The original CVL pumped dye laser system
  The new Dual TiSa and Dye laser RILIS
Operation of the RILIS in 2012
  Total operating time
  Specifics of Dual RILIS operation
  Highlights and new developments
Outlook and development work for 2013 and CERN LS1
  Practical changes to the RILIS installation
  Scheme development
  Laser system upgrades / changes
  Improved laser beam transport system

## Slide 3: Part 1
Introduction to ISOLDE and the RILIS installation
  The original CVL pumped dye laser system
  The new Dual TiSa and Dye laser RILIS
Operation of the RILIS in 2012
  Total operating time
  Specifics of Dual RILIS operation
  Highlights and new developments
Outlook and development work for 2013 and CERN LS1
  Practical changes to the RILIS installation
  Scheme development
  Laser system upgrades / changes
  Improved laser beam transport system

## Slide 4: ISOLDE isotope separator on-line
Production
Mass
separation
Ionization
Single charge:
Surface
Plasma
RILIS
ECR
Post acceleration
1-1.4 GeV p
2 mA
Delivers yearly 3200 h of radioactive ion-beams to 30 experiments by means of two target stations
Jonson, B., & Richter, A. (2000). More than three decades of ISOLDE physics. Hyperfine Interactions, 129, 1–22. doi:10.1023/A:1012689128103
http://isolde.web.cern.ch/ISOLDE/

## Slide 6: RILIS at ISOLDE-PSB
RILIS at ISOLDE-PSB
Mass separator
Laser system
Target
Proton beam
+
+
+
Laser
beams
Target - Ion Source Unit
Ionizer
Target
Extraction
Electrode
+
+
DC
60 kV
Ion beam lines
CVL lasers: nrep=11.000 Hz
Oscillator + 2 amplifiers
2-3 dye lasers with amplifiers,
nonlinear crystals BBO:
Installed in 1993
Mishin, V., Fedoseyev, V. , Kluge, H., Letokhov, V., Ravn, H., Scheerer, F., Shirakabe, Y. et al. (1993).
Chemically selective laser ion-source for the CERN-ISOLDE on-line mass separator facility. NIM B: 73(4), 550–560.
Slava Mishin
(Talk on Friday)
Valentin
Fedosseev

## Slide 7
RILIS LASERS
> 20 m optical path
3 mm diameter ion source
~10 cm
Proton beam
from PSB

## Slide 8: RILIS operation: 1994-2010
2096 h – total
2000 h - on-line
Laser time per beam for the 2010
Laser ON time
in 2010:
Sm | Mg | Cu | Ga | Tl | Be | Pb | Mn | Au | Be | Zn | Ag | At
52 | 154 | 183 | 52 | 184 | 54 | 123 | 228 | 114 | 344 | 299 | 140 | 74

## Slide 9
“A complementary laser system for ISOLDE RILIS” S Rothe et al: Journal of Physics: Conference Series 312 (2011) 052020
Wavelength tuning range (6 mirror sets):
Fundamental (w) 690 - 940 nm (5 W)
2nd harmonic (2w) 345 - 470 nm (1 W)
3rd harmonic (3w) 230 - 310 nm (150 mW)
4th harmonic (4w) 205 - 235 nm (50 mW)
100 mm
Pump laser: Nd:YAG (532 nm), Photonics Industries Ltd. DM60
Repetition rate: 10 kHz
Pulse length: 180 ns
Power: 60 W
Ti:Sa lasers:
Line width: 5 GHz
Pulse length: 30-50 ns
The RILIS Ti:Sa lasers
Featured in the next talk by Sebastian Rothe

## Slide 10: Dual RILIS tuning range
Chart: Wavelength, nm
| 200.0 | 205.0 | 210.0 | 215.0 | 220.0 | 225.0 | 230.0 | 235.0 | 240.0 | 250.0 | 260.0 | 265.0 | 270.0 | 275.0 | 280.0 | 285.0 | 290.0 | 300.0 | 305.0 | 310.0 | 315.0 | 320.0 | 330.0 | 340.0 | 345.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 395.0 | 400.0 | 405.0 | 410.0 | 420.0 | 425.0 | 430.0 | 440.0 | 450.0 | 460.0 | 465.0 | 470.0 | 475.0 | 480.0 | 490.0 | 500.0 | 510.0 | 520.0 | 530.0 | 535.0 | 540.0 | 545.0 | 550.0 | 560.0 | 570.0 | 580.0 | 590.0 | 600.0 | 610.0 | 620.0 | 630.0 | 640.0 | 650.0 | 660.0 | 670.0 | 680.0 | 685.0 | 690.0 | 700.0 | 710.0 | 720.0 | 730.0 | 740.0 | 750.0 | 760.0 | 770.0 | 780.0 | 790.0 | 800.0 | 810.0 | 820.0 | 830.0 | 840.0 | 850.0 | 855.0 | 860.0 | 870.0 | 880.0 | 890.0 | 900.0 | 910.0 | 920.0 | 930.0 | 940.0 | 950.0
TiSa FHG | 25 | 50 | 75 | 75 | 75 | 50 | 25 | 0
Dye THG | 25 | 50 | 100 | 120 | 125 | 125 | 125 | 125 | 125 | 125 | 100 | 80 | 50 | 25
UV-pumped Dye SHG | 20 | 40 | 100 | 100 | 150 | 150 | 200 | 200 | 200 | 150 | 100 | 50
Dye SHG | 500 | 1000 | 1700 | 2000 | 2000 | 2000 | 1800 | 1600 | 1600 | 1600 | 1500 | 1400 | 1300 | 1250 | 1200 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 500 | 100
TiSa THG | 50 | 100 | 125 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 125 | 100 | 50
TiSa SHG | 500 | 800 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 900 | 900 | 900 | 900 | 900 | 800 | 800 | 800 | 800 | 700 | 500
UV-pumped Dye Fundamental | 250 | 500 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 500 | 300 | 200 | 100
Dye Fundamental | 100 | 1000 | 5000 | 7500 | 10000 | 15000 | 18000 | 20000 | 18000 | 15000 | 15000 | 15000 | 15000 | 12000 | 10000 | 8000 | 8000 | 8000 | 6000 | 6000 | 6000 | 5000 | 4000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 1500 | 500
TiSa fundamental | 2000 | 2500 | 3000 | 4000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 4500 | 4500 | 4500 | 4500 | 4500 | 4300 | 4000 | 4000 | 4000 | 3500 | 3500 | 3500 | 3000 | 2500 | 2000
Fedosseev, V. N., Fedorov, D. V, Fink, D., Losito, R., Marsh, B. A., S.Rothe et al. (2012).
Upgrade of the RILIS at ISOLDE; Rev. Sci. Inst 83(2), 02A903. doi:10.1063/1.3662206

## Slide 11: The RILIS Dye + Ti:Sa system
3 Ti:Sa lasers
RILIS cabin layout has been redesigned to accommodate the new lasers
Harmonic generation unit for Ti:Sa system
Photonics Industries Nd:YAG pump laser for the Ti:Sa lasers
Sirah dye lasers with 2nd harmonic generation and UV pumping option
Edgewave Nd:YAG laser for dye pumping or non resonant ionization
Narrow band dye laser with computer controlled grating and etalon for high resolution spectroscopy or isomer selectivity
Dye laser 3rd harmonic generator
The laboratory is now at maximum capacity – extension is planned.
Improved HRS laser beam launch system with a 4th laser beam path for laser transport to ISCOOL
Dye and Ti:Sa synchronization  mixed ionization schemes are possible
Fedosseev, V. N., Fedorov, D. V, Fink, D., Losito, R., Marsh, B. A., S.Rothe et al. (2012).
Upgrade of the RILIS at ISOLDE; Rev. Sci. Inst 83(2), 02A903. doi:10.1063/1.3662206

## Slide 12: RILIS in action

## Slide 13: RILIS in action

## Slide 14: New modes of operation
100W Nd:YAG laser is available for non-resonant ionization in Ti:Sa only schemes
Mixed schemes
Dye and Ti:Sa are exchangeable
Increased efficiencies
New elements
Backup solution
Reduction in down time
Keep one dye set up for future, use Ti:Sa instead
New modes of operation – The Dual RILIS
Prerequisite for dual operation: Temporal synchronization pulses of the two laser systems
The Dual-RILIS is unique amongst laser ion sources
http://isolde-project-rilis.web.cern.ch/isolde-project-rilis/

## Slide 15: Part 2
Introduction to ISOLDE and the RILIS installation
  The original CVL pumped dye laser system
  The new Dual TiSa and Dye laser RILIS
Operation of the RILIS in 2012
  Total operating time
  Specifics of Dual RILIS operation
  Highlights and new developments
Outlook and development work for 2013 and CERN LS1
  Practical changes to the RILIS installation
  Scheme development
  Laser system upgrades / changes
  Improved laser beam transport system

## Slide 16
Beam | Sm 2 runs | Ca 2 runs | Cd | At 2 runs | Au 2 runs | Be 3 runs | Dy | Mg 4 runs | Po 2 runs | Ag 2 runs | Zn | Cu | Mn
Planned | 208 | 272 | 192 | 300 | 172 | 446 | 88 | 296 | 206 | 96 | 198 | 112 | 148
Real | 212 | 359 | 253 | 345 | 262 | 278 | 111 | 378 | 206 | 113 | 124 | 69 | 208
Ion beams of 13 elements were produced with RILIS in 2012
Laser ON time in 2012:
3000 h in 2012
Availability of two complementary laser systems (Dye and Ti:Sapphire) has ensured the increase of RILIS beam time in 2011-2012
RILIS operation: 1994-2012
24 separate runs
344 RILIS operator shifts

## Slide 17: RILIS runs in 2012
Ca
Ca
Cd
Cd
Cd
Ca
Ca
Be
Be
Mg
Mg
Po
Po
At
At
Au
Zn
Zn
Cu
Mn
Mn
Be
Sm
At
Au
Sm
Sm
Be
Be
Dy
Dy
Mg
Mg
Po
Ag
ISOLDE RILIS SCHEDULE 2012
RILIS runs in 2012
Sm
At
Au
Sm
Sm
Be
Be
Dy
Dy
Mg
Mg
Po
Ag
Ca
Ca
Cd
Cd
Cd
Ca
Ca
Be
Be
Mg
Mg
Po
Po
At
At
Au
Zn
Zn
Cu
Mn
Mn
Be
http://isolde.web.cern.ch/ISOLDE/

## Slide 18: Highlights 1 - In-source RIS
Reduction of linewidth from >5 GHz  <1GHz
Addition of a thick etalon to the TiSa cavity
Remote dual etalon control, automatic optimization routine and feedback based frequency stabilization
Mass resolution in the range of M/ΔM = 106
MCP is used for direct ion detection with ~1% efficiency: No activity required for detection.
Direct communication with RILIS for cycle triggering and shared data acquisition is established.
R. N. Wolf et al., Nucl. Instr. and Meth. A 686, 82-90 (2012), (MR-TOF)
B.Marsh, V Fedosseev,, R. Rossel, S Rothe, D.Fink, M. Seliverstov, N. Imai et al, EMIS 2012 Proceedings, in preparation (RILIS)
ISOLTRAP MR-TOF isobar separated
ion detection
Dual etalon, narrow line-width Ti:Sa
See talks of Anatoly Barzakh and Maxim Seliversov on Friday

## Slide 19
Daniel Fink (CERN, Univ. Heidelberg) and Sven Richter (Univ. Mainz): PhD work
LIST + UCx run for Fr suppression for laser spectroscopy of Po
1 cm
  Suppression of >1000 for most surface ions
  Ionization efficiency reduction by ≈20x (Mg,Po)
Highlights 2 – LIST operation
Talk by Sven Richter on Friday morning!

## Slide 20
Introduction to ISOLDE and the RILIS installation
  The original CVL pumped dye laser system
  The new Dual TiSa and Dye laser RILIS
Operation of the RILIS in 2012
  Total operating time
  Specifics of Dual RILIS operation
  Highlights and new developments
Outlook and development work for 2013 and CERN LS1
  Practical changes to the RILIS installation
  Scheme development
  Laser system upgrades / changes
  Improved laser beam transport system
Part 3

## Slide 21: Future developments
Investigate RILIS for refractory metals at ISOLDE
Improved RILIS schemes for the Dual RILIS system
IONIZATION SCHEMES
Installation of a reference cell at RILIS
Pulsed amplification of CW seeded Dye laser or TiSa
Improved motorization of Narrow-band TiSa
IN-SOURCE SPECTROSCOPY
Further optimization of LIST
Improving the laser ion time structure or using a time focus for effective beam gating
SELECTIVITY IMPROVEMENTS
Extension of RILIS cabin
  Enlarged entrance/storage and work area to maximize the useable laser laboratory space
Implement a dedicated, high power Nd:YVO4 laser for non resonant ionization
  High beam quality industrial laser could significantly improve efficiency for many schemes.
  Would simplify RILIS setup, increase reliability and reduce setup time.
GENERAL RILIS DEVELOPMENTS
On-call operation
  Installation of a machine protection and monitoring system to reduce reliance on shift-based operation
  To be implemented during LS1
See talk of Tom Day Goodacre
See talk of Sven Richter
See talk of Anatoly Barzakh

## Slide 22: RILIS room extension
254 cm
320 cm
28 m2
6 m2
REX EBIS
RILIS
IS COOLER
HV cage
100 cm
Required for:
Safety
Reference cell installation
Dye handling
Upgrade of beam observation system
Installation of extra YAG laser
Improved ventilation system
Comfort/ergonomics
Existing laser room + SAS
Extended part (SAS)
DESK
REF

## Slide 23: Independent laser for non resonant ionization
Blaze laser installed for a short test at RILIS in Dec 2012
40W at 10 kHz
17ns Pulse
Low Jitter
Gaussian beam
Much better transmission
efficiency to ion source
A similar efficiency improvement should be expected for the 18 RILIS elements that use non-resonant ionization for the final step!
Laser | Laser Power (on table) | Reference beam power in 3 mm aperture | Transport efficiency
Edgewave | 43 W | 370 mW | 33 %
Blaze | 15 W | 350 mW | > 80%
Blaze | 40 W | 800 mW | ~80 %
Power dependent thermal lensing in the beam transport optics is to be eliminated
B. Marsh et al., Suitability test of a high quality Nd:YVO industrial laser for the ISOLDE RILIS installation.
CERN-ATS-Note-2013-007 TECH
Can be used for Dye and Ti:Sa pumping as a back-up laser

## Slide 24: Upgrade of HRS window
1) Window contamination:
Annual window change is required
Difficult to access for change or inspection
2) Thermal lensing:
Defocussing issue for high power beams must be measured and resolved
Solution
Extend the vacuum chamber and mount an adjustable window outside the magnet shielding
Use the internal and external reflections from the window for thermal lens and contamination diagnostics
Problem with existing window

## Slide 25: Machine protection
Dye Leak: Fire hazard; laser damage risk
Up to 6 dye circulators each containing up to 3 L of ethanol flowing at 7 L/min.
Water cooling for Ti:Sa crystals. Water cooling network for each dye circulator. Water cooled pump lasers
Up to 40 W pump beam focused on dye cell. Almost immediate dye cell damage if dye flow stops.
Dye flow interruption: Fire hazard; laser damage risk
Water leak: Equipment damage risk; electrical safety hazard
Action required: Stop pump lasers, alert the laser operator.
Action required: Block pump beam to dye laser, alert the laser operator.
Action required: Stop dye circulator, Stop or block pump laser, alert the laser operator.
Non invasive
dye flow sensor
(ULTRASONIC)
+
NI CompactRIO
MPS
+
Remote controlled
Laser beam
shutter
+
Laser beam shutter
or pump laser switch OFF
using interlock system
RELAY for circulator interlock
Solution to be tested:
Install water leak sensor cables on laser table and RILIS cabin floor
Include sensor data logger in RILIS monitoring system
Organic solvent
detector
(breathalyzer)
+
NI CompactRIO
MPS

## Slide 26: On-call operation
3 requirements for On-Call operation:
3) Automation
2) Performance monitoring
1) Machine protection / safety
This must be a ROBUST system
(PC independent).
+ Alert system to request
operator intervention.
To maintain RILIS performance
therefore reducing the frequency
of operator interventions.
ESSENTIAL
NON ESSENTIAL
Diagram made by Ralf Rossel; the project is being realized in collaboration with EN-STI-ECE

## Slide 27: Acknowledgements
IS511
Shape coexistence in the lightest Tl isotopes studied by laser spectroscopy
http://greybook.cern.ch/programmes/experiments/IS511.html
IS534
Beta-delayed fission, laser spectroscopy and shape-coexistence studies with radioactive At beams
http://greybook.cern.ch/programmes/experiments/IS534.html
IS456
Study of polonium isotopes ground state properties by simultaneous atomic- and nuclear-spectroscopy
http://greybook.cern.ch/programmes/experiments/IS456.html
Spectroscopy with RILIS
Valentine FEDOSSEEV1, Bruce MARSH1, Sebastian ROTHE1, Daniel FINK1,8, Maxim SELIVERSTOV2, Nobuaki IMAI4, Ralf Erik ROSSEL3, Dmitri FEDOROV2, Anatoly BARZAKH2, Pavel MOLKANOV2, Marica Anna SJOEDIN5, Daniele SCARPA6, Sven RICHTER7, Klaus WENDT7
EN-STI-ECE: Alessandro MASI1, Sergio BATUCA1
1CERN 2Petersburg Nuclear Physics Institute (PNPI)
3Hochschule RheinMain, Wiesbaden
4KEK, Japan
5GANIL/CNRS, France
6LNL – INFN, Italy
7Johannes-Gutenberg-Universitaet Mainz
8University of Heidelberg
9University of Manchester
Thomas DAY GOODACRE1,9
Fellow
Knut and Alice Wallenberg Foundation

## Slide 28: Spare slides

## Slide 29: RILIS scheme setup requirements
 |  | Dye laser schemes |  |  |  |  |  |  |  | Ti:Sa schemes |  |  |  |  | 
Element | Setting time* | Step 1 |  | Step 2 |  | Step 3 |  | Efficiency |  | Step 1 |  | Step 2 |  | Step 3 | 
 | days | l1, nm | Dye | l2, nm | Dye/YAG | l3, nm | Dye/YAG | off-line |  | l1, nm | Fundamental | l2, nm | Fundamental | l3, nm | TiSa/YAG
4Be | 3 | 234.9 | Pyridin 1 | 297.3 | Rhod B | – |  | >7% |  | 234.9 | 939.444 |  |  |  | 
12Mg | 2 | 285.2 | Rhod 6G | 552.8 | Fluorescein 27 | 532.1 | YAG | 10% |  | 285.2 | 855.639 | 552.8 |  | 532.1 | YAG
13Al | 2 | 309.3 | Rhod B | 532.1 | YAG | – |  | 20% |  | 309.3 |  | 532.1 |  | – | 
 |  | 308.2 | Rhod B |  |  |  |  |  |  | 308.2 |  |  |  |  | 
20Ca | 2 | 272.2 | ? | 532.1 | YAG | – |  | 0.50% |  | 422.7 | 845.346 |  | Rhod B |  | DCM
21Sc | 2 | 327.4 | Phenox 9 | 719.8 | Pyridin 2 ? | 532.1 | YAG | 15% |  | 327.4 |  | 719.8 |  | 532.1 | YAG
25Mn | 3 | 279.8 | Rhod 6G | 628.3 | DCM | 635.8 | DCM | 19% |  | 279.8 |  | 628.3 |  | 635.8 | 
27Co | 2 | 304.4 | Rhod B | 544.5 | Fluorescein 27 | 532.1 | YAG | >3.8% |  | 304.4 |  | 544.5 |  | 532.1 | YAG
28Ni | 3 | 305.1 | Rhod B | 611.1 | Rhod B | 748.2 | Styr 8 | >6% |  |  | Dye |  | Dye | 748.2 | TiSA
29Cu | 2 | 327.4 | Phenox 9 | 287.9 | Rhod 6G | – |  | >7% |  | 327.4 |  | 287.9 |  | – | 
30Zn | 3 | 213.9 | DCM | 636.2 | DCM | 532.1 | YAG | 4.90% |  | 213.9 | 855.428 | 636.2 | Dye | 532.1 | YAG
31Ga | 2 | 287.4 | Rhod 6G | 532.1 | YAG | – |  | 21% |  | 287.4 |  | 532.1 |  | – | 
 |  | 294.4 | Pyrr 597 |  |  |  |  |  |  | 294.4 |  |  |  |  | 
39Y | 2 | 414.3 | Styr 9 | 662.4 | Phenox 9 | 510.6 | YAG |  |  | 414.3 |  | 662.4 |  | 510.6 | YAG
47Ag | 2 | 328.1 | Phenox 9 | 546.6 | Fluorescein 27 | 532.1 | YAG | 14% |  | 328.1 |  | 546.6 |  | 532.1 | YAG
48Cd | 3 | 228.8 | Pyridin 1 | 643.8 | DCM | 532.1 | YAG | 10.40% |  | 228.8 | 915.208 | 643.8 | Dye | 532.1 | YAG
49In | 2 | 303.9 | Rhod B | 532.1 | YAG | – |  |  |  | 303.9 |  | 532.1 |  | – | 
 |  | 325.6 | Phenox 9 |  |  |  |  |  |  | 325.6 |  |  |  |  | 
50Sn | 4 | 286.3 | Rhod 6G | 811.4 | Styr 9 | 823.5 | Styr 9 | 9% |  | 286.3 | 858.9 | 811.4 | TiSA | 823.5 | TiSA
51Sb | 3 | 217.6 | Phenox 9 | 560.2 | Rhod 6G | 532.1 | YAG | 2.70% |  | 217.6 |  | 560.2 |  | 532.1 | YAG
60Nd | 2 | 588.8 | Rhod B or Pyrr 597 | 596.9 | Rhod B | 596.9 |  |  |  | 588.8 |  | 596.9 |  | 596.9 | 
62Sm | 3 | 600.4 | Rhod B | 675.2 | Phenox 9 | 676.18 | Phenox 9 |  |  | 600.4 |  | 675.2 |  | 676.18 | 
65Tb | 3 | 579.6 | Pyrr 597 | 551.7 | Fluorescein 27 | 618.3 | Rhod B |  |  | 579.6 |  | 551.7 |  | 618.3 | 
66Dy | 2 | 625.9 | DCM | 607.5 | Rhod B | 532.1 | YAG | 20% |  | 625.9 |  | 607.5 |  | 532.1 | YAG
70Yb | 2 | 555.6 | Pyrr 567 | 581.0 | Rhod 6G | 581.0 | Rhod 6G | 15% |  | 555.6 |  | 581.0 |  | 581.0 | 
71Lu |  | 573.7 | Rhod 6G | 642.5 | DCM | 643.5 | DCM |  |  | 451.9 | 903.8 | 460.7 | 921.4 |  | 
79Au | 5 | 267.6 | Coum 540A | 306.5 | DCM | 673.9 | Phenox 9 | >3% |  | 267.6 |  | 306.5 |  | 673.9 | 
80Hg | 3 | 253.7 | Styr 8 | 313.2 | DCM | 626 | DCM |  |  | 253.7 |  | 313.2 |  | 626 | 
81Tl | 2 | 276.8 | Rhod 110 | 532.1 | YAG | – |  | 27% |  | 276.8 |  | 532.1 |  | – | 
82Pb | 2 | 283.3 | Rhod 6G | 600.2 | Rhod B | 532.1 | YAG | >3% |  | 283.3 |  | 600.2 |  | 532.1 | YAG
83Bi | 2 | 306.8 | Rhod B | 555.2 | Fluorescein 27 | 532.1 | YAG | 6% |  | 306.8 |  | 555.2 |  | 532.1 | YAG
84Po | 4 | 255.8 | Styr 8 | 843.4 | Styr 9 | 532.1 | YAG |  |  | 255.8 | 767.403 | 843.4 | TiSA | 532.1 | YAG
85At | 4 | 216.9 | Phenox 9 | 795.4 | Styr 9 | 532.1 | YAG |  |  | 216.9 | 867.6 | 795.4 | TiSA | 532.1 | YAG
 |  | 224.4 | Phenox 9 | 793.2 ? | Styr 9 | 532.1 | YAG |  |  | 224.4 | 897.6 | 793.2 ? | TiSA | 532.1 | YAG

## Slide 30: Ni: Dye-Dye-TiSa
Chart: Wavelength, nm
| 200.0 | 205.0 | 210.0 | 215.0 | 220.0 | 225.0 | 230.0 | 235.0 | 240.0 | 250.0 | 260.0 | 265.0 | 270.0 | 275.0 | 280.0 | 285.0 | 290.0 | 300.0 | 305.0 | 310.0 | 315.0 | 320.0 | 330.0 | 340.0 | 345.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 395.0 | 400.0 | 405.0 | 410.0 | 420.0 | 425.0 | 430.0 | 440.0 | 450.0 | 460.0 | 465.0 | 470.0 | 475.0 | 480.0 | 490.0 | 500.0 | 510.0 | 520.0 | 530.0 | 535.0 | 540.0 | 545.0 | 550.0 | 560.0 | 570.0 | 580.0 | 590.0 | 600.0 | 610.0 | 620.0 | 630.0 | 640.0 | 650.0 | 660.0 | 670.0 | 680.0 | 685.0 | 690.0 | 700.0 | 710.0 | 720.0 | 730.0 | 740.0 | 750.0 | 760.0 | 770.0 | 780.0 | 790.0 | 800.0 | 810.0 | 820.0 | 830.0 | 840.0 | 850.0 | 855.0 | 860.0 | 870.0 | 880.0 | 890.0 | 900.0 | 910.0 | 920.0 | 930.0 | 940.0 | 950.0
TiSa FHG | 25 | 50 | 75 | 75 | 75 | 50 | 25 | 0
Dye THG | 25 | 50 | 100 | 120 | 125 | 125 | 125 | 125 | 125 | 125 | 100 | 80 | 50 | 25
UV-pumped Dye SHG | 20 | 40 | 100 | 100 | 150 | 150 | 200 | 200 | 200 | 150 | 100 | 50
Dye SHG | 500 | 1000 | 1700 | 2000 | 2000 | 2000 | 1800 | 1600 | 1600 | 1600 | 1500 | 1400 | 1300 | 1250 | 1200 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 500 | 100
TiSa THG | 50 | 100 | 125 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 125 | 100 | 50
TiSa SHG | 500 | 800 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 900 | 900 | 900 | 900 | 900 | 800 | 800 | 800 | 800 | 700 | 500
UV-pumped Dye Fundamental | 250 | 500 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 500 | 300 | 200 | 100
Dye Fundamental | 100 | 1000 | 5000 | 7500 | 10000 | 15000 | 18000 | 20000 | 18000 | 15000 | 15000 | 15000 | 15000 | 12000 | 10000 | 8000 | 8000 | 8000 | 6000 | 6000 | 6000 | 5000 | 4000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 1500 | 500
TiSa fundamental | 2000 | 2500 | 3000 | 4000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 4500 | 4500 | 4500 | 4500 | 4500 | 4300 | 4000 | 4000 | 4000 | 3500 | 3500 | 3500 | 3000 | 2500 | 2000
Ni
305 nm
Dye SHG
611 nm
Dye fund
748 nm
TiSa fund
Step 1
Step 2
Step 3
Higher power from TiSa for AIS transition

## Slide 31: Ca: TiSa-dye-dye
Chart: Wavelength, nm
| 200.0 | 205.0 | 210.0 | 215.0 | 220.0 | 225.0 | 230.0 | 235.0 | 240.0 | 250.0 | 260.0 | 265.0 | 270.0 | 275.0 | 280.0 | 285.0 | 290.0 | 300.0 | 305.0 | 310.0 | 315.0 | 320.0 | 330.0 | 340.0 | 345.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 395.0 | 400.0 | 405.0 | 410.0 | 420.0 | 425.0 | 430.0 | 440.0 | 450.0 | 460.0 | 465.0 | 470.0 | 475.0 | 480.0 | 490.0 | 500.0 | 510.0 | 520.0 | 530.0 | 535.0 | 540.0 | 545.0 | 550.0 | 560.0 | 570.0 | 580.0 | 590.0 | 600.0 | 610.0 | 620.0 | 630.0 | 640.0 | 650.0 | 660.0 | 670.0 | 680.0 | 685.0 | 690.0 | 700.0 | 710.0 | 720.0 | 730.0 | 740.0 | 750.0 | 760.0 | 770.0 | 780.0 | 790.0 | 800.0 | 810.0 | 820.0 | 830.0 | 840.0 | 850.0 | 855.0 | 860.0 | 870.0 | 880.0 | 890.0 | 900.0 | 910.0 | 920.0 | 930.0 | 940.0 | 950.0
TiSa FHG | 25 | 50 | 75 | 75 | 75 | 50 | 25 | 0
Dye THG | 25 | 50 | 100 | 120 | 125 | 125 | 125 | 125 | 125 | 125 | 100 | 80 | 50 | 25
UV-pumped Dye SHG | 20 | 40 | 100 | 100 | 150 | 150 | 200 | 200 | 200 | 150 | 100 | 50
Dye SHG | 500 | 1000 | 1700 | 2000 | 2000 | 2000 | 1800 | 1600 | 1600 | 1600 | 1500 | 1400 | 1300 | 1250 | 1200 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 500 | 100
TiSa THG | 50 | 100 | 125 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 125 | 100 | 50
TiSa SHG | 500 | 800 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 900 | 900 | 900 | 900 | 900 | 800 | 800 | 800 | 800 | 700 | 500
UV-pumped Dye Fundamental | 250 | 500 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 500 | 300 | 200 | 100
Dye Fundamental | 100 | 1000 | 5000 | 7500 | 10000 | 15000 | 18000 | 20000 | 18000 | 15000 | 15000 | 15000 | 15000 | 12000 | 10000 | 8000 | 8000 | 8000 | 6000 | 6000 | 6000 | 5000 | 4000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 1500 | 500
TiSa fundamental | 2000 | 2500 | 3000 | 4000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 4500 | 4500 | 4500 | 4500 | 4500 | 4300 | 4000 | 4000 | 4000 | 3500 | 3500 | 3500 | 3000 | 2500 | 2000
Ca
423 nm
TiSa SHG
586 nm
Dye fund
654 nm
Dye fund
Step 1
Step 2
Step 3
Higher power from TiSa for Step 1
~50W @ 532 nm to pump dye laser for AIS search for step 3 – new scheme found

## Slide 32
Chart: Wavelength, nm
| 200.0 | 205.0 | 210.0 | 215.0 | 220.0 | 225.0 | 230.0 | 235.0 | 240.0 | 250.0 | 260.0 | 265.0 | 270.0 | 275.0 | 280.0 | 285.0 | 290.0 | 300.0 | 305.0 | 310.0 | 315.0 | 320.0 | 330.0 | 340.0 | 345.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 395.0 | 400.0 | 405.0 | 410.0 | 420.0 | 425.0 | 430.0 | 440.0 | 450.0 | 460.0 | 465.0 | 470.0 | 475.0 | 480.0 | 490.0 | 500.0 | 510.0 | 520.0 | 530.0 | 535.0 | 540.0 | 545.0 | 550.0 | 560.0 | 570.0 | 580.0 | 590.0 | 600.0 | 610.0 | 620.0 | 630.0 | 640.0 | 650.0 | 660.0 | 670.0 | 680.0 | 685.0 | 690.0 | 700.0 | 710.0 | 720.0 | 730.0 | 740.0 | 750.0 | 760.0 | 770.0 | 780.0 | 790.0 | 800.0 | 810.0 | 820.0 | 830.0 | 840.0 | 850.0 | 855.0 | 860.0 | 870.0 | 880.0 | 890.0 | 900.0 | 910.0 | 920.0 | 930.0 | 940.0 | 950.0
TiSa FHG | 25 | 50 | 75 | 75 | 75 | 50 | 25 | 0
Dye THG | 25 | 50 | 100 | 120 | 125 | 125 | 125 | 125 | 125 | 125 | 100 | 80 | 50 | 25
UV-pumped Dye SHG | 20 | 40 | 100 | 100 | 150 | 150 | 200 | 200 | 200 | 150 | 100 | 50
Dye SHG | 500 | 1000 | 1700 | 2000 | 2000 | 2000 | 1800 | 1600 | 1600 | 1600 | 1500 | 1400 | 1300 | 1250 | 1200 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 500 | 100
TiSa THG | 50 | 100 | 125 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 125 | 100 | 50
TiSa SHG | 500 | 800 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 900 | 900 | 900 | 900 | 900 | 800 | 800 | 800 | 800 | 700 | 500
UV-pumped Dye Fundamental | 250 | 500 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 500 | 300 | 200 | 100
Dye Fundamental | 100 | 1000 | 5000 | 7500 | 10000 | 15000 | 18000 | 20000 | 18000 | 15000 | 15000 | 15000 | 15000 | 12000 | 10000 | 8000 | 8000 | 8000 | 6000 | 6000 | 6000 | 5000 | 4000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 1500 | 500
TiSa fundamental | 2000 | 2500 | 3000 | 4000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 4500 | 4500 | 4500 | 4500 | 4500 | 4300 | 4000 | 4000 | 4000 | 3500 | 3500 | 3500 | 3000 | 2500 | 2000
Mg
285 nm
Dye SHG
553 nm
Dye fund
532 nm
Nd:YAG SHG
Step 2
Step 1
Mg: Dye-Dye-YAG
Dye only: TiSa is available for preparation for the next RILIS element

## Slide 33
Chart: Wavelength, nm
| 200.0 | 205.0 | 210.0 | 215.0 | 220.0 | 225.0 | 230.0 | 235.0 | 240.0 | 250.0 | 260.0 | 265.0 | 270.0 | 275.0 | 280.0 | 285.0 | 290.0 | 300.0 | 305.0 | 310.0 | 315.0 | 320.0 | 330.0 | 340.0 | 345.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 395.0 | 400.0 | 405.0 | 410.0 | 420.0 | 425.0 | 430.0 | 440.0 | 450.0 | 460.0 | 465.0 | 470.0 | 475.0 | 480.0 | 490.0 | 500.0 | 510.0 | 520.0 | 530.0 | 535.0 | 540.0 | 545.0 | 550.0 | 560.0 | 570.0 | 580.0 | 590.0 | 600.0 | 610.0 | 620.0 | 630.0 | 640.0 | 650.0 | 660.0 | 670.0 | 680.0 | 685.0 | 690.0 | 700.0 | 710.0 | 720.0 | 730.0 | 740.0 | 750.0 | 760.0 | 770.0 | 780.0 | 790.0 | 800.0 | 810.0 | 820.0 | 830.0 | 840.0 | 850.0 | 855.0 | 860.0 | 870.0 | 880.0 | 890.0 | 900.0 | 910.0 | 920.0 | 930.0 | 940.0 | 950.0
TiSa FHG | 25 | 50 | 75 | 75 | 75 | 50 | 25 | 0
Dye THG | 25 | 50 | 100 | 120 | 125 | 125 | 125 | 125 | 125 | 125 | 100 | 80 | 50 | 25
UV-pumped Dye SHG | 20 | 40 | 100 | 100 | 150 | 150 | 200 | 200 | 200 | 150 | 100 | 50
Dye SHG | 500 | 1000 | 1700 | 2000 | 2000 | 2000 | 1800 | 1600 | 1600 | 1600 | 1500 | 1400 | 1300 | 1250 | 1200 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 500 | 100
TiSa THG | 50 | 100 | 125 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 125 | 100 | 50
TiSa SHG | 500 | 800 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 900 | 900 | 900 | 900 | 900 | 800 | 800 | 800 | 800 | 700 | 500
UV-pumped Dye Fundamental | 250 | 500 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 500 | 300 | 200 | 100
Dye Fundamental | 100 | 1000 | 5000 | 7500 | 10000 | 15000 | 18000 | 20000 | 18000 | 15000 | 15000 | 15000 | 15000 | 12000 | 10000 | 8000 | 8000 | 8000 | 6000 | 6000 | 6000 | 5000 | 4000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 1500 | 500
TiSa fundamental | 2000 | 2500 | 3000 | 4000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 4500 | 4500 | 4500 | 4500 | 4500 | 4300 | 4000 | 4000 | 4000 | 3500 | 3500 | 3500 | 3000 | 2500 | 2000
Po
256 nm
Dye THG
843 nm
TiSa fund
532 nm
Nd:YAG SHG
Po: Dye-TiSa-YAG
Higher power from TiSa for Step 2, narrow line-width TiSa for spectroscopy

## Slide 34
Chart: Wavelength, nm
| 200.0 | 205.0 | 210.0 | 215.0 | 220.0 | 225.0 | 230.0 | 235.0 | 240.0 | 250.0 | 260.0 | 265.0 | 270.0 | 275.0 | 280.0 | 285.0 | 290.0 | 300.0 | 305.0 | 310.0 | 315.0 | 320.0 | 330.0 | 340.0 | 345.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 395.0 | 400.0 | 405.0 | 410.0 | 420.0 | 425.0 | 430.0 | 440.0 | 450.0 | 460.0 | 465.0 | 470.0 | 475.0 | 480.0 | 490.0 | 500.0 | 510.0 | 520.0 | 530.0 | 535.0 | 540.0 | 545.0 | 550.0 | 560.0 | 570.0 | 580.0 | 590.0 | 600.0 | 610.0 | 620.0 | 630.0 | 640.0 | 650.0 | 660.0 | 670.0 | 680.0 | 685.0 | 690.0 | 700.0 | 710.0 | 720.0 | 730.0 | 740.0 | 750.0 | 760.0 | 770.0 | 780.0 | 790.0 | 800.0 | 810.0 | 820.0 | 830.0 | 840.0 | 850.0 | 855.0 | 860.0 | 870.0 | 880.0 | 890.0 | 900.0 | 910.0 | 920.0 | 930.0 | 940.0 | 950.0
TiSa FHG | 25 | 50 | 75 | 75 | 75 | 50 | 25 | 0
Dye THG | 25 | 50 | 100 | 120 | 125 | 125 | 125 | 125 | 125 | 125 | 100 | 80 | 50 | 25
UV-pumped Dye SHG | 20 | 40 | 100 | 100 | 150 | 150 | 200 | 200 | 200 | 150 | 100 | 50
Dye SHG | 500 | 1000 | 1700 | 2000 | 2000 | 2000 | 1800 | 1600 | 1600 | 1600 | 1500 | 1400 | 1300 | 1250 | 1200 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 500 | 100
TiSa THG | 50 | 100 | 125 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 125 | 100 | 50
TiSa SHG | 500 | 800 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 900 | 900 | 900 | 900 | 900 | 800 | 800 | 800 | 800 | 700 | 500
UV-pumped Dye Fundamental | 250 | 500 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 500 | 300 | 200 | 100
Dye Fundamental | 100 | 1000 | 5000 | 7500 | 10000 | 15000 | 18000 | 20000 | 18000 | 15000 | 15000 | 15000 | 15000 | 12000 | 10000 | 8000 | 8000 | 8000 | 6000 | 6000 | 6000 | 5000 | 4000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 1500 | 500
TiSa fundamental | 2000 | 2500 | 3000 | 4000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 4500 | 4500 | 4500 | 4500 | 4500 | 4300 | 4000 | 4000 | 4000 | 3500 | 3500 | 3500 | 3000 | 2500 | 2000
At
216 nm
Dye THG
795 nm
TiSa fund
532 nm
Nd:YAG SHG
Step 1
Step 2
Step 3
Higher power from TiSa for Step 2
Dye and TiSa exchangeable for Step 1
At: Dye(TiSa)-TiSa-YAG
~50W @ 532 nm for Step 3

## Slide 35
Chart: Wavelength, nm
| 200.0 | 205.0 | 210.0 | 215.0 | 220.0 | 225.0 | 230.0 | 235.0 | 240.0 | 250.0 | 260.0 | 265.0 | 270.0 | 275.0 | 280.0 | 285.0 | 290.0 | 300.0 | 305.0 | 310.0 | 315.0 | 320.0 | 330.0 | 340.0 | 345.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 395.0 | 400.0 | 405.0 | 410.0 | 420.0 | 425.0 | 430.0 | 440.0 | 450.0 | 460.0 | 465.0 | 470.0 | 475.0 | 480.0 | 490.0 | 500.0 | 510.0 | 520.0 | 530.0 | 535.0 | 540.0 | 545.0 | 550.0 | 560.0 | 570.0 | 580.0 | 590.0 | 600.0 | 610.0 | 620.0 | 630.0 | 640.0 | 650.0 | 660.0 | 670.0 | 680.0 | 685.0 | 690.0 | 700.0 | 710.0 | 720.0 | 730.0 | 740.0 | 750.0 | 760.0 | 770.0 | 780.0 | 790.0 | 800.0 | 810.0 | 820.0 | 830.0 | 840.0 | 850.0 | 855.0 | 860.0 | 870.0 | 880.0 | 890.0 | 900.0 | 910.0 | 920.0 | 930.0 | 940.0 | 950.0
TiSa FHG | 25 | 50 | 75 | 75 | 75 | 50 | 25 | 0
Dye THG | 25 | 50 | 100 | 120 | 125 | 125 | 125 | 125 | 125 | 125 | 100 | 80 | 50 | 25
UV-pumped Dye SHG | 20 | 40 | 100 | 100 | 150 | 150 | 200 | 200 | 200 | 150 | 100 | 50
Dye SHG | 500 | 1000 | 1700 | 2000 | 2000 | 2000 | 1800 | 1600 | 1600 | 1600 | 1500 | 1400 | 1300 | 1250 | 1200 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 500 | 100
TiSa THG | 50 | 100 | 125 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 125 | 100 | 50
TiSa SHG | 500 | 800 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 900 | 900 | 900 | 900 | 900 | 800 | 800 | 800 | 800 | 700 | 500
UV-pumped Dye Fundamental | 250 | 500 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 750 | 500 | 300 | 200 | 100
Dye Fundamental | 100 | 1000 | 5000 | 7500 | 10000 | 15000 | 18000 | 20000 | 18000 | 15000 | 15000 | 15000 | 15000 | 12000 | 10000 | 8000 | 8000 | 8000 | 6000 | 6000 | 6000 | 5000 | 4000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 1500 | 500
TiSa fundamental | 2000 | 2500 | 3000 | 4000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 4500 | 4500 | 4500 | 4500 | 4500 | 4300 | 4000 | 4000 | 4000 | 3500 | 3500 | 3500 | 3000 | 2500 | 2000
Au
268 nm
TiSa THG
306 nm
Dye SHG
674 nm
Dye fund
Step 1
Step 2
Step 3
Higher power from TiSa for Step 1
Au: TiSa-Dye-Dye
~50W @ 532 nm to pump dye laser for Step 3