## Slide 1
ALTO Laser Ion Source
Ruohong Li, Serge Franchoo, Christophe Lau
LA3NET Feb 22, 2013

## Slide 2
Neutron number
Proton number
High resolution mass separators
Laser ionization
Ground State
Ionization Potential
Rydberg states
Thermal photos/
electric field
Auto-ionizing state
Resonance laser ion source
Good ionization efficiency
Z selectivity

## Slide 3
ALTO LINAC
10uA, 50 MeV electron beam
Neutron rich nuclei productions
No contamination from the isobars of neutron deficient nuclei
High productivity around two closed shells N=50 and N=82
β decay of neutron rich nuclei around N=50 and N=82 at ALTO
e- induced photofission
1011 fissions/second

## Slide 4
electron beam
uranium carbide target
extracted ion beam
photofission
ionisation
ISOLDE -type ion source

## Slide 5
e-LINAC
mass separator
Target and ion source
Laser lab

## Slide 6
Pump laser: Nd:YAG laser ( 532nm, 100W )
Two new Radiant Dyes lasers (540-850nm, typically ~8W @ 30W pump laser, ~10ns pulse width and ~3GHz linewidth )
BBO doubling units (270-425nm, typically hundreds mW )
Laser system

## Slide 7
Dye laser
Dye laser
Pump laser
2 X
2 X
ionizer
Up stairs
Down stairs
Mass separator

## Slide 8
18 W at source (transmission = 67%)
120 mW at source (transmission = 24%)
34 781.6 cm-1
826.2 cm-1
cm-1
48387.6 cm-1
x 10
Ga isotopes on-line delivery in 2011
532 nm
287nm
X10 enhancement in ionization
efficiency compared to surface ionization
laser ionization ε~10% & 10 µA
& Z selectivity
blue: surface ionization ε~1%& 1 µA
84Ga->84Ge

## Slide 9
Stable Ga (mass=69) in 2012
34 781.6 cm-1
826.2 cm-1
cm-1
48387.6 cm-1
532 nm
287nm
Two new dye lasers (Radiant Dye)
Collaborated with ISOLDE (Bruce March & Kieran Flanagan)
55.3 %
44.7 %
x 17
287nm (300mW) | 532nm (~10W) | Ions (nA)
off | off | 1.3
√ | off | 1.3
off | √ | 1.3
√ | √ | 22

## Slide 10
Radioactive Ga (mass=82) in 2012
34 781.6 cm-1
826.2 cm-1
cm-1
48387.6 cm-1
532 nm
287nm
ionized both from the ground state (0 cm-1) and metastable state (826.2 cm-1)
55.3 %
44.7 %
294 nm
287nm (250mW) | 294nm (130mW) | 532nm (~10W) | Ions (pA)
off | off | off | 50
√ | off | √ | 150
off | √ | √ | 220
√ | √ | √ | 305
laser enhancement dropped from X18 to X3 with the 287nm+532nm scheme
efforts were made: optimize the alignments of lasers, check the synchronization of the laser pulses, check the wavelength by taking the resonance curve, check the saturation of the atomic transition by the saturation curve.
more beam diagnostics—installing MCP in the beam line to check the pulse temporal profile.

## Slide 11
Off-line reference cell
Develop unknown laser ionization schemes
Test the ionization schemes before on-line runs
Collaborate with : Mainz University Tobias Kron, Klaus Wendt
IPN design office: Fabien Leseigneur , Denis Reynet
oven
laser
laser
Electron multiplier
Pump

## Slide 12
Example: Tellurium(Te) scheme development
Tripling unit
214.281 nm (air) a
< 384 nm
0 cm-1
46652.738 cm-1
IP 72667.8(8) cm-1
5p4 3P J=2
5p3(4So)6s 3So J=1
5p3(4So)6s 5So J=2
44253.000 cm-1
A=3.12 X108
225.903 nm (air) a
A=1.28 X107
63556.7 cm-1
-- 68603.6 cm-1 b
AI
532 nm
540nm-591 nm b
Scan from 384.404nm(1st step 214nm) / 351.929nm (1st step 225nm) to lower wavelength
Nonresonance
Nonresonance
AI resonant ionization
Collaborate with ISOLDE
AI/ Rydberg
3rd laser

## Slide 13
Build and test the reference cell (collaborate with Mainz University)
Instrument and optics upgrading: new wavemeter, transport mirrors and focusing lens for broader wavelength range.
Develop and test Zn and Te ionization schemes (tripling unit: collaborate with ISOLDE)
Develop the function of Second harmonic scanning of the dye lasers.
2013 On-line beam delivery of Zn
Plan in 2013

## Slide 14
Merci beaucoup!
Thank you!