## Slide 1: The LHC accelerator complex
Lucio Rossi – CERN
HiLumi LHC Project Coordinator
The biggest accelerators in space and on earth
Organised by COAST, CERN-TH and CERN-LPCC
CERN, 18 March 2013

## Slide 2: Accelerators?
Name accelerator applies only for the first part
«Ponderator» was proposed to replace «accelerator» in 1948
But of course not likeable so accelerator remains.

## Slide 3: Accelerators gain us one frontier of the physics spectrum
Why accelerators? To investigate Particle Physics
Particle physics looks at matter in its smallest dimensions and accelerators are very fine microscope or, better, atto-scope!
 = h/p ; @LHC: T = 1 TeV    10-18 m
Accelerators
Microscopes
Optical, radio télescopes
Binoculars

## Slide 4: …back to Big Bang
But we are left with the task of explaining how the rich complexity that developed in the ensuing 13.7 billion years came about…
Which is a much more complex task!
Trip back toward the Big Bang: ts1/E2Gev
T  1 ps for single particle creation
T  1 s for collective phenomena QGS (Quark-Gluon Soup)

## Slide 5: Accelerators: the two frontiers
High Precision Frontier
Known phenomena studied
with high precision may show
inconsistencies with theory
High Energy Frontier
New phenomena
(new particles)
created when the
“usable” energy > mc2 [×2]
2 routes to new knowledge about the
fundamental structure of the matter

## Slide 6: What do we need to make progress?
To reach higher energy, i.e., go beyond the LEP/Tevatron energy scale ~100-300GeV
The Large Hadron Collider: using composite particles (p-p) at high energy 7+7 TeV: 0.1-1.5 TeV (and more)
The Linear Electron-Positron Collider will use of e+ e- annichilation 0.25+0.25 TeV: 0.5 TeV with more accuracy
pp “Floodlight”
e+e-

## Slide 7: The method of HEP colliders
Methods of Particle Physics
3) Identify created particles in
Detector (search for new clues)
1) Concentrate energy on particles (accelerator)
2) Collide particles (recreate conditions after Big Bang)
And both of them need high technology like superconductivityy

## Slide 8: Use of e.m. and magentic fields RF fields bunch the beam

## Slide 9: Linear accelerator: Linac E = G x L (GeV; MV/m; km)
Alvarez linac – the first practical linac 32 MeV at Berkeley 1946:
Particle gains energy at each gap.
Drift tube lengths follow increasing velocity.
The periodicity becomes regular as v apporaches c.
His choice of 200 MHz became a de facto standard for many decades.

## Slide 10: Circular accelerators: synchrotrons E  0.3 B R (TeV; T; km)

## Slide 11: Livingstone plot (equivalent fixed target energy)
In this scale we have been able to sustain an exponential growth
However when translated, in useful energy (c.o.m.) the progress is less glorious…

## Slide 12: Energy is not all for a particle beam : emittance

## Slide 13: Emittance is constant (unless friction and instabilities):

## Slide 14: β-function and beam size

## Slide 15: Recap of main properties
Energy
Intensity of beam: number of particle circulating or bunch population Np
Emittance : decrease with energy so we define a normalized one: n =   that is constant (unless instabilities and heatings)
β : focalization length (β* at IP of colliders)
xy (transverse cross section) = β
Brightness: density of partic¨le in the phase space (Np/)

## Slide 16: CERN proton accelerator chain
LHC : 2x(0.45 – 7) TeV
SPS : 26 – 450 GeV
PS : 1.4 - 26 GeV
PSB : 0.05 -1.4 GeV
Linac: 0-50 MeV

## Slide 17: SOURCE and LINAC2
Duoplasmatron source
Linac2 : in evidence the accelerating RF structure

## Slide 18: Upgrade : LINAC4 (2015-16 ?) H- and 160 MeV
Equipment hall
Accelerator tunnel
Surface building

## Slide 19: PSB (Booster): 1.4 GeV
Magnetic structure of PSB
Length : 150 m
Actually are four rings. Each beam is injected in the PS

## Slide 20: The PS complex: injector for LHC and much more…

## Slide 21: PSB upgrade to 2 GeV: brightness 
160 MeV H- injection
Doubling of density in transverse phase planes
Increased intensity
2 GeV upgrade
Courtesy R. Garoby

## Slide 22: PS: 28 GeV
PS ring (magnetic structure)
PS 200 MHz system and 10 MHz system (1/10)

## Slide 23: PS: generation of LHC beam
Each bunch from the PSB is divided by 12 → 6 x 3 x 2 x 2

## Slide 24: PS upgrade (minor)
Increased transverse brightness
2 GeV injection
Increased intensity / bunch
Radioprotection
J.B. Adams – 25 Nov. 1959 – Design intensity: 3 1011 p/p
Courtesy R. Garoby

## Slide 25: SPS: 450 GeV proton beam (in the 1980’s worked as p-pbar)
SPS tunnel (almost 7 km)
SPS complex with experimental area

## Slide 26: SPS upgrade
One four sections cavity
(four power couplers and two terminating power loads)
One section = 11 drift tubes
Increased transverse brightness
Increased intensity
200 MHz Travelling Wave Accelerating Structures
Courtesy R. Garoby

## Slide 27: CERN’s particle accelerator chain: 40 km of tunnels (rings and transfer lines)
2004: The 20 member states
From LINAC to LHC…
?
?
?
?
H

## Slide 28: CERN European Organization for Nuclear Research
2004: The 20 member states

## Slide 29: Superconducting accelerators
Circular Accelerators
  Ebeam = 0.3 B r [GeV] [T] [m]
   superconducting bending and focussing magnets
    high-energy hadron synchrotrons
Linear Accelerators
  Ebeam = E L [MeV] [MV/m] [m]
   superconducting acceleration cavities
    high-energy e+-e-linacs
Rationale for superconductivity in accelerators

## Slide 30: SC: an enabling technology
The LHC has a circumference of 26.7 km, out of which some 20 km of main superconducting magnets operating at 8.3 T. Cryogenics will consume about 40 MW electrical power from the grid.
If the LHC were not superconducting:
If it used resistive magnets operating at 1.8 T (limited by iron saturation), the circumference would have to be about 100 km, and the electrical consumption 900 MW (a good-size nuclear power plant), leading to prohibitive capital and operation costs.
Rationale for superconductivity in accelerators

## Slide 31: Cost structure of the LHC
Total material cost: about 2.5 G€
Magnet+cryogenics = 66%

## Slide 32: LHC dipole magnet
1232 dipole magnets, 15 m long
B field 8.3 T (11.8 kA) @ 1.9 K (super-fluid Helium) – after incident operated up to ~4.7 T  interconnect consolidation during Long Shut-down 2013-2014
2 magnets-in-one design : two beam tubes with an opening of 56 mm.
Operating challenges:
  Dynamic field changes at injection.
  Very low quench levels (~ mJ/cm3)

## Slide 33: LHC: 24 km of 10,000 SC magnets … but much more than magnets
400 MHz SCRF cavities (2x 15 m)
Cryogenics
Kickers for injection
Collimators to clean > 99.9% of the losses
CERN Control Center

## Slide 34
The LHC beam energy is 350 MJ. Already at injection the beam can damage a magnet.
The power of the LHC beams

## Slide 35: After energy, luminosity is the most important parameter of a collider
pp cross section
LHC - 14 TeV

## Slide 36: Luminosity: main ingredients
energy
Beam current
Beam size
Beam current and emittance: involve Inj chain and whole ring
β involve «only» 2 IRs, 600 m.

## Slide 37: Beam envelope scales as 1/β at IPs
Low-β quadrupole triplet

## Slide 38: Integrated Luminosity in LHC (fb-1)
In 2011: at 7 TeV accumulated 5.6 fb-1
In 2012: at 8 TeV accumulated almost 25 fb-1

## Slide 39: Possible evolution of luminosity Full Upgrade: High Luminosity LHC
Shut down to fix interconnects and overcome energy limitation (LHC incident of Sept 2008) and R2E
Shut down to overcome beam intensity limitation (Injectors, collimation and more…)
Full upgrade

## Slide 40: Magnets: 11 T dipoles, 12-13 Quads Crab Cavities : femtosecond accuracy SC links: 150-200 kA, 5 kV, 300-700 long New cryogenic plants and other equipment

## Slide 41: HL-LHC: Change > 1.2 km of LHC…
Works all around the ring
LHCb and Alice not considered for the moment

## Slide 42: Some of the hardware to change…

## Slide 43
27 km tunnel, 4 x12 kW refrigerators

## Slide 44
8 x18 kW 4.2 K refrigerators
8 2.5 kW 1.9 K refrigerators
12 x 13 kA Testing bench
Large SC test facility
2000x7-15 m SC magnets

## Slide 45
2x18 kW 4.2 K + 2 2.5 kW 1.9K
20x 11 T twin dipoles
20 large 13 T quadrupoles & dipoles
Sc test faciltiy at 30 kA -13 T
SC cable for 1 GW d.c. power transmission
First unit of 3 kA in MgB2 and YBCO sucessfully tested

## Slide 47: Main technology is dipole magnets: is it possible ?
Looking at performance offered by practical SC, considering tunnel size and basic engineering (forces, stresses, energy) the practical limits is around 20 T.
Nb-Ti operating dip;
Nb3Sn block test dip
Nb3Sn cos test dip

## Slide 48: The superconductor space
Chart: Applied Field (T)
| 0 | 5 | 15 | 20 | 25 | 30
YBCO: Parallel to tape plane, 4.2 K | 4144.6766 | 3507.9375 | 3148.3332 | 2909.0554 | 2090.4933 | 1888.9952
YBCO: Perpendicular to tape plane, 4.2 K | 4144.6766 | 1445.8386 | 975.0997 | 767.7508 | 655.6687 | 571.6114 | 526.7777 | 481.944 | 442.7183 | 428.1462 | 403.4904 | 386.6773 | 364.2626 | 341.8457 | 328.3952 | 319.4289 | 318.3073
2212: Round wire, 4.2 K | 1265.6716 | 1257.7114 | 1257.7114 | 1225.8706 | 1181.0945 | 1126.3682 | 1040.796 | 973.1343 | 929.3532 | 835.8209 | 780.0995 | 704.4776 | 623.8806 | 577.7114 | 529.3532 | 513.4328 | 509.4527 | 489.5522 | 469.6517 | 453.7313 | 435.8209 | 416.9154 | 398.01 | 380.0995 | 364.1791 | 347.2637 | 330.3483 | 315.4229 | 298.5075 | 282.5871 | 265.4726
Nb3Sn: High Energy Physics, 4.2 K | 1754.8557 | 1454.9349 | 1190.9814 | 1072.6374 | 957.7741 | 855.0933 | 757.6336 | 268.0143 | 190.8587 | 118.9241 | 65.5533 | 28.3097
Nb-Ti (LHC) 1.9 K | 1430 | 1195.7692 | 950.7692 | 703.4615 | 475.7692
Nb-Ti
Nb3Sn
HTS

## Slide 49: The « new » materials 1 – Nb3Sn
Recent 23.4 T (1 GHz) NMR Magnet for spectroscopy in Nb3Sn (and Nb-Ti). 15-20 tons/year for NMR and HF solenoids. Experimental MRI is taking off
ITER: 500 t in 2010-2015! It is comparable to LHC!
HEP ITD (Internal Tin Diffusion):
  High Jc., 3xJc ITER
  Large filament (50 µm), large coupling current...
  Cost is 5 times LHC Nb-Ti
0.7 mm, 108/127 stack RRP from Oxford OST
1 mm, 192 tubes PIT from Bruker EAS

## Slide 50: The successful cable as result of 5 –y R&D (FP6-CARE-NED)
1.25 mm PIT strand, 14 strands @ CERN 2011
Thermo-magnetic instability and FQ issues will continue to play a major role.
However the route is traced and we can expect that in the next 5-6 years , also thanks to HiLumi R&D and industrialization, Nb3Sn for HEP will be consolidated.
Jc is the only Sc current density at 12 T (reference point)
Courtesy L. Bottura

## Slide 51: The « new » materials: HTS Bi-2212
DOE program 2009-11 in USA let to a factor 2 gain. We need another 50% and more uniformity, eliminating porosity and leakage
Round wire, isotropous and suitable to cabling!
HEP only users (good < 20K and for compact cable)
Big issue: very low strain resistance, brittle
Production ~ 0,
cost ~ 2-5 times Nb3Sn (Ag stabilized)

## Slide 52: The « new » materials: HTS YBCO
Tape of 0.1-0.2 mm x 4-10 mm : difficult for compact (>85%) cables
Current is EXCELENT but serious issue is the anisotropy;
>90% of world effort on HTS are on YBCO! Great synergy with all community
Cost : today is 10 times Nb3Sn, target is same price: components not expensive, process difficult to be industrialize at low cost
FP7 Eucard is developing EU Ybco

## Slide 53: New (old) approach to cabling suitable for tapes
An old type of cabling (Roebel) suitable for tapes has been recently rivisited (Karlsruhe, New Research Industry NZ)
Here a first 2 m long test cable done at CERN

## Slide 54: First consistent cross section, 2010 WG and Malta (fits our tunnel)
Magnet design: 40 mm bore (depends on injection energy: > 1 Tev) Very challenging but feasable: 300 mm inter-beam; anticoils to reduce flux
Approximately 2.5 times more SC than LHC: 3000 tonnes!
L. Rossi and E. Todesco

## Slide 55: LHC→HE-LHC/VHE-LHC (F. Zimmerman)
E. Todesco, L. Rossi, P.. McIntyre
HE-LHC: in LHC tunnel (2035-)
ECoM=33 TeV,x1034cm-2s-1
VHE-LHC: new 80 km tunnel (2040?)
ECoM=84-104 TeV,x1034cm-2s-1
J. Osborne, C. Waaijer, S. Myers
LHC is the 1st Higgs factory!
ECoM=8-14 TeV,1034cm-2s-1
total cross section at 8 TeV: 22 pb
1 M Higgs produced so far – more to come
15 H bosons / min – and more to come
20-T dipole magnet
80 km tunnel
8  14 TeV: ggH x1.5
14  33 TeV: HH x6
HL-LHC (~2022-2030)
will deliver ~9x more H bosons!
ECoM=14 TeV,5x1034cm-2s-1
with luminosity leveling
F. Cerutti, P. Janot
16-T or 20-T magnets
HH x42
- pushes magnet technology!
Notes: HELHC

## Slide 56
«Pre-Feasibility Study for an 80-km tunnel at CERN»
John Osborne and Caroline Waaijer,
CERN, ARUP & GADZ, submitted to ESPG
80-km tunnel in Geneva area – “best” option
even better
100 km?
F. Zimmermann

## Slide 57: Is there a limit? Think bigger!
Thanks for your attention !