## Slide 1: Big Data over a 100G Network at Fermilab
Gabriele Garzoglio Grid and Cloud Services Department
Computing Sector, Fermilab
CHEP 2013 – Oct 15, 2013

## Slide 2: Overview
Network R&D Program Motivations and Overview
Network Infrastructure Production and R&D
100G Network R&D Program
Results and Plans

## Slide 3: Fermilab Users and 100G
Using the network for decades in the process of scientific discovery for sustained, high speed, large and wide-scale distribution of and access to data
  High Energy Physics community
  Multi-disciplinary communities using grids (OSG, XSEDE)
Figures of merit
  113 Petabytes written to tape, today mostly coming from offsite
  170Gbps peak LAN traffic from archive to local processing farms
  LHC peak WAN usage in/out of Fermilab at 20-30 Gbps
Compact Muon Solenoid (CMS) routinely peaks at 20-30 Gbps for WAN traffic in/out of Fermilab.
113 PB of data ever written to the Enstore tape archive
20 Gpbs
CMS WAN Traffic (1 of 2 Chnl) @Fermilab: Dec, 2012
30G
2012
2 yrs
2008
Written data: 113 PB

## Slide 4: Network R&D at Fermilab
A collaborative process part of the national program on network involving multiple research organizations (ESNet, I2, LBL, UNL, ANL, NERSC, UFL, UCSD, …)
Builds on core competencies on Big Data inheriting from RunII and CMS expertise
A diverse program of work that spans all layers of computing for scientific discovery
Infrastructure / Network Layers 1-3
OS / Network Driver
Data
Management
Application I/O
Storage
Management
Tools & Services
Network Management
Science Code
- E-Center
- OSG / LHC Dashboard
- End-Site Control Plane System
- 100G High-Throughput Data
- CortexNet Data Selection
- Multicore-Aware Data Transfers
Fermilab Network R&D Facility
- G-NetMon

## Slide 5: Pulling all R&D effort together from the top layers…
Providing tools & services to enable users / apps to optimize use of the network
  Collaborating with the OSG Network Area for the deployment of perfSONAR at 100 OSG facilities
  Aggregating and displaying data through E-Center and the OSG Dashboard for end-to-end hop-by-hop paths across network domains
Developing tools to monitor real-time 100G network traffic through multicore & manycore architectures
Proposed integration with Data Management through network-aware data source selection – CortexNET

## Slide 6: Pulling all R&D effort together from the bottom layers…
Application-level R&D through the High Throughput Data Program
  R&D on 100G for production use by CMS & FNAL high-capacity high-throughput Storage facility
  Identifying gaps in data movement middleware for the applications used for scientific discovery – GridFTP, SRM, Globus Online, XRootD, Frontier / Squid, NFS v4
OS-level R&D to improve data transfer performance
  Optimizing network I/O for 40/100G environments
  Multicore-aware data transfer middleware (MDTM)
  Integrating local network infrastructure with WAN circuit technologies through policy-driven configuration (ESCPS)

## Slide 7: Overview
Network R&D Program Motivations and Overview
Network Infrastructure Production and R&D
100G Network R&D Program
Results and Plans

## Slide 8: A dedicated R&D Network facility
Nexus 7000 w/ 2-port 100GE module / 6-port 40GE module / 10GE copper module
12 nodes w/ 10GE Intel X540-AT2 (PCIe) / 8 cores / 16 GB RAM
Nexus 6000E for 40GE systems
    IPv6 tests / F5 load balancer / Infoblox DNS, Palo Alto firewall
2 nodes w/ 40GE Mellanox ConnectX®-2 (PCIe-3) / 8 cores w/ Nvidia M2070 GPU
- 100G R&D
- Production-like env for tech eval
- Testing of firmware upgrades
* Diagram courtesy of Phil DeMar

## Slide 9: Fermilab WAN Capabilities: In Transition from n x 10GE to 100GE
Legacy 10GE-based MAN being phased out:
  Eight 10GE channels
  Six used for science data
New 100GE-based MAN being phased in:
  One 100GE channel and three 10GE channels
  100GE channel is for science data movement
  10GE channels for general IP traffic and redundancy for science data
* Diagram courtesy of Phil Demar

## Slide 10: Using 100G Channel for R&D As Well
CMS needs 50G of data traffic from the 100G channel
Remaining ~50G for FNAL R&D network
  Potentially higher when CMS traffic levels are low
  LHC in shutdown until 2015
Planning WAN circuit into ESnet 100G testbed
  Potential for circuits to other R&D collaborations
* Diagram courtesy of Phil Demar

## Slide 11: Overview
Network R&D Program Motivations and Overview
Network Infrastructure Production and R&D
100G Network R&D Program
Results and Plans

## Slide 12: Goals of 100G Program at Fermilab
Experiment analysis systems include a deep stack of software layers and services.
Need to ensure these are functional and effective at the 100G scale end-to-end.
  Determine and tune the configuration of all layers to ensure full throughput in and across each layer/service.
  Measure and determine efficiency of the end-to-end solutions.
  Monitor, identify and mitigate error conditions.
Fermilab Network R&D Facility

## Slide 13: 100G High Throughput Data Program
2011: Advanced Network Initiative (ANI) Long Island MAN (LIMAN) testbed.
  GO / GridFTP over 3x10GE.
2011-2012: Super Computing ’11
  Fast access to ~30TB of CMS data in 1h from NERSC to ANL using GridFTP.
  15 srv / 28 clnt – 4 gFTP / core; 2 strms; TCP Win. 2MB
2012-2013: ESnet 100G testbed
  Tuning parameters of middleware for data movement: xrootd, GridFTP, SRM, Globus Online, Squid. Achieved ~97Gbps
    Rapid turn around on the testbed thank to custom boot images
  Commissioning Fermilab Network R&D facility: 12 nodes at 8.5 Gbps per 10G node
  Test NFS v4 over 100G using dCache (collab. w/ IBM research)
Fall 2013 / Winter 2014: 100G Endpoint at Fermilab
  Validate hardware link w/ data transfer apps with UFL and others. Talk to me if you want to participate in these activities.
  Demonstrate storage-to-storage 100G rates
70 Gbps (peak: 75)

## Slide 14: GridFTP / SRM / GlobusOnline Tests
Data Movement using GridFTP
  3rd party Srv to Srv trans.: Src at NERSC / Dest at ANL
  Dataset split into 3 size sets
Large files transfer performance ~ 92Gbps
GridFTP logging was through NFS on 1GE link: file transfers blocked on this.
Lot of Small Files (LOSF) transfer performance improved with pipelining
Optimal performance: 97 Gbps w/ GridFTP 2 GB files – 3 nodes x 16 streams / node
97 Gbps
Pipelining (“FTP cmd in-flight”) mitigates the negative effects of high-latency on transfer performance

## Slide 15: XRootD Tests
Data Movement over XRootD, testing LHC experiment (CMS / Atlas) analysis use cases.
  Clients at NERSC / Servers at ANL
  Using RAMDisk as storage area on the server side
Challenges
  Tests limited by the size of RAMDisk
  Little control over xrootd client / server tuning parameters
Calculation of the scaling factor between 1 NIC and an aggregated 12 NIC for datasets too large to fit on the RAM disk

## Slide 16: Squid / Frontier Tests
Data transfers
  Cache 8 MB file on Squid – This size mimics LHC use case for large calib. data
  Clients (wget) at NERSC / Servers at ANL
  Data always on RAM
Setup
  Using Squid2: single threaded
  Multiple squid processes per node (4 NIC per node)
  Testing core affinity on/off: pin Squid to core i.e. to L2 cache
  Testing all clnt nodes vs. all servers AND aggregate one node vs. only one server
Results
  Core-affinity improves performance by 21% in some tests
  Increasing the number of squid processes improves performance
  Best performance w/ 9000 clients: ~100 Gbps

## Slide 17: Summary
The Network R&D at Fermilab spans all layers of the communication stack
Science discovery by HEP and Astrophysics drive the program of work
Fermilab is deploying a Network R&D facility with 100G capability
ESnet 100G Testbed has been fundamental for our middleware validation program
Fermilab will test the 100GE capability in the Fall 2013 – Winter 2014