## Slide 1: GPU-Based Network Traffic Monitoring & Analysis Tools
Wenji Wu; Phil DeMar
wenji@fnal.gov, demar@fnal.gov
CHEP 2013
October 17, 2013
Notes: Welcome, thanks for coming,
I am Wenji Wu from Fermilab, My topic is “Network Traffic Monitoring & Analysis with GPUs”,
This is a joint work with my colleague Phil DeMar.

## Slide 2: Background
Main uses for network traffic monitoring & analysis tools:
  Operations & management
  Capacity planning
  Performance troubleshooting
Levels of network traffic monitoring & analysis:
  Device counter level (snmp data)
  Traffic flow level (flow data)
  At the packet inspection level The focus of this work
    Security analysis
    Application performance analysis
    Traffic characterization studies
Coarse
Detailed
Notes: There are many uses for network monitoring and analysis,
There are levels of network traffic monitoring and analysis.
The highest level, The next level
The lowest level, and also the finest level is to monitor and analyze network traffic on a per packet basis.

## Slide 3: Problem Space
Emerging high-performance network environments:
  40GE/100GE link technologies now in LAN & WAN
  Servers becoming 10GE-connected by default
  n x 100GE / 400GE backbone links & 40GE host connections loom on the horizon.
Current flow-based & packet-based traffic monitoring & analysis tools break down at 40GE/100GE:
  Flow data is sampled:
    Implemented in device hardware
    May be too coarse for computer security forensics & detailed traffic characterization studies
  Packet-based analysis runs into resource issues:
    10Gb/s = ~14M 64-bytes packets per sec
Notes: Processing so many packets is a big challenge!

## Slide 4: Packet-Based Analysis
Our preferred choice for 40/100GE traffic analysis:
  Flow data limitations (sampled) constrain flow-based analysis
Characteristics of packet-based network monitoring & analysis applications
  Time constraints on packet processing.
  Highly compute and I/O throughput-intensive
  High levels of data parallelism.
    Each packet can be processed independently
  Extremely poor temporal locality for data
    Typically, data processed once in sequence; rarely reused

## Slide 5: Platforms for Packet-Based Analysis (I)
Computing platform requirements monitoring & analysis applications within high performance network :
  High Compute power
  Ample memory bandwidth
  Capability of handing data parallelism inherent with network data
  Easy programmability
Notes: What is the requirements on computing platform for network monitoring and analysis in high speed networks?

## Slide 6: Platforms for Packet-Based Analysis (II)
Three types of computing platforms:
  NPU/ASIC
  CPU
  GPU
Architecture Comparison
Features | NPU/ASIC | CPU | GPU
High compute power | Varies | ✖ | ✔
High memory bandwidth | Varies | ✖ | ✔
Easy programmability | ✖ | ✔ | ✔
Data-parallel execution model | ✖ | ✖ | ✔
Notes: Based on the requirements on the computing platform for network monitoring and analysis in high-speed networks.
NPU/ASIC does not support data parallel execution model.

## Slide 7: Our Solution
Use GPU-based Traffic Monitoring & Analysis Tools:
    Note: This is currently a research area
Highlights of our work:
  Demonstrated GPUs can significantly accelerate network traffic monitoring & analysis
    11 million+ pkts/s without drops (single Nvidia M2070)
  Designed/implemented a generic I/O architecture to move network traffic from wire into GPU domain
  Implemented a GPU-accelerated library for network traffic capturing, monitoring, and analysis.
    Dozens of CUDA kernels, which can be combined in a variety of ways to perform monitoring and analysis tasks

## Slide 8: Key Technical Issues
GPU’s relatively small memory size:
  Nvidia M2070 has 6 GB Memory
  Workarounds:
    Mapping host memory into GPU with zero-copy technique?
    Partial packet capture approach ✔
Need to capture & move packets from wire into GPU domain without packet loss
Need to design data structures that are efficient for both CPU and GPU
Notes: 1. If all 6GB is used for packet storage, it can accommodate 4 million 1500B packets, which is inadequate. 2. Capture traffic into host memory and allow the GPU kernels to directly process packets in host memory with the zero-copy technique. However, performance is bad, because the data access cost is too high.
3. Reduce the storage requirement on GPU, yet provide enough information for network monitoring and analysis.

## Slide 9: System Architecture
Traffic Capture
Preprocessing
Four Types of Logical Entities:
Monitoring & Analysis
Output Display

## Slide 10: Packet I/O Engine for Capture
Key techniques
  Pre-allocated large packet buffers
  Packet-level batch processing
  Memory mapping based zero-copy
Key Operations
Open
Capture
Recycle
Close

## Slide 11: GPU-based Network Traffic Monitoring & Analysis Algorithms
A GPU-accelerated library for network traffic capturing, monitoring, and analysis apps.
  Dozens of CUDA kernels
  Can be combined in a variety of ways to perform intended monitoring & analysis operations
  Examples in following slides

## Slide 12: Packet-Filtering Kernel
Advanced packet filtering capabilities necessary so that we only analyze packets of interest
  We use Berkeley Packet Filter (BPF) as the packet filter
  A few basic GPU operations, such as sort, prefix-sum, and compact.

## Slide 13: Traffic-Aggregation Kernel
Reads an array of n packets at pkts[] and aggregates traffic for same src & dst IP addresses. Exports list of entries; each entry records a src/dst address pair, with associated traffic statistics
Use to build
IP conversations
Multikey-Value Sort
Inclusive Scan

## Slide 14: Unique-IP-Addresses Kernel
1. for each i∈[0,n-1] in parallel do
IPs[i] ≔ src or dst addr of pkts[i];
end for
2. perform sort on IPs[] to determine sorted_IPs[];
3. diff_results[0] =1;
for each i∈[1,n-1] in parallel do
if(sorted_IPs[i] ≠sorted_IPs[i-1]) diff_buf[i]=1;
else diff_buf[i]=0;
end for
4. perform exclusive prefix sum on diff_buf[];
5. for each i∈[0,n-1] in parallel do
if(diff_buf[i] ==1) Output[scan_buf[i]]=sorted_IPs[i];
end for
Reads an array of n packets at pkts[] and outputs a list of unique src or dst IP addresses seen on the packets
CUDA

## Slide 15: A Sample Use Case
Using our GPU-accelerated library, we developed a sample use case to monitor network status:
  Monitor networks at different levels:
    from aggregate of entire network down to one node
  Monitor network traffic by protocol
  Monitor network traffic information per node:
    Determine who is sending/receiving the most traffic
    For both local and remote addresses
  Monitor IP conversations:
    Characterizing by volume, or other traits.

## Slide 16: A Sample Use Case – Data Structures
Three key data structures were created at GPU:
  protocol_stat[]
    an array used to store protocol statistics for network traffic, with each entry associated with a specific protocol.
  ip_snd[] and ip_rcv[]
    arrays that are used to store traffic statistics for IP conversations in send & receive directions respectively
  ip_table
    a hash table that is used to keep track of network traffic information of each IP address node
These data structures are designed to reference themselves and each other with relative offsets such as array indexes

## Slide 17: A Sample Use Case – Algorithm
Call Packet-filtering kernel to filter packets of interest
Call Unique-IP-addresses kernel to obtain IP addresses
Build the ip_table with a parallel hashing algorithm
Collect traffic statistics for each protocol and each IP node
Call Traffic-Aggregation kernel to build IP conversations

## Slide 18: Prototyped System
Prototyped System
Our application is developed on Linux.
CUDA 4.2 programming environment.
The packet I/O engine is implemented on Intel 82599 10GigE NIC
A two-node NUMA system
  Two 8-core 2.67GHz Intel X5650 processors.
Two Intel 82599-based 10GigE NICs
One Nvidia M2070 GPU.

## Slide 19: Performance Evaluation Packet I/O Engine
Packet Capture Rate
CPU Usage
Our Packet I/O engine (GPU-I/O) vs CPU-based packet analysis tools
  No packet drops
  Least CPU usage
Notes: one traffic generator was connected directly to a 10G NIC on the system. A traffic capture thread is launched. It captures packets and copies the headers to a system memory.

## Slide 20: Performance Evaluation GPU-based Packet Filtering Algorithm
Our packet filtering algorithm (red) vs CPU-based & memory-mapped GPU-based tools
Notes: We captured a few millions packets at Fermilab border router, and use them as experiment data.
To evaluate the GPU-based packet filtering algorithm, we run three experiments.
Explicitly copy the experimental data into GPU memory and launch the packet filtering kernel to process the data.
The experiment data is kept in a host memory buffer instead of being copied into the GPU.
We implement a CPU-based packet filtering algorithm.

## Slide 21: Performance Evaluation GPU-based Sample Use Case
Our GPU-analysis (red) vs CPU-based analysis

## Slide 22: Conclusion
Our GPU-based network traffic monitoring & analysis tools seem effective in high-performance network technology environments
Next steps:
  Continue to develop these tools toward production-quality
  Investigate ways to work around limitations (ie., IDS) of partial packet capture
Always looking for potential collaborators in this technology area

## Slide 23: Questions ?
Email: wenji@fnal.gov and demar@fnal.gov
Thank You!