## Slide 1: The new CMS DAQ system for LHC operation after 2014 (DAQ2)
CHEP2013: Computing in High Energy Physics 2013 14-18 Oct 2013 Amsterdam
Andre Holzner, University California at San Diego
On behalf of the CMS collaboration

## Slide 2: Overview
DAQ2 Motivation
Requirements
Layout / Data path
Frontend Readout Link
Event builder core
Performance considerations
Infiniband
File based filter farm and storage
DAQ2 test setup and results
Summary/Outlook

## Slide 3: DAQ2 motivation
Aging equipment:
  Run1 DAQ uses some technologies which are disappearing
    PCI-X cards, Myrinet
    Almost all equipment reached the end of the 5 year lifecycle
CMS detector upgrades
  Some subsystems move to new front-end drivers
  Some subsystems will add more channels
LHC performance
  Expect higher instantaneous luminosity after LS1 → higher number of interactions per bunch crossing (‘pileup’) → larger event size, higher data rate
Physics
  Higher centre-of-mass energy and more pileup imply:
    either raise trigger thresholds, or
    more intelligent decisions at Higher Level Trigger → requires more CPU power
Notes: Buying equipment to just replace the old hardware (with the same interfaces) may even be more expensive than buying state of the art equipment

## Slide 4: DAQ2 requirements
Requirement | DAQ1 | DAQ2
Readout rate | 100 kHz | 
Front end drivers (FEDs) | 640: 1 ~ 2 kByte | 640: 1 ~ 2 kByte ~50: 2 ~ 8 kByte
Total readout bandwidth | 100 GByte/s | 200 GByte/s
Interface to FEDs1) | SLink64 | Slink64/Slink Express
Coupling Event builder software/HLT software2) | no requirement | decoupled
Lossless event building | ✅ | 
HLT capacity | extendable | 
High availabilty/ fault tolerance3) | ✅ | 
Cloud facility for offline processing4) | originally not required | ✅
Subdetector local runs | ✅ | 
See talks of 1) P. Žejdl 2) R. Mommsen 3) H.Sakulin 4) J.A.Coarasa

## Slide 5: DAQ2 data path
FED
~640 (legacy) + 50 (μTCA) Front End Drivers
FEROL
~576 Front End Readout Optical Links (FEROLs)
10 GBit/s Ethernet → 40 GBit/s Ethernet switches, 8/12/16 →1 concentration
RU
72 Readout Unit PCs (superfragment assembly)
Infiniband switch (full 72 x 48 connectivity, 2.7 TBit/s)
IB 56 GBit/s
BU
48 Builder units (full event assembly)
Eth 40 GBit/s
Slink64/ SlinkExpress
IB 56 GBit/s
Eth 40 GBit/s
Eth 10 GBit/s
Ethernet switches 40 GBit/s → 10 GBit/s (→ 1 GBit/s), 1 →M distribution
FU
Filter units (~ 13’000 cores)
storage
custom hardware
commercial hardware

## Slide 6: DAQ2 layout
underground
surface

## Slide 7: FrontEnd Readout Link (FEROL)
Slink64
from FEDs
see P. Žejdl’s talk for more details
Slink Express
from μTCA FEDs
10 GBit/s Ethernet
Replace Myrinet card (upper half) by a new custom card
PCI-X interface to legacy slink receiver card (lower half)
10 GBit/s Ethernet output to central event builder
  Restricted TCP/IP protocol engine inside the FPGA
Additional optical links (inputs) for future μTCA based Front End Drivers (6-10 GBit/s; custom, simple point to point protocol)
Allows to use industry standard 10 GBit/s transceivers, cables and switches/routers
  Only commercially available hardware further downstream

## Slide 8: Event Builder Core
Two stage event building:
  72 Readout units (RU) aggregate 8-16 fragments (4 kByte average) into superfragments
    Larger buffers compared to FEROLs
  48 Builder Units (BU) build the entire event from superfragments
InifiniBand (or 40 Gbit/s Ethernet) as interconnect
Works in a 15 x 15 system, need to scale to 72 x 48
Fault tolerance:
  FEROLs can be routed to different RU (adding a second switching layer improves flexibility)
  Builder Units can be excluded from running

## Slide 9: Performance considerations
Number of DAQ2 elements is an order of magnitude smaller than for DAQ1
Consequently, bandwidth per PC is an order of magnitude higher
CPU frequency did not increase since DAQ1 but number of cores did
Need to pay attention to performance tuning
  TCP socket buffers
  Interrupt affinities
  Non-uniform memory access
 | DAQ1 | DAQ2
# readout units (RU) | 640 | 48
RU max. bandwidth | 3 Gbit/s | 40 Gbit/s
# builder units (BU) | >1000 | 72
BU max. bandwidth | 2 Gbit/s | 56 Gbit/s
CPU0
CPU1
QPI
PCIe
Memory Bus

## Slide 10: Infiniband
Advantages:
  Designed as a High Performance Computing interconnect over short distances (within datacenters)
  Protocol is implemented in the network card silicon → low CPU load
  56 GBit/s per link (copper or optical)
  Native support for Remote Direct Memory Access (RDMA)
  No copying of bulk data between user space and kernel (‘true zero-copy’)
  affordable
Disadvantages:
  Less widely known, API significantly differs from BSD sockets for TCP/IP
  Fewer vendors than Ethernet
  Niche market
Top500.org share by Interconnect family
Infiniband
DAQ1 TDR (2002)
Myrinet
1 Gbit/s Ethernet
10 Gbit/s Ethernet
2013

## Slide 11: File based filter farm and Storage
In DAQ1, high level trigger process was running inside a DAQ application → introduces dependencies between online (DAQ) and offline (event selection) software which have different release cycles, compilers, state machines etc.
Decoupling these needs a common, simple interface
  files (no special common code required to write and read them)
Builder unit stores events in files in a RAM disk
  Builder Unit acts as a NFS server, exports event files to Filter Unit PCs
  Baseline: 2 Gbyte/s bandwidth
  ‘Local’ within a rack
Filter units write out selected events (~ 1 in 100) back to a global (CMS DAQ wide) filesystem (e.g. Lustre) for transfer to Tier0 computing centre
see R. Mommsen’s talk for more details
BU
FU
FU
FU
FU
FU
FU
FU

## Slide 12: DAQ2 test setup
Copper
R720
Copper
C6220
C6220
1U 10/40 Gbit/s Ethernet switch
C6220
10 Gbit
Copper
1-10 GBit/s router
x2
4
4
x16
BU
RG45
FEROL
emulator
FED Builder
RU
RU Builder
RU/BU Emulators
FU
R720
1U 40 Gbit/s Ethernet switch
40 Gbit
Copper
1U 40 Gbit/s Ethernet switch
40 Gbit
Copper
Copper
Copper
R310
R310
R310
A
C6220
C6220
B
C6220
1U Infiniband
FDR switch
x2
x13
x8
C6220
C6220
C6220
B
R720
C6100
C6100
C6100
D
B
10 Gbit
fiber
40 Gbit
Cupper
10 Gbit
Fiber
B
RG45
R310
R310
R310
A
B
C6220
B
x8
x8
10 Gbit
Fiber
C
x3
x3
x3
Copper
FEROL/RU/BU/FU
Emulators
x3
x2
x3
x13
x8
x8
x8
x8
X8
10 Gbit
Fiber
x8
x8
x3
40 Gbit
Copper
x2
x2
x2
x8
FRL/FEROL
x16
x8
x2
10 Gbit
Fiber
10 Gbit
Fiber
x2
C’
A | X3450 @ 2.67GHz
B/C/C’ | Dual E5-2670 @ 2.60GHz
D | Dual X5650 @ 2.67GHz

## Slide 13: InfiniBand Measurements
BU
RU
FED
FEROL
RU
BU
FU
15 RU
15 BU
RU
RU
BU
BU
working range

## Slide 14: Test setup results
FEROL
FEROL
RU
BU
FU
12 FEROLs
1 RU
4 BU
100 kHz
working range
FEROL
BU
BU
BU

## Slide 15: Test setup: DAQ1 vs. DAQ2
Comparison of throughput per Readout Unit

## Slide 16: Summary / Outlook
CMS has designed a central data acquisition system for post-LS1 data taking
  replacing outdated standards by modern technology
  ~ twice the event building capacity than DAQ system for Run1
  accomodating a large dynamic range of up to 8 kByte fragments, flexible configuration
Increase in networking bandwidth was faster than increase in event sizes
  Number of event builder PCs reduced by a factor ~10
    Each PC handles a factor ~10 more bandwidth
    Requires performance related fine-tuning
Performed various performance tests with a small scale demonstrator
First installation activities for DAQ2 have started already
  Full deployment foreseen for mid 2014
Looking forward to recording physics data after the Long Shutdown 1 !