## Slide 1: Puffin
L.T. Campbell & B.W.J. McNeil
University of Strathclyde

## Slide 2: What is an FEL?
McNeil, Thompson, nature photonics | VOL 4 | DECEMBER 2010 |
In a Free Electron Laser (FEL), a beam of relativistic electrons and a radiation field co-propagate an undulator or wiggler
An undulator or wiggler is a periodic array of alternating magnetic poles
This forces the electrons to oscillate in the direction transverse to propagation
This oscillating component of velocity allows an energy transfer between electrons and radiation field
The interaction causes the electrons to bunch spatially, and they begin to coherently amplify the radiation field, giving an exponential growth in intensity

## Slide 3: What is an FEL?
Electrons amplify field at a certain resonant frequency
“slow” amplification process (w.r.t. the FEL resonant wavelength)
Use Slowly Varying Envelope Approximation (SVEA), and use averaged quantities to drive radiation field
Call this ‘averaged model’
McNeil, Thompson, nature photonics | VOL 4 | DECEMBER 2010 |

## Slide 4: FEL Averaged Code - Basic
Radiation field and electrons co-propagate an undulator

## Slide 5: FEL Averaged Code - Basic
Use Slowly Varying Envelope Approximation (SVEA), and use averaged quantities to drive field

## Slide 6: FEL Averaged Code - Basic
Use Slowly Varying Envelope Approximation (SVEA), and use averaged quantities to drive field

## Slide 7: FEL Averaged Code - Basic
Electron velocity < c
To simulate relative electron-radiation ‘slippage,’ pass field on to next slice

## Slide 8: FEL Averaged Code - Basic
Electron velocity < c
To simulate relative electron-radiation ‘slippage,’ pass field on to next slice

## Slide 9: FEL Averaged Code - Basic
In this model, electrons are confined to each slice, within periodic BC’s in phase space i.e. over a slice:
Current assumed constant in each ‘slice’

## Slide 10: FEL Unaveraged Code
In an unaveraged code, we do not perform the SVEA or averaging process, and the radiation field is sampled on a much finer grid – a Particle In Cell (PIC) model

## Slide 11: Unaveraged FEL codes
In an unaveraged code, the radiation field envelope can vary quickly, and so can model the full radiation spectrum self consistently (limited by the Nyquist frequency) – so can model coherent emission arising from current gradients in the beam
Electrons are not confined to slices – can model current redistribution during propagation

## Slide 12: Motivation
FEL’s now operating in hard x-ray (around 1Å) with pulse lengths of 10’s of fs and peak powers of ~1010W, to probe ultrafast, ultrasmall phenomena. Evolves from noise – process known as SASE – and SVEA can model this
Cannot model coherent spontaneous emission arising from current gradients in the beam
Cannot model electron transport fully

## Slide 13: Motivation II
Hard to model different frequencies with SVEA, can only model resonant frequency
New techniques to improve temporal output and shot-to-shot stability may violate SVEA
e.g. EEHG involves violent changes in electron position to prepare the beam
Laser Plasma Accelerators produce short electron pulses which may exhibit a large degree of coherent emission, which averaged codes cannot model
Such short electron pulses could involve large changes in relative electron positions – averaged codes cannot model this

## Slide 14: Puffin
Parallel Unaveraged Fel Integrator
  Unaveraged Free Electron Laser (FEL) code
Puffin is first unaveraged FEL code in 3D
Written in Fortran 90 using MPI
Models a variably polarised undulator FEL
Intended for probing new FEL schemes and ideas

## Slide 15: Numerical Solution - Electrons
Electron beam is discretised into electron macroparticles by method of [1]
[1] – B.W.J. McNeil and G.R.M. Robb, Phys Rev E 65, 046503
Sampling an electron beam with a gaussian current distribution

## Slide 16: Numerical Solution - Electrons
Electron beam is discretised into electron macroparticles by method of [1]
[1] – B.W.J. McNeil and G.R.M. Robb, Phys Rev E 65, 046503
Sampling an electron beam with a gaussian current distribution
Create a grid...

## Slide 17: Numerical Solution - Electrons
Electron beam is discretised into electron macroparticles by method of [1]
[1] – B.W.J. McNeil and G.R.M. Robb, Phys Rev E 65, 046503
Sampling an electron beam with a gaussian current distribution
Create a grid, and into each grid element we assign a macroparticle with charge weight determined by the current distribution

## Slide 18: Numerical Solution - Electrons
Electron beam is discretised into electron macroparticles by method of [1]
[1] – B.W.J. McNeil and G.R.M. Robb, Phys Rev E 65, 046503
To simulate noise assign random Poisson deviate to each macroparticle charge weight & position
Sampling an electron beam with a gaussian current distribution
Create a grid, and into each element we assign a macroparticle with charge weight determined by the current distribution

## Slide 19: Numerical Solution - Field
Solve field with split step Fourier method [1]
  1st half step: Field diffraction solved with Fourier Transforms
  2nd half step: Field source (amplification and absorption by electron macroparticles) and electron propagation
Field Source solved with Finite Element (Galerkin) Method [2]
Involves solution of sparse linear system
  [1] - R.H. Hardin and F.D. Tappert, SIAM Rev. 15, 453 (1973)
  [2] - K.H. Huebner, E.A. Thornton and T.G. Byrom, The Finite Element Method for Engineers

## Slide 20: Matched Electron Beam
Radiation field is modelled with a grid of nodes with linear interpolant, macroparticles move freely throughout field elements
Electron beam is matched to undulator, meaning in transverse space it is focussed such that the beam has a constant radius

## Slide 21: Matched Electron Beam
Electrons will therefore remain confined to an inner set of nodes. Outer field nodes are then used only for diffraction
Low frequency components diffract very quickly out the system. This causes an unphysical low frequency background signal to emerge which may interfere with the FEL interaction. Currently filter out low frequencies during propagation.

## Slide 22: Parallelism
Large data sets
Num of macroparticles ~109 – would like to go orders of magnitude larger, need to distribute large electron arrays
MPI
Parallel Fourier Transforms
Parallel Linear Solver for Sparse Systems
We use:-
  FFTW 2.1.5 for Fourier Transforms
  MUMPS for Linear Solver - Possible change to Hiper for linear solver in future

## Slide 23: Memory Distribution
Not immediately intuitive how to maintain a consistent memory distribution with minimum processor communication
P0
P1
P2
P3
P4
P5
P6
P7
- electron beam
- field
PN
- Nth Processor
(ct-z)

## Slide 24: Memory Distribution
P0
P1
P2
P3
P4
P5
P6
P7
Not immediately intuitive how to maintain a consistent memory distribution with minimum processor communication
- electron beam
- field
(ct-z)

## Slide 25: Parallelism
Electrons propagate freely through radiation field elements at v < c
Store full field array on each processor
Electrons are distributed evenly amongst processors
Since num macroparticles >> num field nodes (6D beam vs 3D field)

## Slide 26: Code

## Slide 27: Machines Used
In house Sun x4600 server
  16 cores
DL1 on NW grid at Daresbury
  30-40 cores
ARCHIE at University of Strathclyde
  200-300 cores
Hartree?
  ???

## Slide 28: Current
Benchmarking performed by Lucian Anton at Hartree

## Slide 29: Need for more processors/parallelism
Currently using around 109 macroparticles
For larger systems would like to increase to at least 1011 – 1012
Linear solver can be replaced to be more efficient, currently it appears to take the most time in each integration step

## Slide 30: Ongoing Work
Output and post-processing
  Previously using custom Matlab interface
  Now using scripts, need to link these into the Matlab GUI
  Data files too large, inconvenient for storage and transport

## Slide 31: Broadband Field - variation with observation angle
ω/ωr
- on-axis spectra, then in order of increasing arbitrary angle:
Avg. code range

## Slide 32: Ongoing Work
Models variably polarized undulator
Radiation field polarization solved self-consistently – electrons only interact with correct polarization
May be useful investigating FEL concepts with variable polarization and multifrequency model

## Slide 33: Ongoing Work

## Slide 34: Ongoing Work

## Slide 35: Ongoing Work
Mode locked FEL
HHG seeding

## Slide 36: Ongoing Work
D. J. Dunning, B. W. J. McNeil, N. R. Thompson, arXiv:1212.2047v1

## Slide 37: End
Thank you