## Slide 1: RP Status for the PSB Injection Dumps
R. Froeschl

## Slide 2: Head Dump - Inputs
Load assumptions from EDMS 963395
  Operational year has 2 phases
    LLRF setup
      max. 1 week at the beginning of the operational year
      278e10 pps
    Normal operation
      17e10 pps
Geometry
  Drawings from Thierry Masson
  Dump core made out of Graphite
  Magnet implemented
  Water cooling circuit only very schematic

## Slide 3: Head Dump - Geometry
Dump
Magnet

## Slide 4: Head Dump - FLUKA simulations to estimate
Decrease of dose rate with time for 2 scenarios
  At the end of the LLRF setup week
  At the end of the operational year
Two time horizons
  < 7days
    to estimate interventions in the tunnel
  < 2 years
    to estimate repair after removal from the tunnel
Validate material choice

## Slide 5: Head Dump – Interventions Stop at end of LLRF week

## Slide 6: Head Dump – Interventions Stop near end of operational year

## Slide 7: Head Dump - Interventions
After 3 hours, the magnet is the dominant source of radiation
Decrease of dose rate slows down significantly after 3 hours
  Waiting time before access of 3 hours seems reasonable
  Expected dose rate at 1m
    less than 700 µSv/h (LLRF week)
      Should clarify whether the LLRF setup has to be done with the full current stated in EDMS 963395
    less than 100 µSv/h (normal operation)

## Slide 8: Head Dump – Repair Stop near end of operational year
Contribution of the dump core for repair after removal from the tunnel is small compared to the yoke
Graphite is a good choice from an RP point of view

## Slide 9: Head Dump - Water activation
Tritium production
  4.6 kBq/year (LLRF setup week + normal operation)
Be-7
  Still to be assessed, no show-stopper expected due to low tritium production level
Short lived activation products
  Still to be assessed , no show-stopper expected due to low tritium production level

## Slide 10: H0/H- Dumps - Inputs
Load assumptions from EDMS 963395
  Continuous load
    9.61e18 H-/y at 14.2 W
  Foil degradation
    max. 8 hours for about 10 times per operational year
    7.99e17 H-/y at 71 W
Geometry
  FLUKA geometry from C. Maglioni
  Dump core made out of SiC
  Magnet implemented
  No water cooling circuit implemented yet

## Slide 11: H0/H- Dumps – Production of Na-22 from Si
Dominant radionuclide after first operational year even for 1 day cool-down
  3.7 GBq
  1.23 mSv/h @ 1meter
  Factor 6 higher than the magnet (Mn-54)
Half-life of 2.6 years
  511 keV(180%)
  1274 keV (99.94%)

## Slide 12: H0/H- Dumps – Future studies
Scenarios with dumps inside the magnets
  Intervention scenarios
  Additional shielding
Scenario with dumps extracted from the magnets
Water cooling

## Slide 13: Conclusions
Head Dump
H0/H- Dumps
Graphite is a well suited material for the dump core from an RP point of view
  After 3 hours dose rates dominated by the magnet and not by the dump
Tritium production very low
  Connection to the (then) underground PSB water cooling circuit should be ok
Dump core is the dominant contributor to the dose rate
Na-22 (half-life 2.6 y) is the dominant radionuclide
Up to a couple of mSv/h at 1 meter distance if unshielded
Shielding options as a function of intervention/removal scenarios to be studied
Water cooling to be studied