## Slide 1: LHC optics estimation
Zimányi Winter School
Budapest
2012, December 3.– 7.
Frigyes Nemes Eötvös Loránd University
on behalf of the TOTEM collaboration
http://totem.web.cern.ch/Totem/

## Slide 2: Experimental layout of the TOTEM experiment
T1: 3.1 < h < 4.7
T2: 5.3 < h < 6.5
T1
T2
CASTOR (CMS)
RP147
RP220
10.5m
14m

## Slide 3: Roman Pot stations
RP stations
2 units at about 5 m distance
Measurement of very small proton scattering angles (few µrad)
Vertical and horizontal pots mounted as close as possible to the beam
BPM fixed to the structure gives precise position relative to the beam
Overlapping detectors: relative alignment (10 µm inside unit between 3 RPs)
Horizontal RP
RP unit: 2 vertical, 1 horizontal pot + BPM
BPM
Vertical RPs
1 Roman Pot
10 planes of edgeless detectors
3.5 cm
Si edgeless detector

## Slide 4: LHC optics in brief
Proton position at a given RP (x, y) is a function of position (x*, y*) and angle (Qx*, Qy*) at IP5:
describes the spread of primary vertex and beam size at RP
beam divergence @IP5 limits the angle measurement precision
Beam size and divergence at IP5 and RP
The effective length and magnification expressed with the phase advance
RP
IP5
measured
reconstructed

## Slide 5
Effective lengths from IP5 to RP @220 m
High β*=1535 m target optics
b* = 1535 m is the target optics. Requires different injection optics. Properties:
beam divergence σΘ* ≈ 0.3 μrad, vertex size σIP ≈ 450 μm
Δμx,y = π/2 → νx,y = 0. Parallel-to-point focusing eliminates the large vertex contribution
the large (270 m) vertical effective length Ly pushes protons vertically into RP acceptance
acceptance in momentum transfer, |t| > 2 · 10-3 GeV2, with 10 σbeam size@RP
β*=1535 m
β*=90 m
Magnification from IP5 to RP @220 m
β*=1535 m

## Slide 6: LOW β*=3.5 m OPTICS

## Slide 7: Low β*=3.5m optics
Objective:
    to measure elastic scattering at high |t|
Properties of the optics:
σIP ≈ 37 μm (magnification is not crucial)
Lx ≈ 0, Ly = 22.4 m
beam divergence σΘ* ≈ 17-18 μrad
Data sources to improve our optics
understanding:
TIMBER database magnet currents
FIDEL team conversion curves, implemented with LSA
WISE field harmonics, magnet’s displacements`
t = -p2 q2
x = Dp/p
The intercepts of all selected reconstructed
tracks in a scoring plane transverse to
the beam at 220 m
Ly
Lx
Effective lengths β*=3.5 m
Elastically scattered proton
candidates
Sector 56
Sector 45

## Slide 8: The effect of machine imperfections β*=3.5m
Optics imperfections can be determined from proton
tracks measured in the Roman Pots. The method is based on:
elastic events are easy to tag
the elements of the transport matrix are mutually correlated
elastic scattering ensures that
Perturbed element | δLy,b1/Ly,b1 [%]
MQXA.1R5 | 0.98
MQXB.A2R5 | −2.24
MQXB.B2R5 | −2.42
MQXA.3R5 | 1.45
MQY.4R5.B1 | −0.10
MQML.5R5.B1 | 0.05
Δp/p | −2.19
R1
Constraints from proton tracks in the Roman Pots β*=3.5m
Machine imperfections:
Strength conversion error, σ(B)/B ≈ 10-3
Beam momentum offset, σ(p)/p ≈ 10-3
Magnet rotations, σ(φ) ≈ 1 mrad
Beam harmonics, σ(B)/B ≈ 10-4
Power converter errors, σ(I)/I ≈ 10-4
Magnet positions Δx, Δy ≈ 100 μm
Imperfections alter the optics !

## Slide 9: Matching the optics β*=3.5m
On the basis of constraints R1-R10 the optics can be estimated.
R3,4
R7,8,9,10
R5,6
Measured ratios
R1-R10
Calculated ratios
R1-R10
dLx/ds, Ly
Match
R1
R2

## Slide 10: Monte-Carlo confirmation of the method (presented @IPAC 2012)
Relative error distributions before and after matching
The Monte-Carlo study included the
effect of:
magnet strengths
beam momenta
displacements, rotations
kickers, field harmonics
elastic scattering Θ-distributions
Conclusion: for β*=3.5m TOTEM can measure the transfer matrix between IP5 and RPs with a precision
Optical function relative error | Before |  | Matched | 
 | Mean [%] | RMS [%] | Mean [%] | RMS [%]
δLy,b1/Ly,b1 | 0.39 | 4.2 | 8.3 · 10-2 | 0.16
δ (dLx,b1/ds)/(dLx,b1/ds) | -0.97 | 1.6 | -0.13 | 0.17
δLy,b2/Ly,b2 | -0.14 | 4.9 | 0.21 | 0.16
δ (dLx,b2/ds)/(dLx,b2/ds) | 0.10 | 1.7 | -9.7· 10-2 | 0.17
RMS < 0.2 %

## Slide 11: ELASTIC SCATTERING WITH β*=3.5 m

## Slide 12: Elastic scattering with β*=3.5m
Results (the matched Ly and dLx/ds are used for reconstruction):
RP approaches the beam down to 7 σbeam size@RP
published in EPL 95 (2011) 41001
ξ ≈ 0
Collinearity Θx
Spread in agreement with beam divergence (17-18 μrad)
Collinearity Θy
Beam divergence

## Slide 13
Published in EPL 95 (2011) 41001:
|t| range spans from 0.36 to 2.5 GeV2
below |t| = 0.47 GeV2 exponential e-B|t| behavior
dip moves to lower |t|, proton becomes “larger“
1.5 - 2.0 GeV2 power low behavior |t|-n
Proton-proton dσ/dt
@ISR
Final result: unfolded elastic scattering distribution β*=3.5m
The measured dσ/dt compared with predictions of several models

## Slide 14: HIGH β* = 90 m OPTICS AND RESULTS

## Slide 15
* = 90m optics achievable using the standard LHC injection optics. Properties:
σΘ* = 2.5 μrad, Lx ≈ 0, Ly ≈ 260 m
vertex size σIP ≈ 212 μm
Acceptance: |t| > 3 · 10-2 GeV2 , RP distance from beam center 10 σbeam size@RP
parallel to point focusing only in vertical plane @RP220
Effective lengths from IP5 to RP @220 m
β*=90 m optics in general
β*=90 m

## Slide 16
Very clean data obtained with β*=90 m
The properties of the measured data:
divergence is reduced with respect to 3.5 m optics (from 17-18 μrad to 2.5 μrad)
lower background compared to 3.5 m ( < 0.1%)
uncertainty of luminosity 4% (CMS)
low intensity bunches and β*=90 m -> no pile-up from single diffraction
RP at 220m
Collinearity Θx
Collinearity Θy
Beam divergence

## Slide 17: Intermediate β*=90 m optics: robustness
Perturbed element | δLy,b1/Ly,b1 [%]
MQXA.1R5 | 0.14
MQXB.A2R5 | −0.23
MQXB.B2R5 | −0.25
MQXA.3R5 | 0.20
MQY.4R5.B1 | −0.01
MQML.5R5.B1 | 0.04
Δp/p | 0.01
Objectives:
First measurement of tot elastic scattering in a wide |t| range
inclusive studies of diffractive processes
measurement of forward charged multiplicity
Sensitivity of the effective length Ly :
1 ‰ perturbations magnet strength, beam momenta
Conclusion: not necessary to improve our understanding about β*=90 m optics
Published in EPL 96 (2011) 21002
Properties:
|t| range of the new set is 0.02 - 0.33 GeV2
B = (20.1 ± 0.2stat ± 0.3syst) GeV−2 confirms that B increases with √s
excellent agreement between the two measurements with different optics
Superimposed
fits with the
combined datasets
β*=90 m
β*=3.5 m
Obtained dσ/dt with β*=90 m optics

## Slide 18
TOTEM has measured the inelastic and elastic cross sections and the total cross section with the luminosity independent method at √s=7 TeV
Measurement of elastic scattering at very low-t and determination of the ρ parameter will be in reach during the high β (β*= 500 m, 1000 m) runs
Several analyses on diffractive physics are going on, results are expected soon
Conclusions

## Slide 19
Thank you for you attention !

## Slide 20
Backup part

## Slide 21
Obtained dσ/dt with the most recent result
EPL 95 (2011) 41001 (2010 Oct data)
EPL 96(2011) 21002 (2011 June data)
Preprint (2011 Oct data)
(RP @ 6.5, 5.5, 4.8 σbeam size@RP )
RP@ 10 σbeam size@RP

## Slide 22: Total Cross-Section with 4 methods
    Low luminosity (CMS) + Elastic d/dt + Optical th. ( EPL 96(2011) 21002 )
      depends on CMS luminosity for low-L bunches, elastic efficiencies and on ρ
    High luminosity (CMS) + Elastic + Optical theorem (to be published)
    High luminosity (CMS) + Elastic + Inelastic (to be published)
      minimizes dependence on elastic efficiencies and ρ independent
    Elastic ratios + Inelastic ratios + Optical theorem (preprint)
      Eliminates dependence on luminosity
sTOT = 98.3 ± 2.8 mb
sTOT = 98.6 ± 2.2 mb
sTOT = 99.1 ± 4.3 mb
sTOT, 7 TeV = 98.0 ± 2.5 mb
sTOT,8 TeV = 101.7 ± 2.9 mb

## Slide 23
Total Cross-Section with the luminosity independent method including the 8 TeV result

## Slide 24
Obtained luminosity values
Luminosity calibration
TOTEM is able to determine the CMS luminosity:
Elastic and inelastic rates are used

## Slide 25
B/S = (8±1)%
σ*=17.8rad
(beam divergence)
|t|=0.4GeV2: B/S = (11±2)%
|t|=0.5GeV2: B/S = (19±3)%
|t|=1.5GeV2: B/S = (0.8±0.3)%
–– signal
–– background
–– combined
Signal to background normalisation
θx/sqrt(2)
σ* → t-reconstruction resolution:
Combined background (t)
-t [GeV2]
(also as a function of θy)
Data
Signal vs. background (t)
Background and resolution determination β*=3.5m

## Slide 26
Missing acceptance in θy*
Beam divergence
|ty| (diagonal 2)
|ty| (diagonal 1)
Correction error (ty):
0.31 GeV2 : 30%
0.33 GeV2 : 11%
0.35 GeV2 : 2%
0.4 GeV2 : 0.8%
0.5 GeV2 : 0.1%
|t|<0.36GeV2 removed
ty-acceptance corrections β*=3.5m

## Slide 27
Critical at low t-acceptance limit
Total -acceptance correction
Accepted (t)
1 2 3 4 5 6
Accepted (t)
Diagonal 1
Diagonal 2
Θ*

|t|<0.36GeV2 removed
No. | t [GeV2] | Θ* [rad] | Accepted  (2 diag.) [°] |  accept. correct. factor
1 | 0.33 | 1.65E-04 | 38.6 | 9.3±4.7%
2 | 0.36 | 1.71E-04 | 76.4 | 4.7±1.8%
3 | 0.60 | 2.21E-04 | 162.5 | 2.2±0.3%
4 | 1.00 | 2.86E-04 | 209.8 | 1.7±0.1%
5 | 1.80 | 3.83E-04 | 246.3 | 1.5
6 | 3.00 | 4.95E-04 | 269.0 | 1.3
Acceptance corrections β*=3.5m