## Slide 1: EIS-BEAM & EIS-MACHINE IN OPERATION QUALITY ASSURANCE MANAGEMENT FOR Safety Unit BE-ASR-SU
EDMS 1255482

## Slide 2
Contents
Introduction
Quality assurance principles for the EIS in operation
Actions to be taken by the EIS group owners & schedule

## Slide 3
To ensure and demonstrate that the safety elements are able to fulfill their safety function (i.e. protection of the personnel against beams hazards and hazards due to the operation of the machines), a set of quality assurance principles have been defined.
Introduction (1/3)
EDMS 1211886
The principles are detailed in a document which aims at compiling and standardizing the best practices already used in groups:
These principles were presented to the Joint-CSAP on 4th October 2012.

## Slide 4
Introduction (2/3)
EIS-Beam and EIS-Machine
(register available on EDMS 1182293)
Equipment concerned:
Ex.: beam stoppers, beam dumps, magnets,
MTV screens, vacuum valves, power converters, …
FTN.STP428 (TT2A)
TBSE 2106 (TT20)
Equipment interlocked with the access safety system
Ex.: low voltage and high voltage circuit-breakers, …

## Slide 5
Introduction (3/3)
Associated equipment in case of an EIS not fail safe (essential services required to ensure its safety function)
Equipment concerned:
Ex.: compressed air, electrical supply, water supply, control system (PLC)…
In case of an EIS fail safe: associated equipment having an impact on the availability of the access safety system (operational purposes)
Ex.: electrical supply…
An intervention on the circuit-breaker supplying the control unit of an EIS power converter will block the access to the area concerned.

## Slide 6
Electronic form, easily accessible (EDMS, CDD)
Identification on site of the EIS with reference to the procedure to follow.
What are the principles ? (1/4)
Training and habilitation of the personnel who will be authorized to intervene.
To be done by the group in charge of the equipment.
Written operational documentation and procedures for the personnel who have
to intervene on an EIS :
At least, a small description of the equipment with focus on the
EIS functions, of the types of controls and checks to carry out with
the precautions to take regarding the EIS functions,…

## Slide 7
40
mm
120 mm
EIS-Beam and EIS-Machine
Associated equipment
Identification on site (1/3)
XXXXXXX
The interlocked cables with the
access safety system
(on the EIS-Beam and EIS-Machine side)
20 mm
90 mm
Ex.: beam stoppers, beam dumps, magnets,
MTV screens, vacuum valves, power converters, …
Ex.: compressed air, electrical supply,
water supply, control system (PLC)…
Labels supplied by the BE Safety Unit and put in place by the equipment owner

## Slide 8
Identification on site (2/3)
BA2, PLC for the power converter
of the Main Dipoles (SMD2)
“Note d’opération: SPS et Lignes de
transfert - EIS équipments”, EDMS 1217238
BB3
Controls rack for the power converter of the Main Sextupoles LSFA

## Slide 9
Identification on site (3/3)
BA1, interlocked cable with the access safety system for the power converter MBIV1003M (TT10)

## Slide 10
What are the principles? (2/4)
Always inform the BE DSO that an intervention on an EIS is needed.
No more intervention shall take place once the “DSO tests” start.
The EIS shall be fully operational.
Written reports of interventions (electronic logbook) and functional tests of the EIS (EDMS, …). Electronic form, easily accessible. To be done by the group responsible for the EIS.
Tests of the safety chains:
  After a LS or Xmas break: “DSO tests” are carried out. Reports are prepared by the DSO and stored in EDMS,
  After a TS or during beam operation: validation test of a specific chain could be required by the DSO depending on the type of intervention carried out.

## Slide 11
What are the principles? (3/4)
During the operation of the accelerator complexes.
Authorization from DSO of BE is required for interventions on EIS:
During shutdown, if an EIS needs to be put in/out of chain.
The DSO of BE :
Defines (with BE-OP) the compensatory measures needed to guarantee
safety of the personnel during access, and when these measures can be removed.
Requests the in/out of chain to GS/ASE via the “CERN Service
Portal” for traceability purpose. The status of the EIS-Beam and EIS-Machine
per complex is stored in EDMS.

## Slide 12
What are the principles? (4/4)
To be created and maintained by the EIS
responsible or power converter responsible
in case of a magnetic EIS.
Identification sheets grouping all the relevant information of an EIS (or a set of EIS if applicable).
Example for a magnetic EIS : EDMS 1243990
Discussions are ongoing to record this information directly in a database (Layout database, InforEAM).

## Slide 13
What needs to be done by EIS responsible?
As presented to the Joint-CSAP on the 4th of October 2012:
The objective is to have the quality assurance principles for the EIS in place by the end of LS1, for the restart of the accelerators.
Group owners are asked:
To write the operational documentation and procedures + identify the EIS on site,
For the written reports of interventions (electronic logbook) and functional tests of the EIS, group owners are encouraged to contact the “Maintenance Framework Implementation Office” to use the CERN standard methods and tools.
To complete the identification sheets of the EIS.

## Slide 14
Thank you for your attention !