## Slide 1: Prospects for light-ion collisions in the LHC
D.Manglunki
with help from
Ph.Baudrenghien, J.Jowett & D.Küchler

## Slide 2: Outline
Disclaimer
Proton and ion injector chains
Running the LHC with different species
Possibilities for the source
Luminosities
Conclusion

## Slide 3: Disclaimer
Very preliminary
Not endorsed by CERN management
Only technical feasibility
Even if feasible, scheduling an actual run would be a hard battle

## Slide 4: LHC proton injector chain
Presently
  Duoplasmatron +Linac2, PSB, PS, SPS
After LS2:
  H- + Linac4
  PSB injection by charge exchange

## Slide 5: LHC Pb ion injector chain
Lead ion injector chain
ECR ion source
  Provide highest possible intensity of Pb29+
RFQ + Linac 3
  Adapt to LEIR injection energy
  Strip to Pb54+
LEIR
  Accumulate and cool Linac 3 beam
  Prepare bunch structure for PS
PS
  Define LHC bunch structure
  Strip to Pb82+
SPS
  Define filling scheme

## Slide 6: LHC ion injector chain
Presently
  ECR+Linac3, LEIR, PS, SPS
Future:
  Possibility of a 2nd ECR + 2nd linear accelerator for medical applications?
The following assumes only one ion source

## Slide 7: LHC ion injector chain
Linac3 can accelerate several species with same Z/A
  Selection can be done later in the chain (see SPS Sulphur run for NA40 & NA41 in 1986)
  Different Z/A can be switched in ~15’in Linac3 (Long LHC filling time)
The rest of the chain (LEIR, PS, SPS) can switch energy/species from one cycle to the next

## Slide 8: Running the LHC with different ion species
Issue: different Z/A, same magnetic field -> different frequencies for same orbit length
  Need “cogging” to adjust collision point in centre of experiment… and keep it there!
p-Pb (just) demonstrated with successful run
  338 bunches of > 1010 charges/bunch (p+ or Pb82+)
  Working at 4/7 of LHC nominal energy
  Peak L = 1.1x1029 cm-2 s-1
p-Pb is the most unfavourable case in terms of Z/A
  Cogging is therefore not an issue for p-O, Fe-O, etc…

## Slide 9: ECR source
The source can “deliver anything”, however…
  It takes time to commission the whole chain with new species (16 weeks minimum for LEIR/PS/SPS)
  Switching between two species within one year is difficult (~ 4 weeks to switch ECR for completely different species) -> competition with Pb-Pb and p-Pb in LHC, and primary ions in North Area (Ar, Xe, Pb)
Oxygen is support gas for Pb
  One can imagine running O for a short period within Pb year
    Opens possibility for O-O and p-O
Other ion mixtures
  N + O , S + O “Easy”
  MIVOC (Metal Ions from Volatile Compounds) for Fe…

## Slide 10: (very rough) estimation of peak luminosity
3 cases: A-A, p-A, A-B
In case of a short run, consider colliding at injection optics (b* = 10 m instead of 50 cm)
Conservative same bunch charge as Pb82+ (~ 1010)
Conservative number of bunches in LHC = 300
Assume same order of magnitude for physical emittances (~2.10-10 m)
Assume running at 7 ZTeV

## Slide 11: Estimations of Luminosity [cm-2 s-1]
 | O-O | N-N | S-S | Fe-Fe
b*=50 cm | 2.5E+29 | 3.2E+29 | 6.2E+28 | 2.4E+28
b*=10 m | 1.2E+28 | 1.6E+28 | 3.1E+27 | 1.2E+27
 | p-O | p-N | p-S | p-Fe
b*=50 cm | 2.0E+30 | 2.3E+30 | 9.9E+29 | 6.1E+29
b*=10 m | 9.9E+28 | 1.1E+29 | 5.0E+28 | 3.1E+28
 | O-N | S-O | Fe-O | Fe-N
b*=50 cm | 2.8E+29 | 1.2E+29 | 7.7E+28 | 3.8E+28
b*=10 m | 1.4E+28 | 6.2E+27 | 3.8E+27 | 1.9E+27

## Slide 12: Conclusion
No apparent show stopper but a serious study should be performed before going ahead
Scheduling might dominate decision
A second source + Linac (presently not approved) would solve some of the issues