## Slide 1: TOTEM Status of Roman Pot CONSOLIDATION & UPGRADE PROGRAM
TOTEM RP 210/220 m stand alone (special runs) TOTEM&CMS (low β*&high luminosity) RP integration of tracking/timing detectors RP – horizontal insertion at low β

## Slide 2: Overview
Presentation of TOTEM RP consolidation & upgrade plans in different meetings: 1) CMS-TOTEM (management) meeting on 5.10.2012 2) LTEX meeting on 8.11.2012 3) 1st LHC workshop on Collider Experiment Interface on 30.11.2012
+ several CMS-TOTEM technical meetings

## Slide 3: Roman Pot consolidation & upgrade strategy
Upgrade of RP detector system at 210m
- Remove RP147m and relocation at 210m - Installation of additional RPs (horizontal) at 210m - Integration of timing and pixel detectors in horizontal RPs
Guideline:
Reinstallation of RP 147m stations at 210m
Re-use of RP 147m infrastructure as much as possible (motor, cables etc.)
The new horizontal RPs could be installed during LS1 and equipped immediately/successively with new tracking & timing detectors.
The present 220m stations must not be affected (touched) by any upgrade activity, until the high beta special runs after LS1 are finished. (Research Board approved stand alone program of TOTEM at full LHC energy)
The timing detectors are installed downstream relative to the tracking detectors. (high material budget).
Depending on the running scenario after LS1 (physics high β*/low β*, calibration, alignment), relevant RPs are inserted or retracted (parking position).

## Slide 4: Present RP installation at IP5
Near 2 vertical RP top/bottom 1 horizontal RP
Far 2 vertical RP top/bottom 1 horizontal RP
Far
2 vertical RP top/bottom
1 horizontal RP
Near 2 vertical RP top/bottom 1 horizontal RP
TOTEM RP-220m (near-far)
CMS ip5 ~ 220 m
outgoing
beam
TOTEM RP-147m (near-far)
Q6
~ 1.5 m
~ 5m

## Slide 5: Remarks on Roman Pot detectors
The TOTEM physics program at high β*, special runs and p-A will be performed with the RP detectors at +/- 220m and relocated RP detectors from +/- 147m in the region of +/- 210m.
Possible additional RP detectors in the region of +/- 210m from IP5 are presently discussed in the framework of “detector upgrade studies” by TOTEM in collaboration with CMS (related to diffractive physics at low β* and high luminosities)

## Slide 6: Main goals of TOTEM experiment
- Measurement of total cross section
Forward multiplicity
Diffractive physics (soft& hard diffraction, jets)
Using luminosity from CMS
ρ parameter from compete fit
Luminosity independent
TOTEM detectors integrated in CMS (T1, T2)
TOTEM detectors integrated in LHC (RP)
TOTEM (stand alone) TOTEM&CMS at low/highβ*, special runs TOTEM&CMS at low β* and high luminosity

## Slide 7: LHC operation
Water cooled cables
TOTEM operation with RP +/- 220 - and +/-210m after LS2 in special runs
TOTEM operation beyond LS2 in special runs – high β

## Slide 8: Roman Pot upgrade overview (schematic)
1 horizontal RP
TIMING Detector
1 horizontal RP
TIMING
Detector
Near 2 vertical RP top/bottom 1 horizontal RP
1 horizontal RP
TRACKING Detector
Far
2 vertical RP top/bottom
1 horizontal RP
1 horizontal RP TRACKING Detector
Existing TOTEM RP-220m (near-far)
New horizontal RP equipped with
timing detectors
TCL-6
CMS ip5 ~ 220 m
outgoing
beam
New horizontal RP equipped with pixel
tracking detectors
Q6
~ 5-10 m
~ 5m
shielding
New
New

## Slide 9: Roman Pot (schematic-phase 1) CALIBRATION & Alignment -RUNNING with high β* & low luminosity
1 horizontal RP
TIMING Detector
1 horizontal RP
TIMING
Detector
Near 2 vertical RP top/bottom 1 horizontal RP
1 horizontal RP
TRACKING Detector
Far
2 vertical RP top/bottom
1 horizontal RP
1 horizontal RP TRACKING Detector
Existing TOTEM RP-220m (near-far)
New horizontal RP equipped with
timing detectors
TCL-6
CMS ip5 ~ 220 m
outgoing
beam
New horizontal RP equipped with pixel
tracking detectors
Q6
~ 5-10m
~ 5m
shielding
New
New
Possibility to test new timing & tracking detectors in the LHC environment –>
Tests in combination with existing RP detectors

## Slide 10: Roman Pot (schematic-phase 1) PHYSICS-RUNNING with low beta* & high luminosity horizontal and vertical RPs (far) are retracted (parking position) & vertical RPs (near) are retracted (parking position) horizontal RP near inserted
1 horizontal RP
TIMING Detector
1 horizontal RP
TIMING
Detector
hor
I
z
1 horizontal RP
TRACKING Detector
1 horizontal RP TRACKING Detector
Existing TOTEM RP-220m (near-far)
New horizontal RP equipped with
timing detectors
TCL-6
CMS ip5 ~ 220 m
outgoing beam
New horizontal RP equipped with pixel
tracking detectors
Q6
~ 5-10m
~ 5m
hor
i
z
ver
t
ver
t
shielding
optional
optional

## Slide 11: Roman Pot (schematic-phase 1) PHYSICS-RUNNING with high β* & low luminosity NEW installed horizontal RPs are retracted (parking position)
1 horizontal RP
TIMING Detector
1 horizontal RP
TIMING
Detector
Near 2 vertical RP top/bottom 1 horizontal RP
1 horizontal RP
TRACKING Detector
Far
2 vertical RP top/bottom
1 horizontal RP
1 horizontal RP TRACKING Detector
Existing TOTEM RP-220m (near-far)
New horizontal RP equipped with
timing detectors
TCL-6
CMS ip5 ~ 220 m
outgoing beam
New horizontal RP equipped with pixel
tracking detectors
Q6
~ 5-10m
~ 5m
shielding

## Slide 12: Roman Pot (schematic-phase 2) PHYSICS-RUNNING with low β* & high luminosity ALL horizontal RPs are inserted
1 horizontal RP
TIMING Detector
1 horizontal RP
TIMING
Detector
1 horizontal RP PIXEL Detector
2 vertical Rp tracking
1 horizontal RP
TRACKING PIXEL Detector
1 horizontal RP TIMING Detector 2 vertical RP tracking
1 horizontal RP TRACKING PIXEL Detector
Existing TOTEM RP-220m (near-far)
New horizontal RP equipped with
timing detectors
TCL-6
CMS ip5 ~ 220 m
outgoing
beam
New horizontal RP equipped with pixel
tracking detectors
Q6
~ 5m-10m
~5m
shielding

## Slide 13: Integration study of new horizontal RPs at 200m
Sector 4/5

## Slide 14: Work packages –> Roman Pot installation (CMS, PH-DT, EN-CV, BE-ABP-ICE, LTEX)
WP1-T: removal of RP@147m (Radio protection, RP stockage, machining of flanges)
WP2-T: transfer of supplies from 147m -> 220m (motor power lines, patch panel, LV, + new HV)
WP3-T: installation of new fibres
WP4-T: RP@147m motor & mechanics (preparation for reuse at 220m, adaptation of mechanics, installation of motors etc.)
WP5-T: Flanges – interface to LHC (adaptation of thin window, rotation by 90° for timing detector, flanges, beam-pipe )
WP6-T: beam-pipe
WP7-T: LHC Impedance study (impedance study – RP was approved for highest luminosities -> RP rotated by 90°, concentration at 220m)

## Slide 15: Roman Pot at 147m & 220m
Relocation of RPs & patch panel from 147m to 200m
patch panel
Position of new RPs
patch panel (relocated from 147m)

## Slide 16: Patch panel at 147m

## Slide 18: Roman Pot & detector package
Temporary location of RP 147m components in H8 TOTEM test beam line after dismounting

## Slide 19: Work packages –> Detector Sensor CMS-TOTEM
WP1-D: Si Pixel (prototype test, integration & preamp, readout)
WP2-D: Timing-Detector (prototype test)
WP3-D: Timing-TDC
WP4-D: Timing-Clock distribution
WP5-D: Readout board interface to CMS

## Slide 20
Possible housing for timing detector
Impedance not favorable
Flange size big enough to integrate the timing detector

## Slide 21: Roman Pot (rotated by 90°) Integration of Cherenkov timing detector

## Slide 22: Integration study of C-timing detector in RP (CMS-TOTEM)

## Slide 23: Horizontal RP with Cherenkov timing detector

## Slide 24: TOTEM-RP study of 3D sensors TOTEM-RD50 (G. Pellegrini) [IBL – CNM]

## Slide 25: Work packages –> Optimization CMS-TOTEM
WP1-O : optimal position of new RPs
WP2-O: optimal shape & size of sensors (pixel size, adaptation, radiation zone)
WP3-O: particle timing – vertex reconstruction
WP4-O: detector position (calibration, alignment)
WP5-O: Material budget (detector performance, machine protection)

## Slide 26: RP Integration study

## Slide 27: Integration study of TCL6 and Roman Pots

## Slide 28: COLLIMATOR requirements for forward physics

## Slide 29: COLLIMATOR TCL4 & TCL6

## Slide 30: RP-TOTEM <-> LHC
In 2011 and 2012 specific RP tests & insertions were performed at standard LHC settings to study:
Roman Pot <-> LHC : RP heating & beam stability
Roman Pot detector : rates & background
Observations during low β* run (2012): [LHC-MPP M. DEILE, December 2012] Insertion of RP horizontal at 220m ->

## Slide 31: List of Insertions at b* = 0.6 m
Date | Pots involved | min. dist. | Observations, Result | Consequence
16.10. | all V all H | 12 s 30 s | no problem dump on XRPH.A6R5.B1 (slow losses, 5s) | no UFO activity
05.11. | all H | 30 s | dump on XRPH.A6R5.B1 (slow losses, 5s) | no UFO activity
14.11. | all H | 32mm ~ 270 s | dump on XRPH.A6R5.B1 (fast losses) | UFO activity in 6L5
16.11. | H, not A6R5.B1 | 14 s ~ 2mm | no problem, beams separated by 4s | slow losses (5s) in each ramp until conditioning (heat up) of beam screen in Q6
(*)
(*) The (fast) UFOs in 6L5 were later found to originate from TCL5 [Tobias]

## Slide 32: Comparison BLMs & Beam Vacuum
Sector 5-6
BLMEI.06R5.B1E10_XRP
BLMQI.06R5.B1E20_MQML
BLMQI.06R5.B2I20_MQML
BLMQI.06R5.B1E10_XRP_MQML
BLMQI.06R5.B2I10_MQML
BLMQI.06R5.B1E30_MQML
BLMQI.06R5.B2I30_MQML
VGPB.2.6R5.B.PR (14 m upstream of Near: Q5 exit)
VGPB.4.6R5.B.PR (14 m upstream of Near: Q5 exit)
VGI.77.6R5.B.PR (6 m upstream of Near)
VGPB.235.6R5.B.PR (4 m downstream of Far: Q6 entrance)
05.11.2012
Note: no pressure increase in any gauge further upstream (cell 5R5).

## Slide 33: Temperature Sensors on Detector Hybrid Boards: Sector 5-6 (Beam 1)
56-220-F-H moving towards beam
other pots in garage
dump at 13:52

## Slide 34: Temperature Sensors on Detector Hybrid Boards: Sector 4-5 (Beam 2)
Main temperature effect from chips changing to run mode; small additional increase (3 deg.) from pots moving very close to
the beam. UFOs cannot be resolved.
Readout chips in sleep mode
Readout chips in
run mode
Run mode
45-220-F-H moving towards beam
45-220-N-H moving towards beam
Sleep mode
Run mode
Sleep mode
other pots in garage
dump at 13:52

## Slide 35: Fill 3188 with RP Insertion, Cell 6R5 _
BLM and vacuum spike,
no dump

## Slide 36: Fill 3188 with RP Insertion, Cell 6L5

## Slide 37: Fill 3188, Cell 7R1 (ALFA)
slight vacuum degradation at injection,
no spike in ramp

## Slide 38: EM coupling of RP (RP in garage position)
The temperature in the Roman Pot increases due to the EM coupling with the LHC
-> cooling of RPs is mandatory when LHC beam is injected
-> modification of evaporative cooling system by integrating a safety mode to operate above dew point in case of vacuum problem
Cooling of RP was switched off

## Slide 39: RP optimization
RP optimization ongoing –highest priority
Ferrite treatment during LS1
TOTEM – RP
OLD TOTEM RP prototype

## Slide 40: Optimization of RF characteristics (first preliminary results B. Salvant, BE-ABP-ICE)
Study of new RP housing
Present RP housing
Study of possible RF shielding
for existing RP
Study is ongoing
Not all issues are solved yet !
result without ferrite
result with ferrite

## Slide 41: Integration study: cylindrical pot with timing/tracking detector

## Slide 42: Roman Pot detector system study of combination: Si strip- Si pixel- timing (schematic)
CMS ip5
RP + 200m
timing
tracking
RP - 200m
beam halo
40 MHz-VFAT Si-strip detector
PIXEL detector
SHOWER
double arm coincidence
trigger
trigger
pileup bunch crossing

## Slide 43: Conclusion (1)
TOTEM has confirmed the complete dismounting of RP 147m stations during LS1 (as early as possible)
The removal of the RPs at +/- 147m allows the installation of TCL4
The RPs of +/- 147m will be reinstalled in the +/- 210 m region
TOTEM has proposed to install additional horizontal RPs around +/-210m of ip5 during LS1
These new horizontal RP detectors will allow tracking & timing at low β* and high luminosity
Integration studies were performed by TOTEM and CMS to integrate a “Cherenkov “timing detector in a (horizontal) RP
The re-use of motor and infrastructure (patch panel, cooling) was studied
Impedance studies for the horizontal RPs are ongoing
Studies are ongoing to improve the RP geometry (RF, material budget)

## Slide 44: Conclusion (2)
The developments of Roman pots as ‘carriers’ for tracking and timing detectors with the potential to approach the LHC beam to very close distances are ongoing.
The combination of the existing TOTEM RPs (alignment, trigger) with new RPs, equipped with tracking and timing detectors is under study.