## Slide 1
Time alignment
All sub-detectors are optimising readout as compromise between robustness and cost. OK, but……..
We must consider special scenarios where more information is required (eg more bits of BXID).
For example,
time alignment within each sub-detector
time alignment of LHCb
(Remember we don’t have the L0 trigger !!!!)

## Slide 2
BX0
BX1
BX2
BX3
BX4
BX5
BX6
BX7
BX8
BX9
BX10
BX11
BX12
BX13
BX14
BX15
BXIDRst
-SODIN
BXIDRstA
BXIDRstB
‘Beam’ data in
A and B
3562
3563
0
1
2
3
4
5
6
7
8
9
10
11
12
13
3562
3563
0
1
2
3
4
5
6
7
8
9
10
11
3561
3560
BXIDA
BXIDB
Beams collide in only one BX (or a few well-spaced BXs)
Detector A sends a packet with data and BXID = 4
Detector A sends a packet with data and BXID = 2
H3653
H0
H1
H2
H3
H4
Data4
H5
H6
H7
H3653
H0
H1
H2
H3
H4
Data2
H5
H6
H7
Difference used to align BXIDResets
delayA
delayB

## Slide 3
Time alignment: useful tools
Example of a SPECIAL MODE:
VELO data packets (30-bits):
9-bit BXID
8-bit Super-pixel Hit Map
13-bit Super-pixel address
Normal running
Time alignment running
12-bit BXID
3-bit SP Hit Count
13-bit Super-pixel address
2-bit ?
Another example (in FE specs!):
TFC-alignment mode:
Replace data with TFC command received for each BX
TFC alignment
12-bit BXID = N
TFC command received at BXID = N
Then compare to see if offsets are correct/consistent

## Slide 4
Time alignment possibilities
Test pulse injection (TFC triggered & phase adjustable)
But is still sensitive to cable delays
Cosmics
Gives absolute timing, but rare……
Laser (or similar, TFC triggered & phase adjustable)
Very useful, but not all detectors are sensitive
Beam
Ultimate tool, but quite expensive!

## Slide 5
We still have time to put helpful features in the front-end designs, so…….
Next meeting in Feb 2014:
sub-detector ideas for time-alignment & commissioning, and how to implement them