## Slide 1
2013.3.18-19, at KEK, Junji Urakawa
Contents :
1. Introduction
2. LUCX and QBT project
3. Necessary technologies for high brightness
4. High reflective mirror development
5. New plans and prospects
Quantum Beam program at LUCX and STF
Overview and prospects

## Slide 2
Evolution of photon source：X-ray source based on accelerator and laser
1980
1990
2000
2010
Second Generation Photon Factory
Third Generation Photon Factory
Chirped Pulse Amplification(1985)
Higher harmonic wave
: Coherent soft-X-ray
Femto-sec Science
Ato-sec. Science
XFEL proposal
ERL proposal
Bunch Slice
Plasma X-ray
Ultra-high field Science
Coherent
Ultra-short Pulse,
Compact X-ray source
Next Generation Photon Source
SLAC-XFEL
DESY-XFEL
SPring8-XFEL,SCLA 2011
2011, ~mJ X-ray pulse is realized

## Slide 3
To stronger and brighter photon beam
Low brightness X-ray
Diffraction
Large sample
Small sample (< 1mm)
Diffraction pattern
High brightness X-ray
Protein crystal
10mm photon source is considered, which means 0.2 mmmrad normalized emittance.
1mrad angular spread collimation means small energy spread.
Smaller source is
realized by focusing
laser beam and
electron beam at IP.
We have to supply
low emittance and
high intensity
electron beam.
Our target is
Brightness 1017
Photons/sec/mm2/mrad2
in 0.1%b.w.

## Slide 4: Development of Brightness of Light Sources

## Slide 5
5
5
January 2009
Photon Flux :
~1010 photons/sec1%bw
Brightness 1013
Photons/sec/mm2/mrad2 in 0.1%b.w.
X-ray exposing time more
than 100sec
Reduce electron beam emittance by 100.
Reduce the energy spread of electron beam by 10.
Reduce electron bunch length at IP , we select high power electron Linac
and optical cavity to generate X-ray based on ICS.
Then, we have a possibility to get 1017and
one shot measurement for X-ray imaging.

## Slide 6: 2. LUCX and QBT project
To downsize the accelerator, we have installed a 3.6cell rf-gun and a 12cell booster.
  3.6cell rf-gun
    Beam test has been started from Jan 2012.
  12cell booster
    This booster was installed in last June.
1.6cell
Rf-gun
3m accelerating tube
3.6cell
RF-gun
12cell booster
New optical cavity for
hard X-ray generation
Microwave resonator cavity
for soft X-ray generation

## Slide 7
X-ray yield
334 photons/train at detector on July 2011 same as 2007.
X-ray yield
1447photons/train
at detector on Oct.
2011
2.1x105photons/sec
at 12.5Hz operation
2～3 times
0.4mJ/pulse
From 2011,
Normal C. Linac
357MHz mode-locked laser

## Slide 8
The mirror of two mirror cavity had the surface damage around 2 to 6mJ/pulse.

## Slide 9
We destroyed the mirror coating two times. First occurred when the waist size was ~100mm with burst amplification and 42cm two mirror cavity. Second occurred when the waist size was 30mm with the burst amplification and the 42cm two mirror cavity. Now we are using 4 mirror cavity with smaller waist size at IP. From our experience, we have to reduce the waist size to increase the laser size on the mirror and need precise power control for the burst amplification. I guess about storage laser pulse energy from 2mJ to 4mJ destroyed the mirror coating with the waist size of 30mm. Also, we found the damaged position was not at the center.
2008
2011

## Slide 10
LUCX accelerator

## Slide 11
LUCX 4-mirror optical super-cavity

## Slide 12
LUCX 4-mirror optical super-cavity

## Slide 13
LUCX 4-mirror optical super-cavity

## Slide 14
LUCX 4-mirror optical super-cavity

## Slide 15
Diagram of optical setup
R. W. P. Drever et al., Appl. Phys. B, 1(1983)97.
Super-cavity enhances the power inside the cavity by accumulating the laser radiation more than thousands of times at the same phase.
>the accuracy of cavity length > less than nano-meter
Main laser (CW)
CCW circulate

## Slide 16
Stabilization of stored energy
The result of stored power stabilization by opposite circulating laser
Before After

## Slide 17
Wavelength | Repetition | Power | Pulse energy
1064nm | 357MHz | 100kW | 300uJ
Size(H) | Size(V) | Pulse duration | Col. angle
89um | 85um | 7ps | 7.5°
Laser-Beam parameters at CP
Energy | Repetition | Charge | N. bunch
22.8MeV | 357MHz | 900pC | 150
Size(H) | Size(V) | Bunch length | Emi (H) | Emi (V)
85um | 95um | 15ps | 10πmmmrad | 7πmmmrad
Laser-Electron Beam parameters at LCS Collision point
Laser (inside the Super Cavity)
Electron Beam

## Slide 18
As X-ray detector,
MCP (Micro-Channel Plate) was used
for detecting LCS X-ray and achieving the X-ray image
X-ray detector -MCP-

## Slide 19
Diagram of Imaging Setup
○MCP is the largest S/N detector
for LCS
○I.I. for gating the LCS from BG
○Large gain with MCP (~10^7)
and I.I. (~10^4)
＞Spatial resolution will be bad
but suitable for first detection
X-ray detector -MCP-

## Slide 20
Timing Scan
Timing search

## Slide 21
Position Scan
Horizontal Vertical
Position search

## Slide 22
Intensity
Intensity dependence

## Slide 23
X-ray image by MCP
Imaging test by 9keV LCS X-ray
Fish backbone Chile pepper
Small flower

## Slide 24
X-ray image by MCP
Imaging test by 9keV/15keV LCS X-ray
Peanut
9keV
15keV

## Slide 25
X-ray detector -SOI pixel sensor-
SOI pixel sensor is the semiconductor detector using SOI (Silicon-On-Insulator) technique
>detection and read out are on same board.
>high S/N and high spatial resolution
Y. Arai et al., Nucl. Instrum. Meth., A636(2011)S31-S36

## Slide 26
X-ray evaluation by SOI sensor
Counts/event
Counts/event
Beam Background
LCS X-ray and
Beam Background
DAQ Data Loss
DAQ Data Loss

## Slide 27
X-ray evaluation by SOI sensor
ADC Count
i.e. X-ray Energy
ADC Count
i.e. X-ray Energy
X-ray Spectrum
(quasi-monochromatic)
X-ray Spectrum
(quasi-monochromatic)
BG subtracted
Beam BG Spectrum

## Slide 28
Energy | Bandwidth (within collimator) | X-ray / pulse (SOI)
8~9keV | 8% b.w. | 36.4 ph/pulse
X-ray/train (SOI) | X-ray/train (Total) | X-ray/sec (Total)
5460 ph/train | 5.1×105 ph/train | 6.38×106 ph/sec (12.5Hz)
CAIN Simulation results | 
1Train (SOI) | 1Train (Total)
7015 | 8.2×106
LCS X-ray specification at LUCX

## Slide 29
X-ray image by SOI sensor
SOI pixel sensor imaging by 9keV LCS X-ray
Chile pepper (Preliminary)

## Slide 30
X-ray image by SOI sensor
SOI pixel sensor imaging by 9keV LCS X-ray
Small fish (Preliminary)

## Slide 31
One turn length : 7.56m, horizontal laser waist size : 109mm in 2s,
Crossing angle : 7.5 degrees, vertical laser waist size : 50mm in 2s,
Horizontal laser size on laser injection plane mirror : 2.92mm,
Vertical laser size on laser injection plane mirror : 6.4mm
Laser pulse energy in cavity : 8mJ, distance between concave mirrors :
1.89m, 7.56m means this cavity has 9 laser pulses.
Use two inch mirrors and increase the threshold damage energy.
Completed this device in this September last year and start the generation
of X-ray from mid. of Feb.. We will confirm the performance soon.

## Slide 32
Energy | 30MeV
Intensity | 0.4nC/bunch
Number of bunch | 1000
Beam size at the collision point (1σ) | 33μm ×33μm
Bunch length | 10ps
Bunch spacing | 2.8ns
Energy | 1.17eV(1064nm)
Intensity | 8mJ/pulse
Waist size(1σ) | 55μm ×25μm
Pulse length | 7ps
Photon flux more than 108 per second
My colleagues got the X-ray
Flux of 106 at 12.5Hz.
Still we have problem
on cavity rigidity.
We need the improvement
of table and installation of
high reflectivity mirrors.

## Slide 33
View of QBTP from Beam Dump
X-ray Detector
Beam Dump
RF Gun Laser
Quantum Beam Technology Program:
Beam commissioning started from mid.
of February 2012.
To contribute the development for
life science innovation and
green innovation
Development for Next Generation Compact High Brightness X-ray
Source using Super Conducting RF Acceleration Technique

## Slide 34
2D four mirror cavity to generate
X-ray with two cylindrical lenses

## Slide 35
Two laser pulses are circulating with the spacing of 6.15ns in a ring
optical cavity.
Laser evolution is
same in tangential
and sagittal plane.
Laser waist size in mm
10 20 30 40 50 60 70 80 90
Stable
Region
Stable
Region
Change to 2D 4-
mirror optical
cavity with two
cylindrical lenses
instead of two
plane mirrors.
profile of Transmitted laser from cylindrical mirrors.
We confirmed the effect of the cylindrical mirrors.

## Slide 36
Beam size 10mm
Change to head collision scheme to get another enhancement of 5 and
to increase laser pulse duration ~20ps.
Quantum project
at STF

## Slide 37
We have a big problem about mirror
support table rigidity.
Figure shows ideal case but real
system has complicated
connections between movers
and table. It was bad selection
which we had. R&D is still under way.
Brightness 1017
Photons/sec/mm2/mrad2 in 0.1%b.w.
Equivalent to 2.5 Generation
Synchrotron Radiation.

## Slide 38
Achieved beam at STF for QBT project 07132012 Hayano V1.0
Laser beam size : about 80mm
Target : less than 20mm
Background level is acceptable.
X-ray signal does not detected so far.
This experiment is under going.
(RF feedback ON) 03.22.2012
50pC/bunch
1ms beam acceleration (15pC/bunch)
(Gun/SCRF RF feedback ON) 06.08.2012
Swap
Measurement of beam emittance by wire
scanner 06.13.2012
2012/07/04測定
WM-PRM-05で一番小さく
絞れた時。
ただし、WM-PRM-07では
大きかった。
WM-PRM-05
σx: 17.5[µm]
σy: 25.3[µm]
このとき、
WM-PRM-07
σx: 55.8[µm]
σy: 29.3[µm]
(ログブックのデータのみ
画像データなし)
σx: 17.5[µm]
σy: 25.3[µm]
σx: 36.2[µm]
σy: 36.1[µm]
Min. beam size＠WM-PRM-07
Min. beam size＠WM-PRM-05
WM-PRM-05
Dispersion measurement
@WM-PRM—05, -07, dispersion measurements
SC phase 240deg 40.58 MeV/c (B1 150.20A)
SC phase 250deg 40.02MeV/c (B1 148.10A)
⊿x ηx ⊿y ηy
WS-PRM-05 85um 6.2mm 14um 1.0mm
WS-PRM-07 42um 3.1mm 14um 1.0mm
(07.04.2012）
07.04.2012
07.04.2012
1ms beam from L-band RF Gun
Accelerated 1ms beam
Min. emittance so far
07.04.2012
WM-PRM-07
WM-PRM-05
Target size : 10μm

## Slide 39
Generation of ultra low emittance electron beam by photo-cathode DC electron source
39
Ceramic tube for
High voltage isolation
cathode
anode
normalized emittance
＝0.054mm-mrad
500kV-DC Gun
550kV achieved and 10mA beam generation test
started. Target value of the emittance is 1.0mm-mrad
as first stage.
3. Necessary technologies for high bright
Since we achieved 500kV DC gun technology,
we are going to develop cryo photo-cathode RF gun from 2013 hopefully.

## Slide 40
3.6 cell RF-Gun
Start of beam acceleration test from 1/11,2012.
11MeV beam at 120MV/m, from 100bunches/pulse
to 1000bunches/pulse beam generation
9.6MeV beam in
a week RF aging
with ~20.3MW RF
input power
PARMELA SIMULATION
Two years ago
In last year
3.6 cell RF Gun Installation

## Slide 41
41
Manufactured and Tested four 9-cell super conducting cavities
Recently, we operated the 9-cell cavity
with 38MV/m.
CW operation
Pulse operation

## Slide 42
Ca. Finesse 4850, design gain ~2000 was confirmed by generation of
gamma-ray last year. Also, laser waist size was less than 13mm.
2-Mirror Cavity --> 4-Mirror Cavity

## Slide 43
Experiments at the KEK ATF
detector
γ
Laser cavity
ATF parameter
1.3GeV
1×1010 electron/bunch
Up to 10 bunch/train
2.16×106 turn/s
Recent Compton activities at KEK
14th Feb 2013
Detail explanation of optical cavity technology

## Slide 44
laser cavity
IP
Plane mirror
Concave mirror
Plane mirror
Concave mirror
Recent Compton activities at KEK
14th Feb 2013

## Slide 45
Finesse: 4040±420 4040±110
PBS
Pockels cell
PD
Decay time measurement
Airy Function
Both Consistent but smaller than expected one, 4850from
mirror reflectivity (99.99%) due to mirror surface
contamination.
Finesse measurement
Recent Compton activities at KEK
14th Feb 2013

## Slide 46
Polarization property
Cavity length
L-pol
R-pol
  geometric phase due to twisted pass
  cavity only resonates with circular polarization state
  Different resonance points of left and right polarization
Recent Compton activities at KEK
14th Feb 2013

## Slide 47
Control method using Polarization property
Different slope in left and right pol.
Recent Compton activities at KEK
14th Feb 2013

## Slide 48
Cavity control
Stack power
control
Stacking power [W]
L-pol
R-pol
1.4% fluctuation
->4pm
110pm
Laser power = 2.6kW
Timing jitter = 8ps
Rough enhancement 1800
or less due to mirror
contamination and injection coupling.
Recent Compton activities at KEK
14th Feb 2013

## Slide 49
Gamma-ray yield
5 bunch/train (7.7mA)
Gamma energy [GeV]
Count
~2.6×108/sec
This is very high brightness
because of high quality
electron beam (1nm
horizontal and 10pm
vertical emittance).
2970±20 MeV
⇒ ~120gs/train
Recent Compton activities at KEK
14th Feb 2013

## Slide 50
Gamma-ray yield each bunch
time [ns]
Gamma yield [A.U.]
time [ns]
Bunch current [A.U.]
no bunch dependence ( yield is proportional to e- current)
5bunches/train
e-
laser
g
5.6ns
Recent Compton activities at KEK
14th Feb 2013

## Slide 51
Input power to injection coupling
mirror :
Burst mode operation : a few kW
Operation (pulsed peak power)
CW mode operation : 200W
More than 20,000 times
in the case of low power
Fiber Amp
Burst Amp
100 times
10uJ/pulse
30mJ/pulse
100nJ/pulse
163 times
162.5MHz mode-locking
100mW mode-locked
Oscillator
2D 4-mirror optical cavity
Fiber laser system developments and
pulse laser storage

## Slide 52
X-ray Imaging by I-MCP+I.I. and SOI
Phase contrast X-ray imaging is next step at LUCX.
X-ray Imaging by SOI Pixel Detector
～30keV
～15keV

## Slide 53
High resolution X-ray detector
Circuit
Insulator(SiO2)
monolithic silicon pixel detector based on SOI
(Silicon On Insulator) technology.
Energy spectrum &
High-resolution X-ray image
can be measured in one detector!
Almost inactive with g-ray more than 100 keV

## Slide 54
4. Mirror development
We made the contract to manufacture 99.999% reflective mirrors
with LMA in Lion France. I requested the transmissivity more 2ppm.
It means the scattering and absorptive loss are less than 6ppm.
We bought many mirror substrates from American companies, 1 inch,
2 inch and special sized mirror with sub-A micro-roughness.
In this Feb., we will make the coating at LMA. Before this,
we can use ordered mirrors to Japanese company ,which has about
(99.99+0.005) % with the transmissivity more than 8ppm.
LIGO developed big mirror with loss under 1ppm many years ago.
We have a plan the development of thin thickness of concave mirror
will start to realize X-ray high transmission.

## Slide 55
We destroyed the mirror coating two times. First occurred when the waist size was ~100mm with burst amplification and 42cm two mirror cavity. Second occurred when the waist size was 30mm with the burst amplification and the 42cm two mirror cavity. Now we are using 4 mirror cavity with smaller waist size at IP. From our experience, we have to reduce the waist size to increase the laser size on the mirror and need precise power control for the burst amplification. I guess about storage laser pulse energy from 2mJ to 4mJ destroyed the mirror coating with the waist size of 30mm. Also, we found the damaged position was not at the center.
2008
2011
From experimental results at LUCX X-ray generation based on ICS.

## Slide 56
Development for stronger mirror : I want to start the collaboration with NAO (Gravitational
Wave Observatory group), Tokyo University (Ohtsu Lab.), Japanese private Co., LMA and LAL
hopefully.
Enlarge mirror size : we started the change from one inch to two inch mirror.
LMA is preparing mirrors with reflectivity of 99.999% and loss (absorption and scattering)
less than 6ppm.
We ordered many substrates with micro-roughness less than 1 A to approach low loss mirror.
We understood the necessity of good clean room to handle the high reflective mirrors
in the case of the mirror which has high reflectivity more than 99.9%.
5. We have to develop how to make the stronger surface which has higher damage threshold.
Photo-chemical
etching occurred
by dressed photon.
Measurement of
surface roughness
for super-polish.
Reduce the loss
,which means low
absorption and
scattering.
We learnt a lot of things which humidity in Japan is high and makes OH contamination to
increase the mirror absorption. 50% humidity is suitable to handle the mirrors, especially high
quality mirrors. We confirmed this problem. Hear next talk.

## Slide 57
High brightness X-ray generation at c-ERL
as a demonstration through beam experiment
Injector
Super-conducting linac
Beam dump
Laser
E-bunch
X-ray
-
Pulse laser optical cavity
35MeV electron beam x 1mm laser = 23keV X-ray
Energy recovery
2015 experiment
1013 photons/(sec・1%b.w.)
5. New plans and schedule
Realize the Brightness 1019Photons/sec/mm2/mrad2 in 0.1%b.w.
SPring-8
World highest
Av. Brightness 1021
Photons/sec/mm2/mrad2 in 0.1%b.w.
from 27m undulator at
SPring8

## Slide 58
Energy | 30MeV
Intensity | 0.4nC/bunch
Number of bunch | 1000
Beam size at the collision point (1σ) | 33μm ×33μm
Bunch length | 10ps
Bunch spacing | 2.8ns
Energy | 1.17eV(1064nm)
Intensity | 8mJ/pulse
Waist size(1σ) | 55μm ×25μm
Pulse length | 7ps
Photon flux more than 108 per second
Brightness 1015
Photons/sec/mm2/mrad2 in 0.1%b.w.
Exposure time less than several second.

## Slide 59
Demonstration experiment for ERL
59
High voltage DC electron source
Detector facility for
Gamma-ray detection
Four mirror optical
cavity for Gamma-ray
generation
Compact ERL is to use laser Compton γ-ray
generation and it’s application
Illustration by Rey Hori
60MeV Electron Beam, 532nm (green laser)
1.3GHz collision, X-ray 130keV
Number of photons per 1% width
5x1013
130keVx5x1013=1.04J/s
330 kGy (X-ray size 0.2mm diameter)
Super conducting cavities
Second phase of
cERL plan in ~2018.
Notes: This viewgraph shows the principle nuclear material detection by laser Compton gamma-rays.
Laser Compton scattering is a scheme to generate monochromatic gamma-rays by collision of a high-energy electron beam and a laser beam. The gamma-ray energy can be easily tunable by changing electron energy or laser wavelength.
If we irradiate a gamma-ray beam tuned at an energy specific to Pu 239, 2143 keV, nucleus of Pu-239 is excited by gamma-ray absorption and re-emitt another gamma-ray instantaneously. Observing this re-emitted gamma-ray, we can detect Pu-239.
This is nuclear resonance fluorescence.
The combination of laser Compton gamma-ray and nuclear resonance fluorescence has several advantages. First, nondestructive detection of radioactive and stable nuclides is possible. Second, We have excellent signal-to-noise ratio in the energy resolved gamma-ray detection. Third, detecting many kind of nuclides by scanning gamma-ray energy is also available. Fourth, we can detect materials through a thick shield. Finally, this is full utilization of high-power lasers and high-brightness electron beams, which show tremendous progress continuously.

## Slide 60
New Quantum Beam Technology Program(QBTP) will be supported by MEXT from 2013.7? to 2018.3 (~5 years project), I hope.
Approved project should include two Japanese Companies at least and the development for CW super conducting acceleration technologies. Normal conducting accelerator system and super conducting accelerator system for compact high brightness X-ray source should be realized by joint research with Japanese companies.
～１２ｍ
～８ｍ
Downsizing
to 6m x 8m
Normal conducting accelerator system for compact high
brightness X-ray
Add 4k refrigerator to use superconducting
cavity keeping compactness in future.
Thank you for your attention.