## Slide 1: The silicon strip vertex detector of the Belle II experiment
Yoshiyuki Onuki
On behalf of BelleII/SVD collaboration
University of Tokyo/Kavli IPMU

## Slide 2: BelleII experiment
Measurements of CKM matrix elements and angles of the unitary triangle
CP & T & CPT test
Observation of direct CP violation in B decays
Measurements of rare decays (e.g., B→tn, Dtn) and the tension vs sin2f1
b→s transitions: probe for new sources of CPV and constraints from the b→sg branching fraction
Forward-backward asymmetry (AFB) in b→sll
Observation of D mixing and charm-meson physics
Searches for rare t decays
Observation of new hadrons and resonances
Precise tests of the phenomena which expected to be contributed from beyond SM with enormous B-meson and t lepton data
BelleII
BelleII experiment is super B-factory with asymmetric energy of e+e- collider

## Slide 3: SuperKEKB collider
e- 7GeV 2.6 A
e+ 4GeV 3.6 A
Target: L = 8x1035/cm2/s
SuperKEKB
Colliding bunches
Damping ring
Low emittance gun
Positron source
New beam pipe
& bellows
Belle II
New IR
TiN-coated beam pipe with antechambers
Redesign the lattices of HER & LER to squeeze the emittance
Add / modify RF systems for higher beam current
New positron target / capture section
New superconducting /permanent final focusing quads near the IP
Low emittance electrons to inject
Low emittance positrons to inject
Replace short dipoles with longer ones (LER)
E.Kikutani / M. Masuzawa
KEKB
1036
ｘ４０

## Slide 4: Luminosity projection

## Slide 5: Detector upgrade
SVD: 4 DSSD layers g 2 DEPFET layers + 4 DSSD layers

## Slide 6: Strip Vertex Detector(SVD)
Layer | Sensor/ladder | Origami | Ladder | Length | Radius | Slant angle | Occupancy
3 | 2 | 0 | 7 | 262 | 38 | 0 | 6.7%
4 | 3 | 1 | 10 | 390 | 80 | 11.9 | 2.7%
5 | 4 | 2 | 12 | 515 | 104 | 17.2 | 1.3%
6 | 5 | 3 | 16 | 645 | 135 | 21.1 | 0.9%
Good vertex resolution(incl. KS→pp)
Low pT tracking (D*→Dpslow)
Low material budget
Fast readout(trig. max~30kHz)
CO2 cooling pipe along with APV chips
BelleII vertex detector(PXD+SVD)
@Low energy high luminosity machine

## Slide 7: Double-sided Silicon Strip Detector(DSSD)
 | Readout strip(p/Rf) | Readout strip(n/z) | Readout pitch(p/Rf) | Readout pitch(n/z) | Chip size (mm2) | Active area (mm2)
Large | 768 | 512 | 75 μm | 240 μm | 124.88x 59.60 =7442.85 | 122.90x57.72 =7029.88
Trapezoidal | 768 | 512 | 50-75 μm | 240 μm | 125.58x(60.63+41.02)/2=6382.60 | 122.76x(57.59+38.42)/2=5893.09
Small | 768 | 768 | 50 μm | 160 μm | 124.88x40.43 =5048.90 | 122.90x38.55 =4737.80
Layer3: Small DSSD
  Manufacturer: HPK
  Chip size: 124.88 mm ×40.43 mm
  Thickness: 320mm
  P-stop layout: Atoll p-stop
Layer4,5,6: Large DSSD
  Manufacturer: HPK
  Chip size: 124.88 mm ×59.60 mm
  Thickness: 320mm
  P-stop layout: Atoll p-stop
Layer4,5,6: Trapezoidal DSSD
  Manufacturer: Micron
  Chip size: 125.58 mm ×60.63(41.02) mm
  Thickness: 300mm
  P-stop layout: Atoll p-stop

## Slide 8: Readout Chip APV25
APV25
Developed for CMS (LHC)
0.25 µm CMOS process
Shaping time 50ns
Input ch. 128ch
Power consumption 350mW
Thickness 100mm(thinned)
Radiation tolerance >30Mrad
ENCC [e] 250e+36e×C[pF]
Multi-peak mode (read out several samples along shaping curve)
Schematics of one channel
40x luminosity with harsh environment from beam background is expected.
We need fast shaping.

## Slide 9: Chip-on-sensor method, Origami
DSSD
Airex
(Polymer foam)
Bonding wire
APV25
DSSD
Airex
Kapton hybrid
APV25
Cooling pipe
Wrapped FLEX
fanout for P-side
Support ribs
Support ribs
Chip-on-sensor for double-sided readout, named “Origami”
All chips aligned on one side  single cooling pipe (Ave. 0.59% X0)

## Slide 10: Breakdown of material budget
DSSD+ Origami | Rib | DSSD | Airex | Origami | CO2 Cooling | 100mm Glue | Total % X0
HPK+1Origami | 0.035 | 0.340 | 0.055 | 0.133 | 0.037 | 0.033 | 0.593
HPK+2Origami | 0.035 | 0.340 | 0.055 | 0.266 | 0.037 | 0.033 | 0.733
Micron | 0.035 | 0.320 | 0.055 | 0 | 0 | 0.011 | 0.421
Micron+Origami | 0.035 | 0.320 | 0.000 | 0.133 | 0 | 0.033 | 0.576
Origami +Z flex
Origami CE flex(length 450mm)
Origami −Z flex
…Three Cu layer FLEX(Taiyo Co.)
Ribs…
Airex foam sandwiched by
Carbon fiber ribs
Glue…Araldite 2011
Glue
Airex
PF2
PF1
PB2
PB1
PA1
PA2
DSSD
Ribs
L6 ladder explosion view

## Slide 11: SVD Ladders
Ladder production cites:
L3 Melbourne(Australia)
L4 TIFR(@Kavli IPMU)
L5 HEPHY(Vienna)
L6 Kavli IPMU(Japan)
Possible contribution for FW&BW module by INFN(Italia)
World wide collaborated ladder production
L6 Ladder
L5 Ladder
L4 Ladder
L3 Ladder
FW module
BW module
Origami module
Origami module
Origami module
BW r/o
FW r/o
BW r/o
FW r/o
FW module
BW module
Cooling pipe
Cooling pipe
Cooling pipe

## Slide 12: Ladder assembly
Strategy
  Active alignment of DSSDs at < O(10mm) with DSSD moving stage.
  Measurement of whole fiducial marks on DSSD by CMM after the assembly.
  Porting L6 production jigs to the other layer
Status
  A full set of L6 ladder production jigs in Kavli IPMU
  Working single and double Origami modules are produced so far.
  Verification of technical milestone w/ assembly of mockup ladder is in progress
  Collaborative research agreement was concluded btw TIFR and Kavli IPMU.
  Commissioning of wire-bonders in each institute is done. Training for production.
Automatic wire bonder
Delvotec 6400
HEPHY, TIFR(@Kavli IPMU)
Automatic wire bonder
Choonpa Co. REBO-7W
IPMU(borrowed KEK)
CMM
Mitsutoyo QV606
Kavli IPMU
XYZθ-stage
Single Origami module
Double Origami module

## Slide 13: Ladder assembly procedure
Active alignment
w/ XYZθ-stage
Gluing Origami module
and FW&BW module
Finish
+10mm
−10mm
Design value
Demonstration of alignment w/ 4DSSDs
DSSDs are aligned and fixed at initial assembly procedure.
The alignment are kept till the end of the procedure.
c2 fit will be performed for the data after the assembly.
The alignment correction parameters can be extracted at mm
precision. → will be used for initial alignment constant.
Assembly-jig
DSSD
…
1st 2nd 3rd 4th
DSSD
Left Top Fiducial Mark
Left Down FD
Right Top FD
Right Down FD

## Slide 14: Mockup IR-PXD-SVD
IR+PXD+SVD precise mockup study @ KEK

## Slide 15: SVD DAQ system
1748 APV25 chips
Front-end hybrids
Rad-hard DC/DC converters
Analog level translation, data sparsification and hit time reconstruction
~2m cable
DOCK
~10m
cable
FADC+PROC
Optical link (>20m)
FTB
COPPER
FTB
COPPER
FADC+PROC
DOCK
Inside of BelleII detector
On top of BelleII
Electronics Hut
FADC-FTB-(COPPER+DatCon) chain test was succeeded on June 2013
DatCon system
BelleII DAQ system
Find RoI
AMC board
AMC board
PXD

## Slide 16: CO2 cooling
Closed CO2 cooling plant under development
Collaboration with CERN
First step is to gain experience with open (blow) system
Control cabinet with touch screen
Accumulator
Liquid pumps
1.3 m
1.6 m
1.2 m
Common CO2 plant with PXD

## Slide 17: SVD construction schedule
Ladder production
  L6 ladder production
    14 workdays per ladder
    13months for 19 ladders
  L5 ladder production
    10months for 15 ladders
  L4 Ladder production
    9months for 13 ladders
  L3 Ladder production
    7months for 8 ladders
L6 Ladder production will start Nov. 2013.
Ladder mount on the SVD support structure will start Jan. 2015.
L6 Ladder production will end Feb. 2015
SVD ready Aug. 2015.
Physics run Oct.2016

## Slide 18: Summary
SuperKEKB will be the highest luminosity machine
Belle detector upgrade
  Consists of 2 layers Pixel(PXD)+4 layers Strip(SVD) Vertex detector
SVD
  Layer3, 4, 5, 6 consist of 7, 10, 12, 16 ladders, respectively.
  Chip on sensor readout scheme, named Origami, for outermost three layers for low material budget.
  Active alignment will be applied in the ladder assembly.
  Production of ladder will start Nov. 2013.

## Slide 19: Backup slide

## Slide 20: FADC
Already partly equipped with components
Used for connectivity test as shown
Firmware development and testing of other parts has started

## Slide 21: Material budget
PA/PE/PB/SMD/ are neglected.
Thickness of epoxy glue in ladder assembly is assumed to be 100 mm, or, 0.033 % X0.
DSSD+ Origami | Rib | DSSD | Airex sheet | Origami | CO2 Cooling | 100 mm Glue | Total
HPK+1ORIGAMI | 0.035 | 0.340 | 0.055 | 0.133 | 0.037 | 0.033 | 0.593
HPK+2ORIGAMI | 0.035 | 0.340 | 0.055 | 0.266 | 0.037 | 0.033 | 0.733
Micron | 0.035 | 0.320 | 0.055 | 0 | 0 | 0.011 | 0.421
Micron+ORIGAMI | 0.035 | 0.320 | 0.000 | 0.133 | 0 | 0.033 | 0.576

## Slide 22
Atoll p-stop
Common p-stop
Combined p-stop
Full wafer design by ourselves
Main sensor (trapezoidal)
Mini sensor (rect.)
Test structures
Baby sensors with various p-stop patterns
Trapezoidal DSSD

## Slide 23: Comparison VA1TA – APV25
VA1TA (SVD)
Commercial product (IDEAS)
Tp = 800ns (300 ns – 1000 ns)
no pipeline
<10 MHz readout
20 Mrad radiation tolerance
noise: ENC = 180 e + 7.5 e/pF
time over threshold: ~2000 ns
single sample per trigger
APV25 (Belle-II SVD)
Developed for CMS by IC London and RAL
Tp = 50 ns (30 ns – 200 ns)
192 cells analog pipeline
40 MHz readout
>100 Mrad radiation tolerance
noise: ENC = 250 e + 36 e/pF
time over threshold: ~160 ns
multiple samples per trigger possible (Multi-Peak-Mode)

## Slide 24: First 2 Origami module assembly@IPMU
Single Origami module assembly@HEPHY
2 Origami module assembly(Jun. 2012)@IPMU
Chart: Leak Current - Bias Voltage
| 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
154 Hamamatsu | 2.379 | 3.313 | 3.896 | 3.956 | 3.99 | 4.017 | 4.04 | 4.063 | 4.085 | 4.108
156 Hamamatsu | 2.318 | 3.27 | 3.965 | 4.033 | 4.066 | 4.094 | 4.118 | 4.146 | 4.204 | 4.33
154 bias only | 1.58 | 1.92 | 2.22 | 2.49 | 2.73 | 2.94 | 3.15 | 3.79 | 3.94 | 4.01
156 bias only | 1.62 | 2.01 | 2.31 | 2.61 | 2.84 | 3.08 | 3.27 | 3.84 | 4.2 | 4.73
First 2 Origami module@new clean room at IPMU
Automatic wire-bonder

## Slide 25: L6 Mockup ladder