AMC13 Module
CMS MicroTCA Overview
E. Hazen – Boston University
Representing the work of J. Rohlf, S.X. Wu, A. Heister, C. Hill, D. Zou, C. Woodall
at Boston University
and the CMS Collaboration worldwide
See http://www.amc13.info for detailed documentation

---
Outline
- CMS is going MicroTCA (.0 but not .4)
  - Brief review of crate configuration
  - Brief tour of cards in production
- AMC13XG Module status report
  - Design Update
  - 10G link testing
  - TTC path temperature coefficient

---
“MTCA.CMS” Crate
(note MTCA.0 but not necessarily MCTA.4)
One specific geometry shown, others possible...

---
“MTCA.CMS” Crate Requirements
- Dual-star backplane with redundant clocks
  - Fabrics A, B routed star-wise to both MCH sites
  - MCH2 CLK1 routed star-wise to AMC FCLKA
- Full-height, double width slots (pref. 12)
- Vertical cooling
Vadatech VT894
New Elma design (due late 2013)

---
MicroTCA installation in CMS
- Subsystems installing uTCA now or soon:
  - HCAL back-end
  - TCDS system
  - Global trigger
  - Calorimeter trigger
  - Muon trigger
- Incomplete list!

---
TCDS: TTC/TTS replacement system
Several MicroTCA crates; various modules

---
Calorimeter Trigger: Layer 1

---
Calorimeter Trigger: Layer 2

---
CMS Muon Track Finder
3 uTCA crates with various modules
(Virtex-7 Version soon)

---
FC7 motherboard for TCDS modules

---
The CERN GLIB
- Conceived as a test board, but may well end up installed at P5 in various systems
- 100+ produced!

---
The AMC13XG

---
What is AMC13?
- It is not an MCH! It is a 13th AMC in MCH-2 slot
- It distributes LHC clock / timing / controls to AMCs
- It collects DAQ data from AMCs
- It provides standard interface to CMS subdetectors:
  - CMS DAQ via 1-3 optical fibers (currently at 5.0 Gb/s)
  - TTC via 1300nm fiber @ 160Mb/sec biphase mark code
    - Future TTC upgrade may be supported
  - TTS via 1300nm fiber with protocol t.b.d.
- Latest version is 10Gb/s capable on backplane and optical links

---
History / Versions
- DTC (2010, 3 built)
  - Based on NAT-MCH
  - Prototype all functions
- AMC13 (2011, 17 built)
  - Based on new T1
  - New port assignments
- AMC13XG (2013, 15 built)
  - Redesigned T1 (only)
  - 10Gb/s links
XC3S200A / XC6V130T
XC6SLX25T / XC6VLX130T (or 240T)
XC6SLX25T / XC7K325T

---
AMC13XG (XG = Ten Gigabit)
Quad SFP+
Optical cage
AVR32 uC
MMC
T3 connector
(JTAG, I2C)
Spartan-6
FPGA
Kintex-7 FPGA
With heatsink
DDR3 SDRAM
Tongue 2 PCB
Clocks
T3 connector board removed
to show internal detail
Tongue 1 PCB
GbE, Fabric A

---
AMC13XG Front Panel
LED2
(MMC Green LED)
LED1
(MMC Red LED)
Serial #
SFP0
(DAQ Loop-back test)
3x SFP+
10Gb/s capable
Functions listed
for initial HCAL
firmware
USB
(MMC console)
SFP1
(DAQ Output)
JTAG
(MMC AVR-32)
SFP2
(Spare)
SFP3
(TTC/TTS)
JTAG
(AMC13 FPGAs)

---
Out of time!
- Summary:
  - CMS adopting MTCA.0 widely
  - “final” AMC13XG design complete
    - built in qty 15
    - Larger scale production starting late 2013
  - Keeping an eye on MTCA.4, trying not to be explicitly incompatible

---
Reserve Slides

---
Why Not .4? Mainly history...
- CMS converged on uTCA in 2009. Requirements:
  - Vendor standard crate
  - Backplane clock and TTC distribution
  - DAQ with ~ 400MB/s * 2 per crate
  - 12 slots preferred due to detector modularity
  - “DTC” prototype completed (NAT-MCH mezzanines)
- Further details settled in 2010:
  - MCH2 site used for AMC13 timing/DAQ module
  - Only fabrics A, B used for infrastructure
  - MCH2 tongues 3, 4 (fabrics D and up) available for user applications
- This is not incompatible with MTCA.4
  (though we “prefer” full-height AMC slots)

---
AMC13XG Block Diagram
FP Input
CLK
F/O
40.xx CLK
To AMCs
CDS
Kintex 7
TTC in
TTS out
SFP
IO
IO
DAQ
10 Gb/s
SFP+
GTX
GTX
GTX
GTX
Fabric A
12 ports
5.0 Gb/s
(10 Gb possible)
GTX
GTX
DAQ
10 Gb/s
SFP+
GTX
GTX
GTX
GTX
GTX
Spare
10 G b/s
SFP+
512 Mbyte
DDR3
GTX
1600MT/s (6.4 GB/s)
Spartan 6
GTP
IO
Fabric B
80 Mb/s (TTC)
May upgrade to
~ 320 Mb/s
GbE
GTP
MCH1
Front
Panel
via T3
JTAG
Flash
LEDs
MMC
uC
IPMI

---
AMC13 Clock Paths

---
AMC13 DAQ Path

---
AMC to AMC13 backplane link
AMC (e.g. HCAL uHTR)
12 point-to-point
links
AMC13
BU provided firmware
80 Mb/s
TTC Protocol
Fabric B
TTC
Receiver
LHC clock
L1A
IO
IO
BC0 etc
Level 1
Trigger
MUX
TP[0:7]
5 Gb/s
8b/10b
Fabric A
BC0
MGT
MGT
CLK
Level 2
DAQ
16
Data
Framing
Buffer
Status

---
Link to CDAQ
5.0 Gb/s optical link with “S-Link like” protocol
Firmware developed by CDAQ (both ends)
Error check coding, retransmission on error
Error monitoring
Full diagnostic and test capability from receive end
AMC13
FEROL
4 blocks (4Kbytes each)
Data from FED
-DATA (64 bit)
-WEN
-UCTRL
-CLOCK
-Backpressure
-link down
-Receive block
-Ack. block
-Order blocks
Main
Logic
SFP itf
Block is sent until it is acknowledged
Send commands
(one at the time)
Internal
Receive CMD
+ ACk

---
T1 PCB Stackup
Nelco 4000SI-13 Material
1	GTL
Impedance control (10G, SDRAM)
Prepreg 2.7
2	GP1
GND
Core 5.0
Split power
3	GP2
Prepreg 5.4
4	G1
Impedance control (SDRAM)
Core 5.0
Overall: 1.6mm
Signal:	18μm
Power: 36μm
Split power
5	GP3
Prepreg 2.7
GND
6	GP4
Core 5.0
Split power
7	GP5
Prepreg 5.4
8	G2
Impedance control (SDRAM)
Core 5.0
9	GP6
GND
Prepreg 5.4
10	G3
Impedance control (10G, SDRAM)
Core 5.0
11	GP7
GND
Prepreg 2.7
12	GBL
Impedance control (10G, SDRAM)

---
Top Layer 1 (signal)
UTCA connector
HS to T2
1.8V
2.0V
DDR3 power
DDR3
Kintex-7
LS to T2
1.0V
1.2V
1.0V aux
3.3V Payload

---
T2 PCB Stackup
Standard FR-4 Material
1	GTL
Impedance control (TTC)
5 mil dielectric
2	GP1
GND
3 mil dielectric
Split power
3	GP2
9 mil dielectric
4	G1
Inner signal
Overall: 1.6mm
Signal:	18μm
Power: 36μm
9 mil dielectric
5	GP3
Split power
9 mil dielectric
Inner Signal
6	G2
9 mil dielectric
GND
7	GP4
5 mil dielectric
8	GBL
Impedance control (TTC)

---
T2 PCB Layout
UTCA connector
Spartan 6 FPGA
Fabric B (TTC)
AVR 32 (MMC)
Clock fanout ICs
Connector to T3
Connector from T1

---
Eye Patterns
on
Serial Links

---
Backplane Test in VT892 Crate
Double-length (loop-back) test
MCH2 connector
AMC1 connector
AMC13XG
(Kintex-7 FPGA)
Jumper
Board
GTX
~5 cm
PCB (Nelco)
20 cm (est)
backplane PCB
NOTE: Preliminary!
still tweaking parameters
Total length: 50 cm (3.3ns)
5.0 Gb/s
10.0 Gb/s
-0.5 Time (UI) +0.5
-0.5 Time (UI) +0.5

---
10GB Fiber Loop-Back Test
MCH2 connector
AMC13XG
(Kintex-7 FPGA)
SFP Transceiver
Avago AFBR-703SDZ
GTX
30M Fiber
~3 cm
PCB (Nelco)
NOTE: Preliminary!
still tweaking parameters
10.0 Gb/s

---
Temperature Sensitivity
of
AMC13 Clock network

---
TTC Clock Delay Testing
904 (E. Laird) and at BU
Goal: Measure phase shift between TTC input and clock on uTCA backplane

---
Repeated Power Cycles
B. 904 (E. Laird et al)
Note: vertical scale inverted
BU (D. Zou et al)
300 ps
700 s
Measure TTC to custom AMC rx card
6 power cycles of whole uTCA crate
Converges in O(200s)
Slow drift seen but very low level,
nearly unmeasurable with this setup
Hypothesis: temperature effect
Measure TTT to 3.5GHz diff probe
on AMC card clock inputs w/ 100Ω
6 power cycles of whole uTCA crate
Vary from 10 min to 8h off time

---
Delay vs position in AMC clock chain
2814 has no
delay/phase spec!
150ps
300ps
0ps
150ps
Measured phase shift vs warm-up
All +/- at least 20ps
These MLVDS drivers have spec'd
Tempco of 10 ps/°C

---
Delay vs Temp @ BU
Change crate temp by blocking cooling.
Temp measured in air near AMC13XG
Δ delay at input to MLVDS drivers
Total plot range corresponds ~ to normal warm-up
Delay
(ps)
Slope: 25.8 ps/°C
Temperature (°C)

---
Phase shift: Conclusions
- Phase shift with temperature is not unexpected, and is much less than the old TTCrx
- The phase is stable after 200s or so warmup
- It is fine for foreseen applications
- ~ half of the shift is in the clock/data separator IC which is the heart of the design
- Improving it would require starting over on the clock path design
- A modest improvement could be gained by switching from uTCA-standard MLVDS to LVDS
  - And, Mr Wu told us so from the start!

---
AMC13 Board Stack
Base configuration has only tongues 1, 2
Base board - With optics and HS links (Fabric A)
Clocks board - distributes LHC clock and controls
Mezzanine connector for T3 with I2C
T3 has JTAG and LEDs