## Slide 1
Future Applications of GEM Detectors at BNL
C.Woody
Physics Department
Brookhaven National Lab
RD51 Collaboration Meeting
January 31, 2013

## Slide 2: New Applications for GEM Tracking detectors at BNL
Minidrift GEM detector
  Application for sPHENIX
  Future use in an EIC detector
  Positron imaging for PET
Fast, compact TPC with Cherenkov PID
  Use for tracking and particle id at EIC

## Slide 3
HCAL Outer
HCAL Inner
EMCAL
Solenoid
VTX

## Slide 4
4.65 m
Df=2p
Dh=±1.1

## Slide 5
4.65 m
Df=2p
Future additional tracking system
- Two additional layers of silicon tracking
- Cylindrical GEM tracker (possible radial minidrift)
Dh=±1.1

## Slide 6: Forward sPHENIX
Current VTX and FVTX detectors
Forward GEM trackers

## Slide 7: EIC Detector – Conceptual Design
Central Detector
Forward/Backward Detectors
Large acceptance: -5 < h < 5
Asymmetric
Nearly 4p tracking and EMCAL coverage
HCAL coverage in central region and hadron direction
Good PID
Vertex resolution (< 5 mm)
Electron is scatted over large range of angles (up to 165˚)
Low Q2 → low momentum (few GeV)
Requires low mass, high precision tracking
GEM TPC w/PID
Planar GEM Trackers
GEM Tracker
PID devices
Central TPC + Forward minidrift GEM Trackers
Si

## Slide 8: Minidrift GEM Detector with XY Readout
Std. 10x10cm CERN 3-GEM Det.
ArCO2 (70/30)
Gain ~ 6500
~17mm Drift Gap
Drift Time ~600ns
SRS /512 channels APV 25
30 x 25ns Time Samples
Martin Purschke’s newly
developed RCDAQ
affords high flexibility
COMPASS style Readout:
256 x 256 X-Y Strips
~10cm x 400um pitch
Drift Gap
Transfer 1
Induction
Transfer 2
GEM 1
GEM 2
GEM 3
Mesh
X-Y Strips
Pitch: 400um
17mm
1.5mm
2mm
1.5mm
Preamp/Shaper
Primary Charge
Fluctuation
X
Y

## Slide 9: Beam Test in October 2012
Thank You RD51, ATLAS and everyone who made this possible !
Vinnie Polychronakos
Joerg Wotschack
Theo Alexopoulos
Konstas Ntekas
And many others…
And of course Bob Azmoun from our group !

## Slide 10: Test Beam Data – Micromega Detectors
Beam Profile – Extrapolated Tracks from Micromegas
X
Y
Projection plane
Beam particle

## Slide 11: Vector Reconstruction in GEM Detector
Error on reconstructed vector
Error on arrival time: ~ ± -1.8ns
 error on z-coordinate ~ 60 mm
 error on reconstructed vector
due to time resolution alone
~ 1 mrad (@ 40 degrees)
Linear Fit to determine arrival time = x-int.
30 samples x 25ns = 750ns window
Raw Data: Waveforms in Time
Vector Signature: “Charge square”
Vector Recon:
X -coord. = middle of pad
Y-coord. = drift time * Drift Vel.
Fit (x,z) points to line
B. Azmoun
Main error on reconstructed vector is due to charge fluctuations

## Slide 12: Angular Resolution
Track Recon. Fails
(Rely on Charge Centroid)
Uncertain Boundary
Track Recon. Successful
MC Simulation of Angle and Position Resolution
T. Cao, Stony Brook
At small angles, it is not possible to measure a vector and the best position information is obtained from the centroid of the charge distribution
At angles > ~ 5 degrees, it is possible to determine a vector with an accuracy ~ 0.3 degrees (~ 5 mrad)
Reconstructed angle in GEM detector assuming beam track is at zero degrees with no divergence
(not using MM data)

## Slide 13: Test Beam Data – GEM Detector
Beam Profile from GEM detector – Charge Centroid (0 degrees)
X
Y
Difference in coordinate position (GEM Detector – Micromega Track Projection)
X
Y
s ~ 300 mm
s ~ 145 mm

## Slide 14: Test Beam Data – GEM Detector
GEM detector – Vector Reconstruction (40 degrees)
GEM position at projection plane
X
Y
(GEM – MM) coordinate
(GEM – MM) angle
s ~ 975 mm
s ~ 220 mm
s ~ 10 mrad
s ~ 8.5 mrad

## Slide 15: Minidrift GEM Detector with VMM1 Readout
VMM1 FEC USBPC
VMM1 Labview Control panel
Preliminary Results (64 ch.):
Measured Fe55 spectrum
Measured Sr90 vectors at ~35o
Brief test (~ 1 day) of minidrift GEM with VMM1 readout at BNL
Despite the very short time available, got the detector and readout up and running very quickly in the lab
Unfortunately, no time to test in the test beam at CERN

## Slide 16
TPC with Particle ID (HBD)
Idea originally proposed for PHENIX (~ 2000)
In the end decided to build just the HBD portion
Idea now resurrected for EIC
Drift regions
HV plane (~ -30kV)
TPC GEM Readout Plane
Readout Pads
DR ~ 1 cm
f ~ 2 mm
CsI GEM Readout Plane for RICH
Cherenkov “blob”
Ionization drift
Fast, compact TPC
Common CF4 gas (windowless)
10 cm/msec
Excellent UV transparency
e±

## Slide 17: Prototype TPC/Cherenkov Detector
3 sided kapton foil field cage
Open wire field cage
CsI coated triple GEM detector
(10x10 cm2)
TPC readout triple GEM detector
(10x10 cm2)
E drift
Č
e±

## Slide 18: TPC Test Set Up
32cm Drift Cell
10x0.3mm pad
Readout (24ch.)
Top Fe55 Source
Bottom Fe55 Source
SS Vacuum Vessel
HV Feed-thru (60kV)
Class IV YAG Laser
Photodiode
-Trigger
24 ch. Readout Electronics

## Slide 19: Drift Velocity Measurements
PD -Trigger
Laser
Drfit Electrons toward Readout
(Triple GEM + preamp/shaper)
HV (~32kV)
Lens to Focus
laser to a point
Photo-ionized gas
Electron cluster
Ionization “spot” produced by YAG laser
Photodiode provides trigger
Drift time is measured as the arrival
time of the charge cluster at the readout
plane
B. Azmoun

## Slide 20: Charge Attachment Measurements
Drfit Electrons toward Readout
(Triple GEM + preamp/shaper)
HV (~32kV)
Top Fe55 x-ray Source
Bottom Fe55
x-ray Source
Fe55 source deposits known charge at the
top of the drift cell
Charge is measured at the readout plane
after 32 cm drift
Ratio determines fraction of charge collected

## Slide 21: Gas Transmittance Measurements
VUV Spectrometer for measuring transmission of gases down to ~ 120 nm
Transmittance of pure CF4
Collimated VUV light
VUV sensitive PMT‘s
Gas Sample

## Slide 22: GEM Trackers for Positron Imaging
Efficiency for conventional Positron Emission Tomography is very low for imaging thin objects such as skin, plant leaves, etc.
  Large fraction of positrons escape without converting
Range of positrons for PET isotopes is many cm in gas
It is therefore possible to track the escaped positrons, generating a line of response similar to the one produced by back-to-back gammas in conventional PET, and use this for image reconstruction
Main problem is in multiple scattering of the positrons, primarily in the window of the detector

## Slide 23: Positron Escape Probability
Leaf Experiment
Plexiglass plates stop escaping positrons which are then imaged by PET

## Slide 24: Positron Imaging Could be Complimentary to PET Imaging of Plants
Two Ring Ratcap PET imager
PET image of the stems of a corn plant

## Slide 25: Position and Angular Resolution for Measuring Escaped Positrons
Detector Resolution
(stand alone Monte Carlo)
Spatial resolution due to multiple scattering in a 50 mm thick mylar window (Geant4)
T.Cao, Stony Brook
Position resolution is limited by scattering in detector window

## Slide 26: Test with Collimated Beta Source
~50mm
Sr-90
Brass Source Holder
Tungsten Collimator
1.00mm hole
Preamp/Shaper
Capacitively couped to bottom GEM electrode
Trigger on bottom GEM
90Sr source (e-, Emax = 2.3 MeV)
Tungsten collimator with 1 mm hole
Need to reject background from g conversions due to bremsstrahlung
Trigger on bottom GEM
Requires good single electron detection efficiency ( high gain)
s = 7.6°
Trigger timing determines displacement of vector relative to track, although no influence on angular resolution.
4.5° due to multiple scattering

## Slide 27: Planar Image vs Vector Reconstruction
Planar image using only position information
Same image using vector information
Monte Carlo simulation of image reconstruction of a 1 cm disc of FDG
Planar image from actual data of a 1 cm disc of FDG

## Slide 28: Imaging a Source Phantom
2 mm diameter hole partially filled with 11C/18F solution
25 mm mylar window
Lucite cylinder
FWHM=5 mm
Using only vertical tracks: collimator mode
e+

## Slide 29: Summary
BNL is working on several new projects involving GEM detectors
  Minidrift
    Tracking for sPHENIX and EIC
    Positron tracking for medical imaging
  TPC/HBD
    Tracking and particle id for EIC
EIC tracking collaboration is also interested in large area GEM detectors for tracking (FIT, UVa), 3D readout (Yale) and RICH particle id (Stony Brook)