## Slide 1: The Actuator and Control unit
CERN wire-scanner development review 18.04.2013
J.Emery for the BWS team

## Slide 2: Future Actuator and Control unit
Scanner control, monitoring and supplies BWS_SCMS
Digital control (FPGA)
Long range resolver interface
Resolver
3-phases PWM
Motor
Optical encoder interface
Optical encoder
Condition monitoring of variables could act on the feedback like: - Mechanical vibration - Electrical connections - Motor power consomption

## Slide 3: Plan
Actuator parts selection
Laboratory bench & limitations
Collaboration with the heig-vd on the motor supply
Preliminary results
Perspectives
2 first points are from ‘Design and construction of a new actuator for the LHC Wire Scanner’, PhD. Thesis 2013, Mohammed Koujili

## Slide 4: Motor description
Rotor must be compatible with high temperature and vacuum
Multiple types of motor studied Induction Motor (IM), Switched Reluctance Motors (SRM), Permanent Magnet Assisted Reluctance Motor (PMASynRM), Permanent Magnet Synchronous Motor (PMSM)
High power density => lower mass and inertia at equivalent torque
Frameless => insertion of a vacuum barrel between the stator and rotor
Use of Samarium-Cobalt (SmCo) for the permanent magnets for its high temperature stability
Sizing based on expected inertia
Stator
Rotor
Air gap
Permanent magnet

## Slide 5: Motor caracteristiques

## Slide 6: Resolver RO3620
Special resolver without windings on the rotor
Compatible with temperature and vacuum
Vacuum barrel in between rotor and stator, like the motor
Usable like any other resolver
See Jose’s talk for more details
Rotor
Stator
Calibration improves absolut positionning
and is most likely usefull for our applicaiton
Air gap

## Slide 7: Laboratory test bench setup
Simulink position feedback loop

## Slide 8: Position control feedback using vector control
Motor
Resolver
Power supply
Developped on the laboratory bench
Under devloppment (with heig-vd)
Position
Speed
Current
Park transform

## Slide 9: Performances of the bench
Speed: 110 rad/s (Needs 128 for the SPS)
But with tests with low inertia
Linear driver used for power stage (as for last 2 WS designs)
But we are close to their maximum dissipation ability
Go for more efficient power control

## Slide 10: Prototype validation in the laboratory
Laser calibration bench similar that PSB and PS
Oscilloscope
Interface encodeur optique
Interface photodiode
Mesure des vibrations
Switch mode power supply and filters

## Slide 11: Study of Switch Mode Power Supply (SMPS) principle for the wire-scanner actuator
On-going mandate with the heig-vd, Industrial and Automation Institute (IAI)
Models development of - Power supply - Output filtering - Long cable to be used - Motor for high frequency - Simulation of the EMI
Validation of the position feedback stability of such system
Implementation of this system with their electronics
EMI measurements and comparison with current implementaion using linear drivers
Our motor!

## Slide 12: Switch mode output filter principle
Results: Reduction of ElectroMagnetic Interferences (EMI) Better compatibility with signal cables neaby this cable
Shielded power cable 6mm2

## Slide 13: Models for the SMPS simulation
Switch mode
Filter
Cable
Motor

## Slide 14: Position feedback stability study by simulation after integration of the SMPS
Position
Position Profile
Current correctors
Speed
Pos
Park
PWM
Result: Stable system following the expected profile (includes latest inertia value 1.04E-3, See Sebastian’s talk)

## Slide 15: Preliminary study results
Principle validated with long cables by simulation and experience
Position feedback is stable and correct dynamic
Physical implementation on their bench with our motor finished
Filtering reduces considerably the emitted interferences (see measure, using parallel cable as receiver)

## Slide 16: Location of the position feedback in the future system
Scanner control, monitoring and supplies BWS_SCMS
Long range resolver interface
3-phases PWM
Optical encoder interface
Digital control (FPGA)
Filter
Filtering
Feedback implementation

## Slide 17: Perspectives
Actuator parts integrated on the mechanical prototype
Linear motor drivers where limiting performances
Successful collaboration with the heig-vd to study alternative
Validation of switch mode power supply with filtering
Stability of the position feedback verified
Next step Integration of this technics on the laboratory bench
Then Integrate this technics in the electronics for the prototype!
Questions?