## Slide 1: Construction and Commissioning of the SuperNEMO Tracker Demonstrator
Stefano de Capua on behalf of the SuperNEMO Tracker Group
Forum on Tracking Detector Mechanics Oxford, 19-21 June 2013

## Slide 2: Overview
Introduction to SuperNEMO.
The Demonstrator.
Tracker detector.
Construction of the Tracker detector:
  Cleaning
  Cell construction
  Testing
  Integration in the Tracker frame
Results from tests on the first cassette.
Next steps.

## Slide 3: SuperNEMO
SuperNEMO is the successor of NEMO3, which ran in the LSM laboratory (Modane) in 2003-2011.
The installation will begin in 2014 and first data are expected in 2015.
International collaboration (10 countries, ~150 people).

## Slide 4: Physics goal
Study the mechanism of the bb decay and search for neutrinoless bb decay:
Experimentally:
2n2b
0n2b
k: constant
A: molecular weight
M: source mass
t: time of measurement
Nbkg: background events
r: energy resolution

## Slide 5: Measurement principle
We want to: 1. measure the energy of the two electrons with good resolution. 2. identify the two electrons individually (Ee1, Ee2, cosq).
Choice of calorimeter+tracker technique.
Reconstruction of final state topology (vertex, E1, E2, cosq, Dt).
Particle identification (a, b±, g): 1. background rejection. 2. measurement of physics signal.
Source separated from detector: several isotopes.

## Slide 6: From NEMO3 to SuperNEMO
 | NEMO3 | SuperNEMO
isotope | 100Mo (70%), 82Se, 150Nd, 130Te, 116Cd, 96Zr, 48Ca | 82Se (48Ca or 150Nd)
isotope mass | 7 Kg | ~100 Kg
efficiency | 18% | 30%
contamination in bb foils | 208Tl ~ 100 mBq/Kg 214Bi < 300 mBq/Kg | 208Tl ≤ 2 mBq/Kg 214Bi ≤ 10 mBq/Kg
Rn in the tracker | 5 mBq/m3 | ≤ 0.15 mBq/m3
calorimeter resolution | 8% @ 3 MeV | 4% @ 3 MeV
sensitivity | T1/20n ≥ 1024 yr mbb < 300-900 meV | T1/20n ≥ 1026 yr mbb < 40-100 meV
2003-2011

## Slide 7: SuperNEMO detector
20 modules surrounded by passive shielding (iron, water, plastic).
Source:
  2.7x4 m2
  5-7 Kg per module
  82Se (48Ca and 150Nd under consideration)
Tracker: drift wire chambers in Geiger mode.
Calorimeter: ~600 plastic scintillators coupled to low radioactivity PMTs.
Challenge: large scale production under ultralow background requirements.
Intermediate step to demonstrate the feasibility -> the Demonstrator (one module out of 20).
source foil
calorimeter
tracker
4 m
6 m

## Slide 8: The Demonstrator
A zero background experiment!
Installation in the LSM.
Match radiopuririty requirements.
Prove BKG ~ 10-4 cts/keV/kg/yr.
Achieve NEMO3 sensitivity in 4.5 months!
Full production (2034 Geiger cells).
2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Demonstrator module construction and commissioning
Construction and deployment of successive SuperNEMO modules
Demonstrator module running

## Slide 9: Radiopurity
Radiopurity requirement is very demanding!
Choice of material very challenging.
  stainless steel.
  copper.
  Delrin.
Many bespoke solutions adopted.
  Delrin-clad internal cables.
  Feedthroughs.
Demonstrator: 20 tons <1.5 mBq (Rn emanation into tracker)
Brazillian nut: 4 grams ~400 mBq (Radium decays)

## Slide 10: Tracker cell design
UK (Manchester, UCL, MSSL) is responsible for the construction of the Tracker detector.
Decay vertex reconstruction, e± identification, e/g separation.
The wires (stainless steel) of a cell are strung between two endcaps.
Diameter of anode (cathode) wires is 40 (50) mm, 44 mm for the cell.
Gas mixture: 95% He, 1% Ar, 4% ethyl alcohol.
Operating voltage: ~1700 V
Measurement of radial and longitudinal coordinates.
cathode
ring
cathode wires
cathode ring bar
cathode wires bar
injected moulded Delrin block
HV bar
anode signal
differential of anode signal
cathode signal
T1
T2

## Slide 11: Tracker cell performance
Extensively studied with a 90-cell prototype.
Cosmic rays + plastic scintillators trigger for tracking studies.
Anode efficiency | 98%
Cathode efficiency | 91%
plasma propagation time | 52 ms
Transverse hit resolution | 0.7 mm
Longitudinal hit resolution | 1.3 cm

## Slide 12: Tracker cell construction
Step 1: cleaning of all components.
Step 2: quality control of anode wires.
Step 3: construction of a cassette (18 cells).
Step 4: cassette quality control procedure.
Step 5: transport to MSSL and Tracker integration.

## Slide 13: Step 1: cleaning
  For stainless steel (frame material and wires):
    wipe clean with acetone
    rinse with tap water
    degrease in a biological bath
      Bio-Circle™ L at 41oC
      Contamination (oils, salts) broken down by microorganisms
    Rinse with tap water then distilled water
[class-1000 clean room]

## Slide 14: Step 1: cleaning
Ultrasonic bath in basic solution at 80oC.
5% base (Tickopur R33) in distilled water.
Rinse with distilled water.
Ultrasonic bath in distilled water (final rinse).
Drying at 60 oC.
Samples stay in drying cabinet until extraction and packaging.
Tested with HPGe after cleaning.
Pre-cleaned wire spool
Ultrasonic tanks
Venturi dryer, motor drive and take-up spool

## Slide 15: Step 1: cleaning
Multiple loops of wire in ultrasonic tanks:
Tickopur R33 (base)
Distilled water rinse
Forced-air (Venturi) dryer
Motor driven take-up spool
ultrasonic tank with looped wire

## Slide 16: Step 1: cleaning
All chemicals used are safe for most materials including copper and plastics.
Delrin: same procedure
  Delrin offcut through procedure, examined under microscope before and after: no signs of damage (e.g. pitting, discoloration).
  Delrin-coated copper wire cleaned and tested recently to be OK.
Copper: propose same procedure and:
  final passivation step in citric acid bath (plus final rinse) to minimise oxidation.

## Slide 17: Step 2: anode wire quality check
Dedicated test bench for wire quality control: 1.4 km/day can be tested.
We measure the signals due to cosmic muons passing through the cell (trigger rate, amplitude, plasma propagation time,…).
Anode and cathode signals (both ends) are read out.
We can detect dust and self-triggering points and measure their position.
Gas: He + 4% alcohol

## Slide 18: Step 2: anode wire quality check
m

## Slide 19: Step 3: cassette construction
5 cassettes/week (i.e. 90 cells per week) have to be constructed once in production phase.
A wiring robot has been designed in MSSL, built and optimised/finalised with software in Manchester.

## Slide 20: Step 3: cassette construction

## Slide 21: Step 3: cassette construction

## Slide 22: Step 3: cassette construction
Oxford U. is producing
feedthroughs and
associated connectors.
Internal harness
feedthroughs
connectors
Internal wire harnesses

## Slide 23: Step 3: cassette construction
First (dirty) cassette completed
at the end of April.
Ready for step 4!

## Slide 24: Step 4: cassette testing
Quality control criteria:
No self-triggering points.
No plasma-blocking points.
Monitoring of the 18 cells:
  Current
  Plateau width
  Operating voltage
  Cosmic rate
  Anode signal amplitude
  Cathode signal amplitude
  Cathode efficiency
  Plasma propagation time

## Slide 25: Step 4: cassette testing

## Slide 26: Step 5: transport to MSSL
first (dirty) cassette delivered to MSSL for installation test onto the C-frame.
we aim for 5 cassettes/week: C0 (1/4 of the Demonstrator) ready
in ~6 weeks.

## Slide 27: Step 5: Tracker integration
C0 (1st quarter of the Tracker frame) has been completed.
All optical modules installed.
Being tested for radon emanation.
Plastic
scintillator
Light
guide
PMT

## Slide 28: Step 5: Tracker integration
Ready to try installing a Tracker cassette.

## Slide 29: The Radon concentration line
Radon concentration in the Tracker is required to be < 0.15 mBq/m3.
Radon is able to diffuse through solids and may diffuse through gas seals and into the detector.
Monitoring during construction!
Gas from tracker pumped through a carbon trap and the radon in the gas is absorbed.
The trap is heated and radon pushed into detector via helium purge.
Radon progenies collected on a PIN diode and identified by energy deposit.
Sensitivity of ~0.05 mBq/m3 for a 3.8 m3 sub-module achievable.
Vacuum
pump
Carbon trap
Radon
detector

## Slide 30: Summary
SuperNEMO Tracker R&D phase is now concluded and all the objectives have been reached.
We are now entering the construction phase of the first SuperNEMO module (The Demonstrator).
UK is responsible for the construction of the Tracker detector.
Results from the first 18 cells built are very promising.
The Tracker frame has been completed and all optical modules installed.
Next:
Start mass production of cells in a proper clean environment.
Start assembling the Tracker and measuring the emanation of radon.

## Slide 31: Thanks for listening!
Collaboration meeting in Prague,
03/2013

## Slide 32: Spares

## Slide 33: FEAST
Front-End Asics for Supernemo Tracker
technology 0.35 mm CMOS
time resolution 12.5 ns, 48 bits counter
54 channels (18 anodic, 27 cathodic, 9 generic)
test performed by Manu Chauveaux (MCR), Sébastien Drouet and Laurent Leterrier (LPC)

## Slide 34: Analog signal from FEAST
Analog signals from FEAST, using cell01 @ 1750 V
3 configurable thresholds : VLN, VHN and VHP
5 registers : 1 start (R0) + 4 stop (R1 to R4)
t(R1) ≈ t(R3) and t(R2) ≈ t(R4)
t(R1) + t(R2) ≈ t(R3) + t(R4) ≈ 50 ms

## Slide 35: Results from FEAST test

## Slide 36: Results from FEAST test
Category | Efficiency | (%)
t(R1) + t(R2) ≈ t(R3) + t(R4) ≈ 50 ms | 73.1 | 
t(R1) + t(R2) ≈ 50 ms | 73.7 | 98.7
only t1 (center or endcap) | 25.0 | 
t(R3) + t(R4) ≈ 50 ms | 93.4 | 99.0
only t3 (center or endcap) | 5.6 | 
OR of all combinations |  | 99.6
8175 events [delay time > 5 ms]

## Slide 37: Diffusion chamber
Possible radon seals:
RTV, silicone : C1~C2 → transparent!
Mylar/Tropac/PVA : C1/C2 ≥~10,000
film material under test
C1
C2
Radon source: 38 kBq/m3

## Slide 38: Tracker cell operation

## Slide 39: Background
external
internal