## Slide 1: MM mechanical prototypes
Full wedge option
At CERN

## Slide 2: Purpose
Demonstrate feasibility
Setup of basic infrastructure
Gain experience with
  construction/assembly ideas/schemes
  Materials
  Procedures
  Precision (for me not the main objective)
Produce objects that can be measured
Establish an Assembly Manual

## Slide 3: CERN mechanical prototype
Full-wedge small sector quadruplet
  Eta and stereo doublet
All panels of equal thickness: 11-12 mm
  Standard Al profiles of t=10 mm as frames
  Al honeycomb of t=10 mm
  Skins = 0.5 mm (FR4)
  Glue gaps ≈ few 100 µm
Drift gap spacers: 5 mm
Total thickness: 75–80 mm

## Slide 4: Dimensions
10+
10+
10+
10+
10+
5
5
5
5
MM multiplet stack
(10+: 11 or 12 mm)
70 – 80 mm
Space for electronics
(50 mm in phi)
Dead area: 50 mm
Space for electronics: 50 mm
20 mm
Electronics boards
Eta strips
Stereo strips

## Slide 5: Collaborative effort
CERN, Lecce, Saclay, … more collaborators are welcome
Drawings and calculations: Lecce and CERN
Infrastructure and tooling: CERN, Saclay
Technical work: CERN, Lecce, Saclay
Evaluation: all (two summer students for mechanical)

## Slide 6: What could/should be included
Realistic materials and glues
Realistic thickness and segmentation of PCBs
Space for on-chamber electronics boards
Simplified cooling and cabling channels
  We foresee to insert heating wires into the cooling channels to simulate electronics/cooling
Gas channels and seals (to allow for gas pressure tests)
Mesh frame (but not necessarily the mesh)
T-sensors (a few) to allow for test measurements
Other ???

## Slide 7: The table
Size: 4 x 2.5 m
Flatness: ≤ 20 µm
Location: B16
Available: mid May

## Slide 8: Assembly scheme

## Slide 9
X 5
Vacuum
Clarinet gas
Skin (G10)
Precision insert
Rohacell honeycomb
Vacuum
Using Skin suction Tool
Vacuum
Expansive glue
Vacuum
Precised shim

## Slide 10: Stiffback
Simple stiffback structure with suction heads (following small test structure) used for 2 x 1 m2 prototype
CERN-DT group is working on a more final system using a perforated honeycomb structure with a perforated lower skin
Work in progress
  Small 50 x 50 cm2 system under construction
  Large system if prototype successful
60 mm