## Slide 1
Gianluigi De Geronimo
Microelectronics Team, Instrumentation Division Brookhaven National Laboratory
VMM ASIC
―
Status Report - April 2013
Notes: Microelectronics, in general and then specific for science

## Slide 2
Outline
VMM1 - tested
  architecture and results (brief)
  issues
VMM2 - in design
  architecture
  fixes (issues from VMM1)
  new features
  pinout and packaging (tentative)
  schedule (tentative)
Notes: Consists of 23 slides, three parts

## Slide 3
CA
shaper
logic
or
neighbor
addr.
channel (64x)
TGC out (ToT, TtP) x 16
ART (flag, parallel address)
logic
mux
mux
mux
analog ampl
analog time
parallel addr
mux clock
time
peak
Architecture of VMM1
dual polarity, adj. gain (0.5-9 mV/fC), adj. peaktime (25-200 ns), DDF shaper
discriminator with sub-hysteresis and neighboring (channel and chip)
address of first event in real time at dedicated output (ART)
16 direct timing outputs: time-over-threshold or time-to-peak
peak detector, time detector <1 ns
multiplexing with sparse readout and smart token passing (channel and chip)
threshold & pulse generator, analog monitor, mask, temperature sensor, 600mV BGR, 600mV LVDS
power 4.5 mW/ch, size 6 x 8.4 mm², process IBM CMOS 130nm 1.2V, test structures

## Slide 4
charge resolution ENC < 5,000 e- at 25 ns, 200 pF
analog dynamic range Qmax / ENC > 12,000 → DDF
Charge
Timing
  σt
  ≈
  ENC τP
  Q
timing resolution < 1 ns
(at peak-detect)
  λP
  ρP
  ≈ 0.3-0.8
Resolution Measurements

## Slide 5
CA
shaper
logic
or
neighbor
addr.
channel (64x)
issues in VMM1 → fixes in VMM2
TGC out (ToT, TtP) x 16
ART (flag, parallel address)
logic
mux
mux
mux
analog ampl
analog time
parallel addr
mux clock
time
peak
Note: VMM2 will maintain all the functionalities of VMM1
Architecture of VMM2

## Slide 6
power distribution
  voltage drop across power and ground wire-bonds
front-end
  stability at large capacitance (affects peaking time and gain)
  saturation at high rate
  leakage from ESD protection (disables positive charge operation)
  test pulse linearity, settling time, range (needs optimization)
  ESD protection (may need optimization)
discrimination
  digital pick-up in sub-hysteresis (affects low amplitudes)
  threshold dispersion and trimming (needs optimization)
signal processing
  peak detector stability (affects low amplitudes)
direct timing (TGC)
  digital pick-up on pulse tail
  delay and time walk (needs optimization)
  possible locking in TtP mode
test and readout
  internal reset optimization
  dedicated input for test-pulse strobe
Issues in VMM1 → Fixes in VMM2

## Slide 7
CA
shaper
logic
or
neighbor
addr.
channel (64x)
trigger
fixes
6b ADC
TGC out (ToT, TtP, PtT, 6bADC) x 64
TGC clock (160 MHz)
TGC out (ToT, TtP) x 16
ART (flag, parallel address)
time
peak
additional gain settings (TGC, MM)
external trigger
TGC: 64 outputs, 6-bit ADC 25ns serialized with dedicated clock
Note: VMM2 will maintain all the functionalities of VMM1
Architecture of VMM2
logic
mux
mux
mux
analog ampl
analog time
parallel addr
mux clock

## Slide 8
25ns
50ns
75ns
100ns
125ns
150ns
175ns
200ns
CK
charge event
analog pulse
OUT
peak-found
end of conversion
end of encoding
reset end (ready for next event)
timing edge
D5 - D0
160 MHz external clock
Conversion ends ~25ns after peak-found, programmable
Dead time from charge event <100ns
Amplitude data D5-D0 shifted at each clock edge
TGC ADC and Serializer

## Slide 9
CA
shaper
logic
or
neighbor
addr.
channel (64x)
trigger
fixes
6b ADC
TGC out (ToT, TtP, PtT, 6bADC) x 64
TGC clock (160 MHz)
ART (flag, serial address)
ART clock (160 MHz)
ART (flag, parallel address)
time
peak
additional gain settings
external trigger
TGC: 64 outputs, PtT, 6-bit ADC 25ns serial with dedicated clock
ART: flag and address serialized with dedicated clock
Note: VMM2 will maintain all the functionalities of VMM1
Architecture of VMM2
logic
mux
mux
mux
analog ampl
analog time
parallel addr
mux clock

## Slide 10
25ns
50ns
75ns
100ns
125ns
150ns
175ns
200ns
CK
charge event
analog pulse
ART
peak-found
FL D5 - D0
reset
160 MHz external clock
Flag and address serialized
Address data D5-D0 shifted at each clock edge
ART Serializer

## Slide 11
CA
shaper
logic
or
neighbor
addr.
channel (64x)
trigger
fixes
6b ADC
TGC out (ToT, TtP, PtT, 6bADC) x 64
TGC clock (160 MHz)
spr
1-bit
thr
1-bit
addr
6-bit
ampl
10-bit
time
10-bit
BC
12-bit
L1A
8-bit
ART (flag, serial address)
ART clock (160 MHz)
12b BC
Gray-code counters
DATA 48-bit
2-bit
FIFO
10b ADC
10b ADC
DATA sync
BC clock (40 MHz)
L1A trigger
DATA clock (80 MHz)
8b L1A
logic
logic
mux
mux
mux
analog ampl
analog time
parallel addr
mux clock
time
peak
2-bit DATA output with dedicated sync and 80 MHz clock
additional gain settings
external trigger
TGC: 64 outputs, PtT, 6-bit ADC 25ns serial with dedicated clock
ART: flag and address serialized with dedicated clock
10-bit ADCs 200ns for amplitude and timing, digital memories
Gray-code counters for BC-ID (12-bit) and L1A-ID (8-bit)
Note: VMM2 will maintain all the functionalities of VMM1
Architecture of VMM2

## Slide 12
front-end
  additional gain settings to match signal sfrom TGC and MicroMegas
  option to route monitors to PDO, TDO outputs for baseline acquisition
signal processing
  multi-phase current-output peak detector 1
  ADC 10-bit 200ns on PDO and TDO 1
  digital buffer, multiplexing, and logic for continuous acquisition 1
  counters and latches for BC-ID (12-bit) and L1A-ID (8-bit) 1
ART (address in real time)
  serialized flag and address
trigger
  external trigger for non-data-driven operation
direct timing (TGC)
  from 16 to 64 channels (initially packaging-limited to 32)
  pulse at peak (like ART)
  ADC 10-bit 25ns with serial output after flag 1
  fixed ramp discharge (PtT) 2
layout and packaging
  pads count from 176 to 208
  dual-mode wire-bond (MM, TGC)
radiation tolerance
  off-ITAR switch circuit (CERN), optimization 2
1 Major developments
2 If time allows
New Features

## Slide 13
LQFP208
Pinout and Packaging
projected die size ~ 9mm x 9mm

## Slide 14
task | status
fixes | in progress ~50%
external trigger | complete
ART serializer | in progress ~30%
current-output PD | complete
6-bit ADC and serializer | complete
10-bit ADC and digital buffer | in progress 70%
counters and latches | queued
analog gain | queued
physical layout | June-July 2013
fabrication | August 2013 (tentative)
Schedule and Status
Venetios Polychronakos (BNL)
Neena Nambiar, Emerson Vernon, Alessio D’Andragora, Jack Fried (BNL)
Jessica Metcalfe (BNL & CERN), Ken A. Johns, Sarah L. Jones (University of Arizona, USA)
Nachman Lupu, Lorne Levinson (Technion Haifa, Israel)
Georgie Iakovidis (BNL, USA and NTU Athens, Grece),
ATLAS Collaboration, CERN
Acknowledgment
14