## Slide 1: Remotely operated collimator exchange vehicle
Remote manipulations / diagnostics in radioactive areas and handling of radioactive material Workshop, Geneva, Switzerland 6th May 2013
JL.GRENARD (CERN)
Engineering Department / Transport Group
Notes: Method:
individual interviews with group leaders based on the April schedule -> to gather bottom-up data,
EN retreat on 1st July -> the aim was to bring the MTP in line with the last schedule & saving requests from the Council in June
ENMB on 26th July -> validate with group leaders the top-down arbitration

## Slide 2: Reason of the vehicle
Collimators are one of the most radioactive element in the LHC tunnel
Around 100 collimators installed all around the LHC
But mainly at IR 3 and IR 7

## Slide 3: Present situation
Installation of the collimator with a trailer equipped with a crane
Most of the collimators are installed on a plug in system (mechanical, water, power, control)
Handling of the collimator at the gravity center (collimator balanced before installation)

## Slide 4: Handling at IR7
Access shaft for old and new collimator
Remote trailer crane
Shielding
Shielding
Control station
Storage place for the vehicle
Not showned but has to be taken in consideration : ventilation doors

## Slide 5: Different solutions
Dedicated handling device using the LHC monorail
  No flexibility
  Space constrain
  Complexity of the machine
Stopped after the decision
Installation of a shielded wall at IR 7

## Slide 6: New remote controlled trailer crane
Shielding at each extremity
Power connected to the monorail
Motorized lifting spreader
Side collision detection
Recovery manual hydraulic control
Boom collision detection

## Slide 7: New remote control trailer crane
Key characteristics
lifting capacities: 1t
Max speed : 3km/h
Width: 780mm
Length: 2600mm
Height: 2010mm
Same concept of previous
Can pass key passage (UJ76)
CE marked

## Slide 8: New remote control trailer crane

## Slide 9: New remote control trailer crane
First testing @ CERN April 2013 : very promising
More tests would be organized in the next coming weeks in collaboration with EN-STI

## Slide 10: Vision system
The crane will be equipped with several cameras

## Slide 11: Vision system
Optical fiber transmission of the video signal
-> proven experience from other remote handling activities
(TAX repair, HiRadMat experiences handling)
Reason of the optical fiber : most reliable technology for real time visualization
Disadvantage-> the optical fiber as to managed

## Slide 12: Vision system
Vision based on pan tilt zoom cameras
Possibility of recording
Some extra support vision for example with remote controlled vehicle TELEMAX

## Slide 13: Recovery method
Included in the design
Loss of communication
Manual mode
Manual unloading mode without power

## Slide 14: Operation point of view
Will be operated by a team of two
-> one operating the crane
-> one operating the video cameras
Access in the area will be forbidden during all those operations
Under supervision of DGS/RP
Under supervision of equipment owner EN/STI

## Slide 15: Operation point of view
Equipment Owner EN/STI
Handling Team Leader EN/HE
Radioprotection DGS/RP
Operational team EN/HE
Handling instructions
Coordination / planification of work
Planification of Doses
Radioprotection instructions
Equipment
instructions
ALARA Committee

## Slide 16: Training of operators
Already 5 peoples ready and trained for the use of the vehicle (remotely but with direct vision)
Use of the mock up of the LHC tunnel to training the operators
Specialist will be in charge of the organization of the intervention

## Slide 17: Other possible use
Handling of passive absorbers
Handling of shielding blocks (up to 1t)
Some additional tooling could be developed depending on need, the vehicle could be considered as a ‘’platform’’

## Slide 18: Points to note
Use of a cable to avoid lateral and longitudinal forces on the handled element
Careful ! The plug-ins can induce extra forces if not in the correct position
Water plugin not aligned with the gravity center

## Slide 19: Conclusion
Will be use during LS1 to exchange collimators