## Slide 1: A new high resolution general purpose TDC
Jorgen Christiansen
CERN/PH-ESE

## Slide 2: Time to Digital Converters in HEP
Large HEP systems with many (100k or more) channels
  Time resolution, precision and stability required across whole system.
  Time correlations to be made across “all” channels
    Use and distribution of common time reference to all channels
    Large dynamic range
  Single shot measurements (with some exceptions, e.g. RICH)
  Short dead time
  No reason to aim at much better TDC time resolution than detector and system can effectively use (TDC contribution to total system time resolution should though not be significant )
  Detector (e.g. MCP, SIPM, MGRP, etc. for high resolution applications) and analog interface critical

## Slide 3: Other TDC applications
  Laser ranging,
  PLL’s,
  3D imaging
  TOF-PET
  Etc.
  General differences to HEP systems
    Small local systems
    Few channels
    Limited dynamic range
    Averaging can often be used to improve effective RMS resolution
E. Charbon, DELFT

## Slide 4: TDC applications in HEP
Drift time in gas based tracking detectors
  Low resolution: ~1ns
  Examples: CMS and ATLAS muon detectors
TOF, RICH TOP
  High resolution: 10ps – 100ps
  Example: ALICE TOF
Background reduction
Signal amplitude measurement: TOT
Va’vra RICH2007

## Slide 5: HPTDC
HPTDC used in large number (>20) of HEP applications:
  ALICE TOF, CMS muon, STAR, BES, KABES, , ,
  Commercial modules: CAEN, Cronologic, Bluesky
~50k chips produced
250nm technology (in principle still available)
  New production masks required.
  Packaging problems (original company does not anymore support this package)
  Production test based on old obsolete IC tester
  Process trimming to get internal memories to work reliable
Few thousand chips still on stock.
Design and production effort:
  ~ 6-8 man years

## Slide 6: HPTDC features
32 channels(100ps binning) or 8 channels (25ps binning)
LVDS (differential) or LVTTL (single ended) inputs
40MHz time reference (LHC clock)
Leading, trailing edge and time over threshold (for leading edge time corrections)
Non triggered or Triggered
  Programmable latency, window and overlapping triggers
Buffering: 4 per channel, 256 per group of 8 channels, 256 readout fifo
Token based readout with parallel, byte-wise or serial interface
JTAG control, monitoring and test interface
SEU error detection.
Power consumption: 0.5W – 1.5W depending on operating mode.
Problems:
  INL correction required to benefit from 25ps binning (substrate coupling from logic part of chip) 40ps RMS without INL correction 17ps RMS with INL correction
  Reliability problem in on-chip memory resolved by process trimming

## Slide 7
Good old HPTDC

## Slide 8: New TDC
Needs for different projects ?.
  HEP, (Especially at CERN as good justification for us)
  Other ?
Requirements:
  Time resolution
    High resolution (1-10ps) : TOF type applications
    Mid resolution (~100ps): ?
    Low resolution (~1ns): Drift time measurements (can be done with FPGA’s but rad tol an issue)
  Channels,
  Triggering,
  Buffering,
  Readout,
  Radiation tolerance
  ?
  When and how many
Analog front-end application specific (e.g. NINO)
  We are not (yet) proposing to make new analog front-end - discriminator
Collaboration to assemble sufficient resources
Other ongoing TDC developments ?

## Slide 9: Possible spec of new “super” HPTDC
32, 64 or 128 channels
  Depends on system configuration and chip packaging what is best.
6.1ps binning (with 40MHz reference),
  RMS resolution = ~ 2-3 ps (possibly a bit worse if going for lower power)
  Low power modes: 12.5ps, 25ps, 50ps, 100ps
    Disable resistive interpolation (factor 4 in resolution and power)
    Run DLL at lower (1/2 – 1/4) frequency (factor 2-4 in resolution and power)
SLVS (low voltage differential) inputs with on-chip termination.
  LVDS compatible ? (higher chip cost as double gate transistors required)
    Resistor network to “convert” to SLVS
40MHz time reference (low jitter PLL to be integrated)
  Other reference frequencies required ?
Leading, Trailing, and TOT measurements (leading +width).
Dynamic range: Counter size limited: 16bit - 32bit Readout bandwidth -> Two modes: Large, Small ?
Non triggered
Triggered with programmable latency, window and overlapping triggers.
Buffering: ~256 hits per channel, ~1024 hits readout FIFO.
Readout: SLVS (LVDS , Single ended needed ?)
  E-link (serial: 40, 80, 160, 320 Mbits/s) of the GBT optical link chip.
  Parallel (byte/word) readout.
  Other ?
Control/monitoring via “I2C” (1.2v CMOS levels) . Or E-link, JTAG ?.
Radiation tolerance
  TID: should be OK to several Mrad (if not using double gate transistors)
  SEU detection ( protection on control path ?).
  Not rad hard as then strict export/use restrictions
Power consumption: Max 1 – 2 W
  Significantly lower for lower resolution modes ~1/4
Technology: 130nm CMOS

## Slide 10: Way ahead
Political justification to start project
  Your help appreciated/vital
Timing core designed, tested and characterized (Lukas)
  Extend to required number of channels
  Power optimization
  Timing capture: clock sampling or hit sampling
  Course counter
Low jitter PLL: Few ps jitter PLL not trivial
  Based on PLL from GBT if it can be modified with limited efforts ( 3-6 months)
  Buy PLL IP block if one with sufficently low jitter can be found ( ~50k)
HPTDC Verilog model to be modified/simplified and re-verified
  Individual buffers per channel simplifies Verilog model as hits in chronological order.
~3 years for final design
  Year 1: Specs, Verilog model, PLL
  Year 2: Synthesis, P&R, Verification, Prototype
  Year 3: Testing, Production version, Packaging, Prod test.
Manpower:
  ¼ senior/rusty designer,
  3 years fellow, Support from experiments/users vital
  2 x technical student (6-12Months) for test/prod.
Funding:
  (PLL: 50k, 2014, if GBT PLL not appropriate)
  (P&R 50k, 2015, if short on manpower)
  MPW Prototype: 100k, 2015
  Final production masks: 450k, 2016 (1/2 or less if shared with other project)
  Packaging: 50k (depending on package type)
Contributions/collaboration from others ?.
  Design: PLL, HDL, Hit receiver, P&R
  Test and qualification
  Financial

## Slide 11: Architecture outline
R
R
R
R
R
R
R
R
Delay cell
R
R
R
R
PLL
Capture Register
Encoding
Channel
buffer
Trigger matching
Readout
FIFO
Hits
(32 - 64)
(Trigger)
Clk
Config and monitoring
DLL
Resistive
interpolation
I2C

## Slide 12: TDC ASIC’s for physics
Only very few flexible TDC ASIC’s are available for HEP (e.g. HPTDC).
  Resolution
  Number of channels
  Data buffering, triggering and readout
  Radiation tolerance
Flexibility can be obtained by FPGA based TDC’s but
  Limited resolution
    many experimental circuits being tried: Gate delays, fast carry chains, Vernier principle using different loading, Wave union,
  Channel count
  Radiation tolerance
  Cost, power and integration for large scale system

## Slide 13: Difficulties in the ps range
Calibration is a must, but at what rate
  We therefore tend to prefer auto calibrating architectures based on DLL’s (basic offset calibration still required)
Slew rate of signals much slower than resolution aimed at (digital signals do not exist in the ps domain)
Matching gets critical and mis-match compensation becomes a must if aiming at ~ps resolution.
  Automated on chip (for commercial applications)
  With help from “outside” (OK in HEP). We can even work with imperefct TDC’s if it can be appropriately corrected in software.
Distribution of timing signals gets critical (R-C delays in Al, Cu wires, via’s, contacts, etc.)
Metastability in timing capturing circuit gets significant/critical.
Interpolation to high ratios gets increasingly sensitive to power supply noise (even for the digital approaches), substrate coupled noise, etc.
Routing delays are significant and difficult to balance (especially for loop feedbacks and parallel load of many registers)
Phase error across DLL (phase error in PD and end-begin effect)
Testing a TDC with ps resolution is far from trivial
  Stochastic testing for linearity (Code Density Test).
  Fixed delays for jitter and stability.
  Time sweep if you can find the appropriate instrument (resolution and jitter) and can afford it
System level performance is what counts in HEP !
  Detector, analog front-end, discriminator, time walk compensation, board design, power decoupling, connectors, cables, stability (jitter) across full system, timing distribution across full system, calibration, , ,

## Slide 14: Warnings when it comes to compare TDC performance
If only obtained on simple test circuit
  No additional circuitry introducing noise (substrate, ground, Vdd, crosstalk)
If only demonstrated over small dynamic range
If not clearly demonstrating correct alignment between coarse and fine interpolation(s).
If results shown with averaging over many hits.
If only showing jitter/effective resolution at some fixed measured intervals
Temperature, voltage, process variations
Mismatch not analyzed and only show measurements from one single chip/channel.
Why make a 1ps “resolution” TDC if effective RMS resolution is much worse than this ?.
  Reminder for perfect TDC: RMS = bin/v12 = bin/3.5
  Global aim: RMS <= Bin size.
  (Exception if averaging of multiple measurements can be made)
How to use efficiently in a large system ?

## Slide 15: clients/users
LHCb Torch
Totem
HPS (CMS), FP420 (ATLAS)
Panda
CBM
CAEN
Crispin Williams
Other ?

## Slide 16: Back up slides

## Slide 17
Start – stop measurement
  Measurement of time interval between two local events: Start signal – Stop signal
  Used to measure relatively short time intervals with high precision
  For small systems (1 channel)
  Like a stop watch for a local event
Time tagging
  Measure time of occurrence of events in relation to a given time reference Time reference (Clock) Events to be measured (Hit)
  Used to measure relative occurrence of many events on many channels on a defined time scale
  Such a time scale will have limited range but can be circular (e.g. LHC machine orbit time)
  For large scale HEP systems
  Like a normal watch with a common 24h scale
Start
Stop
Time scale (clock)
Ch1
Ch2
ChN

## Slide 18: Interface to front-end and time walk compensation schemes
Basic discriminator
  Significant time walk (depending on signal slew rate)
Double threshold
  Interpolate to “0” volt amplitude
  Needs two discriminators and two TDC channels, Limited efficiency reported in practice.
TDC plus pulse amplitude (peak or charge) measurement with ADC
  ADC measurement expensive and slow (may be needed anyway)
Time walk
Thr
Thr2
Thr1
Time walk
Thr
Amp1
Amp2

## Slide 19
Constant Fraction Discriminator: CFD
  Compensate directly in discriminator
  Works very well for fixed pulse shape with varying amplitude.
    Needs delay: Made as distributed RC within ASIC’s(but also works as filter)
  If signal shape not constant then ?.
Leading edge + Time Over Threshold (poor mans ADC)
  Minimal extra hardware (also measure falling edge time)
  Has been seen to work quite well in several applications.
  If signal shape not constant then ?.
  TOT now very often seen in HEP for indirect amplitude measurement with moderate resolution
Original
Delayed
Fraction of
original
Crossing point
independent
of amplitude
Enable (thresholded)
Time walk
Thr
TOT
Thr

## Slide 20
Alternative: Very fast analog sampling
  Pulse matching – highest possible flexibility and performance
  High power – low channel density
  64GHz 8b ADC’s now feasible, 2W
    100GbE optical
  Large amount of data to read out and process (unless done on chip).
  Multiple sampling capacitor array chips made in HEP community
    Sampling rate: 1 – 5Gs/s
    Analog bandwidth: Few hundred MHz - GHz
    Resolution: 8 – 12 bits
    Memory size
    Channel count
    Triggering - Buffering
    ADC
    Readout

## Slide 21: Time measurement
Coarse count: ~1ns
  Multi GHz counters can be made in modern ASIC’s.
  Gray code
    Only one bit changing
  Dynamic range: Large
1st. Level fine interpolation:
  Extract timing difference between signal and reference (clock)
    Dynamic range: 1 (2) clock cycle
  A: Use same interpolation reference as counter (Clock).
  B: Use Different “reference”
Alignment between coarse and fine needs special care.
  Must be done with precision of full resolution
  If badly done then large error (coarse count) in small time window around coarse time change.
  Example: Use of two phase shifted binary counters and selecting one based on fine interpolation.
Counter
Register
Clock
Hit
N
N+1
N+2
N+3
N+4
N+5
N
N+1
N+2
0 – 1 clock
1 – 2 clocks
Clock
Cnt
Hit
Coarse
Fine
Fine
Start
Stop

## Slide 22: Time to amplitude
Time to Amplitude Conversion: TAC
  Classical type high resolution TDC implemented with discrete components
  Delicate analog design
  Requires ADC
  Slow conversion time –> dead time
  Not using same reference as coarse time
Dual slope Wilkinson ADC/TDC
  Time stretcher
  Measure stretched time with counter
  Slow: Analog de-randomizer
  Example: NA62 GTK in-pixel design
Start
Stop
ADC
V
Start
Stop
Start/stop
Stop/start
I
I/k
V
Start
Stop
I
I/k
T= (1+k)(Stop- Start)
C
I
T*I\C

## Slide 23: Delay line based
Basic principle
  Use “gate” (inverter) delays
    Normally two inverters
  Gate delays have large process, voltage and temperature dependency
  Using inverting cell
    Rise and fall time ( N and P transistors) does not match well over process, voltage and temperature.
    Different tricks can be used to make inverting and non inverting buffer have “same” delay but remains problematic.
  Fully “digital”
  Capture:
    Use hit as clock to capture state of delay chain
    Use delay signals to capture state of hit signal (high speed sampler)
Delay Locked Loop
  Control delay chain to cover exactly one clock cycle.
    Compensates for Process, Voltage and Temperature effects (but not miss-match)
    Uses same timing reference as course count and self calibrates to this.
  Begin-end effects, Phase error, Jitter, Delay cell matching
  Such a delay locked loop is a very quite circuit as all transitions are perfectly distributed over clock period (not the case for the Hit signal)
  Half digital / half analog
Register
Start
Stop
Start
Register
Clock
Hit
PD
Charge
pump
23

## Slide 24: Delay elements
Current starved inverters/buffers
  N-side, P-side, Both
  Only one of the two current starved
Regulate delay chain power supply with local LDO
  Careful interfacing to other circuits
Differential delay cell
  Consumes DC power -> More power
  Only needs one cell per delay (better resolution)
  (Less sensitive to power supply noise)
  (Generates less noise)
  Different types of loads can be used
    Inductive peaking can gain ~20%
  ~25ps possible in 130nm, worst case
Pseudo differential and many more
LDO
VDD
CP
In
Bias
Bias
In
Bias
24

## Slide 25: Sub-gate delay. 2nd. interpolation
Vernier principle
  Difference in delays can be made much smaller than delay in cell R=T2-T1
  Basic Vernier chain gets impractical long
  Performance gets miss-match dominated
  Delay difference can be implemented in many ways:
    Capacitance loading
    Transistor sizing
    Different current starving
    etc,.
  How to lock to reference ?
    DLL’s locked to different references
    DLL’s with different number of delay cells locked to same reference.
T1
T2
Start
Stop

## Slide 26
DLL arrays
  An array of DLL’s can use the Vernier principle
    DLL’s auto lock to common timing reference
  Example: Improve binning from 25ps to 6.25ps
    4 equal DLL’s driven by fifth DLL with slightly larger delay
      Potentially very miss-match sensitive
    1 DLL driving many small DLL’s
      Less miss-match sensitive (miss-match correction still advantageous)
      Non trivial layout to assure matching routing capacitances and R-C delays
T1
T2=5/4T1
4
5

## Slide 27
Passive delays
    In modern IC technologies wiring delays already the dominating source of delays.
    No easy way to “lock” to global reference
      Some kind of adjustment required
  R-C delay
    The adjustment of any tap affects all the other taps
      Used in HPTDC. In practice a bit of a pain (but works)
  Transmission line
    Short delays can be made with on-chip transmission lines
    Predefined and characterized transmission lines exists in may chip design kits.
    Lossy so signal shape changes down the line.
Can be used on hit signals instead of on DLL signals
    Flexibility on channel count versus resolution (used in HPTDC)
    This scheme can be used with many approaches

## Slide 28
Looped Vernier (beating oscillators)
  Two delay chains/loops propagates timing signals with slightly different delay.
    Start – Stop type
  Start oscillators with start and stop signals
    Latch loop1 count (start) when stop occurs
    Latch loop2 count (stop) when edge in loop2 catches up with edge in loop1.
    Store in which vernier cell the two edges meet.
  Appears elegant but hard to implement:
    Loop feedback time and re-coupling must be “zero” delay
      Circular layouts tried (but not so good for matching)
    All this per channel
    No direct lock to a reference
    Long conversion time -> Dead-time
    Some errors accumulate during recirculation
T1
T2
Start
Stop
Cnt1
Cnt2
Ver
Start
Stop
Cnt1
Coarse
Cnt2
Fine time interpolation expanded to be sum of Cnt2 plus Vernier
Vernier point where loop2 edge ”meets” with Loop 1 edge

## Slide 29
Analog interpolation between delay cells
  Resistive voltage division across neighbor delay cells.
    Rise times in delay chain longer than delay of cell.
    Purely resistive division “autoscales” with delay of delay cell
    Only carries current during transitions.
  Parasitic capacitance makes this resistive division a mixture of resistive division and R-C delays
    Relatively low resistor values required to prevent being R-C dominated.
    With equal resistances the bins are not evenly spaced -> re-optimize individual resistors
    Does not any more fully “autoscale” to delay of delay cell.
  Can be done on single ended and differential delay cells
R
R
R
R
R
R
R
R
Delay cell

## Slide 30
Time amplifier in “metastable window” of latch (with internal feedback).
  Any type of latch have a small time window where it enters a metastable region and it takes some time to resolve this
  A small change of timing on the input gives a “large” change of timing on the output: Time Amplifier
  For very high time resolution cases.
    Only small window where time amplification occurs
    Non linear, Very sensitive to power supply, etc.
    Hard to use in practice
    For 3rd level interpolation
Plus other “exotic” schemes.
  (implementation nightmare)
0
1
10ps
10ps
1ns

## Slide 31: Central timing block
For multi channel TDC’s it is attractive to have a central timing block used to drive array of individual channels
  Minimal complexity per channel.
  Only one block to calibrate.
  Power consumed in timing block less critical (but timing distribution to channels gets significant)
For very high resolution TDC’s this gets increasing difficult as required signal propagation delays larger than required resolution (miss-match !).
Buffer delays large than resolution: miss-match sensitive
For highly distributed TDC functions on large chips (e.g. pixel chips) it gets routing and power prohibitive even for low time resolution.
  Alternative: Centralized DLL locked to reference generates control voltage to distributed delay loops (miss-match !)
Centralized timing block locked to global reference (e.g. DLL array)
Register
Ch0
Register
Ch1
Register
ChN
Reference
(Clock)

## Slide 32: Time capture registers
The latches/registers used to capture the timing event gets critical in the ps range
Fast capture/regeneration registers required
  Timing signals have large rise/fall times compared to required resolution.
  Small and well defined metastability window with good resolving capability.
  Single ended (e.g. classical master slave FF) or differential (sense amplifier for fast SRAM’s)
Mismatch between registers
  Assuming multiple registers must latch at same instance
Routing of hit signal to registers must be done with care

## Slide 33: Example HPTDC
Features
  32 channels(100ps binning), 8 channels (25ps binning)
  LVDS (differential) or LVTTL (single ended) inputs
  40MHz time reference (LHC clock)
  Leading, trailing edge and time over threshold (for leading edge time corrections)
  Non triggered
  Triggered with programmable latency, window and overlapping triggers
  Buffering: 4 per channel, 256 per group of 8 channels, 256 readout fifo
  Token based readout with parallel, byte-wise or serial interface
  JTAG control, monitoring and test interface
  SEU error detection.
  Power consumption: 0.5W – 1.5W depending on operating mode.
Used in large number (>20) of HEP applications:
  ALICE TOF, CMS muon, STAR, BES, KABES, , ,
  Commercial modules from 3 companies
  ~50k chips produced
250nm technology (designed ~10 years ago for LHC experiments)
On-chip clock
crosstalk corrected
Offline:
40ps –> 17ps RMS

## Slide 34: HPTDC Time measurement
Combination of
  Counter with PLL for clock multiplication (x1, x4, x8)
    Double phase shifted counters to resolve possible metastability in coarse count measurement.
  DLL with 32 taps for clock interpolation
    Use of differential delay cell for power supply noise immunity
  R-C delay line on hit signals for very high resolution
    Channel reduction by factor 4 (8 channels per chip)
Low resolution: 781 ps
Medium resolution: 195 ps
High resolution: 98ps
Very high resolution: 24ps (8 channels)
Very high resolution
  R-C delay line dependent on IC processing (Only small difference between chips seen) R-C delay line independent of temperature in range of 20 deg Infrequent calibration required Calibration can be obtained with code density test with physics hits Option of correcting integral errors from DLL 8 channels per chip Not possible to pair leading and trailing edges
Ch0
Ch1
Ch2
Ch3

## Slide 35: TDC’s for pixel applications
For large pixel array chips with TDC function the routing and power to distribute required TDC signals to whole array may get power/routing prohibitive
  Local TDC in each pixel or shared among neighbor pixels (super-pixel)
    Local TAC with dual slope Wilkinson ADC
    Local delay loop (oscillator) only running when hit has been seen.
      Controlled from central DLL locked to timing reference
  Route hit signals (e.g. or’ing of pixels if rate allows) to centralized TDC block
SPAD with TDC: ~100ps binning
NA62 GTK: 100ps binning
  A: TAC per pixel with CFD and analog de-randomizer
  B: DLL for leading and TOT per column
Timepix3: ~1ns binning
  Local oscillator only running when hit occurs. Controlled from central DLL
SPAD array, E. Charbon, Delft
GTK in-pixel, G. Mazza, Turin
GTK EOC, A. Kluge, CERN

## Slide 36: Conclusions
Many different schemes and variants to get ~ps resolution in ASIC’s.
Combination of several to get dynamic range and resolution
  Fast (Gray) counters +
  DLL’s +
  Vernier - delay difference +
  R-interpolation +
  Time amplifier
  Etc.
Stability, jitter and miss-match critical at this level of timing resolution.
Global system timing resolution is what counts in HEP

## Slide 37: NEW HEP Versatile TDC ?
64 or 128 channels
5 – 10 ps bin, RMS: 2 – 5 ps, Delay Locked Loop based
  Option A: R(-C) interpolation
  Option B: Array of delay locked loops on same reference
  Option C: Single DLL on clock + DLL on hits
  Adjustment features to allow compensation of miss-match effects.
  RMS to be better that bin size (resolution)
Global time reference compatible with major experiments (e.g. 40MHz for LHC)
  Internal PLL for clock multiplication (jitter critical)
Flexible data buffering, triggering and readout
  Use general scheme as used in HPTDC
Max 10mW per channel
Timing part of such TDC currently under study
  130nm CMOS
Finalization depending on actual needs (and funding and manpower)
Versatile front-end/discriminator more delicate

## Slide 38
PLL
1.25GHz
DLL
Coarse counter
21 bit
25ps
DLL
DLL
DLL
2 x 21 bit
4 x 32 time taps
25ps + 6.26 ps

## Slide 40: Time capture
Hit sampling interpolator signals
  Hit based intrinsic zero-suppression
  Need of course counter
  Double pulse resolution determined by time to empty sampling register
    Small hit buffer per channel
  Efficient to share buffer resources
  Needs to sync to logic clock
  HPTDC
Interpolator signals sampling hit
  Continuous sampling
  Can digitize input signal without any double pulse constraints
  Requires high speed pipelined logic afterwards to reduce data
  Buffer sharing difficult.
New Super-HPTDC ?