## Slide 1
Review on Functional Requirements
for LHC Transverse Instability Diagnostics (2)
Scope and Aims of the Review:
collect user requirements
present capabilities of existing systems and options for upgrades
ensure technology and infrastructure in place to optimally use available instruments (triggers, logging, software)
identify missing technologies and systems that need further development
prioritize requests (feasibility, resources, impact)
identify requests that cannot be fulfilled for the start-up after LS1
recommend allocation of resources to management

## Slide 2: Motivation
Do we need to comment on the need?
  Already limited in 2012 performance by instabilities.
  It is going to be worse in 2015:
    High intensity
    Less tolerance to losses due to higher energy
We (all) need to understand

## Slide 3: Requirements
All through the cycle:
  bunch by bunch tunes (10-4 resolution) to provide snapshot of the machine just before the instability occurs.
  Accurate knowledge of chromaticity at the moment of the instability with a precision of ~2 units
    Systematic measurement every week if not possible online.
6 seconds around the moment of the instability
  Continuous “turn by turn” “bunch by bunch” positions during the instability. Resolution of few um.
  Intra-bunch time domain signals: resolution (100 um sufficient?)
  Continuous bunch by bunch intensity at high rate (10 Hz?). BI can remind us what we have
  Continuous bunch by bunch transverse emittance at high rate (already exists if BSRT is calibrated to also give absolute emittance). Sufficient what we have. BI can remind us what we have?
This should be stored on reception of a trigger:
  External (SW-button). Could be used for tuning of the trigger level.
  Automatic (based on a device measuring instabilities).
    Which instrument?
    Which observable and trigger level?
    Precision of the trigger?

## Slide 4: Requirements
Storage of the parameters during the cycle:
  1Hz?
Storage of the instability data (a la PM)
  No compression. For ever?
Offline tools for analysis not addressed but need to be specified
  are the basis for providing specs for on-line acquisitions

## Slide 5: Requirements vs. availability All through the cycle
Bunch by bunch tunes (10-4 resolution) to provide snapshot of the machine just before the instability occurs.
  Possible with the damper but with lower resolution (0.001)
  Possibility to have this resolution on a small number of bunches (gated BBQ+damper pick-ups) with low damper gain
  Excluded to use the Schottky?
Accurate knowledge of chromaticity at the moment of the instability with a precision of ~2 units
    Systematic measurement every week if not possible online
    Any possible mean to measure chromaticity on line?
    Longitudinal oscillations on small number of bunches?
    Excluded to use the Schottky?

## Slide 6: Around the instability (+/- 3 s)
Continuous “turn by turn” “bunch by bunch” positions during the instability. Resolution of few um.
  Possible with damper
Intra-bunch time domain signals
  Could be possible with HT monitor and new scopes (400 kCHF)
  Is the resolution sufficient?
  Is the MIM technique giving us what we need? Why the resolution is better?
  ABP/BI to see whether this covers what we need

## Slide 7: Trigger
PM style trigger could be implemented but:
  Identify one channel
  Latency?
  Issues for the sequencing?
White Rabbit?
BST?
Which instrument? Damper?
CO to look for options with BI/RF?

## Slide 8: Others
Do we have sufficient information for the characterization of the longitudinal properties?

## Slide 9: Applications
How do we analyze all that?

## Slide 10: Logging
Provided we specify there is some flexibility for long term storage