## Slide 1: Accelerator Needs from Medical and Industrial Applications for the next 50 years
Ken Peach
Particle Therapy Cancer Research Institute
(Oxford Martin School)
&
John Adams Institute for Accelerator Science
University of Oxford
final EuCARD meeting & EuCARD2 kickoff meeting
11th June 2013

## Slide 2: Outline
What is problem? Where is the Challenge?
Medical Applications
Industrial Applications
Neutron Radiography
Energy
Security Applications
Are lasers the answer?
Summary

## Slide 3: Predicting the future
“In the long run we are all dead”
      John Maynard Keynes A Tract on Monetary Reform (1923)

## Slide 4: What is the Problem? What is the Challenge?

## Slide 5: Today’s accelerators are …
Large
  Limited by either Magnetic Field
    R ~ P/(0.3B) [R in m, P in GeV/c, B in T]
      e.g. P=0.8 GeV/c , B=1 T, R=2.7 m
  or Gradient
    L=E/V [L in m, E in MeV, V in MV/m]
      e.g. E=300 MeV, V=10 MV/m, L= 30 m
        Examples are for a Proton Therapy Machine with proton radiography as an option

## Slide 6: … and today’s accelerators are …
Expensive
  Large high-field magnets
  High power RF
    … and …
Difficult to move

## Slide 7: Moving an Accelerator …
Artist’s Impression
A version of the salesman problem

## Slide 8: Medical Applications

## Slide 9
Radionuclide Production

## Slide 10: Coulomb Barrier for p, d, 3He, 4He
From IAEA Technical report 468 (2009)

## Slide 11: An example
From IAEA Technical report 468 (2009)

## Slide 12: A list of 49 “useful” radionuclides
From IAEA Technical report 468 (2009)

## Slide 13: IBA Cyclone 30 – industrial production

## Slide 14: Siemens 11 MeV Eclipse cyclotron

## Slide 15: Current commercial radiopharmaceutical cyclotrons
JM Le Goff/CERN

## Slide 16: AMIT Technical Specification
Courtesy of P. Arce/CIEMAT, D. M. Lewis/CERN: Development and design of low energy, small cyclotrons;
The Accelerator-Driven Production of Medical Isotopes Workshop held at the Cockcroft Institute 8/9 -12-2011

## Slide 17: The challenge
Custom radiopharmaceuticals
  Created close to the patient
    Small enough to be moved …
      Shielding!!!!!!!!!!!!!!!!!!
    Cheap enough for every doctor’s surgery
      Tens of thousands of something, not millions …
  Not just the radiopharmaceutical
    But also the agent
      e.g. targeted radiotherapy
        cancer-specific molecules as delivery agents

## Slide 18: Using radiopharmaceuticals
Positron Emission Tomography
Also for therapy?
Excerpt of PET-CT clinical images from a 69-yrs old female with metastases in the pelvic area, evidenced by hypermetabolic spots, one near the sigmoid colon (at right), another in a lymphatic node (at left).

## Slide 19
Charged Particle Therapy
(protons … carbon ions…)

## Slide 20: Parameters

## Slide 21: IBA & Varian cyclotrons
Cyclotrons are essentially fixed energy extraction

## Slide 22: PIMMS (CERN/TERA) Synchrotron Hall @ CNAO
Ugo Amaldi/TERA
Courtesy Amaldi
2012

## Slide 23: The gantry

## Slide 24: The challenges
> 2Gy/minute rate for volumes ~1L
Dose uncertainty <2%
Dose conformity <2% (to plan)
Lateral position precision <1mm
(Kinetic) Energy uncertainty <3 MeV
Cost
  10M (Accelerator) + 10M (Infrastructure) + 10M/Treatment Room
Size

## Slide 25
Other Medical Accelerators

## Slide 26: X-rays
Images: -P Gerard
Axxent Xoft
“brachytherapy”
Radiotherapy CT scanner
cyberknife

## Slide 27: Industrial Applications

## Slide 28: Industrial Accelerators
Direct Voltage
  Van de Graaf, Cockcroft Walton …
    Protons, ions to a few MeV (~5)
Linacs
  Electron beam
    Up to 16 MeV
  Ion beam
    Up to ~70 MeV
Rings
  Cyclotrons
    Ions up to ~70+ MeV
  Betatrons
    Electrons up to a few 10s of MeV
  Synchrotrons
    Up to several GeV

## Slide 29: Ion Implantation
Semiconductors
  Precision composition
Metals
  hardening
Glass
  Hardening
  Modified optics
    Note: All digital electronics depends upon ion implantation

## Slide 30: Electron Beam Materials Processing
Usually low energy
  Few hundred keV
  Used for precision
  engineering
  (cutting, welding)

## Slide 31: Electron Beam Irradiators
Low energy (<300 keV)
    Curing, laminating
  up to 1 MeV
    Also polymerisation
Medium energy (<5 MeV)
  Polimerisation
  Sterilisation (medical)
High Energy (~10 MeV)
  Food irradiation
  Waste water treatment
  Gemstone colour enhancement

## Slide 32: From Ion Implantation to Meta-materials
Can we move from embedding ions in substrates to building complex (meta)-materials?
  3-d printing at the milli-scale
    e.g. customised “factory-on-a-chip”

## Slide 33: Electron Beam Welding

## Slide 34: Why not proton beam welding?
Requirements
  10-100 MeV
  103 - 108 W/mm3
  2 - 50 mm/s
  (~1012-1014 p/s)
So why not
  Size
  Cost
  Shielding!!!

## Slide 35: A possible mobile EPM device

## Slide 36: Neutron RADIOLOGY

## Slide 37: Neutron Radiology
neutron
X-ray
162 pages!
From this
Chadwick
to this
IAEAL 12-00724
Images from IAEAL 12-00724

## Slide 38: Applications
From IAEAL 12-00724

## Slide 39: Applications
From IAEAL 12-00724

## Slide 40: A typical Neutron Generator

## Slide 41: A practical implementation
http://www.sciner.com/Neutron/

## Slide 42: Energy

## Slide 43: Neutral Beam Accelerator for ITER
Vacuum Vessel
Beam Source
Beam Direction
Accelerator/Extractor Grid
33 MW of beam power required
(2 Neutra;l Beam Injectors planned)

## Slide 44: Accelerator-Driven Inertial Confinement
NDCX-II @ LNBL
Induction Linac
Li ions, 1.25 MeV, 50nC, 38A, 8.6J/cm2

## Slide 45: Accelerators for Energy
Fusion is a Big Business
  Billions of somethings ($, €, £…)
  Mega (amps, watts, joules…)
  Heavy Engineering
    99% uptime is poor!
      15 minutes downtime per day
    Maintenance
      Radiation …
    Safety

## Slide 46: Security Applications

## Slide 47: Cargo Scanners

## Slide 48: Siemens SILAC 6-9 MeV scanner

## Slide 49: SILAC parameters

## Slide 50: Are Lasers the Answer?

## Slide 51: Classical Accelerator Types
Type | Magnetic Field | RF | Radius
Electrostatic | × | × | 
Betatron | Variable | × | Fixed
Linear accelerators (Linacs) | × |  | 
Cyclotron | Fixed |  | Variable
Synchrotron | Variable |  | Fixed
FFAG (Fixed Field Alternating Gradient) | Fixed |  | ~Fixed

## Slide 52: Maxwell’s Equations
Gauss's law
Gauss's law for magnetism
Maxwell–Faraday law
Maxwell-Ampère law
Mix electric &
magnetic fields
=
Einstein Gravitational Equation

## Slide 53: Riding the electromagnetic wave
http://www.youtube.com/watch?feature=player_detailpage&v=wHN0eldgXqQ#t=22s
It is difficult to control, but not impossible
Thanks to Dan Warren for help with the video

## Slide 54: Laser-plasma accelerators
Electron
Proton/ion
e-
Z+
Simulation Jimmy Holloway, UCL

## Slide 55: But not SO compact …
Vulcan@RAL
NIG @ LLNL

## Slide 56
TARANIS Laser at Queen’s University Belfast
Type: Ti:Sapphire-Nd:glass
Wavelength: 1053nm
Pulse duration of ~500fs
Beam energy up to 30J
Beam profile Flat top relay imaged
Repetition rate One shot every 12 minutes
T. Dzelzainis et al, LPB, 28, 451 (2010)
Courtesy Dave Neely (RAL)

## Slide 57: A compact high-power fibre laser
Laser-Plasma Proton Therapy
Courtesy Laurie Nevay/Oxford

## Slide 58: Which accelerators are useful?
Low energy (< or << 1 GeV)
Low Power (<<< MW) [often <W)
Modest emittance

## Slide 59: Accelerator-on-a-chip?
Electron/proton/ion beams
  Few MeV ; nAmA ; small spot (mm not mm)
  Low emittance (mm·mrad)
would have many uses
  Micro-surgery
  Welding/edtching/engraving
  Micro-lithography
  Meta-materials
    3-d micro-printing
  …
Can this be packaged on a chip?

## Slide 60: An idea
Assume 1 cm length for acceleration
  100 MV/m per MeV
Could suitable materials be engineered?
  Not today …
    … but in 50 years?
2.54 cm
0.76 cm
Staude et al, Optics Express 20 5607 (2102)

## Slide 61: Summary

## Slide 62: Summary
Medical, Industrial and Security need
  keV to a few MeV
  nA to mA
  Stringent control on both
  Usually small emittance
Challenges: accelerators are
  Large
  Expensive
  Often no mobile (or not very mobile)
In 50 years they may be
  Small, Cheap and mobile …
    Shielding????
    Do small precise accelerators need shielding?