## Slide 1: LINAC STABILISATION (including FF) Mechanical stabilisation and nano positioning with Angstrom resolution
The research leading to these results has received funding from the European Commission under the FP7 Research Infrastructures project EuCARD
K. Artoos , C. Collette (ULB), M. Esposito, C. Eymin, P. Fernandez Carmona , S. Janssens, R. Leuxe, H. Mainaud Durand, M. Modena
A. Jeremie, J. Allibe, L. Brunetti, J.-P. Baud, G. Balik , G. Deleglise, S. Vilalte,
B. Caron, C. Hernandez

## Slide 2: Outline
Ground motion and CLIC Requirements
Obtained results
Short view on ultimate performance limitations

## Slide 3: Ground motion
~40 nm
1 nm
20 km

## Slide 4
Vertical MBQ | 1.5 nm at 1 Hz
Vertical Final Focus | 0.2 nm at 4 Hz
Lateral MBQ, FF | 5 nm at 1 Hz 5 nm at 4 Hz
Integrated r.m.s. displacement
BUT Final requirement is Integrated Luminosity
Luminosity, beam size and alignment
Possible mitigation techniques:
Alignment
B.P.M. + dipole correctors
B.P.M. + Nano positioning
Seismometers + Dipole correctors
Mechanical stabilization with seismometers
Requirements Mechanical stability:
f

## Slide 5: Nano positioning
« Nano-positioning» feasibility study
Modify position quadrupole in between pulses (~ 5 ms)
Range ± 5 μm, increments 10 to 50 nm, precision ± 0.25 nm
Lateral and vertical
In addition/ alternative dipole correctors
Use to increase time to next realignment with cams

## Slide 6: Other requirements stabilisation support
Accelerator environment
High radiation
Stray magnetic field
Stiffness-Robustness
Applied forces (water cooling, vacuum, power leads, cabling, interconnects, ventilation, acoustic pressure)
Compatibility alignment
Transportability/Installation
Available space
Integration in two beam module
620 mm beam height
Integration in cantilever tube FF

## Slide 7: Concept for MBQ
Inclined stiff piezo actuator pairs with flexural hinges (vertical + lateral motion)
(four linked bars system)
X-y flexural guide to block roll + longitudinal d.o.f.+ increased lateral stiffness.
(Seismometers)/ inertial reference masses for sensors
Alignment
Eucard deliverable

## Slide 8
Type 1
Collocated pair
X-y proto
Seismometer FB max. gain +FF
(FBFFV1mod): 7 % luminosity loss
(no stabilisation 68 % loss)
Concept demonstration
actuator support with staged test benches
EUCARD
deliverable

## Slide 9: X-y prototype: Demonstration Nano positioning Resolution, precision, accuracy
Capacitive sensor
3 beam interferometer
Optical incremental encoder
Actuators equipped
with strain gauges

## Slide 10: X-y positioning: Study precision, accuracy and resolution
The precision required (0.25 nm):
demonstrated with optical rulers
in a temperature stable environment , in air
for simultaneous x and y motion.
Still increase speed

## Slide 11: Final focus concept
Direct disturbances:
Acoustic noise, cooling …
      RIGID GRIDER
Active Isolation
KICKER
QD0 (FF magnet)
Final Focus (FF)
Position at I.P.
Beam
(e-)
Beam
(e+)
Detector
FFM
magnetic axis
Desired beam position
(FF)
Post collision BPM
Pre-isolator

## Slide 12: Concept demonstration
Balik et al, “Active control of a subnanometer isolator“, JIMMSS. (accepted)
Spec : 0,2 nm RMS @ 4 Hz
Result : 0,6 nm RMS @ 4 Hz
Indication of sensor limit

## Slide 13: Concept demonstration
B. Caron et al, 2012, 236-247, Contr. Eng. Pract. , 20 (3). ; G. Balik et al, 2012, N.I.M. A., 163-170
GM B10
GM B
Reduction of luminosity losses down to 2% for different GM models
Demonstration feasability for CLIC MBQ and FF, «can we do better ?»

## Slide 14
Performance limitations
of a mechatronics system
Noise
Mechanics
Material
Control
Temperature
Electrical noise (Johnson,…)
Electromagnetic noise
SEU
Digitalisation, quantisation
Spurious noise, cross talk
Elasticity, elastic limit, stress limit
Damping
Fatigue
Ageing (Radiation, Curie-T, humidity)
Dimensions, mass, stiffness
Range
Degrees of freedom
Precision guidance
Modal behaviour
Freely adapted from J. Moerschell
Non linearity
Bandwidth, instabilities
Control delay
Parameter uncertainties
Controller authority, collocation

## Slide 15
Machine precision vs size
C. Collette

## Slide 16
Mass/Actuator Resolution/
Range/k/ Bandwidth
Stress < depolarisation stress
A For same Range: P
A
Bandwidth is limited by
Remark about load compensating springs:
Actuator slew rate
Frequency
Amplitude
Range
Force
Load compensation reduces range + bandwidth
Improves resolution *

## Slide 17
Machine precision vs size
C. Collette
Technological limitation for larger components

## Slide 18
Resolution limitations
Sensors
Stabilisation
Limitations:
Thermal stability (*alignment)
EM stray fields
Sensor resolution (wavelength light)
Expected maximum one order of magnitude improvement resolution in next decade (Without major technological innovation)
Low freq. is where you can win the most
Michelson
Stabilised LASER

## Slide 19: Nano positioning sensors
Heidenhain : 1nm resolution < 1000 CHF
Renishaw: 1 nm resolution < 1000 CHF
Smallest LSB can be used as quadrature …. 0.1 nm resolution is already possible
Technological innovation: digital optical encoders

## Slide 20
Conclusion
Material
Noise
Mechanics
Control
Temperature
Electrical noise (Johnson,…)
Electromagnetic noise
SEU
Digitalisation
Spurious noise, cross talk
Elasticity, elastic limit, stress limit
Damping
Fatigue
Ageing (Radiation, Curie-T, humidity)
Dimensions, mass, stiffness
Range
Degrees of freedom
Precision guidance
Modal behaviour
Non linearity
Bandwidth, instabilities
Control delay
Parameter uncertainties
Controller authority, collocation
In the Eucard grant we demonstrated technical feasibility of the CLIC stability requirements
In a laboratory environment one can expect to go an order better in the next decades, in an accelerator environment it is more complicated

## Slide 22: Synergies between projects: Generic R&D

## Slide 23: Integrated luminosity simulations
No stabilization | 68% luminosity loss
Seismometer FB maximum gain (V1) | 13%
Seismometer FB medium gain (V1mod) | 6% (reduced peaks @ 0.1 and 75 Hz)
Seis. FB max. gain +FF (FBFFV1mod) | 7%
Inertial ref. mass 1 Hz (V3mod) | 11%
Inertial ref. mass 1 Hz + HP filter (V3) | 3%
Courtesy J. Snuverink, J. Pfingstner et al.
Commercial
Seismometer
Custom Inertial Reference mass
Stef Janssens
Notes: Compari

## Slide 24: Comparison sensors
Sensor | Resolution | Main + | Main -
Actuator sensor | 0.15 nm | No separate assembly | Resolution No direct measurement of magnet movement
Capacitive gauge | 0.10 nm | Gauge radiation hard | Mounting tolerances Gain change w.  Orthogonal coupling
Interferometer | 10 pm | Accuracy at freq.> 10 Hz | Cost Mounting tolerance Sensitive to air flow Orthogonal coupling
Optical ruler | 0.5*-1 nm | Cost 1% orthogonal coupling Mounting tolerance Small temperature drift Possible absolute sensor | Rad hardness sensor head not known Limited velocity displacements
Seismometer (after integration) | < pm at higher frequencies | For cross calibration |