Future Linear Colliders:
Electron-positron collisions
at high energy
UiO FYS3510 & FYS4560 visit to CERN
May 7th, 2013
Kyrre N. Sjøbæk
K. Doyle,
Artwork for CLIC CDR

---
Outline
- Overview: What is a linear collider
  - Linear vs. circular collider
  - CLIC and ILC
- Physics at linear colliders
  - Higgs couplings
  - New physics beyond the standard model
- Accelerator physics
  - RF acceleration
  - CLIC scheme
- CLIC project timeline
- Visit CTF3 show room

---
What is a collider?
- Colliders:
  - Accelerate two particle beams in opposite directions
  - Focus the two beams at the same spot
  - Alternative: Fixed-target experiments (less usable energy)
- Some of the kinetic energy converted into new particles
  - Measure these!

---
Circular vs. linear collider
- Circular collider:
  - Create two
    contra-rotating beams
  - Collide them in one
    or more positions
    along the ring
  - Re-use the same beams billions of times
  - Synchrotron radiation
Example: LHC
P prop {E^4} over {m^4 r^2}
LHC: 7 TeV, max fill: 3.6 kW or 6.71 keV/proton/turn
LEP: 100 GeV, max fill: 18 MW or 2.1 GeV/e±/turn
What is a particle beam?
Bunch
LHC:
1.15 * 1011 protons
Bunch spacing
LHC:
25 ns = 7.5 m
Bunch train
LHC has (maximum) 2808 bunches / beam
LHC data: LHC Design Report Volume I
LEP data: D Brandt et al, Accelerator physics at LEP

---
Circular vs. linear collider
- Linear collider
  - Two linear accelerators facing each other
  - Collide particles at a single interaction point
  - No synchrotron radiation
  - No bending magnets
  - Each beam collides once

---
CLIC and ILC
	CLIC	ILC
Energy [GeV]	500 – 3000	200 – 500
Luminocity [1034 cm-2 s-1]	Peak 1% : 1.4 – 2.0 full spectrum: 2.3 – 5.9	2
Accelerating gradient [MV/m]	80 – 100	31.5
Bunches/ train	234 – 312	1000 – 5400
Particles/ bunch [1010]	6.8 – 3.7	10 – 20
Bunch spacing [ns]	0.5	180 – 500
Wall-plug power [MW]	272 – 589	230
Site length [km]	13.2 – 48.3	31
- Two projects to build the next big particle physics machine
- TeV-scale electron-positron colliders
- Different technologies and possibilities
sqrt s
Data from ILC Reference Design Report
and CLIC Conceptual Design Report

---
CLIC – how compact is it?
Gradient = 100 MV/m
Max. superconducting ~40 MV/m
“Laser straight” tunnel

---
The physics case
for a linear collider
Electrons
vs protons
- Proton collider:
  Colliding particles are quarks and gluons
  - “Broadband” collision energy
  - Initial state not known
  - Lots of “extra junk”
- Electron collider:
  Colliding fundamental particles
  - Initial state decided in the control room

---
Beamstrahlung at high-energy, tightly focused electron colliders
(Log scale)
Andre Sailer,
CLIC seminar 22/4/2013
Top 1%

---
“Livingstone” plot
Adapted from R. Corsini who adapted from W. Panofsky
2020
2030
CLIC
ILC
SSC

---
The physics case
for a linear collider
The Higgs Boson
- Threshold scans
- Neutrino end states
- Higher crossections at higher energy
- Higgs self-coupling
- Branching ratios

---
????
Beyond the standard model
The physics case
for a linear collider
- The standard model doesn't fully describe the universe
  - Dark matter
  - Matter-antimatter asymmetry
  - Unification?
- Many theories, few conclusions (yet)
- CLIC can measure what the LHC discovers
- Example: SUSY
  - CERN LCD note 2012-003, “Model 3”

---
????
Beyond the standard model
The physics case
for a linear collider
- Stage 1:
  - Higgs precision measurements
  - Top quark
- Stage 2:
  - ttH, H self-coupling
- Stage 3:
  - Cross check
  - Even more states
Stage 3:
3000 GeV
Stage 2:
1400 GeV
Stage 1:
500 GeV

---
Accelerator physics:
RF acceleration basics
- Constant voltage (DC)
  - Used in Van de Graaff generators,
    electron tubes, and
    first stages of accelerators
  - Energy = q*V
  - Can't go to very high energies
    - High voltages creates sparks
      =>Maximum some MegaVolts
    - Circular accelerators not possible
- Time-varying field
  (Radio Frequency = RF)
  - Less chance of sparks
  - Can go to high energies
  - Synchronize particles and field
DC
RF

---
Basic RF accelerator theory:
Pillbox cavity
Blue line: Ez(z) at given time
Red line: Particle position at given time
(optimal injection phase)
Electric field in pillbox
as function of time and position
(fundamental oscillation mode TM010)

---
Periodically loaded waveguide
Structure:
CLIC_G middle cell, repeated 6 times
f = 11.9942 GHz
d = 8.3037 mm
Ψ = 120°
v = vph = c
Dashed lines: disc loads
(“Irises”)

---
Periodically loaded waveguide
CLIC damped structure, 11.9942 GHz
SLAC SLC structure,
2.856 GHz

---
Powering accelerator structures:
Drive beam (the CLIC way)
- Decelerate “drive beam”, extract energy from beam to microwaves
  - Drive beam: 12 GHz high current / low energy beam
- Deceleration by wakefield in “PETS” structures
- Works efficiently at high power, high frequency, short pulses
- “Beam transformer”

---
Powering accelerator structures:
Klystrons (the conventional way)
- Klystron tube:
  narrowband microwave amplifier
  - Amplification:
    ~100 W -> 10 MW
  - Input voltage: ~100 kV
- Most efficient at long pulses,
  ~1 GHz frequencies
- Complex devices
  with limited lifetime
Pulsed devices

---
CLIC layout

---
CLIC project timeline

---
CLIC construction schedule
(stage 1 & 2)
coord. along collider
year

---
BACKUP
SLIDES
Here may be dragons...
http://www.flickr.com/photos/jrobblee/4702245780

---
Periodically loaded waveguide
- Disc loaded waveguide
- Traveling wave reflected by disks
- Used at high-energy linear accelerators
Main parameters:
- Frequency
- Period d
- Phase advance/period
- Number of periods
RF out
RF in
Period d
Accelerating structure
RF in
Beam in
Beam in
RF out
Beam out

---
Creating the drive beam

---
CLIC “spin-off” benefits
- Research into high-gradient accelerators
  - Shorter linear accelerators
    - Medical accelerators for hadron therapy
    - XFELs for imaging molecules
  - Basic science:
    Understanding the mechanisms
    of vacuum arc breakdown
- Controlling tight, high-intensity beams
- Educating a new generation of accelerator experts