## Slide 1: Status of the Silicon Strip Vertex Detector of the Belle II Experiment
Vertex 2013 Lake Starnberg
Thomas Bergauer (HEPHY Vienna)

## Slide 2
Belle and Belle II
Components
  Sensors
  Electronics
  Mechanics and Cooling
  Ladder assembly
  Mockups
Summary

## Slide 3: Belle I at the KEKB accelerator (1999-2010)
Belle I:
Measurements of CKM matrix elements and angles of the unitary triangle
CP & T & CPT test
Observation of direct CP violation in B decays
probe for new sources of CPV
KEKB accelerator:
Center of mass energy: Y(4S) resonance (10.58 GeV)
High intensity beams (1.6 A & 1.3 A)
Integrated luminosity of 1 ab-1 recorded in total
E.Kikutani / M. Masuzawa

## Slide 4: SuperKEKB/Belle II Upgrade: 2010–2015
40-fold increase in peak luminosity to 81035 cm-2s-1  11010 BB / year
50-fold increase in integrated luminosity until 2023 w.r.t. Belle I
Refurbishment of accelerator and detector required
  nano-beams with cross-sections of ~10 µm x 60 nm
  2 cm diameter beam pipe at interaction region
Crab cavities:
Redesign the lattices of HER & LER to squeeze the emittance
e- 7GeV 2.6 A
e+ 4GeV 3.6 A

## Slide 5: Belle Silicon Vertex Detector (SVD) until 2010
4 straight layers of 4" double-sided silicon detectors (DSSDs)
Outer radius of r~8.8 cm
  Acceptance angle 17°…150°
Up to three 4” sensors were daisy-chained and read out by one hybrid located outside of acceptance region (VA1 chip)

## Slide 6: Belle SVD limitations
Previous SVD limitations were
  occupancy (10%-18% in innermost layer)  need faster shaping or smaller detector elements
  dead time  need faster readout and pipeline
Belle II needs detector with
  high background tolerance
  pipelined readout
  robust tracking
  low material budget in active volume
Previous SVD is not suitable for Belle II !

## Slide 7: New Layout for Belle II SVD (2015-)
Four layers with 6” double-sided strip detectors at larger radii and forward part
Large, individually read out sensors
FE readout electronics inside acceptance region
Maintain low material budget
  Lightweight mechanics
    Thin cooling pipes (CO2)
Fast readout
Layer 3 to 6: 4 layers of double-sided strip sensors
Layer | Radius | Ladders
6 | 135 mm | 16
5 | 104 mm | 12
4 | 80 mm | 10
3 | 38 mm | 7
Layer 1-2: Two layers of
DEPFET pixels

## Slide 8: Current Status
Transition from R&D to production phase
Milestones defined by Belle II schedule
  SVD ladder assembly Nov. 2013 – Sept. 2014
  Ladder mount: Sept. 2014 – August 2015
  SVD ready by August 2015
  VXD (PXD+SVD) ready by January 2016
  VXD installation June 2016
Components
  Sensors
  Front-end and backend electronics
  Mechanics design
  CO2 cooling
  Ladder assembly and lab infrastructure
  Mockups

## Slide 9
Belle and Belle II
Components
    Sensors
  Electronics
  Mechanics and Cooling
  Ladder assembly
  Mockups
Summary

## Slide 10: Double-sided strip sensors from 6” wafers
Sensor Properties:
Double-sided with perpendicular strips
AC-coupled readout with poly-silicon resistor
N-bulk, 300/320 micron thickness
Three layouts only:
  Rectangular small for layer 3 (HPK)
  Rectangular large for layers 4-6 (HPK)
  Trapezoidal for forward layers 4-6 (Micron)
 | Readout strips(p/Rf) | Readout strips(n/z) | Readout pitch (p/Rf) | Readout pitch(n/z) | Sensors # (+ spares) | Active area (mm2)
Large | 768 | 512 | 75 μm | 240 μm | 120+18 | 122.90x57.72 =7029.88
Trapezoidal | 768 | 512 | 50-75 μm | 240 μm | 38+6 | 122.76x(57.59+38.42)/2=5893.09
Small | 768 | 768 | 50 μm | 160 μm | 14+4 | 122.90x38.55 =4737.80

## Slide 11: Rectangular sensors (HPK)
Small DSSDs
  Delivery of 24 pcs. scheduled for end of September
  Two mechanical samples available
Large DSSDs:
  Production finished
  150 pcs in hand
Laser dicing
Saw dicing
Prototypes
Bad strip ratio =5%
P-implant open
Classification of bad strips (ID>26)
Large DSSD IV
Number of bad strips

## Slide 12: Trapezoidal Sensors for Forward Region
Trapezoidal sensor for forward region
Different p-stop layouts on test sensors
Each layout type with four variants (narrow/half narrow/ wide / half wide)
  Testbeam and irradiation study to determine best structure
Atoll
Common
Combined

## Slide 13: eta distribution for atoll p-stop
Charge accumulation in unimplanted region

## Slide 14: Signal-to-noise-ratios
Chart: Atoll p-stop
| narrow | half-narrow | half-wide | wide
 | 32.8 | 35.9 | 36.8 | 33.4
 | 21.5 | 23.1 | 24.9 | 23.8
Chart: Common p-stop
| narrow | half-narrow | half-wide | wide
 | 31.1 | 33 | 34.3 | 33.3
 | 24 | 25 | 23.3 | 22.6
Chart: Combined p-stop
| narrow | half-narrow | half-wide | wide
 | 30 | 31.8 | 33.7 | 34.7
 | 16.6 | 17.3 | 17.6 | 17
Dark colors: non-irradiated, Light colors: irradiated
Atoll pattern (half-wide) performs best, both irradiated and non-irradiated
  Chosen for final sensor, 100 wafers currently being processed by Micron
Test sensors have been Gamma-irradiated with Co-60 (70 Mrad) in Mol (Belgium)
Tested before and after at CERN beam test (H6A 120 GeV hadrons)

## Slide 15: Beam test results
Performance of full modules verified in several beam tests at CERN (2008-2012)
  Including CO2 cooling
  Using EUDET and own beam telescope
Double Origami module
FW wedge module

## Slide 16
Belle and Belle II
Components
  Sensors
  Electronics
  Mechanics and Cooling
  Ladder assembly
  Mockups
Summary

## Slide 17: Readout System Concept
1748 APV25 chips
Front-end hybrids
Rad-hard DC/DC converters
Analog level translation, data sparsification and hit time reconstruction
~2m cable
8 DOCK boxes
~10m
cable
48 FADC+PROC
Optical link (>20m)
48 FTB
COPPER
FTB
COPPER
FADC+PROC
DOCK
Inside of SVD
Crates on top of Belle II
Electronics Hut
DatCon system
Belle II DAQ system
Find RoI
AMC board
AMC board
PXD

## Slide 18: Readout Chip: APV25
Developed for CMS (LHC) by Imperial College London and Rutherford Appleton Lab
  70.000 chips installed
0.25 µm CMOS process (>100 MRad tolerant)
128 channels
192 cell analog pipeline  almost no dead time
50 ns shaping time  low occupancy
Multi-peak mode (read out several samples along shaping curve)
Noise: 250 e + 36 e/pF  must minimize capacitive load!!!
Thinning to 100µm successful
APV25
Origami FE
FW+BW FE

## Slide 19: Origami Chip-on-Sensor Concept
Chip-on-sensor concept for double-sided readout
Flex fan-out pieces wrapped to opposite side (hence “Origami“)
All chips aligned on one side  single cooling pipe
DSSD
Airex
(Polymer foam)
Bonding wire
APV25

## Slide 20: APV25 – Hit Time Reconstruction
Possibility of recording multiple samples (x) along shaped waveform (feature of APV25)
Reconstruction of peak time (and amplitude) by waveform fit
  Using LUT in FPGA
Is used to remove off-time background hits
2...3 ns RMS accuracy at typical S/N
Measurement

## Slide 21: Occupancy Reduction Belle -> Belle II

## Slide 22
Belle and Belle II
Components
  Sensors
  Electronics
    Mechanics and Cooling
  Ladder assembly
  Mockups
Summary

## Slide 23: SVD Ladders
L6 Ladder
L5 Ladder
L4 Ladder
L3 Ladder
FW module
BW module
Origami module
BW r/o
FW r/o
BW r/o
FW r/o
Cooling pipe
Cooling pipe
Cooling pipe
Clamp holding CO2 pipe on APV
Origami module
Origami module
  Pipe Outer  1.6 mm
Thermally conductive gap pad

## Slide 24: Ladder of Layer 6
Basic element “atomic unit” is one ladder
Only FW and BW module can be assembled independently
No single Origami module with one sensor possible
FW module
BW module
Possible separate modules:
Origami flexes
APV25 chips
Airex spacer
Silicon Sensors
PCB Hybrid
PCB Hybrid
Pitch adapters
Ribs

## Slide 25: Material Budget of a ladder
Largest peak contribution by
  Cooling pipe
  Support ribs
Average Material Budget: 0.59%X0
n-side
p-side
Components:
Single cooling pipe
Thinned APV25 (100µm)
3-layer flex circuit
Connection to Strips:
  PA on top side
  wrapped PA for bottom
1mm Airex sheet
6” DSSD
CF support ribs

## Slide 26: Support Ribs
3mm Airex core with laminated 0.15mm CF sheets
Very stiff, yet lightweight thanks to the sandwich construction
Sensor
Support Ribs
Sag max. 44 μm
Sag max. 66 μm

## Slide 27: CO2 cooling system
IBBelle Prototype “MARCO” (Multi-Purpose Apparatus for Research in CO2)
  Power ~ 1 kW
Based on concept by NIKHEF (B. Verlaat)
CO2 plant shared with PXD
Development in collaboration between PXD group (MPI), CERN and NIKHEF
Ladder production sites uses small open (blow) CO2 system
Control cabinet with touch screen
Accumulator
Liquid pumps
1.3 m
1.6 m
1.2 m
Vienna open CO2 system

## Slide 28
Belle and Belle II
Components
  Sensors
  Electronics
  Mechanics and Cooling
  Ladder assembly
  Mockups
Summary

## Slide 29: SVD ladder assembly flow
Three modules types:
  Forward (FW)
  Backward (BW)
  Origami
Ladder assembly sites:
Layer | Institute
3 | Melbourne (AUS)
4 | TIFR India @ IPMU
5 | HEPHY Vienna (AT)
6 | Kavli IPMU (Japan)
FW & BW | INFN Pisa (possibly)

## Slide 30: Assembly Jigs
Assembly base
Sensor jig
XYZθ-stage
Huge number of different jigs (up to 17) necessary:
Assembly bench

## Slide 31: Alignment of Jigs
Using linear bushings (+0/-13µm) & precision pins (g6)
Assembly base & bench are reference
  All linear bushings are fixed bearings  high precision holes (H7)
All other jigs are aligned to them, e.g. Sensor jig
Linear Bushing
Precision Pin
Assembly Bench
Assembly Base
Fixed bearing
Sensor Jig
Aligned bearing

## Slide 32: Ladder assembly equipment
Coordinate Measurement machines (Mitutoyo)
Glue dispensing robots
  CMM used as glue robot in Vienna
Fully-automatic wire bonders
(lot of) manpower and ideas
Automatic wire bonder
Delvotec 6400
HEPHY, TIFR)
Automatic wire bonder
Choonpa Co. REBO-7W
IPMU(borrowed KEK)
CMM
Mitutoyo QV606
(IPMU)
CMM
Mitutoyo Euro-C776
(HEPHY)
Travelling trolley for vacuum tube
CMM modified for
Glue dispersion
(HEPHY)

## Slide 33: Ladder assembly procedure
alignment
w/ XYZθ-stage
Finish
Assembly-jig
DSSD
…
Two weeks per ladder expected
Bonding/glue-curing interlaced
Animation of (simplified) procedure

## Slide 34
Belle and Belle II
Components
  Sensors
  Electronics
  Mechanics and Cooling
  Ladder assembly
  Mockups
Summary

## Slide 35: Mockup IR-PXD-SVD
mockup study @ KEK

## Slide 36: Going real!
Mockup IR-PXD-SVD

## Slide 37: PXD+SVD Testbeam @ DESY
Test of “full” VXD
  2 Layers DEPFET
  All 4 layers of SVD (one sensor per layer only)
  Inside PCMAG superconducting magnet
  MARCO CO2 cooling plant
  Full readout chain
4 weeks beamtime at DESY TB24 in January 2014
  Connectivity test end of June in Vienna to test connection between SVD FADC, FTB, DataCon
  Installation in zone starting end of November 2013

## Slide 38
Belle and Belle II
Components
  Sensors
  Electronics
  Mechanics and Cooling
  Ladder assembly
  Mockups
Summary

## Slide 39: Summary
SuperKEKB will be the highest luminosity machine in the world
Belle II detector will consist of new, enlarged Silicon Vertex Detector
  2 layers DEPFET Pixels (PXD) and
  4 double-sided strip layers (SVD)
Strip Detector (SVD)
  Double Sided Strip Detectors
    Optimal p-stop geometry identified by SNR measurements before and after irradiation
  Chip-on-sensor readout scheme, named Origami, for outermost three layers for low material budget, using CF ribs and CO2 cooling
  Readout with hit time reconstruction for improved background tolerance
  Mass production of ~50 ladders starts this fall, SVD ready by 2015

## Slide 40: Backup Slides follow
The End.

## Slide 41: Belle Detector (1999–2010)
µ / KL detection
14/15 lyr. RPC+Fe
CsI(Tl)
16 X0
Si vertex detector
4 layers DSSD
SC solenoid
1.5 T
8 GeV e-
3.5 GeV e+
Aerogel Cherenkov counter
n=1.015~1.030
Central Drift Chamber
small cell +He/C2H5
TOF counter

## Slide 42: Belle II Detector
electron (7GeV)
positron (4GeV)
KL and muon detector:
Resistive Plate Counter (barrel outer layers)
Scintillator + WLSF + MPPC (end-caps, inner 2 barrel layers)
Particle Identification
Time-of-Propagation counter (barrel)
Prox. focusing Aerogel RICH (fwd)
Central Drift Chamber
He(50%):C2H6(50%), Small cells, long lever arm, fast electronics
EM Calorimeter:
CsI(Tl), waveform sampling (baseline)
(opt.) Pure CsI for end-caps
Vertex Detector
2 layers DEPFET + 4 layers DSSD
Beryllium beam pipe
2cm diameter

## Slide 43
Spatial Resolution of the Belle II Detector
Notes: Slide 2 on the PXD – MC simulation to define the thickness of the DEPFET sensor

## Slide 44: Sensor Types and Vendors
Layer | # of Ladders | Rect. Sensors [narrow] | Rect. Sensors [wide] | Wedge Sensors | APVs
6 | 16 | 0 | 64 | 16 | 800
5 | 12 | 0 | 36 | 12 | 480
4 | 10 | 0 | 20 | 10 | 300
3 | 7 | 14 | 0 | 0 | 168
Sum: | 45 | 14 | 120 | 38 | 1748

## Slide 45: HPK Pinholes

## Slide 46: Sensor Parameters
Rectangular Sensors
Trapezoidal Sensors

## Slide 47: Current Barrel Layout
Slanted Sensors
Origami
Cooling Tubes
Hybrid Boards
Layer | Sensors/ Ladder | Origamis/ Ladder | Ladders | Length [mm] | Radius [mm] | Slant Angle [°]
3 | 2 | 0 | 7 | 262 | 38 | 0
4 | 3 | 1 | 10 | 390 | 80 | 11.9
5 | 4 | 2 | 12 | 515 | 104 | 16
6 | 5 | 3 | 16 | 645 | 135 | 21.1

## Slide 48: Origami Prototype Modules
Single Origami module (layer 4)
Double Origami module (layer 5)

## Slide 49: Material budget
PA/PE/PB/SMD/ are neglected.
Thickness of epoxy glue in ladder assembly is assumed to be 100 mm, or, 0.033 % X0.
DSSD+ Origami | Rib | DSSD | Airex sheet | Origami | CO2 Cooling | 100 mm Glue | Total
HPK+1ORIGAMI | 0.035 | 0.340 | 0.055 | 0.133 | 0.037 | 0.033 | 0.593
HPK+2ORIGAMI | 0.035 | 0.340 | 0.055 | 0.266 | 0.037 | 0.033 | 0.733
Micron | 0.035 | 0.320 | 0.055 | 0 | 0 | 0.011 | 0.421
Micron+ORIGAMI | 0.035 | 0.320 | 0.000 | 0.133 | 0 | 0.033 | 0.576

## Slide 50: Breakdown of material budget
Origami +Z flex
Origami CE flex(length 450mm)
Origami −Z flex
…Three Cu layer FLEX (Taiyo Co.)
Ribs…
Airex foam sandwiched by
Carbon fiber ribs
Glue…Araldite 2011
Glue
Airex
PF2
PF1
PB2
PB1
PA1
PA2
DSSD
Ribs
L6 ladder explosion view

## Slide 51: Comparison VA1TA – APV25
VA1TA (SVD)
Commercial product (IDEAS)
Tp = 800ns (300 ns – 1000 ns)
no pipeline
<10 MHz readout
20 Mrad radiation tolerance
noise: ENC = 180 e + 7.5 e/pF
time over threshold: ~2000 ns
single sample per trigger
APV25 (Belle-II SVD)
Developed for CMS by IC London and RAL
Tp = 50 ns (30 ns – 200 ns)
192 cells analog pipeline
40 MHz readout
>100 Mrad radiation tolerance
noise: ENC = 250 e + 36 e/pF
time over threshold: ~160 ns
multiple samples per trigger possible (Multi-Peak-Mode)

## Slide 52: Status of Belle II Readout Electronics
Pre-production is driven by DESY beam test (January 2014)
  first version of all boards to be used there
Design is done; most parts of hardware exist already











Ready and tested
PCBs ordered, expected soon
PCB being designed

## Slide 53: Cooling Boundary Conditions
Power dissipation per APV: 0.40 W
1 Origami sensor features 10 APVs
Total SVD power dissipation: 607 W
heat amount [W] | APV | pipe | end-ring | cone (L3/4) | cone (L5+6) | cable | Origami | hybrid | total
end-ring (FWD) | 92.8 | 20.0 | 7.0 | 18.9 | 13.8 | 29.2 |  | 13.3 | 195.0
end-ring (BWD) | 92.8 | 15.0 | 9.1 | 32.2 | 6.8 | 29.2 |  | 13.3 | 198.4
Origami (L6) | 94.0 | 19.6 |  |  |  |  | 7.4 |  | 121.0
Origami (L5+4) | 68.0 | 20.0 |  |  |  |  | 5.2 |  | 93.2
total | 347.6 | 74.6 | 16.1 | 51.1 | 20.6 | 58.4 | 12.6 | 26.6 | 607.6

## Slide 54: Baseline Schedule
Start of SVD assembly
SVD ready
set up production sites and build prototypes

## Slide 55: Mechanics
End rings
With integrated
Cooling channels
Carbon Fiber Cones
BWD
APV25 cover
End mount
Kokeshi pin = origin of ladder
Individual rings for L5, L6
Combined L3+4 end rings
rib
insert

## Slide 56: Glue Dispension
X
Y
(0,0)
Chart: Y position(㎜)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0 | 51.0 | 52.0 | 53.0 | 54.0 | 55.0 | 56.0 | 57.0 | 58.0 | 59.0 | 60.0
5min* | 79 | 82 | 88 | 94 | 102 | 109 | 115 | 116 | 114 | 112 | 112 | 112 | 114 | 114 | 115 | 113 | 112 | 114 | 113 | 111 | 111 | 112 | 112 | 112 | 113 | 112 | 111 | 109 | 107 | 106 | 106 | 105 | 104 | 103 | 103 | 102 | 102 | 102 | 102 | 101 | 101 | 101 | 101 | 100 | 100 | 98 | 97 | 94 | 94 | 94 | 94 | 92 | 92 | 90 | 90 | 89 | 85 | 78 | 69 | 64
10min* | 63 | 78 | 97 | 98 | 100 | 101 | 102 | 100 | 99 | 98 | 98 | 99 | 99 | 98 | 96 | 97 | 98 | 98 | 99 | 99 | 98 | 98 | 98 | 98 | 98 | 98 | 99 | 99 | 99 | 99 | 100 | 99 | 97 | 98 | 96 | 96 | 98 | 98 | 97 | 96 | 96 | 96 | 97 | 96 | 96 | 97 | 96 | 96 | 94 | 93 | 91 | 91 | 90 | 91 | 91 | 90 | 86 | 78 | 71 | 61
15min* | 67 | 79 | 89 | 99 | 104 | 105 | 106 | 105 | 104 | 104 | 104 | 104 | 104 | 104 | 104 | 103 | 102 | 102 | 105 | 104 | 102 | 102 | 103 | 104 | 104 | 104 | 103 | 101 | 101 | 101 | 103 | 103 | 102 | 100 | 99 | 99 | 100 | 99 | 98 | 98 | 98 | 98 | 97 | 96 | 96 | 95 | 95 | 95 | 96 | 94 | 93 | 92 | 92 | 94 | 95 | 94 | 94 | 87 | 76 | 68
20min* | 79 | 84 | 97 | 105 | 110 | 112 | 107 | 109 | 111 | 109 | 110 | 108 | 111 | 108 | 111 | 111 | 110 | 112 | 114 | 115 | 113 | 114 | 111 | 114 | 116 | 111 | 113 | 105 | 106 | 106 | 106 | 105 | 107 | 109 | 110 | 110 | 106 | 106 | 103 | 104 | 106 | 102 | 103 | 103 | 99 | 101 | 102 | 104 | 105 | 105 | 106 | 107 | 107 | 108 | 108 | 109 | 105 | 97 | 92 | 80
Chart: Thickness of PA2+glue
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0 | 51.0 | 52.0 | 53.0 | 54.0 | 55.0 | 56.0 | 57.0 | 58.0 | 59.0 | 60.0
0.4MPa | 87 | 97 | 101 | 107 | 98 | 101 | 104 | 105 | 102 | 100 | 100 | 101 | 104 | 106 | 106 | 104 | 102 | 101 | 102 | 101 | 100 | 101 | 102 | 105 | 105 | 103 | 99 | 98 | 99 | 100 | 101 | 102 | 100 | 101 | 103 | 104 | 102 | 101 | 100 | 100 | 100 | 100 | 101 | 101 | 99 | 96 | 98 | 99 | 98 | 98 | 99 | 99 | 98 | 98 | 95 | 92 | 85 | 78 | 70 | 58
0.2MPa | 61 | 67 | 79 | 91 | 101 | 100 | 104 | 100 | 99 | 98 | 99 | 98 | 98 | 98 | 96 | 93 | 94 | 93 | 95 | 95 | 97 | 98 | 99 | 98 | 95 | 95 | 95 | 94 | 92 | 92 | 93 | 93 | 94 | 93 | 93 | 94 | 92 | 92 | 93 | 92 | 93 | 92 | 95 | 95 | 94 | 94 | 95 | 94 | 92 | 91 | 91 | 90 | 92 | 94 | 93 | 91 | 80 | 67
0.15MPa | 52 | 62 | 76 | 84 | 85 | 84 | 80 | 78 | 81 | 83 | 84 | 84 | 82 | 80 | 80 | 78 | 82 | 80 | 80 | 78 | 76 | 76 | 78 | 81 | 84 | 90 | 90 | 81 | 76 | 75 | 80 | 82 | 83 | 82 | 78 | 76 | 75 | 77 | 77 | 78 | 78 | 76 | 77 | 76 | 77 | 77 | 77 | 77 | 77 | 76 | 76 | 76 | 75 | 76 | 76 | 74 | 74 | 70 | 68 | 65
Bonding region
Bonding region
Varying pressure
Varying curing time

## Slide 57: Idea of Ladder Mount Stage
Rotation axis
with encoder
Ladder mount arm
Coordinate measurement
SVD cone and end ring on the CFRP rod
16 September 2013
PRELIMINARY!!!