## Slide 1: Novel Powering Schemes for Pixel and Tracking Detectors
Lutz Feld
RWTH Aachen University
22ND INTERNATIONAL WORKSHOP ON VERTEX DETECTORS
16-20 SEPTEMBER 2013, LAKE STARNBERG

## Slide 2: Outline
The Power Challenge
Powering Options
  Serial Powering R&D
  DC-DC Powering R&D
Implementation of DC-DC powering into the CMS Pixel System
  System design
  System test results
Summary

## Slide 3: Powering today
CMS Tracker cable routing
Example: CMS tracker
~15’000 modules in ~2000 power groups
ASICs supplied at 2.5V and 1.25 V
front-end power: 33 kW
total current: 15 kA
cable length ~50m
loss in cables: 34 kW
cable channels fully used
29 racks with up to 6 crates of power supply modules
cables
CMS Tracker material budget
50% power lost in cables

## Slide 4: The Power Challenge
higher channel density
  pattern recognition
  resolution
more functionality
  hit correlation (triggering)
  A/D conversion
  sparsification
  …
higher speed
technology scaling
  250 nm  130 nm  65nm  …
  decreasing power per transistor
  2.5V  1.5V  0.9V  …
  decreasing voltage margins
[Y. Taur, VLSI-TSA, 1999]
upgradePS
4x10cm2
2000+33000 ch.
P(FE-ASICs)=4W
100 mW/cm²
6.1x11.7cm2
768+768 channels
P(FE-ASICs)=3.6W
50mW/cm²
today

## Slide 5: Implications at the System Level
again CMS tracker as example:
front-end power 35kW 70kW
front-end supply voltage 2.5V  1.25V
front-end current increases by factor 4
cable losses increase by factor 16
cannot increase conductor cross-section to compensate
should rather be reduced to improve material budget
need a novel powering scheme which
is able to provide more power
at a lower current
with sufficient voltage control at modules
with sufficient slow control features
with sufficient fault tolerance
with minimal extra material

## Slide 6: Possible Solutions
add circuitry to each ASIC so that it can be supplied with 2.5V or higher
  e.g. 2:1 charge pump
  is widely used for CPUs
  adds passive components next to each ASIC
  switching noise may interfere with signal read-out
add circuitry so that a number of modules can be supplied with 2.5V or higher
  e.g. DC-DC converter (charge pump or buck converter)
  fewer components than in 1.
  switching noise still an issue but further away from signal path
cascade modules
  derive required voltages from the same current flowing through a chain of modules
  rather different from today’s powering scheme
implemented in several ASICs
(ATLAS FE-I4, CMS CBC, …)
not covered in this talk

## Slide 7: Power Distribution Options
P = U·I = (rU) ·(I/r)  supply power at higher voltage i.e. lower current  cable loss Ploss=R·I2 is reduced by factor r2!
DC-DC Powering r=conversion ratio
PS
module
DC-DC
module
DC-DC
Conventional Powering
PS
module
module
Serial Powering r=number of modules in chain
PS
module
module
shunt
shunt
well established
excessive cable losses
system design is kept simple and close to current systems
only one new component
switching noise is a concern
no switching
each module has different ground potential
modules in a chain are coupled, need safety features
thinner and less cables
material budget reduction

## Slide 8: Serial Powering in more Detail
current determined by biggest load in the chain
load variations in a module can affect the whole chain
read-out and control signals must be AC or opto coupled
apart from this, additional components are small ICs
with many modules in the chain the gain factor r can be quite high (e.g. 10-20)
current source
module
shunt regulator
bypass shunt
module
shunt regulator
bypass shunt
module
shunt regulator
bypass shunt

## Slide 9: Serial Powering: ATLAS Pixel
End of stave card
Faulty TABs – not used
LVDS + NTC
Module 6
Module 5
Module 8
Module 2
Power cable
serial power chain of 4 modules on a stave
shunt
LDO
ShuLDOs can be operated in parallel
 different voltages can be supplied
 | Noise (e-) |  |  | 
Noisy module | Module 8 | Module 6 | Module 5 | Module 2
No noisy module | 131.2 | 145.1 | 144.6 | 130.8
Module 8 | --- | 149.1 4 | 148.4 3.8 | 133.3 2.5
Module 6 | 134 2.8 | -- | 147.4 2.8 | 134.2 3.4
Module 5 | 134.5 3.3 | 150 4.9 | -- | 134.2 3.4
Stability test: make module noisy by lowering the threshold
measured noise increase of max 5e- on the other modules in the chain is not of concern
[thanks to Laura Gonella for the Bonn group]

## Slide 10: Serial Powering: ATLAS Strips
Distributed SP Architecture
  Shunt transistors within ABCN25 FE ASIC, 20 per hybrid
  One control block per hybrid (SPP chip or commercial parts)
Three short (8 hybrid) prototypes built
  Some with protection circuitry (SPP chip commercial parts)
  Good results in “Chain of Modules” Configuration
Longer (24 hybrid) prototype to follow in the coming months
  With integrated protection from SPP chip
0V
2.5V
5V
7.5V
10V
Distributed SP Architecture (within the hybrid)
[thanks to Peter Phillips (RAL)]

## Slide 11: DC-DC Powering: Buck Converters

## Slide 12: Converter ASIC Development at CERN
T2
T1
control
circuits
several iterations: AMIS4/5, FEAST
developed by CERN-PH-ESE (St. Michelis, F. Faccio)
radiation-tolerant design in AMIS I3T80 0.35µm CMOS technology (ON Semiconductor): TID above 200Mrad, displacement damage up to 7e14 1MeV neutrons/cm2
Iout < 3A, more is possible with proper cooling
Vin < 12V
fs configurable from 1MHz to 3.5MHz
Vout adjustable from 1.2V to 4V
Vin=10V, L=460nH, Vout=2.5V, f=1.7MHz
[Stefano Michelis, TWEPP 2012]
CMS phase-1 pixel system
[2012 JINST 7 C01072]
AMIS5

## Slide 13: CMS Pixel Upgrade
current pixel detector specified for LHC design luminosity of 1 1034 cm-2s-1
LHC planning: ~ 21034 cm-2s-1 between 2015 and 2018  pixel detector would have 50% dead time (at 50 ns bunch crossing interval)  CMS plans to exchange pixel detector in shutdown 2016/17
new pixel detector
  4 barrel layers, 2x3 disks (now 3 layers, 2x2 disks)
  new read-out ASIC
  less material inside tracker acceptance
  factor 1.9 more channels
  factor 1.9 increase in
  power consumption
cable plant must be re-used: heat load would increase by factor 4
 need a new powering scheme!

## Slide 14: Implementation into the CMS Pixel system

## Slide 15: Implementation into the CMS Pixel system
layer 1
layer 4
layer 2
layer 3
”digital
converters” (3.0V)
”analogue
converters” (2.4V)
served by cable 1
served by cable 2
cable 2
cable 1
13 converter pairs per bus board
6 - 7 pairs powered from one power supply
each converter pair serves 1 - 4 pixel modules
Iout < 3A per converter

## Slide 16: System integration issues
DC-DC converters are a new component  no working experience  unclear which control and protection features are essential chosen approach:
  converters switch off in case of over-temperature and under-voltage and switch back on when conditions are again fine, output current is limited
  solid state fuse to disable converters with excessive current permanently
  converters can be dis-/enabled and status is read via slow control communications
  no remote sensing  voltage drops need careful attention
no electromagnetic interference with pixel modules (and the rest of CMS)
single event upsets in converter ASIC at some low level must be tolerated
‘bus board’ needed to distribute (large) currents to and from converters
tight space constraints
converters should be accessible/replaceable
cooling needed (1-2W per converter)

## Slide 17: DC-DC Converter Development
AC_PIX_V10 A with AMIS5: 2.8cm x 1.7cm
100 DC-DC converters have been built so far
based on CERN ASICs AMIS4/5, and soon FEAST
Vin =10V
Vout = 3.0V or 2.4V
switching frequency fs = 1.5MHz
2-layer PCB
pi-filters at in- and output
Shield (0.3mm plastic with 30µm Cu + 1µm Sn)
has 3 functions:
shield magnetic emissions
cooling contact for the coil
segregation of “noisy“ parts from output filters
with shield; total weight ~3g
Toroidal plastic core inductor L = 450nH

## Slide 18: Effectiveness of Shield
Strong reduction of magnetic emissions and output noise
Common Mode output noise spectrum,
measured with spectrum analyzer
B-field, measured with pick-up probe
above coil/shield
No shield
With shield
No shield
With shield
pick-up probe voltage (mV)
pick-up probe voltage (mV)

## Slide 19: Efficiency
Vout= 2.5V
Vout= 2.5V
Standard deviation [%] from 5 converters
Mean efficiency [%] of 5 converters
very good and uniform efficiency around 80%

## Slide 20: System tests with 24 converters and 2 pixel modules
50m
2m

## Slide 21: Cold Test
two-phase CO2 cooling system at -20°C
fully equipped bus board (24 converters)
pipes are thin: 1.7/2.0 mm in lab; 1.8/2.2mm in CMS
programmable load can be applied to each converter
Protoype bus board with 24 DC-DC converters
Aluminium cooling bridges
Chart: T [°C]
| DC-DC off | 0A | 1A | 2A | 3A
Coil below shield | -13.3385 | -1.1662 | 0.79823 | 7.8167 | 19.0956
Chip below shield | -12.0559 | -0.37303 | 1.4376 | 8.0599 | 18.6824
Cooling bridge, no shield | -11.9776 | -7.0887 | -6.1465 | -2.6591 | 2.9128
Cooling bridge, shield | -13.3167 | -8.0828 | -7.2634 | -4.2662 | 0.47521
Pipe | -14.926 | -14.853 | -14.8024 | -14.6424 | -14.2634

## Slide 22: Module noise with 24 converters running
Two pixel modules operated by standard power supply
a pair of converters with
24 converters operating in parallel
Load changes as expected from LHC orbit gaps
 drop from 2A to 0A for 3µs every 89µs
Module 1
Module 2
DC-DC converters do not
increase pixel module noise

## Slide 23: Summary
future pixel and strip tracking systems need improved powering schemes to cope with
  increasing granularity
  extended functionality
  decreasing ASIC supply voltage
different options available:
  charge pump in each ASIC
  DC-DC converters to power single or multiple modules
  serial powering of modules
all options have been shown to work in small systems (typically 4 modules)
serial powering under study for ATLAS pixel and strips
DC-DC powering under study for CMS pixel and strips, CMS HCAL, ATLAS strips, LHCb, Belle II, Panda
system integration has to be carefully analyzed and studied and should guide the choice of an appropriate powering scheme
DC-DC powering of CMS pixel detector described in detail as a case study

## Slide 24: Additional Material

## Slide 25: DC-DC Converter Requirements for CMS Pixel Upgrade
radiation hardness: 2x1014neq/cm2, 100 kGy for 500 fb-1
magnetic field tolerance: 3.8T
input voltage 10V
output voltage 2.4V / 3.0V
conversion ratio 3:1 – 4:1
max output current 3-4A
efficiency at least 75%
size of converter: 30x20x14 mm3
converter need to be cooled
slow control features: enable, power good
protection features: over-temperature, over-current, under-voltage
stability against fast load variations (orbit gaps)
material budget uncritical (z=2000-2300 mm, r=190 mm)
1184 converters in pixel system
1800 converters to be produced
commercially
not available
typical and
achievable
what is
needed?
project
specific

## Slide 26: The Shield
0.3mm plastic galvanically coated with 30µm Cu + electro-less 1µm Sn
two methods are considered for the body:
  rapid prototyping
  injection molding

## Slide 27: Thermal Performance
 Coil temperature
 Chip temperate
Cooling block
temperature:
+5°C
-10°C
-24°C
Coil temperature
- without shield
- with shield
good thermal performance even beyond 3A

## Slide 28: DC-DC Bus Board Design and Tests
488mm x 40mm x 1.6mm
Chart: DC-DC converter position
| L1C1D1 | L1C1D2 | L4C1D4 | L4C1D5 | L4C1D6 | L2C2D1 | L2C2D2 | L2C2D3 | L3C2D4 | L3C2D5 | L3C2D6 | L1C1A1 | L1C1A2 | L4C1A3 | L4C1A4 | L4C1A5 | L2C2A1 | L2C2A2 | L2C2A3 | L3C2A4 | L3C2A5 | L3C2A6
Callculated | 27.302 | 29.46 | 33.1167 | 30.4732 | 38.4626 | 25.4231 | 18.2884 | 29.2387 | 37.5489 | 34.5515 | 43.6102 | 12.944 | 13.718 | 32.4779 | 27.5366 | 28.8168 | 19.4272 | 13.718 | 21.738 | 34.5011 | 28.7687 | 29.8673
Measured before TC | 21.16 | 22.1 | 29.25 | 24.48 | 32.41 | 19.41 | 15.54 | 25.6 | 35.11 | 31.44 | 38.99 | 13.43 | 13.31 | 32.16 | 27.14 | 27.74 | 20.71 | 13.78 | 21.8 | 35.25 | 27.97 | 29.52
Measured after TC | 21.45 | 22.69 | 29.19 | 24.69 | 32.45 | 19.75 | 15.25 | 25.13 | 35.5 | 30.89 | 39.78 | 13.38 | 13.18 | 31.93 | 26.78 | 27.51 | 19.87 | 13.49 | 21.38 | 34.72 | 27.79 | 29.18
Calculation Measured before TC Measured after TC
Input and output voltages, control signals
8 Cu layers a 70µm
Protoype for 24 converters studied
Voltage drops to be well understood (no remote sensing!)
  Reasonable agreement with calculation
  No degradation after 120 thermal cycles between -10°C and +40°C under load

## Slide 29: Load Regulation
output voltage stable against load changes

## Slide 30: Synchronization of Converters
oscillators can lock to each other and cause large transients
coupling of DC-DC converters on common power line might increase input noise
simulations show that synchronous switching should be tolerable
still we would like to check:
  did not observe locking or frequency change , even when a close-by frequency was imposed on input cable (740mVpp) or radiated by an external coil (~10mW)
fs of 8 converters vs. time
Time [min]
Frequency [Hz]
Intensity [dB]
Frequency [Hz]
Intensity [dB]
Measurement number
converter frequency crossing

## Slide 31: Mock-up of Supply Tube

## Slide 32: CMS Pixel Power Distribution