## Slide 1
N. Biancacci
MSWG 15-03-2013
CERN PS impedance localization update
Transverse impedance localization method
Application to the PS
Conclusion and Outlook

## Slide 2
Acknowledgement
PS operators, G.Arduini, R.Calaga, H. Damerau, R. De Maria, S.Gilardoni, M.Giovannozzi, C.Hernalsteens, M.Migliorati, E.Métral,
N.Mounet, G.Rumolo, B.Salvant, G.Sterbini, S.Persichelli, R.Wasef

## Slide 3
Transverse Impedance Localization Method
[1] "Localizing impedance sources from betatron-phase beating in the CERN SPS", G. Arduini, C. Carli , F. Zimmermann EPAC'04.
[2] “Transverse Impedance Localization Using dependent Optics” R.Calaga et al., PAC’09.
Global measurements: variation of tune frequency with intensity.
Local measurements: variation of phase advance between BPMs with intensity.
)
The method for local measurements was proposed and applied by G. Arduini et al. in 2004 and 2009 in SPS [1,2] and benchmarked with HEADTAIL.

## Slide 4
The aim of the measurement is: correlating the phase advance beating variation with intensity with a local source of impedance. In “optical” terms, an impedance would behave as a (de)focusing intensity dependent quadrupole.
Transverse Impedance Localization Method

## Slide 5
Global impedance
Local impedance
Theory
Impedance budget
Machine
Measurement accuracy
Estimations
Measurements
Impedance Budget Flowchart
RECONSTRUCTION

## Slide 6
Global impedance
Local impedance
Theory
Impedance budget
Machine
Measurement accuracy
Estimations
Measurements
Impedance Budget Flowchart
RECONSTRUCTION

## Slide 7
Impedance budget
S.Persichelli
A PS impedance database is being constructed @ 2 GeV.
Kickers
Rewall+SC
Mounet-Métral code
SC
dipolar
quadrupolar

## Slide 8
Global PS impedance estimations
We estimated a partial impedance budget at injection:
Resistive wall + Indirect space charge;
Kickers (Tsutsui)
Cavities 80MHz (negligible)
Ver. plane: 4.5 MOhm/m.
Hor.plane= 2.8 MOhm/m.
+SC

## Slide 9
Case M=100, X=[1e11->1e12]
N=
Local PS impedance estimations
N=
N=
The impedance-induced beating can be calculated and compared with the accuracy expected or required from measurement:
Impedance-induced beating amplitude from theory (Sacherer)

## Slide 10
Global impedance
Local impedance
Theory
Impedance budget
Machine
Measurement accuracy
Estimations
Measurements
Impedance Budget Flowchart
RECONSTRUCTION

## Slide 11
The uncertainty chain:
Machine
BPM system
A
Noise Signal Ratio
Phase advance accuracy
Phase advance slope accuracy
FFT

## Slide 12
Accuracy of phase advance measurements
To be reduced (noise level, kicker strength, BPMs gain, BPM transfer function)
To be increased: It is the width of the scan of intensity. Upper threshold can be TMCI. Lower is BPM sensitivity.
To be increased: N=Number of turns. Depends on ability on hardware and data trasmission from BPM to storage.
To be increased: M= number of measurements. Usually a 100 points it’s the case.
Given a set of M measurements of with equal error bars , obtained along an intensity scan X, we can calculate using standard straight line least squares:
This quantity has to be compared with the impedance-induced phase beating amplitude!

## Slide 13
The impedance-induced beating appears to be small with respect to the measurement accuracy usually achieved (NSR~5%) during MDs.
Local PS impedance estimations
MD on 05-02-2013_#2
Only big impedance source are expected to be localized.

## Slide 14
Global impedance
Local impedance
Theory
Impedance budget
Machine
Measurement accuracy
Estimations
Measurements
Impedance Budget Flowchart
RECONSTRUCTION

## Slide 15
The measurement were done with single bunch at injection energy 2GeV, with a TOF beam.
Intensity scan is usually from ~1e11 to ~1e12 ppb.
TFB was used as vertical kicker.
The smallest bunch length is 90ns (4) with 200kV on 10MHz cavities.
H.Damerau, S.Persichelli
Measurements

## Slide 16
Measurements
PS-05-02-2013_#3 Bunch length~107ns (rf@100kV)
Ztot~6.3 MOhm/m (from tune shift)
PS-05-02-2013_#2
Bunch length~90ns (rf@200kV) Ztot~6.5 MOhm/m (from tune shift)

## Slide 17
RECONSTRUCTION
Global impedance
Local impedance
Theory
Impedance budget
Machine
Measurement accuracy
Estimations
Measurements

## Slide 18
For the moment we chose the reconstruction points as everything in the machine except monitors, vacuum port and magnets. So:
  Cavities;
  Kickers;
  Wirescanners;
  TFB;
  Septa;
  Wall current;
Response matrix size: 49 reconstructors x 40 BPMs.
Reconstruction
Before reconstruction:
After reconstruction:
Check how the measured and reconstructed slope overlap;
Do stress-test to check the stability of the solution:
Switch off corrector
residual norm increase > 30%?
Y
N
Keep corrector sequence
Choose shorter sequences

## Slide 19
Measurements
PS-05-02-2013_#3 Bunch length~107ns (rf@100kV)
Ztot~6.3 MOhm/m (from tune shift)
PS-05-02-2013_#2
Bunch length~90ns (rf@200kV) Ztot~6.5 MOhm/m (from tune shift)

## Slide 20
reconstructed
Theory
Low bound from accuracy estimation
Reconstruction

## Slide 21
Reconstruction
After stress-test:

## Slide 22
PS-05-02-2013_#3 Bunch length~107ns (rf@100kV)
Ztot~6.3 MOhm/m (from tune shift)
Ztot~5.9 MOhm/m (from recons.)
PS-05-02-2013_#2
Bunch length~90ns (rf@200kV) Ztot~6.5 MOhm/m (from tune shift) Ztot~6.4 MOhm/m (from recons.)

## Slide 23
KFA71
BFA21+KFA21
PS-05-02-2013_#3 Bunch length~107ns (rf@100kV)
Ztot~6.3 MOhm/m (from tune shift)
Ztot~5.9 MOhm/m (from recons.)
PS-05-02-2013_#2
Bunch length~90ns (rf@200kV) Ztot~6.5 MOhm/m (from tune shift) Ztot~6.4 MOhm/m (from recons.)

## Slide 24
Conclusion and Outlook
Conclusion:
Understood the role of noise in the measurement.
Transverse impedance model is going to be built.
At least 5 good localization measurements collected in 2012/2013 MD time.
Two probable impedance locations localized in KFA71 and BFA21(S+P)+KFA21.
Outlook:
Analyze remaining measurements and crosscheck localization results.
Improve stress test on the solution (vary residual norm threshold, etc…)
Crosscheck with simulations,
…

## Slide 25
Backup

## Slide 26
Reconstruction points