## Slide 1: SA2 “Testbeds as a Service”
LHCONE Meeting
May 2/3 2013
Geneva, CH
Jerry Sobieski (NORDUnet)

## Slide 2: GN3+
GN3 is done...... GN4 is not yet specified.....
“GN3 Plus” is a 24 month project to carry the GEANT services forward while GN4 architecture emerges
  Begins April 1, 2013
Production Services:
  SA1: Core Backbone Services (GEANT core network engineering)
  ​SA2: Testbeds as a Service​
  SA3: Network Service Delivery​ (BoD, Wave services, VPN)
  SA4: Network Support Services​​
  SA5: Application Services​​ (edu*)
  SA6: Service Management & Operation (NOC)
  SA7: Support to Clouds​
Research Activities
  JRA1: Network Architectures for Horizon 2020
  JRA2: Technology Testing for Specific Service Applications
  JRA3: Identity & Trust Technologies for GÉANT Services
Network Activities
  NA1: Management​
  NA2: Communications & Promotion​​NA3: Status & Trends​
  NA4: International & Business Development

## Slide 3: SA2+: Testbeds as a Service
Objective: Provide rapid prototype network testbeds to the network research community
  Draws from numerous predecessor projects:
    FEDERICA, Network Factory, OFELIA, NOVI, MANTICHORE, GEYSERS, DRAGON, GENI, PLANET LAB, ....
Activity leader: Jerry Sobieski (NORDUnet)
  T1: Hardware and Systems Engineering: TL TBD
  T2: Software Development TL: Blazej Pietrzak (PSNC)
  T3: Service Management TL: Peter Szegedi (TERENA)
  T4: Multi-Domain Interoperability TL: TBD
2 Key aspects to the Testbeds Service:
  “Packet” Testbeds – dynamically allocated, virtualized networks over packet oriented infrastructure with a pan-European footprint.
  “Photonic” Testbeds – manually engineered testbeds over dark/dim fiber for photonic and/or long haul transport services research.

## Slide 4: SA2: Packet Testbeds
Phase 1: GEANT
  Dynamically allocated virtualized resources:
    General purpose computational nodes
    Router nodes
    Storage resources
    Other hardware nodes: e.g. OpenFlow switch fabrics, ...
    Network transport resources between nodes
  GN3+ Resource pool will be geographically distributed across ~four GN3+ pops initially.
  Intend to have approximately four participating NREN Resource pools
Phase 2: Global interoperability architecture
  Develop and deploy scalable secure virtualized network environments beyond the GEANT footprint
A SA2 testbed instance is, by default, insulated from other testbeds or other production services
Carefully managed access beyond the testbed hotzone can be requested in order to access external services
An API will be provided to interface to the service and to allow the user to control the testbed elements
A GUI will be provided (using the API) to provide basic interactive

## Slide 5: Photonic Longhaul Testbeds
Leverage unused LH fiber segments for photonic/optical technology field tests
Five (5) segments available:
  London-Paris, 673km
  Frankfurt-Geneva, 749km
  Amsterdam-Frankfurt, 665km
  Amsterdam-Brussels, 290km
  Milan-Finkenstein-Vienna, 643km+ 462km
SA2 Engineering will work with “well defined” research programs to engineer these segments for their research

## Slide 6: SA2 Testbeds Phase 1
Compute Resources
Storage Resources
Geographically distributed physical resource pool
Network Transport Resource
(e.g NSI BoD service)
GN3+SA2 Virtualization/Allocation Layer
Testbed X Ctrl Agent
Testbed Y Ctrl Agent

## Slide 7: SA2 Testbeds Phase 2
Geographically distributed physical resource pool
Domain C services
Domain A services
Domain B services
CMS global environment Agent

## Slide 8: Virtualized HEP Services
Domain C services
Domain A services
Domain B services
CMS domain service(s)
CMS experiment J
CMS workflow K
CMS process M

## Slide 9: GÉANT Open Calls
GÉANT Open Calls are structured around three key themes:
  Use cases to run on existing GÉANT production and experimental network facilities.
    Ex: Mixed mode guaranteed+scavenger, or policing/shaping at 100G to support LHCONE
  Self-contained Research and Technology Development (RTD) work packages to support on-going project activities.
    CDN networks
  RTD to promote, develop and demonstrate Innovation in a Multi-Domain Research and Education Networking Environment.
    LHCONE virtualization over multiple domains....
Lightweight proposals, due by end of June
Approximately 150 kEUR- 300 kEUR per award (total approx 3M EUR)
To be completed by March 2015 (end of GN3plus project)
See www.geant.net

## Slide 10: Basic Self-Contained Testbed
Transport Links
Computational Nodes

## Slide 11
N1
N4
N3
N2
L1
L2
L3
L4
L5
P0
P0
P1
P2
P3
P4
P5
P1
P0
P1
P0
P1
P0
P1

## Slide 12: Resource Graph
N2
N1
N3
q

## Slide 13: Resource Graph
CA