## Slide 1
X-band SLED type Pulse Compressor.
Made in CERN.
I. Syratchev
April 10 2013

## Slide 2
Why do we need the pulse compression technology!?
There is a general knowledge, that for the similar average power, it is much easy to build RF power amplifier (like klystron) with moderate peak power and long RF pulses, than the device with short pulses and high peak power. The same true for the klystron modulator. From the other hand, NC accelerating structure normally needs relatively short RF pulses, factor 3-10 shorter then the convenient klystron pulse.
The pulse compression is a technology which allows to increase the peak RF power in exchange for the RF pulse length reduction. The method has a limited efficiency. First due to the ohmic losses in the RF storage element and second, if the system parameters are kept constant during the pulse (passive method), because of the transient processes in a system.
RF amplifier
RF energy storage element

## Slide 3
Cavity (ies)
BOC
RF Pulse compressors
Delay
Line (s)
RF energy storage element (s):
Operational regime:
Active. The properties of the RF storage network (coupling/phase) can be controlled externally. It allows to increase efficiency.
Passive. The phase/amplitude modulation of the RF power source
After decade of development, the powerful enough active elements are still not available.
The length of the delay line is proportional to the pulse length. At a low frequency/long pulse SLED II, BPC and DLDS become impractical!

## Slide 4
1)
2)
TE015, Q0~105
The story started at SLAC in 1973
3) 1800 phase flip

## Slide 5
Later on…
CERN, 1985
Still in operation at CTF3

## Slide 6
And continued…
TE015, Q0~105
KEK, ATF&KEKB, Japan 1992.
Pohang Accelerator Laboratory
Korea, 1994?
TE015, Q0~105
TE015, Q0~105
BINP, Novosibirsk, Russia, 2000?
For almost 35 years more then hundred of S-band SLED type pulse compressors are successfully operated worldwide.

## Slide 7
SLED type pulse compressor at higher frequencies
Q0=2x105
Q0=1x105
Frequency, GHz
H01N cavity performance
Q0=1.65x105
(Spring 8)
Longitudinal index (N)
SLED power gain/efficiency plot
Exercise:
F=6 GHz, TKL=2500 ns, Tout = 500 ns (C=5), target efficiency 70% (Pg=3.5)
X=6.7. To satisfy, the cavity unloaded Q-factor should be: 3.2x105
Q0=3x105 (6 GHz)
To keep reasonable compression efficiency at a higher frequencies, it is necessary to increase the cavity longitudinal index N, thus the relative length of the cavity.
SLED
Q0=1.8x105
(LIPS)

## Slide 8
Barrel
Open
Cavity RF pulse compressor
The second generation of the SLED type pulse compressor

## Slide 9
-d
d
2h
2a
 = 
 = 
r
z
r0
The eigen-frequency of the Barrel cavity with
Emnq oscillation is the solution of:
mn is a root of the Bessel function that for the
big m can be approximated as:
The optimal radius r0, when the external caustic
has the smallest height comes from:
where  and  are derived from:
Finally the height of the external caustic and Q-factor
of the cavity are:
Barrel cavity short theory.
Cavity profile:
Whispering gallery mode
for Copper:

## Slide 10
The concept of the BOC (originally VPM – VLEPP Power Multiplier) was proposed in 1990 (Balakin, Syratchev). In 1994 the fist X-band VPM was tested in KEK.
input
reflected
output
150MW
Open cavity
Closed cavity
Q0 = 1.9x105
Test cavity (TM25,1,1)
Diameter 0.263 m

## Slide 11
Internal view
of coupling holes
3 GHz BOC RF pulse compressor for CTF3 (2000)
XX century
XXI century

## Slide 12
5.7 GHz BOC RF pulse compressor for PCI (2012)
BOC’s unloaded Quality factor
Goal: ≥ 190000
HFSS: 210000
Measured: 204000
Beta: 9.4

## Slide 13
The third generation of the SLED type pulse compressor
with beating modes in a cavity (BMC). 2009 (GYCOM, Russia).
H10->H01 mode converter
Mode mixing taper
Beating wave cavity
3-db hybrid
Q0 ~ 2x105
Measured Q0 ~ 1.6x105 (expected ~ 2x105 )
Tuning plungers heating up problem.
Backlashes problem with plungers movement.
First BMC is now successfully operated at XBOX #1.

## Slide 14
X-band SLED pule compressor at 2013 (back to the roots)
Cavity operating mode H0,1,32
Integrated cooling
Compact mode launcher
Double-height -3dB hybrid, made at CEA/CERN
Manual resonant frequency de-tuners
Common vacuum circuit
Fixed tuners
Objectives:
Compact (inexpensive) RF design
Relaxed fabrication tolerances
Fixed frequency tuners (frequency control by temperature)
Detuning option.

## Slide 15
 36.27
Iris thickness 2 mm with inner filler radius 1 mm
target
Q0 = 1.78x105
5.85
Q Loaded
beta
Cavity operating mode H0,1,32 , length 0.444 m, Q0 (HFSS) = 1.78x105
Storage cavity design
Adiabatic taper
Coupling iris

## Slide 16
The frequency tuning sensitivity with the piston repositioning is 2 MHz/mm. To provide reflection in a steady state <-20 dB, the cavities need to be synchronized to the level better than 0.1 MHz, that will require mechanical repositioning or re-machining the piston surface in steps <4.5 microns.
To provide reliability and robustness of the cavity tuning, it is decided to make the position of the tuning piston fixed. That means that iterative re-machining process of the piston will be required. To reduce the sensitivity of the iterations, the area of the intervention is defined in a special way:
Magnetic field on the piston surface
450
Re-machining direction
Re- machining of the 450 chamfer at the piston inner diameter gives tuning sensitivity of 1.1 MHz/mm – about 20 times less than retouching the flat part.
Cavity frequency tuning by re-machining piston surfaces
Fine tuning
Coarse tuning
Frequency down
Frequency up

## Slide 17
11.9712
11.9674
Re-machined pistons:
#1 -> +0.8-0.003/+0.009 mm
#2 -> +0.99+0.006/+0.007 mm
Expected: 11.9872 GHz
11.98715
Measured at 30 0C
PC cavities tuning. 1-st step.
Predicted compression:
250 ns
Original:
1st tuning:
Zoom

## Slide 18
PC cavities tuning; 2-nd step + final tuning with chamfer.
Fc=11.990528 GHz
Fit to theory: beta=5.85 (expected 5.85); Q0~2.0x105!!! (expected 1.78x105 )
The pulse compressor performance is above expected!
Operational temperature at vacuum (for 11.9942 GHz): 29.35 0C

## Slide 19
De-tuning cavity with a ‘small’ piston allows to make PC transparent (no compression)
+25 MHz
Other issues
Cavity matching is about -30 dB
(to be confirmed after final assembly)

## Slide 20
Simulations vs. measurements
HFSS simulations using file from Raphael, gave the frequency: 11.9994 GHz.
The only possible explanations for ~ 30 MHz discrepancy through fab. errors are:
Cavities diameter is bigger by ~ 1.5 mm, or
The cavity length is longer by ~ 1.5 mm, or
Some combinations of the two