## Slide 1
Heinz Graafsma
Head of FS-DS; DESY-Hamburg
and University of Mid-Sweden; Sundsvall
Status and main challenges for detectors in Synchrotron Applications.

## Slide 2: The Detector Challenge:
1900 1960 1980 2000
PETRA-3
Second generation
First generation
X-ray
tubes
ESRF (2000)
ESRF (1994)
Synchrotron Sources
brilliance

## Slide 3: The Detector Challenge:

## Slide 4: But is there hope ?
Europe has a long tradition in developing detectors for science; at least in part thanks to CERN
Europe has a large number of Storage Ring and FEL sources; which are centrally run  this allows for centralized and larger scale instrumentation development
There is a surprisingly large number of Hybrid Pixel Array Detector systems; mostly photon-counting
PSI/SLS and CPPM-Marseille over 10 years ago started to use HEP HPAD detector technologies for dedicated photon science systems.

## Slide 5: (some) major running systems:
PILATUS + EIGER
XPAD
MYTHEN + GOTTHARD
PIXIRAD
pnCCD
MEDIPIX
….

## Slide 6: (some) major systems under development
MEDIPIX
  LAMBDA (DESY)
  EXCALIBUR (DIAMOND)
AGIPD (for EXFEL) (3 German + 1 Swiss partner)
LPD (for EXFEL) (2 British partners)
DSSC (for EXFEL) (7 German + Italian partners)
JUNGFRAU (for SWISSFEL) (PSI)
PERCIVAL (for low-E FEL applications) (DESY, STFC, Elettra, Diamond)
…

## Slide 7: (some) major systems under development
MEDIPIX
  LAMBDA (DESY)
  EXCALIBUR (DIAMOND)
AGIPD (for EXFEL) (3 German + 1 Swiss partner)
LPD (for EXFEL) (2 British partners)
DSSC (for EXFEL) (7 German + Italian partners)
JUNGFRAU (for SWISSFEL) (PSI)
PERCIVAL (for low-E FEL applications) (DESY, STFC, Elettra, Diamond)
…

## Slide 8: The FEL-Challenge: Different Science
Completely new science
Fast science 100 fsec
“Single shot” science
x109

## Slide 9
K. J. Gaffney and H. N. Chapman, Science 8 June 2007
What is the Goal ?

## Slide 10: The European Free Electron Laser

## Slide 11
4.5 MHz
What are the Challenges ?

## Slide 12
The Adaptive Gain Integrating Pixel Detector
C1
Leakage comp.
C2
C3
Discr.
Control logic
Trim
DAC
Vthr  VADCmax
Analogue encoding
Normal Charge sensitive amplifier
High dynamic range:
Dynamically gain switching system
Extremely fast readout (200ns):
Analogue pipeline storage

## Slide 13
At the P10 beamline
Beam direction (coming from sample)
AGIPD sensor
Chip tester box
It took about 1 ½ hours to set up, after about 2 hours we saw the first image
Not in the picture: Sample, Alexanders PC, people, …

## Slide 14
Looking at the direct beam
photons/second
Logarithmic color scale
Gain switching experimentally proven
104 photons / pulse
Single photon sensitivity
4.5 MHz frame rate

## Slide 15
The Analogue Storage
Sensor
ASIC per pixel
ASIC periphery
Chip output driver
Mux
HV
+
-
THR
DAC
SW
CTRL
Analog Mem
Analog Mem
CDS
RO Amp
Calibration circuitry
Adaptive gain amplifier
352 analog memory cells
…
…
RO bus (per column)
Pixel matrix
Notes: Mention random vetoing possibility.

## Slide 16
AGIPD 1.0 Pixel electronics
200 x 200 micron2 pixels
352 storage cells + veto possibilities.
Minumum signal (noise) = 330 electrons = 0.1 photon of 12 keV
Maximum signal = 33 106 electrons = 104 photons of 12 keV
4.5 MHz frame rate
64 x 64 pixels per ASIC
2 x 8 ASICs per module (128x512 pixels, no dead area)
4 modules per quadrant

## Slide 17: Soft is really hard
PETRA III beamline(s)
250-3000 eV
up to 5x1012 photons/s delivered to the sample
FLASH
15-300 eV (in future possibly up to ~550 eV)
Higher energies in harmonics
1012-1014 photons/pulse delivered to the sample
Pulse duration 10-200 fs
(up to 800x)10 pulses/s
Synchrotron Free Electron Laser

## Slide 18: Technology Options Include
CCD
Limited maximum full-well capacity
Limited frame rates
Blooming
In our “region of interest” (single-photon at 250eV to 105+ photons): lower dynamic range than CMOS sensors
Hybrid Detector
Optimize sensor and electronics separately
Pitch limited by feasible bump bond size
Added complexity of bump bonding
CMOS Sensor
Profit from industry developments
Depleted region is the epilayer, currently limited to ~ 20mm
In-pixel conversion to voltage/amplification
On-chip digital conversion possible
credit: Jim Janesick, Pixelvision Inc.
credit: HLL MPG
credit: Medipix Collaboration
credit: RAL-STFC
from Turchetta 2010

## Slide 19: Tests chip at DESY

## Slide 20: Percival in a nutshell
Ongoing development project between DESY, RAL / STFC, and Elettra; Diamond in the process of joining
Aim: develop X-ray imager for FLASH & FERMI, soft X-ray beams at PETRA III, ELETTRA, and DIAMOND, and for the use of CFEL scientists at other facilities
250eV-1keV, 16Mpixel, 120Hz frame rate, 1-105 photons/pixel
Sensor developed at RAL, Readout developed at DESY (with Elettra), Diamond provides the DAQ
  Only digital information coming off the chip
  Readout development build upon / re-use XFEL and AGIPD developments already done on-site
Project underway, first test circuits produced first images
Project timeline
  First small backthinned test sensors in hand ~summer 2013
  First full backthinned system ~ end 2014

## Slide 21
Smaller HPAD pixels with
  Reduced dynamic range (no gain switching);
  Reduced number of frames?
New Technologies including:
  3D CMOS: second layer (more functionality)
What could be next?

## Slide 22
3D-CMOS
1) bump-bond to the detector (TSV)
2) amplification & double sampling
3) store the analog signal in a memory cell in 1st/2nd layer (544 memory depth)
4) signal readout
5x5 mm2 double-tier dice
MPW, via CMP
submitted 2011
to be delivered early 2013
Standard Cells

## Slide 23
Smaller pixels with
  Reduced dynamic range (no gain switching);
  Reduced number of frames?
New Technologies including:
  3D CMOS: second layer (more functionality)
  65 nm CMOS technology (more functionality)
  3D CMOS + 65 nm CMOS
What could be next?
Notes: HGF Portfolio activity

## Slide 24: HGF-Detector Program; Pillar-1 : The “Helmholtz-Cube”
What we have today
Replace standard sensor with: 3D and edgeless sensors, as well as High-Z
Replace standard bump-bonds with new interconnect techniques
Replace standard ASIC and wire bonds with thinned ASICs and TSV as well as ball-grid arrays
Replace standard ASIC with 3D-ASICs
Develop new high speed IO’s
Employ innovative materials

## Slide 25
new sensors
Thinned and 3D ASICs
Innovative materials
Advanced interconnect
High-speed I/O
HGF-Detector Program; Pillar-1 : The “Helmholtz-Cube”
What we want tomorrow

## Slide 26
With DEDICATED detector developments it is possible to solve the X-ray detection challenge.
It is a long and expensive process; needs persistence and good goals.
Collaborative approach is most effective; provided each partner is a real added value
Europe is still ahead and should make sure it stays.
Summary