## Slide 1: CERN campus: mapping of the building versus energy consumption and an example of design and construction of a green building.
Luigi Scibile CERN, General Services and Infrastructure Department
Head of the Site Engineering Group
Main contributors: F. Audinet, H. Burckhart, M-L. Gabassi, M. Gansser,
F. Magnin, C. Martel, M. Poehler

## Slide 3: Content
The CERN campus: situation and outlook
Mapping heating space energy consumption
Models, simulations and estimates
Example of application of energy concepts

## Slide 4: The CERN site
590 hectares of available land
2 main sites
  Meyrin (CH)
  Prévessin (FR)
15 satellite sites
650 buildings - 10m2 up to 20.000m2
60% of the buildings are 30+ years old
2 Heating plants (3 x 15 MW + 3 x 5 MW)
22km + 7km of district heating network
80 km of tunnels
250 km of roads
10.000 professionals on site daily
100.000 tourist visitors annually

## Slide 5: The CERN campus: Meyrin and Prévessin sites
Work facilities
  (offices, labs, workshops, etc.)
Social facilities
  (restaurants, hostels, banking services, post office, clubs and a kinder garden)
Visitor facilities
Prévessin site
Meyrin site

## Slide 6: Two sites with a history
1960-75
1970-80
1980-10
1950-60
1975-85
1985-10
MEYRIN
PREVESSIN

## Slide 7: Two sites with a future
MEYRIN
PREVESSIN

## Slide 8: The CERN campus: situation and outlook
Buildings:
  Renovation of building envelop, lighting systems, HVAC systems (safety and energy efficiency).
  New buildings energy concept (RT2012, SIA380).
Energy efficiency:
  Renovation of the heating process regulation at all levels (district heating plants and local control, -gas -NOx).
  Implementation of local energy measurements (today only available at high aggregation level).

## Slide 9: The CERN campus: situation and outlook
Example: local energy measurement.

## Slide 10: Mapping heat energy consumption/usage
Given the limitation of the energy measurements
Meyrin Site

## Slide 11: Mapping heat energy consumption/usage
Model where heat energy is used (requirements)
Model where/how energy is dissipated
65.9
GWh
46.2
GWh
Overall
Simulation results

## Slide 12: Mapping heat energy consumption/usage
Consolidation benefits
Planning tool
Identify synergies for waste heat recovery

## Slide 13: Example of application of energy concepts
Building 774
RT2012 standard
Renewable energy and energy recovery
Designed to interact with other sources

## Slide 14: Example of application of energy concepts
Offices
Meeting rooms
Laboratories
Conference rooms
Cafeteria
SRB panels
Absorption
unit
Excellent insulation
Triple-glazed windows
Fixed shading structure
Building design
Systems design

## Slide 15: Conclusions and outlook
Energy is a key aspect in the renovation of old infrastructures and in new building designs.
The model of the heat consumption/usage of the sites provides us an invaluable tool to target interventions and plan for future developments and synergies (energy recuperation).
New infrastructures are designed with built-in capability to have synergies with eventual energy recuperation.

## Slide 16: Questions and answers
Thank you for your attention
QUESTIONS?
For additional material and contacts:
http://gs-dep.web.cern.ch/en/content/gs-se