## Slide 1
High-power and high-gradient developments for the CLIC project

## Slide 2
500 GeV c.m.
3TeV c.m.
1.5 TeV c.m.
What is CLIC?
A highly developed concept, design and hardware study for a collider capable of delivering e+e- physics in the energy decade of 0.3 to 3 TeV – the lepton physics compliment to the LHC.
CLIC multi-lateral collaboration - 48 Institutes from 25 countries

## Slide 3
Primary accelerator features
Reach the high end of the energy range through high, 100 MV/m, accelerating gradient by using short-pulse, around 200 ns, normal-conducting rf.
Deal with the resulting high peak power requirement by going to high rf frequency, X-band, produced by the so-called drive beam scheme. At the lowest energies it is also possible to use klystron/rf pulse compressor units. Accelerating structure input powers are around 60 MW.
Deal with the luminosity and resulting high average power requirement by producing, transporting and colliding low-emittance, multi-bunch beams. This requires high-performance damping rings, micron-level main-linac precision and alignment, accelerating structure higher-order-mode damping, nanometer-level main-linac quadrupole stabilization and a sub-nm stabilized final focus etc.

## Slide 4
CLIC accelerating structure development
In order to reach 3 TeV with a facility which, for example, could be built in the area around CERN, so < 40 km, an accelerating gradient of around 100 MV/m is required.
In order to maintain low beam emittance along the main linac, accelerating structures must be built with a few micron tolerances and aligned along 10s of meters with roughly 10 micron tolerances.
In addition, in order to provide sufficient luminosity in an energy efficient way, trains of bunches are accelerated. This means that accelerating structures must be equipped with higher order mode in order to suppress .

## Slide 5: CLIC test structures; fabrication and test T18 TD18T24TD24TD24R05
1. T18_Disk_#2
2. TD18_Disk_#2
3. T24_Disk_#3
4. TD24_Disk_#4
5. TD24R05 under test now
undamped
damped

## Slide 6: 1st generation of CLIC X-band test structure prototypes T18/TD18 Parameters at tp=100 ns, <Ea>=100 MV/m
In TD18, all quantities are close to T18 at the same average gradient, except for the pulsed surface heating temperature rise which is factor 5 higher in the last cell.
T18_vg2.6_disk:
TD18_vg2.4_disk:
Very strong tapering inspired by the idea of having constant P/C along the structure
2007
A. Grudiev, IWLC2010

## Slide 7: 2nd generation of CLIC X-band test structure prototypes T24/TD24 Parameters at tp=100 ns, <Ea>=100 MV/m
In TD24, all quantities are lower than in TD18 at the same average gradient. In particular pulsed surface heating temperature rise reduced by factor 2.
T24_vg1.8_disk:
TD24_vg1.8_disk:
Weaker tapering (quasi const gradient) together with smaller aperture (11% instead of 12.8%) reduce surface fields significantly compared to T18/TD18.
2007

## Slide 8: Reduce Hp/Ea and DT by reducing corner radius in the cell
TD24
TD24R05
Alexej Grudiev

## Slide 9
Accelerating gradients achieved in tests.
Status: 4-9-2012
HOM damped

## Slide 10
How we got there: High-power design laws
The functions which, along with surface electric and magnetic field (pulsed surface heating), give the high-gradient performance of the structures are:
global power flow
local complex power flow
New local field quantity describing the high gradient limit of accelerating structures.
A. Grudiev, S. Calatroni, W. Wuensch (CERN). 2009. 9 pp.
Published in Phys.Rev.ST Accel.Beams 12 (2009) 102001
Hs/Ea
Es/Ea
Sc/Ea2

## Slide 11: Simplified Parameter Diagram
Drive Beam Generation Complex
Pklystron, Nklystron, LDBA, …
Main Beam Generation Complex
Pklystron, …
Two-Beam Acceleration Complex
Lmodule, Δstructure, …
Idrive
Edrive
τRF
Nsector
Ncombine
fr
N
nb
ncycle
E0
fr
Parameter Routine
Luminosity, …
Ecms, G, Lstructure
Variable | Meaning | Current value
Idrive | Drive beam current | 101A
Edrive | Drive beam energy | 2.37GeV
τRF | Main linac RF pulse length | 244ns
Nsector | Number of drive beam sectors per linac | 4
Ncombine | Combination number | 24
fr | Repetition rate | 50Hz
N | Main beam bunch charge in linac | 3.72e9
nb | MB bunches per pulse | 312
ncycle | Spacing between MB bunches | 6 cycles
E0 | MB energy at linac entrance | 9GeV
Ecms | Centre-of-mass energy | 500GeV
G | Main linac gradient | 100MV/m

## Slide 12: Optimization Ingredients
Define a figure of merit (FoM) to evaluate one given CLIC design/parameter set
  e.g. FoM=-cost
Define a few free parameters to fully describe the design/parameter set
  The other parameters are unambiguously defined by the free parameters
  Currently: gradient G and a few structure parameters (fRF, Δφ, a, Δa, LS, …)
Use optimisation algorithm to find maximum
FoM(free parameters)
  Currently: a simple full search
Allow some human intervention

## Slide 13
TD18#3 at SLAC
TD18#2 at KEK
Stacking disks
Temperature treatment for high-gradient developed by NLC/JLC
How we got there: heat treatment and material structure
Attempting to understand why it works.

## Slide 14
Micron precision turning and milling
Accelerating structure tolerances drive transverse wakefields and off-axis rf induced kicks which in turn leads to emittance growth – micron tolerances required.
Multi-bunch trains require higher-order-mode wakefield suppression – cells require milled features.
High-speed diamond machining also seems to be beneficial for high-gradient performance through minimizing induced surface stresses.
Development done “in industry”

## Slide 15: New choke design CDS-C
Features include “two-section”, “impedance matching”, “detuning”
1.6mm
1.2mm
2.0mm

## Slide 16: Damping result
 | W⊥ (s=0.15m) V/m/mm/pC
WDS | 5
CDS-A | ~30
CDS-C | 4~5
Freq(GHz) | Q | (R/Q)⊥
15.7 | 5.4 | 80.3
18.6 | 6.9 | 63.2
23.7 | 3.8 | 14.8
28.4 | 12.4 | 10.9
38.2 | 11.6 | 9.9
s | CDS | WDS
Fc | 1 | 1
Frms | 4 | 5
Fworst | 25 | 20

## Slide 17: Full structure optimization CDS-C Parameter
 | CDS-C | CLIC-G
a(mm) | 3.15, 2.35 | 3.15, 2.35
Q(Cu) | 4895, 5385 | 5538, 5738
Zs(MΩ/m) | 59, 83 | 81, 103
vg(%c) | 1.38, 0.73 | 1.65, 0.83
Esurf(MV/m) | 245 | 235
Sc (MW/mm^2) | 5.66 | 5.39
Delta T(K) | 23.0 | 47.5
Pin (MW) | 67.5 | 60.5
Filling time(ns) | 75.4 | 64.8
RF-beam eff. | 23.8% | 27.5%

## Slide 18: Flatness measurement before and after Etching
65nm
400nm
Note: different scale

## Slide 19: Bonding
Already cut into halves
One piece at CERN

## Slide 20
Evolution of machining capability
Up to the 1980’s
1980’s - 1990’s
2000’s - 2010’s
Larger machines
Multiple axis ( X/Y/Z and C)
Future ?
Intelligent machines ?
  Robotisation ?
Pallet machining?
  Robotisation ?
First machines at research institutes and universities
Start of industrialization
Optical recording
contact lenses
Single point diamond turning
Up to the 1990’s
1990’s - 2000’s
2010’s
Future ?
Ultra precision diamond milling (lagging more than a decade behind on turning)
Limited to fly cutting
mirror optics
Laser scanner mirrors
First proto type machines
Micro fluidics
Accelerator parts
Milling as add-on on lathes
Lens arrays
Intra ocular lenses

## Slide 21
High-gradient testing using klystrons
In order to test enough accelerating structures we have an on-going campaign to establish a number of klystron-based test stands.
We have received an XL-5 klystron from SLAC from a batch order from SLAC and have an order out with CPI for two more.
A side benefit is that these test stands, with accelerating structures, turn out to be very close to the rf units one could use for:
an entry energy CLIC
a normal conducting FEL linac
a Compton-source linac
a medical linac
We wish to advance mutually beneficial work with these types of projects, and we hope today helps.

## Slide 22
Klystron-based test stands for CLIC
NEXTEF at KEK
XBox1 at CERN
ASTA at SLAC?
XBox2 at CERN

## Slide 23: TD24R05#2 Processing history

## Slide 24: TD24R05 Eacc versus #ACC-BD

## Slide 25: Difference in processing speed among 5 disk-stack-type CLIC-prototype structures
T24
T18
TD18
TD24
51ns
91ns
132ns
TD24R05
Number if ACC-BD’s until reaching the same level in (Tp, Eacc)
Speed
1. T24
 2. TD24R05
 3. T18
 4. TD24
 5. TD18
Still to be revised for better comparison (130126)

## Slide 26
The final X-box1 RF layout
Due to the delays caused by the klystron repairs, the conditioning software based on the CERN control system could not be finished  Urgent need for control, interlock and feedback systems!
 Decision to use a National Instruments PXI based system for all Xbox-1 controls and DAQ
8ch 250MSps/s 14 bit ADCs for RF (log detectors) and DC sampling, one FPGA for 4chs used for interlocking on reflected power and DC spikes
I/Os for temp. gauges and interlock signals
Stepper motor control and encoder read back
Ion pump current readout for all pumps

## Slide 27
Gallery
Bunker
Layout of the CERN x-band test stand
(X-box 1)
Clockwise from top-left:
Modulator
Pulse compressor
DUT + connections
Accelerating structure

## Slide 28
Full conditioning history TD24R05

## Slide 29
100ns-150ns history TD24R05

## Slide 30
X-Box#2 – under prepration.
Bld. 150
D. Gudkov, CERN

## Slide 31: Site preparation
21.02.2013
08.05.2013
Pre-approved by safety for radiation and seismic risks (more to come)
Shielding reinforced, area cleared,
Utilities to be deployed during summer
Modulator in place. Walls to be closed now.
Continuous work

## Slide 32
Two paths for test stands and linac power units
50-75 MW tubes
NEXTEF, Xboxes 1 and 2
Potentially 100 Hz range linacs in the 8-9 GeV range.
7-10 MW tubes combined
Xbox3
Potentially kHz range linacs in the 1-2 GeV range.
Industrial supply is crucial!

## Slide 33
Drive beam ON
Drive beam OFF
CLIC Nominal, loaded
CLIC Nominal, unloaded
Power production using PETS and two-beam acceleration

## Slide 36
Introduction
Unloaded
Loaded (CLIC)
Testing of accelerating structure with nominal beam loading was a missing block in our testing program. Such a test will be done using CTF3 (1.2 A) drive beam and RF power delivered from X-box1 (90 MW) via modified 30 GHz low loss transfer line (60MW).
The main target of this experiment is to compare loaded and unloaded accelerating structure breakdown trip rate.
Increasing current
Gradient along the structure
CLIC nominal
Unloaded

## Slide 37
Accelerating gradients achieved in tests.
Status: 4-9-2012
loaded

## Slide 38
RF
Beam
Complete Dog-leg test RF network layout (calculated RF transfer efficiency ~0.75)
Mode converter type#2
 50 mm circular waveguide
The number of 12 GHz new RF components were fabricated by CERN and CEA to re-adjust ‘old’ 30 GHz low losses transfer line to the new frequency.

## Slide 39
Another option for low energies, e.g. 350 GeV:
X-band klystron driven

## Slide 40
Klystron XL4 series
X-band klystrons (industrialized)
Efficiency
32.5%
18 tubes built to date (not counting rebuilds)
design
performance
CLIC’k klystron:
59 MW
418 kV, 324 A (µK=1.2)
Efficiency 0.436
Klystron XL5 series
CLIC’k klystron:
59 MW
404 kV, 308 A (µK=1.2)
Efficiency 0.474
KMD and X-Band Overview, January 5, 2011 Erik Jongewaard
CLIC’k target
5 tubes have been fabricated at SLAC (1.5 are in operation). The first tube is ordered from industry (CPI)

## Slide 41
PPM, KEK
1994
…A superconducting focusing solenoid system for an X band klystron has been developed. The system consists of a conduction cooled superconducting solenoid, a GM refrigerator and high Tc material current leads. The system cools down to the operation temperature of about 4 K by 4 days just by turning on the refrigerator….
PPM focusing vs. Superconducting Solenoids
In the past 2 decades, the SC technology has progressed a lot. It is worth revising the use of SC (cryogen-free) solenoids for the klystrons again. If cost effective, such an approach will bring benefits for the technology as a whole.

## Slide 42
Scaled (244 ns) 12 GHz DM SLED II performance
CLIC_G
_502
_1
_2
XL5 klystron measured
Klystron peak power for the fixed layout: 2 x Kl(PPM)+PC -> 6 x structures
RF transport efficiency 0.9 is included
Used input: Klystron efficiency 0.55 (measured). Modulator efficiency 0.7 (expected)
Case | CLIC_G | CLIC_502 | #1 | #2
Gradient, MV/m | 100 | 80 | 67 | 57
Length, m | 0.23 | 0.23 | 0.48 | 0.48
P peak, MW | 61.3 | 74.2 | 84 | 76
Efficiency, % | 28.5 | 39.6 | 41.9 | 49.5
F. Merit [a.u.] | 3.81 | 3.3 | 2.79 | 3.41
50 Hz
Designing the linac

## Slide 43
~17.7 m, 16.3 cm
2-pack solid state modulator
59 MW
1.95 s
PPM klystrons
118 MW
1.95 s
492 MW
244 ns
2 m, 1.83 active
x 8 accelerating structures,
100 MV/m loaded gradient
CLIC’k RF unit layout
TE01 900 bend
TE01 transfer line (? m)
Inline RF distribution network
Common vacuum network
460 kV, 2 s flat top
x 4.64
The alternative PC schemes certainly must be considered (especially for the low energy machine), but for our evaluation, we will keep DM SLED II as a base line option, as its performance was confirmed through the high RF power testing.
Compared to NLC, the energy gain per unit in CLIC’k case is 26% lower (need more klystrons per meter), but the unit active length is ~ 2 time shorter.

## Slide 44
Mode launcher
Alternative#1. One channel design.
Such a pulse compressor is under construction at KEK
Potentially, the factor >2 cost reduction compared to DM SLED II can be anticipated – one channel and much less sophisticated RF network. Indirect savings will come from halving the number of pipes needed to be installed in a tunnel.
Compared to DM SLED II, OC SLED is 8% less efficient.
High RF power capability is the biggest issue.
Another design of the mode launcher may solve this problem
E surf = 180 MV/m at 490 MW
E surf = 90 MV/m at 490 MW
490 MW
30 MW/channel

## Slide 45
Power supply for
2 x modulator
2.5 m
1.5 m
4.0 m
DFM2
Modulator & Space reservation issues
Because of the high accelerating gradient and thus the need for high RF power density (245 MW/m), there is a very severe demand on space reservation (~ 1 klystron/m) in the service tunnel to insure a high enough technical gradient. As a first approximation, the DFM2 modulator can be fitted. More studies (which should include space reservation for all the other systems) will be needed to prove such a concept.

## Slide 46
Not the main line but a growing theme – applying CLIC technology to other projects.
I will now show a few slides on a proton cancer therapy application.
But we try to work more and more with XFELs, Compton sources etc.

## Slide 47
Design project B: cyclinac for single-room proton facility

## Slide 48: TULIP 24 – baseline design
24 MeV
230 MeV

## Slide 49: Backward wave high-gradient accelerating structure for proton acceleration based on CLIC technology

## Slide 50: Optimization plots - fields

## Slide 51
Physical processes of breakdown

## Slide 52: Relevant data points of BDR vs Eacc
Steep rise as Eacc, 10 times per 10 MV/m, less steep than T18
TD18
T. Higo, KEK

## Slide 53: TD18_#2 BDR versus width at 100MV/m around 2800hr and at 90MV/m around 3500hr
Similar dependence at 90 and 100 if take usual single pulse?
TD18
T. Higo, KEK

## Slide 54
Diffusion bonding of structure under H2 at 1 bar
    Also done at TED with degreasing and etching at CERN before bonding
    Applied weight: 33.7 kg equivalent to ~ 0.08 – 0.12 MPa;
    Same thermal cycle as couplers but with flat top at 1010°C
    No deformations observed on the external diameter after bonding
Disks after etching
Coupler
Assembly of disks in the furnace
Geometrical measurements on external diameter after bonding
Alignment = 9µm for ACS#1 and 12.6 µm for ACS#2
Angle = 90.0514° for ACS#1 and 90.0087° for ACS#2
Structure n°1
Structure n°2

## Slide 55
TD24R05 conditioning in Xbox-1

## Slide 56: T24#3 BDR evolution at 252ns normalized 100MV/m
Assuming the same exponential slope as that at 400hr
We understand the BDR has been kept decreasing.
From T. Higo

## Slide 57: What are the field emitters? Why do we look for dislocations?
The dislocation motion is strongly bound to the atomic structure of metals. In FCC (face-centered cubic) the dislocation are the most mobile and HCP (hexagonal close-packed) are the hardest for dislocation mobility.
A. Descoeudres, F. Djurabekova, and K. Nordlund, DC Breakdown experiments with
cobalt electrodes, CLIC-Note XXX, 1 (2010).

## Slide 58: Dislocation-based model for electric field dependence
Now to test the relevance of this, we fit the experimental data
The result is:
Power law fit
Stress model fit
[W. Wuensch, public presentation at the CTF3, available online at http://indico.cern.ch/conferenceDisplay.py?confId=8831.] with the model.]

## Slide 59: Electron emission
Copper surface
typical picture 
geometric perturbations (b)
Fowler Nordheim Law (RF fields):
High field enhancements (b) can field emission.
Low work function (f0) in small areas can cause field emission.
oxides
alternate picture 
material perturbations (f0)
inclusions
peaks
grain
boundaries
cracks
(suggested by Wuensch and colleagues)
(b, f0, Ae, E0)
IFN

## Slide 60: Schottky Enabled Photo-electron Emission Measurements
Experimental parameters
  work function of copper = f0 = 4.65 eV
  energy of l=400nm photon = hn= 3.1 eV
  Laser pulse length
    Long = 3 ps
    Short = 0.1 ps
  Laser energy ~1 mJ (measured before laser input window)
  Field (55 – 70 MV/m)
ICT
g
e-
First results
from Tsinghua
Data 2010-10-04
Should not get
photoemission

## Slide 61: Long Laser Pulse (~ 3ps) E=55 MV/m@ injection phase=80  55sin(80)=54
Q(pC)
laser energy (mJ)
photocathode input window
First results
from Tsinghua
Data 2010-10-04
Q I
single photon emission

## Slide 63: Modelling DC discharges
First we have to understand breakdowns in DC, before we can generalise to RF
Simple and cost-efficient testing of breakdown behaviour with two DC setups at CERN
  We adjusted also out theoretical model to the DC experimental conditions
However, results are completely general!
e.g. Cu
r=1 mm
d=20 μm
~ 4-6 kV

## Slide 64
Evolution of b & Eb during conditioning experiments
Measurements of b after each sparks (Cu electrodes)
b ↔ next Eb
correlation
b · Eb = cst
b ↔ previous Eb
no correlation
Antoine Descoeudres

## Slide 65
spark
Evolution of b during BDR measurements (Cu)
breakdown as soon as b > 48 ( ↔ b · 225 MV/m > 10.8 GV/m)
consecutive breakdowns as long as b > bthreshold
length and occurence of breakdown clusters ↔ evolution of b
b·E = 10.8 GV/m
Antoine Descoeudres

## Slide 66: Simulated system
Fully coupled electric field – mechanical interaction
  Electric field deforms sample
  Deformed sample causes local field enhancement
Dc El. field ramped from 0 … 10 000 MV/m
Comsol Multiphysics 4.3
  Nonlinear Structural Materials Module
  AC/DC module
3D-simulations, 2D-snapshots
Simulated materials:
  Soft copper
  Single crystal copper
  Stainless steel

## Slide 67: Deformation at realistic electric field strength
Void formation starts at fields > 400 MV/m
Material is plastic only in the vicinity of the defect
Thin slit may be formed by combination of voids or by a layer of fragile impurities
Field enhancement factor ~2.4
Thin material layer over the void acts like a lever, decreasing the pressure needed for protrusion formation

## Slide 70: DC Spark System Turn on Time
Sample size = 50
The spread in voltage fall times (and current rise times) is extremely small compared to the RF case.
The measured current rise time always shorter than voltage fall time due to initial charging current overlap.

## Slide 71: Summary of turn on times
Test | Frequency | Measurement | Result
Simulation |  |  | 0.25ns
New DC System | DC | Voltage Fall Time | 12-13ns
Swiss FEL (C-Band) | 5.7GHz | Transmitted Power Fall Time | 110 - 140ns
KEK T24 (X-Band) | 12GHz | Transmitted Power Fall Time | 20-40ns
CTF/TBTS TD24 (X-Band) | 12GHz | Transmitted Power Fall Time | 20-40ns
CTF SICA (S-Band) | 3GHz | Transmitted Power | 60-140ns
The turn on time does not seem to be related to the bandwidth of the structures but to the frequency or possibly the intrinsic size.

## Slide 72: Pulsed surface heating limit
Cell # (cell #1 is a input matching cell):
4
5
6
7
8
9
10
11
12
13
15
14
17
?16?
Images courtesy of M. Aicheler: http://indico.cern.ch/getFile.py/access?contribId=0&resId=1&materialId=slides&confId=106251
18
Last
regular
cell: 19
It seems that cell #10 (regular cell #9 ~ middle cell) exhibits the level of damage which could be considered as a limit.
A. Grudiev
TD24

## Slide 73
Features in high current region of TD18
Damping waveguide
Inner cell
Current density around 2x108A/cm2 during test

## Slide 74
Electromigration
Our current(!) explaination is that these features are due to electromigration. Electromigration is the transport of atoms in a conductor due to momentum transfer from the current.
This can cause the formation of voids and breakup of the material.
The effect has been a problem in semiconductor interconnects – at current densities of

## Slide 76
So does this evolve…
…into this?
An effect of surface tension plus electromigration?
If the such localized flow features exist, the surface currents will preferentially flow though them.
We get a current enhancement, increasing pulsed surface heating and electromigration.
These combined effects could then have a positive feedback and produce an instability.

## Slide 77
Forming a community
HG2012 at KEK
https://indico.cern.ch/conferenceDisplay.py?ovw=True&confId=208932
http://indico.cern.ch/conferenceDisplay.py?confId=231116
Now in our seventh year. Focus steadily expanding to include broad high-gradient normal-conducting rf community.

## Slide 78
MeVArc – Multidisciplinary and multi-application workshop dedicated to breakdown physics
This year 5-7 November – hosted by CERN. More information soon.
http://www.regonline.com/builder/site/default.aspx?EventID=1065351

## Slide 79
Your project…
…with CLIC technology!
Last slide