## Slide 1: Production of radioactive molecular beams
Christoph Seiffert
CERN-ISOLDE \TU Darmstadt
Supported by the Wolfgang Gentner programme

## Slide 2: CERN/ISOLDE
https://mediastream.cern.ch/MediaArchive/Photo/Public/2008/0812015/0812015/0812015-A4-at-144-dpi.jpg

## Slide 3: The Nuclear Chart
P
N
Isoltrap: 233Fr, 229Rn - new isotopes (K. Blaum et al.)
Windmill: Asymmetric b-delayed fission of 180Tl
(A. N. Andreyev et al.)
First b-NMR experiment on soft matter
(M. Stachura et al.)
Witch: Fundamental Symmetries
b-decay of 35Ar
(M. Breitenfeld et al.)
Collaps: Size and Shape of Exotic Nuclei
Halo nucleus 11Be
W. Nörtershäuser et al.
Biophysics
Precision measurement of 82Zn mass
(S. Kreim et al.)

## Slide 4: The Nuclear Chart
P
N
Strong physics interest
  8-Boron:
    Neutrino source, β-beams
    Halo nuclei
    Boron as semi conductor dopant
  9-Carbon:
    Investigations on 10-N
    Decay structure

## Slide 5: The Nuclear Chart
P
N
Short lived isotopes of some light nuclei not available
Reasons:
  High boiling points
  High adsorption enthalpy
  Chemical reactivity
9-C seen once for 24h. Why?
Isotope | Half life | Boiling point [C]
8-B | 770ms | 3927
9-C, 17-C | 123ms/175ms | 3642

## Slide 6: The Nuclear Chart
P
N
Short lived isotopes of some light nuclei not available
Reasons:
  High boiling points
  High adsorption enthalpy
  Chemical reactivity
Isotope | Half life | Boiling point [C]
8-B | 770ms | 3927
9-C, 17-C | 123ms/175ms | 3642
Extract isotopes as molecular ions: CO+, BF2+

## Slide 7: Production of Radioisotopes
1.4 GeV proton
fragmentation
fission
spallation
238U
142Cs
11Li
201Fr
X
Y

## Slide 8: Selection Process
HRS
GPS
beam lines
FE 6
FE 7

## Slide 9: Steps In Isotope Extraction
Ionization
Isotope production
Effusion: interaction with target and line
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)
Diffusion
Molecule formation

## Slide 10: Isotope Production
Ionization
Isotope production
Molecule formation
Effusion: interaction with target and line
Protons
1.4 GeV proton beam from Booster
Depending on target material isotope production with cross section σ
Diffusion

## Slide 11: Isotope Production
Computed with ABRABLA
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)
I0=np*σ*δA

## Slide 12: Steps In Isotope Extraction
Ionization
Isotope production
Effusion: interaction with target and line
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)
Diffusion
Molecule formation

## Slide 13: Diffusion
Arrhenius equation
  D0: maximum diffusion coefficient [cm2/s]
        Ea: activation energy
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)

## Slide 14: Studies on Boron
Diffusion studies with boron neutron depth profiling method (bndp) [10-B(n,α)7-Li ]
  Step 1: Implantation of 10-B as 10-BF2 into target materials
12.5 keV 10-B in Carbon
B
F
+
F
B
F
+
F

## Slide 15: Studies on Boron
Diffusion studies with boron neutron depth profiling method (bndp) [10-B(n,α)7-Li ]
  Step 1: Implantation of 10-B as 10-BF2 into target materials
  Step 2: Measurement of (initial) distribution
    σ[10-B(n,α)7-Li ]=3840 barn
    Pu-Be source: 1.1*10^8 neutrons/second @4Pi
    Same effect used in cancer therapy
α detector

## Slide 16: Studies on Boron
Diffusion studies with boron neutron depth profiling method (bndp) [10-B(n,α)7-Li ]
  Step 1: Implantation of 10-B as 10-BF2 into target materials
  Step 2: Measurement of (initial) distribution
    σ[10-B(n,α)7-Li ]=3840 barn
    Pu-Be source: 1.1*10^8 neutrons/second @4Pi
  Step3: Heating of Sample

## Slide 17: Studies on Boron
Diffusion studies with boron neutron depth profiling method (bndp) [10-B(n,α)7-Li ]
  Step 1: Implantation of 10-B as 10-BF2 into target materials
  Step 2: Measurement of (initial) distribution
    σ[10-B(n,α)7-Li ]=3840 barn
    Pu-Be source: 1.1*10^8 neutrons/second @4Pi
  Step3: Heating of Sample
  Step4: Repeat step 2 and step 3

## Slide 18: Studies on Boron
Study on chemical behaviour and diffusion properties
Boron can be extracted as a fluoride
Diffusion studies with boron neutron depth profiling method (bndp) [10-B(n,α)7-Li ]
  Step 1: Implantation of 10-B as 10-BF2 into target materials
  Step 2: Measurement of (initial) distribution
    σ[10-B(n,α)7-Li ]=3840 barn
    Pu-Be source: 1.1*10^8 neutrons/second @4Pi
  Step3: Heating of Sample
  Step4: Repeat step 2 and step 3
Goal: Choice of target material which allows fast diffusion and therefore efficient extraction

## Slide 19: Studies on Boron
α (1.418MeV)
Overnight measurement (Oct-2013)

## Slide 20: Chemical Interactions
Ionization
Isotope production
Molecule formation
Effusion: interaction with target and line
Diffusion

## Slide 21: Chemical interactions
Materials found in an ISOLDE target:
Tantalum
Molybdenum
Copper
Rhenium
I=I0 *exp(-λ*(tdiff+teff)) *ε(chemical loss)*ε(ion source) *ε(formation)

## Slide 22: Chemical interactions
Chemical equilibrium of Ta and CO
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)
Chemical equilibrium of Al2O3 and CO

## Slide 23: Chemical interactions
Chemical equilibrium of Ta and CO
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)
Chemical equilibrium of Al2O3 and CO
Substitute materials which react with Carbon and Boron

## Slide 24: Adsorption on surfaces
  Sticking time:
http://www.buetzer.info/fileadmin/pb/HTML-Files/WebHelp/Die_Adsorption_von_Gasen_und_gel_sten_Stoffen.htm
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)

## Slide 25: Effusion
(1)Production of exotic, short lived carbon isotopes in ISOL-type facilities, Hana Franberg, Uni Bern 2008
(2)Chemisorption on Rhenium: N 2 and CO JOHN T. YATES, JR., AND THEODORE E. MADEY National Bureau oj Standards, Washington, D. C. 20234
(3)TPD measurements, Roman Bulanek, University of Pardubice, CZ
(4) (Im)possible Isol beams, U.Koester et al, Eur.Phys.J.Special Topics 150, 285-291 (2007)
Adsorption enthalpies for CO and CO2:
Adsorbent | CO [kJ/mole] | CO2 [kJ/mole]
MgO | -131 (1) | -164(1)
HfO | -66(1) | -133(1)
SiO2 |  | -22(1)
Al2O3 | -35 (3) | -65(1)/ -35 (3)
Y2O3 | -16 (3) | -80 (3)
Cu | -96 | 
Mo | -126.4 | 
Re | -145(2)/ NA | NA
Ta | -962(4)/NA | NA
Adsorbent |  | 
MgO | -131 (1) | -164(1)
HfO | -66(1) | -133(1)
SiO2 |  | -22(1)
Al2O3 | -35 (3) | -65(1)/ -35 (3)
Y2O3 | -16 (3) | -80 (3)
Cu | -96 | 
Mo | -126.4 | 
Re | -145(2)/ NA | NA
Ta | -962(4)/NA | NA
For > - 40 kJ/mole Chemisorption: strong interaction, irreversible, monolayer
For < - 40kJ/mole Physisorption : weak interaction (VDW Force), reversible, multilayer
  Sticking time:

## Slide 26: Chemical interactions
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)
  teff= Σ i= Σ ni*
Location | ni
Target walls | ~10^2
Grain walls | >10^6
Location | max [kJ/mole]
Target walls | ~270
Grain walls | 150
Location | 
Target walls | ~270
Grain walls | 150
tmax=t1/2 =123ms
9C

## Slide 27: Chemical interactions
http://www.buetzer.info/fileadmin/pb/HTML-Files/WebHelp/Die_Adsorption_von_Gasen_und_gel_sten_Stoffen.htm
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)
  teff= Σ i= Σ ni*
Location | ni
Target walls | ~10^2
Grain walls | >10^6
Location | max [kJ/mole]
Target walls | ~270
Grain walls | 150
Location | 
Target walls | ~270
Grain walls | 150
tmax=t1/2 =123ms
9C
Structural material | Target material
Tantalum | Al2O3
Molybdenum | HfO2
Rhenium | Y2O3
Copper | MgO
SiO2 | CaO

## Slide 28: Release Studies on CO+
Release studies at Off-line mass separator
  Injection of bursts of gas of interest (13-CO2, 13-CO, noble gases)
  Release gives information about release efficiency and time structure
  Investigation of different ion sources and materials

## Slide 29: Release Studies on CO+
Release studies at Off-line mass separator
  Injection of bursts of gas of interest (13-CO2, 13-CO, noble gases)
  Release gives information about release efficiency and time structure
  Investigation of different ion sources and materials

## Slide 30: Steps In Beam Production
Ionization
Isotope production
Effusion: interaction with target and line
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)
Diffusion
Molecule formation

## Slide 31: HELICON Ion Source
An ion source for molecular beams
  No hot tantalum surface
  Helicon developed by Pekka Suominen & Matthias Kronberger
[1]Production of molecular sideband radioisotope beams at CERN-ISOLDE using a Helicon-type plasma ion source , M.Kronberger et al, NIM B
Gas | HELICON | VADIS
CO | 2.5 % | -
CO2 | 0.3% | 0.3%
I=I0 *exp(-λ*(tdiff+teff))*ε(ion source) *ε(formation)* ε(chemical loss)
HELICON ion source
VADIS ion source
Ionization efficiencies

## Slide 32
Thank you!
Work supported by the Wolfgang-Gentner-Programme of the Bundesministerium für Bildung und Forschung (BMBF)