## Slide 1
HOM Couplers for CERN SPL Cavities
Comparison of different design approaches
K. Papke, F. Gerigk, U. van Rienen
Work supported by the Wolfgang-Gentner-Programme of the Bundesministerium für Bildung und Forschung (BMBF)

## Slide 2: Outline
Overview
RF Characteristics
Mechanical Issues
Heat Loss Investigation
Summary
Outlook

## Slide 3: Overview
PSB
SPS
Linac4
LP-SPL
PS
LHC /
HE-LHC
160 MeV
1.4 GeV
4 GeV
26 GeV
50 GeV
450 GeV
7 TeV
Linac2
50 MeV
Proton flux / Beam power
PS2
Present
Optional Future
1978
1975
1959
2008
LP-SPL: Low Power-Superconducting Proton Linac
PS2: High Energy PS (~ 5 to 50 GeV – 0.3 Hz)
HE-LHC: “High Energy” LHC (³ 14 TeV/ring)
PS2
SPL
LINAC4
SPS
PS
R. Garoby, SPL Seminar 2012

## Slide 4: Overview
RF Power Coupler
Bulk Niobium 5 Cells cavity
Helium Tank
CEA’s tuner
HOM Coupler
Bi-phase helium tube
Magnetic shielding
Inter-cavity support
Bellows
Double walled tube
O. Capatina, SPL Seminar 2012

## Slide 5: Overview
HOM-Coupler
Very high impedance for the notch frequency (704.4MHz)
Low impedance for “all” other modes
Extracted power
Resonant circuit
Antenna
Cavity
HOM-Coupler used to extract or dissipate unwanted, higher order modes in the cavity induced by the beam

## Slide 6: Overview
Bulk Niobium 5 Cells SPL cavity
O. Capatina, SPL Seminar 2012
Approaches for HOM coupler
probe
coupler
modified TESLA
design
hook
coupler
Design goal of HOM filter: block the transmission of the accelerating mode, while transmitting HOMs, which have significant (R/Q) values

## Slide 7: Overview
modified TESLA
design
Probe
coupler
Hook
coupler
Design approaches for HOM coupler
Number of factors such as RF transmission behaviour, power dissipation, multipacting sensitivity, field emission, heat loss, mechanical restrictions
Heat loss
Multipacting
Mechanical issues
RF characteristics

## Slide 8: RF Characteristics
E- and H-field coupling
Notch inductance which together with the red labeled capacitance creates the notch filter
Notch capacitor couples to the outer conductor
Mutual inductance of the resonant circuits
fixing of the whole inner conductor
may support liquid helium for cooling
Capacitive coupling for impedance matching
Every part of the coupler (also the non labeled) affects more or less its frequency dependent impedance characteristic
Coaxial port (50 Ohm)
8

## Slide 9: RF Characteristics - Requirements
M.Schuh, F. Gerigk. “Influence of higher order modes on the beam stability in the high power superconducting proton linac“, Phys. Rev. ST Accel. Beams, 2011
Schematic layout of the linac
(Conceptual design of the SPL II)
H- source
RFQ
chopper
DTL
CCDTL
PIMS
3 MeV
50 MeV
102 MeV
352.2 MHz
β=0.65
β=1.0
750 MeV
4/5 GeV
704.4 MHz
160 MeV
For SPL dipole HOMs are considered less problematic
In case of recirculators or synchrotrons dipole HOMs should be also considered
HOM spectra for the medium and high beta Cavities:
Medium beta cavity (beta = 0.65)
High beta cavity (beta = 1)

## Slide 10: RF Characteristics - Design Process
Initial estimation for design by transmission line models
Calculation of the lumped circuit elements for a desired frequency spectrum
Transformation in Transmission Lines gives the lengths of the coupler parts
Approximation
by lumped circuit model
Initial
design
10

## Slide 11: RF Characteristics - Design Process
For analysing and optimizing, simplified replacement circuit models were used and synthetized to a coupler model using transmission line theory (TML)
11
Notch filter
TML
Initial design
3D Simulation to optimize design
TM01, TE11
TEM
TM01 – TEM – Transmission

## Slide 12: Mechanical Issues
Reasonable tolerance for mechanical design: ± 0.2 mm
Notch filter for TESLA design easy to tune to ± 0.02 mm
Higher notch filter band width for Probe and Hook design to bypass the notch tuning
Cooling circuits at first foreseen (maybe not necessary)
Cooling circuits
Additional inductive post increases band width of Notch filter
Notch capacitance
(± 0.02 mm tol.)
Frequency tuning of the notch filter
40 MHz band width
(± 0.2 mm tol.)
modified TESLA design
Probe coupler (sub part)
Probe coupler

## Slide 13: Heat Loss Investigation
Coupled Simulation performed by HFSS (EM Field calculation) and ANSYS (steady state thermal analysis)
H-Field of fundamental Surface loss density derived from the H field of the accelerating mode (mode with the highest energy)
1 G. Ciovati, et al., “Residual Resistance Data From Cavity Production Projects at Jefferson Lab“, IEEE TRANSACTIONS ON APPLIED SUPERCONDUCTIVITY, 2011
2 T. Junginger, et al., “RF and Surface Properties of Superconducting Samples“, CERN-ATS-2011-037, 2011
Surface loss density
Design | Ploss [mW] | Tmax [K]
Probe | 10.1 | 3.93
TESLA | 12.8 | 2.84
Hook | 10.0 | 4.08
Flange | < 0.1 | 2.01
Tube | 11.5 | 2.08
Cavity cell | 101.5·103 | 2.89
Surface resistant increases exponential with temperature (tolerance of +/-100%) 1,2
Thermal conductivity dependent on the material purity (RRR)
worst case study/ Iterative scheme
Here: Rs = 200 n is assumed (worst case)

## Slide 14: Summary
14
TM01 – TEM (monopole coupling)
TE11 – TEM (dipole coupling)
High beta cavity (beta = 1)
HOM Bandwidth
High
Probe
TESLA
Hook
Low
Tuning
Difficult
TESLA
Hook, Probe
Easy
Notch Bandwidth
High
Hook, Probe
TESLA
Low
Thermal & mechanical robustness
TESLA
Hook, Probe
High
Low
Cavity preferences
TESLA, Probe
Hook
High beta
Medium beta
Probe
TESLA
Hook
Different designs of HOM coupler have been optimized for the requirements of the SPL cavities regarding RF behavior, mechanical issues and thermal losses
Qualitative results for the designs:

## Slide 15: Outlook
Fabrication of 2 prototypes (Probe, mod. TESLA)
Further filter designs under consideration
Heat loss investigation for pure copper models  much cheaper, maybe sufficient
Improvements of RF behavior for bulk coupler (if active cooling isn’t necessary)
Investigation of Multipacting barriers
Project extension onto LHC crab cavities
Probe
TESLA
B.P. Xiao: Proposal of filter design for LHC crab cavities
Thank you for your attention