## Slide 1: Investigation of Tuning Schemes of High-Q Ferrite-Loaded Cavities
Presentation of PhD Project
01.03.2013 – 29.02.2016
CERN Supervisor: Dr.-Ing. Christine Völlinger
TEMF Supervisor: Prof. Dr.-Ing. Harald Klingbeil
Johannes Eberhardt
CERN, Beams Department / TU Darmstadt, TEMF Institute

## Slide 2: Tuning Schemes of Ferrite Cavities
Motivation
State of the art
Scope of the work
First results for G-510 material characteristics
Next steps and challenges

## Slide 3: Motivation – Which Application?
CERN injector complex update programme
PS2: novel accelerating cavity with 18 – 40 MHz tuning range required

## Slide 4: Motivation – How does an Accelerating Cavity work?
accelerating gap
beam pipe
cylindrical structure
ERF
HRF
λ/4

## Slide 5: Motivation – Why Ferrite Loaded?
Tuning 18 – 40 MHz →
ferrite ring

## Slide 6: State of the Art – Examples
Name | Tuning Range | Biasing Method | Type of ferrite
CERN PS | 2.8 – 9.6 MHz | Parallel | Ni-Zn
TRIUMF Booster | 46 - 62 MHz | Perpendicular | Yttrium Garnet
New PS Update Cavity | 18 – 40 MHz | Parallel, Perpendicular or both? | Yttrium Garnet

## Slide 7: State of the Art – Parallel Biasing
μr ~ slope of tangent line
increasing H1ll to H2ll shifts μr,1 to μr,2

## Slide 8: State of the Art – Perpendicular Biasing
μr ~ slope of secant from origin to B-H curve.
Higher Magnetic Field strength needed
Operating point is closer to saturating magnetization 4πMs reduced RF losses and higher Q values.

## Slide 9: State of the Art – 2 Directional Biasing
First applying H1⊥→ operating point close to saturating magnetization
Rotating direction to H2ll → modest increase in bias field

## Slide 10: Scope of the Work – Overview
Developing an accelerating cavity with 18 – 40 MHz tuning range using a simulation tool
Characterize dispersion of G-510
Verify results by simulation
Characterize bias field dependence of G-510
Verify results by simulation
Elaborate simulation model for perpendicular biasing to give an estimation of frequency range
Decision if perpendicular biasing is sufficient

## Slide 11: First Results – G-510
Coaxial short-circuit technique to determine
Measuring S11 for empty and filled sample holder
Analytical calculation of (S11) for sample holder

## Slide 12: First Results – Verification by Simulation
Simulation of sample holder with (f) and (f) as input

## Slide 13: First Results – G-510
Same method but for different bias field
= 13.0
= 2.0
≈ 6.5

## Slide 14: First Results – Verification by Simulation
Simulation of sample holder with (f) and (f) for = 200A

## Slide 15: Scope of the Work – Overview
First Results:
Characterize dispersion of G-510
Verify results by simulation
Characterize bias field dependence of G-510
Verify results by simulation
Next steps:
Elaborate simulation model for perpendicular biasing to give an estimation of frequency range
Decision if perpendicular biasing is sufficient

## Slide 16
Thank you for your attention!