## Slide 1: Muon Accelerators for the Next Generation of High Energy Physics Experiments
Katsuya Yonehara
on behalf of MAP
Accelerator Physics Center, Fermilab
June 08, 2013

## Slide 2: The Aims of the Muon Accelerator Program
  Muon accelerator R&D is focused on developing a facility that can address critical questions spanning two frontiers…
  The Intensity Frontier:
  with a Neutrino Factory producing well-characterized n beams for precise, high sensitivity studies
  The Energy Frontier:
  with a Muon Collider capable of reaching multi-TeV CoM energies
  and a Higgs Factory on the border between these Frontiers
The unique potential of a facility based on muon accelerators is physics reach that SPANS 2 FRONTIERS
http://science.energy.gov/~/media/hep/pdf/files/pdfs/p5_report_06022008.pdf

## Slide 3: Outline
Physics Motivations
Muon Collider Concept
Muon Collider and Neutrino Factory Synergies
The MAP Feasibility Assessment
Concluding Remarks
Backup item (Central part of MAP R&D)
R&D Challenges
Recent R&D Highlights

## Slide 4: THE PHYSICS MOTIVATIONs

## Slide 5: The Physics Motivations
m – an elementary charged lepton:
  200 times heavier than the electron
  2.2 ms lifetime at rest
Physics potential for the HEP community using muon beams
  Tests of Lepton Flavor Violation (mu2e conversion)
  Anomalous magnetic moment a hints of new physics (g-2)
  Can provide equal fractions of electron and muon neutrinos at high intensity for studies of neutrino oscillations – the Neutrino Factory concept
  Offers a large coupling to the “Higgs mechanism”
  As with an e+e− collider, a m+m− collider would offer a precision probe of fundamental interactions – in contrast to hadron colliders

## Slide 6: Muon Accelerator Physics
Large muon mass strongly suppresses synchrotron radiation
  a Muons can be accelerated and stored using rings at much higher energy than electrons
  a Colliding beams can be of higher quality with reduced beamstrahlung
Short muon lifetime has impacts as well
  Acceleration and storage time of a muon beam is limited
  Collider a a new class of decay backgrounds must be dealt with
Precision beam energy measurement by g-2 allows precision Higgs width determination
Muon beams produced as tertiary beams:
  Offers key accelerator challenges… Beam Cooling
Beamstrahlung in any e+e- collider
E/E  2

## Slide 7: The Physics Needs: Neutrinos (I)
In the neutrino sector it is critical to understand:
  dCP
  The mass hierarchy
  q23 = p/4, q23 < p/4 or q23 > p/4
  Resolve the LSND and other short baseline experimental anomalies [perhaps using beams from a muon storage ring (nSTORM) in a short baseline experiment]
  And continue to probe for signs new physics
P. Huber

## Slide 8: The Physics Needs: Neutrinos (II)
CP violation physics reach of various facilities
Can we probe the CP violation in the neutrino sector at the same level as in the CKM Matrix?
P. Coloma, P. Huber, J. Kopp, W. Winter – article in preparation
0.025 IDS-NF: 700kW target, no cooling, 2×108 s running time
10-15 kTon detector

## Slide 9: The Physics Needs: Colliders
E. Eichten

## Slide 10: Muon Collider Reach
E. Eichten

## Slide 11: Muon Accelerator Physics Scope
Intensity Frontier
Energy Frontier
→“muon source”

## Slide 12: Muon Accelerators
Program Baselines
And Potential Staging Steps
(muon source)

## Slide 13: Muon Collider Concept
Proton source:
For example PROJECT X at 4 MW, with 2±1 ns long bunches
Goal: Produce a high intensity m beam whose 6D phase space is reduced by a factor of ~106-107 from its value at the production target
Collider: √s = 3 TeV
Circumference 4.5km L = 3×1034 cm-2s-1 m/bunch = 2x1012
s(p)/p = 0.1%
eN = 25 mm, e//N=72 mm
b* = 5mm
Rep. Rate = 12 Hz
Muon Collider Block Diagram

## Slide 14: MAP Designs for a Muon-Based Higgs Factory and Energy Frontier Collider
Exquisite Energy Resolution Allows Direct
Measurement
of Higgs Width
Site Radiation mitigation with depth and lattice design: ≤ 10 TeV

## Slide 15: 126 GeV Higgs Factory
Major advantage for Physics of a + Higgs Factory: possibility of direct measurement of the Higgs boson width (~4MeV FWHM expected)
Reduced cooling:
N =0.3mmrad,
||N =1mmrad
s-channel coupling of Muons to HIGGS with high cross sections:
Muon Collider of with L = 1032 cm-2s-1 @ 63 GeV/beam (50000 Higgs/year)
Competitive with e+/e- Linear Collider with L = 2. 1034 cm-2s-1 @ 126 GeV/beam
Sharp resonance: momentum spread of a few × 10-5
Han and Liu
hep-ph 1210.7803
Precision energy measurement provided by g-2 effect and residual polarization in muon beams
Emittance evolution in cooling channel

## Slide 16: Demonstration of cooling channel - MICE
Currently preparing for MICE Step IV
Includes:
  Spectrometer Solenoids
  First Focus Coil
Provides:
  Direct measurement of interactions with absorber materials
  Important simulation input
MICE
Spectrometer Solenoids
RF-Coupling Coil (RFCC) Units
First Spectrometer Solenoid Now Commissioned!
First Coupling Coil Cold Mass Being Readied for Training
Fermilab Solenoid Test Facility

## Slide 17
One IP in the latest
design

## Slide 18: Multi-TeV Collider – 1.5 TeV Baseline
Parameter | Unit | Value
Beam energy | TeV | 0.75
Repetition rate | Hz | 15
Average luminosity / IP | 1034/cm2/s | 1.1
Number of IPs, NIP | - | 2
Circumference, C | km | 2.73
* | cm | 1 (0.5-2)
Momentum compaction, p | 10-5 | -1.3
Normalized r.m.s. emittance, N | mmmrad | 25
Momentum spread, p/p | % | 0.1
Bunch length, s | cm | 1
Number of muons / bunch | 1012 | 2
Number of bunches / beam | - | 1
Beam-beam parameter / IP,  | - | 0.09
RF voltage at 800 MHz | MV | 16
Larger chromatic function (Wy) is corrected first with a single sextupole S1, Wx is corrected with two sextupoles S2, S4 separated by 180 phase advance.
Y. Alexahin

## Slide 19: Wall Plug Power Estimates
300 MW
Estimate assumes a base 70MW
Facility Power
requirement as in
LC analyses.
Muon Collider

## Slide 20: Luminosity Production Metric
Luminosity Metric:
Ndet × Lavg / Ptot
Muon Collider

## Slide 21: Muon Collider and neutrino factory synergies

## Slide 22: Muon Collider - Neutrino Factory Comparison
NEUTRINO FACTORY
MUON COLLIDER
Share same complex
n Factory Goal: O(1021) m/year
within the accelerator
acceptance

## Slide 23: Muon Accelerator Staging Study (MASS)
Two approaches exist:
  A dedicated “green field” construction project
  A staged development based on evolving capabilities at an existing facility
    Desirable if high quality physics can be produced along the way…
    Can provide clear decision points with well-understood risks for moving forward
    Incremental deployment of expensive or technically challenging elements
2008 P5 Roadmap called for a “world-leading Intensity Frontier program centered at Fermilab”
  Can a Muon Accelerator effort support this goal as well as provide a path to return to an Energy Frontier facility in the US?
  Can a staged Muon Accelerator effort provide both physics output and the necessary accelerator R&D along the way?
  What are the timescales associated with such an effort?

## Slide 24: All proposed muon-based accelerators would easily fit at Fermilab
nSTORM (entry level Neutrino Factory)
Intensity Frontier Neutrino Factory
Also a muon-based Higgs Factory or Energy Frontier Muon Collider
nSTORM would provide important physics output and critical R&D leverage
K.Long
NuFACT12

## Slide 25: Neutrinos from Stored Muons (arXiv: 1206.0294 (LOI), Fermilab P-1028)
DOES NOT
Require the
Development of
ANY
New Technology
An entry-level NF?
NuSTORM Workshop held Sept 21-22 @ FNAL:
(https://indico.fnal.gov/conferenceDisplay.py?confId=5710)
A.Bross
NuFACT12
3.8 GeV/c
stored m
10-100kW

## Slide 26: nStorm as an R&D platform
A high-intensity pulsed muon source
100<pμ<300 MeV/c muons
  Using extracted beam from ring
  1010 muons per 1 μsec pulse
Beam available simultaneously with physics operation
  Sterile n search
  n cross section measurements needed for ultimate precision in long baseline measurements
nSTORM also provides the opportunity to design, build and test decay ring instrumentation (BCT, momentum spectrometer, polarimeter) to measure and characterize the circulating muon flux.

## Slide 27
LBNE
To Homestake
Buncher/
Accumulator
Rings
Project X Stage I
Project X Stage II
Project X Stage III
Linac + RLA to ~5 GeV
NF Decay Ring:
ns to Homestake
Front End+4D+6D
RLA to 63 GeV +
300m Higgs Factory
nSTORM + Muon Beam R&D Facility
A Muon Accelerator Facility for Cutting Edge Physics on the Intensity and Energy Frontiers
Based on Project X Stage II

## Slide 28: The Muon Accelerator Program Timeline
At Fermilab, critical physics production could build on Phase II of Project X

## Slide 29: The MAP Feasibility Assessment

## Slide 30: The Feasibility Assessment
Feasibility Assessment: Phase I
Feasibility Assessment: Phase II
Beyond the Feasibility Assessment
FY13 − FY15:
Identify baseline design concepts
Identify high leverage alternative concepts
Identify key engineering paths to pursue:
  RF
  High Field Magnets
Develop critical engineering concepts (eg, 6D Cooling Cell)
Support major systems tests
  MICE Step IV
  MICE RFCC construction & testing
FY16 − FY18:
Technical demonstration of critical baseline concepts
  eg, 6D Cooling cell
Pursue high leverage alternative concepts
Assess technical and cost feasibility of baseline concepts
Support major systems tests
  MICE Step V/VI
  6DICE planning
FY19 
Plan contingent on the feasibility assessment!
Can we launch the design effort towards a staged implementation of a NF & MC?
Advanced systems tests
  6DICE?
  Support physics?

## Slide 31: Concluding Remarks

## Slide 32: Some Thoughts…
The unique feature of muon accelerators is the ability to provide cutting edge performance on both the Intensity and Energy Frontiers
  This is well-matched to the direction specified by the P5 panel for Fermilab
  The possibilities for a staged approach make this particularly appealing in a time of constrained budgets
  nSTORM would represent a critical first step in providing a muon-based accelerator complex
World leading Intensity Frontier performance could be provided with a Neutrino Factory based on Project X Phase II
  This would also provide the necessary foundation for a return to the Energy Frontier with a muon collider on U.S. soil
A Muon Collider Higgs Factory
  Would provide exquisite energy resolution to directly measure the width of the Higgs. This capability would be of crucial importance in the MSSM doublet scenario.
  The first collider on the path to a
  multi-TeV Energy Frontier machine?

## Slide 33: Conclusion
Through the end of this decade, the primary goal of MAP is demonstrating the feasibility of key concepts needed for a neutrino factory and muon collider
a Thus enabling an informed decision on the path forward for the HEP community
Muon Collider Concept
A challenging, but promising, R&D program lies ahead!

## Slide 34: THE R&D CHALLENGES
Backup slide

## Slide 35: Technology Challenges – Tertiary Production
Neuffer
A multi-MW proton source, e.g., Project X, will enable O(1021) muons/year to be produced, bunched and cooled to fit within the acceptance of an accelerator.

## Slide 36: Technology Challenges - Target
The MERIT Experiment at the CERN PS
  Proof-of-principle demonstration of a liquid Hg jet target in high-field solenoid in Fall `07
  Demonstrated a 20m/s liquid Hg jet injected into a 15 T solenoid and hit with a 115 KJ/pulse beam!
  a Technology OK for beam powers up to 8 MW with a repetition rate of 70 Hz!
Hg jet in a 15 T solenoid
with measured disruption length ~ 28 cm
1 cm

## Slide 37: TechnoIogy Challenges – Capture Solenoid
A Neutrino Factory and/or Muon Collider Facility requires challenging magnet design in several areas:
  Target Capture Solenoid (15-20T with large aperture)
  Estored ~ 3 GJ
  O(10MW) resistive coil in high radiation environment
  Possible application
  for High Temperature Superconducting magnet technology

## Slide 38: Technology Challenges - Cooling
Tertiary production of muon beams a
  Initial beam emittance intrinsically large
  Cooling mechanism required, but no radiation damping
Muon Cooling a Ionization Cooling
    dE/dx energy loss in materials
    RF to replace plong
MICE
Spectrometer Solenoids
RF-Coupling Coil (RFCC) Units
  The Muon Ionization Cooling Experiment: Demonstrate the method and validate our simulations

## Slide 39: Ionization Cooling

## Slide 40: Technology Challenges - Cooling
Some components beyond state-of-art:
  Very high field HTS solenoids (≥30 T)
  High gradient RF cavities operating in multi-Tesla fields
Development of a cooling channel design to reduce the 6D phase space by a factor of O(106-107) → MC luminosity of O(1034) cm-2 s-1
R. Palmer
Emittance Reduction via Ionization Cooling
The program targets critical magnet and cooling cell technology demonstrations within its feasibility phase.

## Slide 41: Technology Challenges – RF
A Viable Cooling Channel requires
  Strong focusing and a large accelerating gradient to compensate for the energy loss in absorbers
  a Large B- and E-fields superimposed
Operation of RF cavities in high magnetic fields is a necessary element for muon cooling
  Control RF breakdown in the presence of high magnetic fields
  The MuCool Test Area (MTA) at Fermilab is actively investigating:
    Operation of RF cavities in the relevant regimes
    Breakdown mitigation techniques
MTA Beamline

## Slide 42: RF Breakdown in Magnetic Fields
The RF breakdown could be related by heating through field emission with external magnetic field and RF field:
  External magnetic field
  Ohmic heating
Possible solutions
  ExB
  Choice of materials
  Surface preparation
  Lower initial temperatures
E field contour
B=0 T
B=1 T
Magnetic insulation
D. Li

## Slide 43: Technology Challenges - Acceleration
Muons require an ultrafast accelerator chain
a Beyond the capability of most machines
Several solutions for a muon acceleration scheme have been proposed:
  Superconducting Linacs
  Recirculating Linear Accelerators (RLAs)
  Fixed-Field Alternating-Gradient (FFAG) Machines
        EMMA at Daresbury Lab is a test of the promising non-scaling type
  Rapid Cycling Synchrotrons (RCS/VRCS)
  Hybrid Machines
EMMA

## Slide 44: An Initial Acceleration Scheme: RLAs
RLA I
RLA II
Pre-linac
244 MeV
900 MeV
3.6 GeV
0.9 GeV
3.6 GeV
12.6 GeV
86 m
0.6 GeV/pass
202 m
255 m
2 GeV/pass
S.A. Bogacz

## Slide 45: Superconducting RF Development
Cavity going into test pit
in Newman basement (Cornell University)
Pit: 5m deep X 2.5m dia.
400mm BT
Cavity length: 2 m
Major dia.: 1.4 m
201 MHz SCRF R&D

## Slide 46: Technology & Design Challenges – Ring, Magnets, Detector
Emittances are relatively large, but muons circulate for ~1000 turns before decaying
  Lattice studies for 126 GeV, 1.5 & 3 TeV CoM
High field dipoles and quadrupoles must operate in high-rate muon decay backgrounds
  Magnet designs under study
Detector shielding & performance
  Initial studies for 1.5 TeV, then 3 TeV and 126 GeV
  Shielding configuration
  MARS background simulations
MARS energy deposition map for 1.5 TeV collider dipole

## Slide 47: Technology Challenges: Heat Load in Arc Magnets (N.Mokhov)
Energy deposition: in the ring dipole cold mass @LHe temp 25 W/m - a factor of ~5 too high!
W rods 80 W/m
in the quadrupole cold mass @LHe temp 38 W/m
in masks between magnets 1.5-3 kW/m
Solutions:
 abandon the open-midplane design, put W absorber inside the dipole bore
 sweep away the decay electrons before they obtain considerable vertical displacement: use combined-function magnets
Vertical view
Cross-section view
Horizontal view
Decay products trajectories :
e


n

## Slide 48: Backgrounds and Detector
Much of the background is soft and out of time
Nanosecond time resolution can reduce backgrounds by three orders of magnitude
Requires a fast, pixelated tracker and calorimeter.
Non-ionizing background ~ 0.1 x LHC
But crossing interval 10ms/25 ns 400 x
GeV/c
ns
 | Cut | Rejection
Tracker hits | 1 ns, dedx | 9x10-4
Calorimeter neutrons | 2 ns | 2.4x10-3
Calorimeter photons | 2 ns | 2.2x10-3

## Slide 49: Recent R&D Progress – Some Highlights
Backup slide

## Slide 50: MAP Design & Simulation
Cooling Channel Concepts
High Performance Computing
Code Parallelization (G4Beamline, ICOOL)
  Performance improvements > 104
Enables Multi-Objective Parallel Optimization of Accelerator Designs
MAP Design Efforts
Program Baselines
Staging Study (MASS) Contributions
Capture Solenoid (15-20T):
~3 GJ large aperture magnet
Liquid Hg Jet Target
HCC
Guggenheim

## Slide 51: Recent Progress I - MICE
Currently preparing for MICE Step IV
Includes:
  Spectrometer Solenoids
  First Focus Coil
Provides:
  Direct measurement of interactions with absorber materials
  Important simulation input
MICE
Spectrometer Solenoids
RF-Coupling Coil (RFCC) Units
First Spectrometer Solenoid Now Commissioned!
First Coupling Coil Cold Mass Being Readied for Training
Fermilab Solenoid Test Facility

## Slide 52: Recent Progress II – Cavity Materials
Breakdown tests with Be and Cu Buttons
Both reached ~31 MV/m
Cu button shows significant pitting
Be button shows minimal damage
a Materials choices offer the possibility of more robust operation in mangetic fields
Cu
Be

## Slide 53: Recent Progress III – Vacuum RF
Vacuum Tests at B = 0 T & B = 3 T
  Two cycles: B0 a B3 a B0 a B3
No difference in maximum stable operating gradient
  Gradient » 25 MV/m
Demonstrates possibility of successful operation of vacuum cavities in magnetic fields with careful design
All-Seasons
Cavity
(designed for both vacuum and high pressure operation)

## Slide 54: Recent Progress IV: High Pressure RF
Gas-filled cavity
  Can moderate dark current and breakdown currents in magnetic fields
  Can contribute to cooling
  Is loaded, however, by beam-induced plasma
Electronegative Species
  Dope primary gas
  Can moderate the loading effects of beam-induced plasma by scavenging the relatively mobile electrons
5/22/12
Beam on
E0 = 25 MV/m
54
Pure GH2
1% Dry Air (0.2 % O2) in GH2
1% Dry Air
(0.2 % O2)
in GH2 at B = 3 T
E0 = 25 MV/m
~50× change in
RF dissipation

## Slide 55: Recent Progress V: High Field Magnets
Progress towards a demonstration of a final stage cooling solenoid:
Demonstrated 15+ T (16+ T on coil)
  ~25 mm insert HTS solenoid
  BNL/PBL YBCO Design
  Highest field ever in HTS-only solenoid (by a factor of ~1.5)
Will soon begin preparations for a test with HTS insert + mid-sert in NC solenoid at NHFML a >30 T
BSCCO-2212 Cable -
Transport measurements show that FNAL cable attains 105% Jc of that of the single-strand
Multi-strand cable utilizing chemically compatible alloy and oxide layer to minimize cracks

## Slide 56: MAP Recent Technology Highlights
Successful Operation of 805 MHz “All Seasons” Cavity in 3T Magnetic Field under Vacuum
MuCool Test Area/Muons Inc
World Record HTS-only Coil 15T on-axis field 16T on coil
PBL/BNL
Demonstration of High Pressure RF Cavity in 3T Magnetic Field with Beam
Extrapolates to m-Collider Parameters
MuCool Test Area
Breakthrough in HTS Cable Performance with Cables Matching Strand Performance
FNAL-Tech Div T. Shen-Early Career Award
The Path to a Viable Muon Ionization Cooling Channel
Pure GH2
1% Dry Air (0.2% O2) in GH2
E0 = 25 MV/m
~50X reduction in
RF power dissipation
1% Dry Air
(0.2 % O2)
in GH2 at
B = 3T