## Slide 1: Hard Disk Drive - Reliability Overview
Dr. Amit Chattopadhyay
Sr. Engineering Manager, Recording Sub-Systems
Advanced Reliability Engineering
Western Digital, San Jose

## Slide 2: Outline
State of affairs in HDD Field Reliability
1
a
Macroscopic objects at molecular dimensions: Head-disk Interface
b
Critical Parameters: Clearance and Workload
c
HDD reliability modeling
2
Drive parametric measurements: Virtual Failures
a
Importance of workload and temperature
b
c
3
Data Center Fleet Management: In-field Health Monitor
HDD complexity leads to a myriad of possible failure modes
Historical model: derivation and limitations

## Slide 3: Core problem in HDD reliability
Try to avoid something analogous to a ‘BP’ moment (Deepwater Horizon oil spill of 2010) - Avoid an un-manageable catastrophe midway (or beyond) through a product’s warranty life
  Referred to as ‘wear-out’ mode in reliability  unbounded Failure Rate at large times
For the drives out in the field, develop a predictive analysis for failures
QUESTIONS
How do we define a product’s “lifetime”?
How do we get visibility into what happens during this lifetime?
Can we help our customers perform effective Fleet Management in real time?

## Slide 4: Current HDD Reliability Landscape
Clearance trend in recent WD products
Increases in areal density have largely come by decreasing the head-disk spacing
  The Magnetics vs Tribology dilemma
Current head-media spacings are at molecular dimensions: 1 – 2nm
  Operating at these clearances can impact the HDD failure rates, and the failure pareto
  As much as 70% of the failure pareto is attributable to low-clearance operation
Operation at ever-decreasing spacings requires special attention be paid to:
  Anamolous physical phenomenon in ultrathin films
  Non-linear response functions, e.g. Adhesive and frictional forces
  Mechanical tolerances
  etc
Tribology problems explode

## Slide 5: Head-Media Interface Failures: A Conceptual Model
The clearance between slider and disk is a dominant factor dictating HDI reliability ( 70% of all failures).
Insufficient clearance results in an increased probability of head-disk interaction and eventual failure due to HFW, modulation, or head degradation
In order to ensure acceptable reliability in this spacing regime, one must minimize the probability of contact……
1 – 2 nm
Head-disk Interaction
0.5nm
1.5nm
2.0nm
2.5nm
1.0nm
DISK
1.6nm
Increased failure probability
Reduce mean
clearance
 = 2.1nm
0.5nm
1.5nm
2.0nm
2.5nm
1.0nm
Clearance Distribution
Head-disk Interaction
DISK

Model
Notes: 5

## Slide 6: Influence of Clearance Mean / Sigma
 = 0.5nm
 = 0.35nm
 = 0.7nm
HDDs require control of macro-scale mechanics to atomic dimensions!
Toy model: Failure rates as a function of both the mean clearance and the required standard deviation in clearance are shown below
Design Criteria

## Slide 7: Influence of Clearance Mean / Sigma
 = 0.35nm
 = 0.5nm
 = 0.7nm
HDDs require control of macro-scale mechanics to atomic dimensions!
Toy model: Failure rates as a function of both the mean clearance and the required standard deviation in clearance are shown below
WD produces 200 million drives per year, with each having multiple heads…….. …..something on the order of 1 billion head-disk interfaces / year
The Std dev in clearance for these interfaces must all be held to within the Van der Waals diameter of a single carbon atom = 0.34nm
Design Criteria

## Slide 8: HDI: Head-Disk Interface a major challenge area
Slider
HDD are complex devices that push the envelope of our physics understanding in a number of areas
A monolayer of lubricant is used on disk surface to reduce adhesion / friction between slider and disk
Lubricant pick-up by the slider is normal
Pole Tip
Disk
Lube chains
(0.8nm x 80nm)
“end-groups”

## Slide 9: Head-Disk Interface:
Slider
HDD are complex devices that push the envelope of our physics understanding in a number of areas
A monolayer of lubricant is used on disk surface to reduce adhesion / friction between slider and disk
Lubricant pick-up by the slider is normal, but lubricant pick-up in excess of one layer can pose a serious reliability risk
  HFW, OTW, modulation, and head degradation
Optical image
Chemical image
Red = excess lube

## Slide 10: Interface: at the edge of classical thermodynamics
Slider
HDD are complex devices that push the envelope of our physics understanding in a number of areas
A monolayer of lubricant is used on disk surface to reduce adhesion / friction between slider and disk
Lubricant pick-up by the slider is normal, but lubricant pick-up in excess of one layer can pose a serious reliability risk
  HFW, OTW, modulation, and head degradation
Monomolecular films can show anamolous behavior
Fractal Formation
Terraced Spreading
4nm height
5th monolayer
3rd monolayer
Stable bilayer
Stable bilayer
1st Stable monolayer
Film Thickness (A)
1 monolayer
3 monolayers
Lube Fractals
Terraced Spreading
  Non-classical thermodynamics: physical properties are dependent on the amount of material present
Optical image
Chemical image
Red = excess lube

## Slide 11: …..with some Chemistry and Materials Science
Protective diamond-like carbon (DLC) overcoats are used on both the head and disk surfaces
  Constant pressure to thin these overcoats for the purpose of decreasing the magnetic separation distance …..and thereby improving magnetic signal / areal density
  Current DLC thicknesses on the order of 2nm
  As these thicknesses are reduced, various reliability risks can arise
Disk example: migration of magnetic material to head-disk interface
  Corrective action required modification to carbon deposition energetics / process
Head example: contact stress can result in wear of the pole tip
  Corrective action required stricter process control measures
  Process optimization of sp3 / sp2
Magnetics
Carbon
Co+2
Co+2
Co+2
Co+2
Co+2
Co+2
Co+2
Co+2
Co+2
Co+2
Co+2
N+
N+
N+
N+
Co
O
Co
O
H
O
H
Co+2
Co+2
Co smear
Carbon wear
2nm

## Slide 12: HDI failure rates: critical component attributes
Maintaining sufficient clearance, and hence ensuring interface reliability is a multi-dimensional problem.
HDD reliability is certainly not boring
  New issues seem to accompany development of each new product generation
  Since HDD complexity complicates reliability modeling, must focus on most likely failure modes
Any simple reliability model is bound to have some weaknesses given this complexity
Contaminants
Pad Size
DFH Bulge
Size / Roughness
HDI Failure Rate
Media
Overcoat Material
composition
Deposition
technique
Active sites
Microwaviness
hardness

Polarity
Thickness
D:G Ratio
Density
Surface
Roughness
Lubricant
Molecular Weight
PFPE Backbone
C1/C2/C3
Surface mobility
Bonding Ratio
Bonding kinetics
End Group Structure
Humidity sensitivity
Polarity
Additives
Concentration
type
Film Thickness
Surface Energy
Disjoining Pressure
Polydispersity
Operating
Environment
Drive Parameters
Filter type / location
Humidity
Temperature
Rotational Velocity
Defect Mapping
Channel
Seek Profile
Head Design
Positive
Pressure
Fly Height
Profile
Min.FH
Pole tip
protrusion
ABS
Overcoat
composition
Overcoat Thickness
stiffness
Roll
Pitch
Particulate loading
Pressure/
altitude

## Slide 13: Time to Failure: The “Bathtub” Reliability Model
Classical Reliability Model
“The Bathtub Curve"
Time
Failure Probability
Infant mortality region
  Failure rate decreases with increasing time
  Result of defects etiher designed into, or inadvertently built into a product
    Indicative of quality “escapes”
    Marginal materials
    Drives with the least margin for some critical design tolerance.
    Manufacturing anomaly
Steady State region
  After the weak drives are removed from the population, the failure rate reaches a fixed value for the service life of the drive
Wear-out Region
  At long times, one enters the wear-out region where normal wear and tear of the system components results in an increasing failure rate with time

## Slide 14: Time to Failure: The “Bathtub” Reliability Model
Classical Reliability Model
“The Bathtub Curve"
Time
Failure Probability
Infant mortality region
  Failure rate decreases with increasing time
  Result of defects etiher designed into, or inadvertently built into a product
    Indicative of quality “escapes”
    Marginal materials
    Drives with the least margin for some critical design tolerance.
    Manufacturing anomaly
Steady State region
  After the weak drives are removed from the population, the failure rate reaches a fixed value for the service life of the drive
Wear-out Region
  At long times, one enters the wear-out region where normal wear and tear of the system components results in an increasing failure rate with time

## Slide 15: Time to Failure: The “Bathtub” Reliability Model
Classical Reliability Model
“The Bathtub Curve"
Time
Failure Probability
Infant mortality region
  Failure rate decreases with increasing time
  Result of defects etiher designed into, or inadvertently built into a product
    Indicative of quality “escapes”
    Marginal materials
    Drives with the least margin for some critical design tolerance.
    Manufacturing anomaly
Steady State region
  After the weak drives are removed from the population, the failure rate reaches a fixed value for the service life of the drive
Wear-out Region
  At long times, one enters the wear-out region where normal wear and tear of the system components results in an increasing failure rate with time

## Slide 16: Time to Failure: The “Bathtub” Reliability Model
Classical Reliability Model
“The Bathtub Curve"
Time
Failure Probability
Infant mortality region
  Failure rate decreases with increasing time
  Result of defects either designed into, or inadvertently built into a product
    Indicative of quality “escapes”
    Marginal materials
    Drives with the least margin for some critical design tolerance.
Steady State region
  After the weak drives are removed from the population, the failure rate reaches a fixed value for the service life of the drive
Wear-out Region
  At long times, normal wear and tear of the system components results in an increasing failure rate with time
  This type of behavior results in costly excursions to both WD and our customers
  This regime must be avoided at all costs

## Slide 17
Standard Weibull Treatment
  Gives time dependence of unreliability, F(t)
  Where: t = time
   = time constant
   = shape parameter
In the limit of small failure rates (<10%) the failure rate vs time simplifies to a power function of time:
Classical reliability theory – time dependence
Field Reliability vs Time
Since failure rate assumed to depend on time alone, MTTF has been used to quantify the intrinsic reliability of HDD’s
  MTTF defined by the time required for 63.2% of all drives in a given population to fail
But…..use of MTTF alone is meaningless
Reason behind the workload specs introduced by all HDD manufacturers
POH = power-on hrs
1st year
2nd year
3rd year
β < 1: Failure rate decreases with time

## Slide 18: Historical reliability model – impact of temp
Numerous studies conducted on HDD failure rates at elevated temperature
Consistent reports of HDD failure rates increasing exponentially with increasing temperature
  Arrhenius equation:
  Ea = activation energy
  A, R = constants
  T = Temperature (kelvin)
Rule of thumb:
  Failure rate doubles for approximately 15 C increase in temp
  Note: We make use of this acceleration by testing all products at the upper temp spec limit
Maxtor:
Ea = 51.9 kJ mole-1
Seagate:
Ea = 36.4 kJ mole-1
WD:
Ea = 39.3 kJ mole-1
Samsung:
Ea = 30.6 kJ mole-1
Microsoft:
Ea = 44.4 kJ mole-1
2X
15C

## Slide 19: Historical reliability model – duty cycle
A duty cycle term is typically added to general reliability expression
  Qualitatively accounts for the intuitive notion that HDD reliability should scale with how much the drive does
  Usually defined as a power law
Combination of all three effects, i.e. POH, DC and Temp, yields the classic reliability model
  This model has been used in the HDD industry for decades
How good is this at describing reality?
Usage Term
Thermal Term

## Slide 20: Failure Rate vs Expanded Temp Range
  Failure rate dependence at cold shows inverse Arrhenius behavior
    Magnetic challenges due to higher media coercivity
    Stronger adhesive forces between heads and media/lube
  Failure rates are relatively independent of temp between 15 – 40C
-5C +5C +15C +30C +40C +50C +60C +70C
Drive Basecast Temperature [C]
+0.4 eV
-0.9 eV
Inverse Arrhenius
Conventional Behavior
Ea = activation energy
k = 8.62 x 10-5 eV/K
T = absolute temperature (Kelvin)

## Slide 21: Duty Cycle
180 GB/hr
120 GB/hr
Ln (cumulative failures)
Ln (test time)
β1 = 0.8
β2 = 0.8
Is the concept of “Duty Cycle” valid?
  DOE with same drives built at the same time
  Two tests with equivalent duty cycles (>95%)
  ……..but differing workloads (1.5:1)
Results clearly show that failure rates scale with workload…..not duty cycle
Standard (time-based) Weibull Analysis
Chart: RDT Test Time (hrs)
| 0.0 | 24.0 | 48.0 | 72.0 | 96.0 | 120.0 | 144.0 | 168.0 | 192.0 | 216.0 | 240.0 | 264.0 | 288.0 | 312.0 | 336.0 | 360.0 | 384.0 | 408.0 | 432.0 | 456.0 | 480.0 | 504.0 | 528.0 | 552.0 | 576.0 | 600.0 | 624.0 | 648.0 | 672.0 | 696.0 | 720.0 | 744.0 | 768.0 | 792.0 | 816.0 | 840.0 | 864.0 | 888.0 | 912.0
Tribo RDT Cum failure % | 0 | 0.007 | 0.01 | 0.01 | 0.01 | 0.01 | 0.017 | 0.023 | 0.03 | 0.03 | 0.043 | 0.043 | 0.043 | 0.043 | 0.05 | 0.05 | 0.053 | 0.057 | 0.06 | 0.06 | 0.063 | 0.067 | 0.07 | 0.073 | 0.077 | 0.08 | 0.083 | 0.083 | 0.083 | 0.09 | 0.09 | 0.093 | 0.097 | 0.097
Pre-RDT Cum failure % | 0 | 0.0055556 | 0.012963 | 0.022222 | 0.035185 | 0.048148 | 0.055556 | 0.061111 | 0.066667 | 0.072222 | 0.074074 | 0.075926 | 0.083333 | 0.087037 | 0.092593 | 0.096296 | 0.10185 | 0.10741 | 0.10926 | 0.11111 | 0.11481 | 0.11481 | 0.12037 | 0.12593 | 0.12963 | 0.13333 | 0.13519 | 0.13889 | 0.13889 | 0.14074 | 0.14259 | 0.1463 | 0.1463 | 0.14815
182 GB/hr
Time to Failure Plot
Convex curvature
(β < 1)
Usage
Thermal Term
MTTF1
MTTF2
Same drive / same DC / two workloads = different MTTFs
Conclusions:
MTTF typically used to specify reliability of HDDs
Since MTTF is not uniquely defined……
MTTF alone is an insufficient measure of drive reliability!

## Slide 22: Historical Reliability Model – Duty Cycle
Functional duty cycle is a useless concept for predicting HDD failure rates
  Nebulous / ill-defined
  Every data center claims they run at 100% duty cycle, however, actually “usage” varies dramatically between data centers and within a given data center
  No quantitative data available
Workload is a much better measure for drive usage
  Defined as the total data transfer (sectors written + read)
  Tightly coupled to the dominate failure modes in test and field that are caused by close proximity between heads and media.
  Quantifiable from internal drive logs, thereby facilitating accurate field AFR predictions
  All HDD manufacturers now explicitly specify workload ratings
Usage Term
Thermal Term

## Slide 23: Rough Drive Quality Scale
Introduced to allow comparison of basic quality requirements
Priority list for enablers
Reflective of
  Intrinsic quality spec: MTTF
  Workload
  Temperature
Normalized to Desktop
Reliability Landscape and Trends
8.6 RE (Nearline Enterprise)
2.7 SE (Scaled Enterprise)
15.3 XE
1 == Desktop; Cold Storage
0.6 Mobile

## Slide 24
AFR = Annualized Failure Rate
Typical Workloads for different market segments –
XE (800 TB/yr)
RE: Nearline Enterprise (550 TB/yr)
Cloud (180 TB/yr)
Desktop usage (55 TB/yr)
10x increase in usage from typical DT drive to Enterprise
Reliability Landscape and Trends

## Slide 25
“Dynamic Fly Height” (DFH) concept
  Head-disk spacing is controlled by resistive heating of the pole tip region of the head
  Thermal actuation is only performed during read and write operations
  Head-disk interface failures  when flying at 10nm
Minimization of time spent in close proximity
Thermal Expansion
Element spacing
Nominal FH
DFH Off
DFH On
1.5nm
10nm
Disk

## Slide 26
“Dynamic Fly Height” (DFH) concept
  Head-disk spacing is controlled by resistive heating of the pole tip region of the head
  Thermal actuation is only performed during read and write operations
  Head-disk interface failures  when flying at 10nm
Minimization of time spent in close proximity
Thermal Expansion
Element spacing
Nominal FH
DFH Off
DFH On
1.5nm
10nm
Disk

## Slide 27
“Dynamic Fly Height” (DFH) concept
  Head-disk spacing is controlled by resistive heating of the pole tip region of the head
  Thermal actuation is only performed during read and write operations
  Head-disk interface failures  when flying at 10nm
  Head – disk interactions, if they occur, will be limited to times of DFH actuation
  Limits contact frequency
  Contact area decreased
  Much improved clearance sigma
Since contact only occurs during DFH actuation, and since DFH actuation only occurs during reads / writes, then workload will be critical to HDD reliability
Modification of our reliability prediction / testing methods needed
Minimization of time spent in close proximity
Thermal Expansion
Element spacing
Nominal FH
DFH Off
DFH On
1.5nm
10nm
Disk

## Slide 28: Validation of Workload Impact on HDD reliability
Weibull Analysis
Standard (time-based) Treatment
Same drive + 100% DC / two workloads = different MTTFs
180 GB/hr
120 GB/hr
Failure Rate (%)
POH
MTTF1
MTTF2
120 GB/hr
180 GB/hr
120 GB/hr
MPbF1 = MPbF2
Failure Rate (%)
Same drive +100% DC / two workloads = unique MPbF
Workload-based Treatment
TB Transferred (WL x POH)
Failure rates scale with the total TB transferred
Results demonstrate that TB transferred is the critical reliability parameter….not time POH
Natural reliability metric: Mean Petabytes to Failure (MPbF)
 This naturally leads to a DWM (Drive Workload Monitor) (like an odometer)
Minimum requirement: Simultaneously define max workload spec and MTTF
  This is now done by all HDD manufacturers

## Slide 29: Workload Specifications: An example
A workload Weibull analysis is performed on RDT data (1200 drives / 1000hrs / high workload script)
Cumulative failure rate vs total TB transferred is plotted
Weibull Projections
RDT Test

## Slide 30: Workload Specifications: An example
Weibull Projections
A workload Weibull analysis is performed on RDT data (1200 drives / 1000hrs / high workload script)
Cumulative failure rate vs total TB transferred is plotted
Field
RDT Test
Temperature derating from test  field is then applied
Resulting plot gives expected field reliability as a function of usage

## Slide 31: Workload Specifications: An example
Weibull Projections
A workload Weibull analysis is performed on RDT data (1200 drives / 1000hrs / high workload script)
Cumulative failure rate vs total TB transferred is plotted
Temperature derating from test  field is then applied
Resulting plot gives expected field reliability as a function of usage
Data validates that this drive can meet a 1.2M hr MTTF at a specified workload of 550TB/yr
Field
RDT Test
3.0 PB
560TB/yr x 5yr
MTTF spec = 1.2M hrs

## Slide 32: Workload Specifications: An example
Weibull Projections
A workload Weibull analysis is performed on RDT data (1200 drives / 1000hrs / high workload script)
Cumulative failure rate vs total TB transferred is plotted
Temperature derating from test  field is then applied
Resulting plot gives expected field reliability as a function of usage
Data validates that this drive can meet a 1.2M hr MTTF at a specified workload of 550TB/yr
If HDD is used at lower workloads, a commensurate increase in MTTF (decrease in Failure Rate) will be realized
Field
RDT Test
3.0 PB
560TB/yr x 5yr
MTTF spec = 1.2M hrs
120TB/yr x 5yr
MTTF = 3.0M hrs

## Slide 33: Reliability Test Enhancements (last few years)
Field failure rates scale with usage / workload
RDT workloads can be insufficient to “see” the entire drive warranty period in many applications
  Leaves WD and customers vulnerable to late-in-life field excursions
Need existed to enhance our reliability testing to ensure future products display the required field quality?
Problem Statement
RDT testing must be performed for longer times (brute force),
  Extended Lifetime Test (19 week)
or …….
  High workload test scripts
    Tribo RDT (highest WL script)
    Client (new version has 4X WL increase)
    Universal Enterprise (double workload of predecessor)
  Use of head parametric data to identify “virtual” failures
    Virtual failures = increased failure probability
Testing Options

## Slide 34: Are there precursors to HDD failure?
Controlling the clearance distribution is critical for long-term field reliability
Those heads in the low-clearance wing are far more prone to failure
Must maintain 3 process
Degradation gets severe enough that the head can no longer function.
Failure (typically ECC) then results
Tear down confirms wear of carbon on pole tips due to occurrence of head-disk contacts
Head-disk Interaction
0.5nm
1.5nm
2.0nm
2.5nm
1.0nm
DISK
 =1.6nm
Degrading population


## Slide 35: “Virtual” Failures
Controlling the clearance distribution is critical for long-term field reliability
Those heads in the low-clearance wing are far more prone to failure
Must maintain 3 process
Degradation gets severe enough that the head can no longer function.
Failure (typcially ECC) then results
Tear down confirms wear of carbon on pole tips due to occurrence of head-disk contacts
Head-disk Interaction
0.5nm
1.5nm
2.0nm
2.5nm
1.0nm
DISK
 =1.6nm
Degrading population

Contact between the head and disk leads to degradation of the magnetic / electrical propeties of the head
Monitoring degradation in the parametric data can be used to identify “virtual” failures
Critical Parameter A
0
1
2
3
4
5
RDT Run Hours
Overall Strategy:
  The TMR reader is the best sensor we have in the drive
  Use it to calibrate the head-media interface through magnetic ‘critical parameter’ degradation
  We use about 7 critical parameters to perform in-situ characterization during test
Degradation vs time

## Slide 36: Degradation precedes vast majority of real failures
Drive triggered all three degradation limits at 400-500 hrs in factory RDT
Drive then failed for head-degradation at 933 hours
2nd Level / Teardown FA
  Scope signal on failed head showed base line popping
  SEM on failed head showed DLC wear (others showed no wear).
Parameter C
Parameter A
Parameter B
Tribo-RDT trigger limit
4 order drop in BER
4.5 dB drop
510hrs
460hrs
400hrs

## Slide 37: “Live” Parametric Monitoring During ORT/RDT
A web-based tool is available to monitor the progress of any drive running RDT/ORT in the factory in real time
  Gives temporal information on drive health that was previously unavailable
  Provides much clearer insight into nature of root cause leading to failure
  Allows tracking of: a) individual drives / parameters, b) entire drive population, or c) various drive configurations.
Representative Results
Comparison of RDTs
Head A + Media A
Head A + Media B
Head B + Media B
RDT Test Time (days)
Individual Drive (any parameter)
Trigger Level
Entire RDT Population
Total
A
B
C
E
D
Degradation Rate (%)
RDT Test Time (days)
RDT Test Time (hrs)
Critical Parameter Degradation

## Slide 38: Product Improvements Driven by Parametric Measurements
Improvement driven by Parametric measurement
Head design
Media design
Clearance
Head design
(new reader)
  Parametric data provides far more granularity on product quality compared to “real” drive failures
  Quality team continually monitors Virtual Failures and uses this data to qualify any new component and / or design enhancement
  Engineering uses data to drive improvements into each HDD design

## Slide 39: Failure probability contour plots
Field failure probability can be plotted as a function of both the critical parameter and the degradation in the critical parameter.
Both parameters are important
Failure Probability Contour Plot
1x
10x
5x
Critical parameter A
Critical parameter A
Critical parameter A
For the vast majority of the population, degradation in critical parameter A is more important than the absolute value of A
This is not universally true for all parameters
  Degradation patterns are being used to perform virtual FA
  Some degradation scenarios are more serious than others
Methodology is being extended for WD’s “In-field Health Monitor”

## Slide 40: Evolution of Parametric Monitoring
Decreasing head-media clearance
More Head-Disk contact events
Higher levels of magnetic critical parameter degradation
Precursor to real failure of the drive
Internal Benchmarking: Measurement of critical parametric data now routinely performed in Reliability testing (2+ years experience)
Natural progression is to measure, and store critical parametrics at a regular interval during field operation
External dry-run: Partnership with Enterprise customers on small fleet sizes.

## Slide 41: Why Extend parametric measurements to the field?
After nearly two decades, it is generally accepted that the SMART attributes are not strongly correlated to HDD failures
  “....models based on SMART parameters alone are unlikely to be useful for predicting individual drive failures”.
  (Google: Pinheiro et al., Proc. 5th USENIX Conf. on File and Storage Technologies, February 2007)
The obvious question arises…..“Can we use our parametric degradation approach to improve predictability of drive failures in the field”?
    In-field parametric monitoring (IFPM)
  WD is pursuing parametric data collection for data center fleet management
  Potential to identify poorly performing drives / heads before actual failure is the “Holy Grail” of HDD reliability
  Drives with the capability to perform critical parameter measurements (during drive idle time) have been developed and are just now becoming available
  Health monitor algorithms need to be optimized (6 – 9 months)

## Slide 42: WD’s 1st fleet management system: IFPM
The In-Field Parametric Monitoring (IFPM) system will measure, and store, critical parameters periodically throughout the HDD lifetime, and output a relative health index.
IFPM Health Index
(derived from critical parameters)
Drive Count
Real Failure Rate
Low Score (Bad)
High Score (good)
A ‘Gas Gauge’ - Failure Probability Increases as ‘Health Index’ gets worse

## Slide 43: WD’s 1st fleet management system: IFPM
WD Confidential
Phase 1 – Drives equipped with initial parametric monitoring
  Subset of parameters available now
  Start field data collection with partners
Phase 2 – “Complete” set of critical parameters will become available shortly
Phase 3 – Algorithm development
  Data collected from select customers
  Refinement of failure probability algorithms
  Define a “relative health index”
Phase 4 – Ability to check relative health index of any drive on demand
Since the health index with change with usage, IFPM will be coupled to the DWM (Drive Workload Monitor)

## Slide 44: Meaningful Predictive Modeling
Powerful models that predict failures of individual drives need to make use of signals beyond SMART
One of the main motivators for SMART was to provide enough insight into disk drive behavior to enable such models to be built
IFPM + workload monitor + SMART may prove effective at overcoming our current inability to build predictive models.

## Slide 45
Thank You

## Slide 46
All time is not equivalent in driving HDD failures
The critical time for is the time spent in close proximity to the disk
  Significant levels of head-disk interactions are limited to times of DFH actuation
  This relatively subtle modification / realization has significantly changed the way in which HDD reliability is viewed
  Since actuation only occurs during reads and writes….actuation time is directly proportion to the total data transferred
Failure rates will be dependent on the total data transferred
Overwhelming majority of failures occur when reading / writing / transferring data
Failure probability for HDI issues drops to near zero when pole tip is retracted
Failure probability for motor, PCBA, etc issues that depend on absolute POH time constitute only small percentage of total failures
How does workload enter into the classical analysis?

## Slide 47: Virtual Failure Rates - Definition
  Virtual failure rates (parametric degradation) are monitored in all WD reliability testing
        Very clearly defined pass / fail criteria
  Virtual failures defined in terms a number of critical parameters
  Critical parameters identified from analysis of field return data
      Writer health
      Reader health (magnetic and electrical measurements)
      Magnetic element spacing change
      Physical head-disk spacing change
      Bit error rate
VF
Writer Degradation
Writer Degradation

## Slide 48: VF parameters = higher field failure probabilities
Writer Health
 Writer Health
VFR Trigger
Field / test data used to identify parameters critical to HDD reliability
 Error Rate
Error Rate
 Physical Spacing
 Mag Spacing
VFR Trigger
Mag Spacing
Physical Spacing
wear
Increase
Decrease
contamination
Increase
Increasing Degradation