## Slide 1: Straw electronics
Straw Readout Board (SRB)

## Slide 2: Full SRB - IO
Handling 16 covers
  Input 16*2 400(320eff) Mbits/s
Control
  TTC
  LEMO
  VME
Output
  to PC farm – 2*1Gb/s ethernet
  VME to SBC
  L0 trigger

## Slide 3: SRB – components
TTC
LEMO
L0 OUT
COVERS
TTCRx
COVER CONTROL, DATA, SYNCH
EVENT PROCESSOR
2(4)GB DDR3
DATA TO PC FARM
TIME
REMAP
L0 PROCESSOR
VME INTF
ON-LINE
MONITOR
L0 LOOK_UP
TABLE

## Slide 4: SRB – control flow
Selectable control
TTC
LEMO
VME
Clock delay to compensate time of flight
VME to
- Setup
- Control,
- On-line monitoring
- Data

## Slide 5: SRB – data flow
16x2x320Mbit/s
~10Gbit/s
2.5Gbit/s
2x Gbit ethernet
VME

## Slide 6: SRB – trigger data flow
16x2x320Mbit/s
~10Gbit/s
2.5Gbit/s
2x Gbit ethernet
VME
L0 PRIMITIVES

## Slide 7: Trigger
First mentioned in TD
Possibility to use Straw detector for L0 if proved to be useful
View is split to corridors
  6 straws
Corridors overlap on each side by 2 straws
2 or more trailing edges in a corridor in a defined time window qualify a track
Can be already used as a coarse position ~13mm

## Slide 8: Trigger
Position can be improved using leading edges
Leading edges from 6 straws put into the time pipeline corresponding to the full drift time in straw, step 25ns
Trailing edge track signal starts pattern recognition
Leading edges are run though look-up table and output position code
Time-corresponding position codes from all views are combined
To look-up table
6 straws leading edges

## Slide 9: Trigger
1 SRB with modified firmware collects primitives from 8 SRBs serving 1 chamber
  Left/right ambiguity solved using 3 views
4 SRBs from 4 chambers send L0 primitives to L0 processor
Time estimate
  Event to Cover to SRB – <500ns
  Time-reordering of hits - 10us
  Track finding - <1us
  Collection of hits and combination < 10us
  Sending L0 primitives in < 22us

## Slide 10: SRB
Design started
  Schematics
  Big part of prototype board firmware could be reused
  New parts
    Time reordering
    Event buffer management
    data format for pc-farm
    Online monitoring
    L0 trigger
Ready for PCB layout in October
Prototype December
Price estimate
  Components < 1 kCHF
  PCB + assembly < 1 kCHF
  Total < 2 kCHF