## Slide 1: Straw Requirements
Peter Lichard, Vito Palladino.
Collaboration Meeting, Liverpool.

## Slide 2: Straw detector output
Straw detector
  4 chambers
    4 views each (x,y,u,v)
½ view is served by SRB (Straw Readout Board)
  2 SRBs/view
  8 SRBs/chamber
  32 SRBs/detector
2 x 1Gbit/s ethernet interfaces per SRB
1 chamber connected through 10Gbit link (+1 spare) to pc-farm
  16 Gbit links merged in a switch

## Slide 3: Data rates
Single straw rate 60kHz (average)
  48 bits/event (24 bits leading, 24 bits trailing)
  Coarse time in header
L0 1MHz rate with time window 250ns
  Total data rate per SRB with protocol (UDP,IP,..)
    440 Mbit/s
  Total data rate per chamber with protocol
    3.6 Gbit/s
  Full detector ~16Gbit/s

## Slide 4: Details
UDP header (bytes) | 12
max UDP length (bytes) | 65500
MEP header (bytes) | 8
event header (bytes) | 8
max IP length (bytes) | 9000
IP header (bytes) | 38
edge hit size (bytes) | 3
Event rate (Hz) | 1.00E+06
Hits per view | 6
Time window (s) | 2.50E-07
Rate (tracks) per View (Hz) | 1.80E+07
events in time window | 1.40E+01
event data (bytes) | 102
event size header+dati (bytes) | 110
max number of events in UDP packet | 595
data rate (bytes/s/view) | 110000000
UDP packets/s/view | 1680
effective IP packet length (bytes) | 8962
number of IP packets/s/view | 12278
total data to tranfer (Mbit/s/view) | 884.016
total data to tranfer (Mbit/s/station) | 3536.064