Study of several prototypes of new CHOD
A. Khudyakov on behalf of Russian group INR/IHEP.

---
Bolotov Vladimir Nikolaevich
1933 - 2013

---
Reminder: one of the main functions of the hodoscope is to trigger the events with high multiplicity, including those caused by the conversion of photons in the mirrors of RICH.
With a total load of 50 MHz, to obtain the hodoscope efficiency rate of 98% a time resolution of ≈ 400 ps is required. An additional requirement is a small amount of the material
The scheme of the experiment setup NA62.

---
Prototypes
Scintillators
- BC 408 produced by Saint-Gobain (formerly Bicron)
- EJ-200 produced by Eljet
- Produced by IHEP
All prototypes are wrapped in Tyvek
Light collection:
- WLS fibers
- Direct light collection
  Require large sensitive area but we can't put PMT inside aperture....
  There are new 6×6 mm2 SiPMs!

---
Light collection with WLS fiber
Single tile
Fast WLS fibers BCF-92 are used
d = 1mm
excitation time 2.7ns

---
Direct light collection
Collect light from corner
Collect light from face
Problem of corners: we don't get	direct light from there:
Light have to traverse tile twice
Averaged time resolution is worse
Other geometries are possible

---
Light detectors
3x3 mm SiPM
Must be read out by WLS fibers
Only 9 fibers per SiPM could be used
6x6 SiPM (New!)
Could be used for direct light collection
Or more fibers could be used
Made by SensL, Hamamatsu
PMT
No restriction on number of fibers
Must be placed outside of aperture => light needs to be transferred by clean fiber

---
New: SensL MicroFB series
Available in 3×3 and 6×6 mm2 sizes
Surface mount
Cheap if 500+ is ordered (≈20 Euro/SiPM)
VERY promising for direct light collection
Blue sensitive:
SensL, λmax ≈ 430nm
CPTA, λmax ≈ 600nm

---
New: SensL MicroFB series
Have fast output
- Rise times <100ps; 2ns recovery
- Short impulse response from 1-2ns
- FWHM
- Reduced signal output capacitance
- Higher count rate resolution ability
- Ability to clearly distinguish the first photon arrival time
Not tested yet!

---
Test stand
Standard setup for measurements with cosmics:
Trigger counters in coincidence
115×115×15 mm3
S1 is time setting
Counter being studied

---
DAQ schema

---
Trigger time resolution
σ(tS1 – tS2) = 560 ps
So σ(t) ≈ 580/√2 ≈ 400 ps
provided that counters are identical
Any measurement below 400 ps are
unreliable
tS1 - tS2

---
WLS readout
PMT is Hamamatsu R7899-20 with extended
green sensitivity
Tile		CPTA SiPM		PMT		SensL SiPM
Scint.	Size (mm3)	σt(ps)	Nph	σt(ps)	Nph	σt(ps)	Nph
EJ-200	100×100×20	680	29	590	40	540	38
EJ-200	180×100×20	1030	22	-	-	570	-
EJ-200	270×100×20	1110	21	820	37	670	35
BC-408	150×150×20	910	22	-	-	-	-
Fibers are not glued!

---
Direct light collection
PMT is small Hamamatsu R7400U
Tile		PMT		SensL
Scint.	Size (mm3)	σt(ps)	Nph	σt(ps)	Nph
EJ-200	100×100×20	<400	111	<400	141
IHEP	90×90×20	<400	69	<400	100
BC-408	150×150×20	-	-	-	94
IHEP	150×150×20	-	-	-	54
Central 110×110 area

---
Measurement in the corner
Additional measurements were made to asses effects of the corner with
150x150x20 mm3 BC-408 tile
Time distribution for all events
Event 15x15 mm area at the corner. Arrival time shifted by ~1ns

---
Measurements on beam halo
The second phase of measurements was performed during the spring run 2013 on beam halo of the 21 channel U-70 (a zone the installation OKA).
Layout of the counter’s working on the beam halo.
σ(SBig – STr) = 285 ps
σ(SBig) = 250 ps (measured elsewhere)
σ(STr) ≈ 150ps
Trigger counters

---
Dependence on coordinate
Edge
Corner
Beam position during tests
Mean timer could be used to correct for impact point. For that we need long and narrow tile
The dependence of the mean time of signal arrival on the coordinate of beam
1ch = 45ps

---
Dependence on Nph
Reasonably described by:
%sigma% = P_1 cdot {{1} over {sqrt {N_{ph.e.}}}} + P_2
Depedence of σt on number of photoelectrons

---
New CHOD possible design
Vladimir Obraztsov (Institute for High Energy Physics (RU))
https://indico.cern.ch/conferenceDisplay.py?confId=234148
Variant 1
- Tile 90х90х20 mm3
  60 SiPMs
- Tile 180х90х20 mm3
  40 PMs
- Tile 270х90х20 mm3
  40 PMs
- Tile 270х180х20 mm3
  48 PMs/SiPMs
  Total:
  - 60 SiPMs + 128 PMs/SiPMs
  - 188 el. channels

---
Additional Time Resolution measurements of CHOD prototypes at Protvino
IHEP@INR
V.Obraztsov on behalf of S.Kholodenko, A.Khudyakov, V.Samoilenko
Extended version of the talk at the weekly meeting 16.05
https://indico.cern.ch/getFile.py/access?contribId=1&resId=0&materialId=slides&confId=255916
Possible CHOD design with mini-PMT R9880-U
Variant 2
- Tile 90х90х20 mm3
- 480 tiles
  Total:
  - 480 PMs/SiPMs
  - 480 el. channels

---
NEWCHOD
Preliminary construction ideas
I.M.
03/06/2013
https://indico.cern.ch/getFile.py/access?contribId=1&resId=0&materialId=slides&confId=255916
Variant 3
- Standard tile: 265×107×30mm3
  265 = 1070/4
  107 = 1070/10
- 148 tiles
  Total:
  - 296 SiPM’s
  - 296 el. channels

---
Possible designs with direct light
2 SiPMs. First hit is selected so we always work on direct light
2 SiPMs with mean timer. We need to adjust geometry to ensure that we work on direct light
1 SiPM with triangular tile

---
Current status
- σt ≈ 500 ps is possible with WLS fibers
- Direct light collection is viable option
  - σt < 500 ps
  - Less material: 1 cm thick scintillator
  - Mechanically simpler
- It's seems CPTA's SiPMs have poor time resolution
So: Fibers or direct light collection?

---
Backup slides

---
Calculating intrinsic time resolution
The time resolution of the trigger counters system (time distribution of the counter S2 relative to S1) is described by a Gaussian with a resolution:
Where σS1, σS2 – time resolutions of the counters S1 and S2, respectively.
%sigma%_Tr ^2 = %sigma%_S1 ^2 + %sigma%_S2 ^2
Similarly, one can write two more equations with resolution of the counter relative to the trigger counters S1 and S2 (pairs SHS1 and SHS2). After solving a system of three equations we get the intrinsic resolution of the studied counter SH.
%sigma%_{S_H} = SQRT { {(%sigma%^2_{{S_H}{S_1}} + %sigma%^2_{{S_H}{S_2}} - %sigma%^2_{{S_1}{S_2}})} over {2} }

---
Calculating number of photoelectrons
SiPM
PMT
Amplitude spectra for the photomultiplier R7400U (left) and a silicon photo detector SiPM (right). The spectra were obtained by irradiation with light diode (LED).
While for the large amplitudes the number photoelectrons Nph.e. can be calculated as follows:
N_{ph.e.} = {{langle A rangle}^2 } over {RMS ^2}

---
Calculating number of photoelectrons (2)
A number of the photoelectrons was defined form the amplitudes spectra, obtained while irradiating photo receivers by the LED.
Photoelectrons number vs average amplitude dependencies (Fig. 14 and Fig.15) are linear. These calibrating data permit to transfer the registered amplitude of the signal from the ADC channels to the photoelectrons.
Calibration dependence of photoelectrons from average amplitude signal for SiPM.
Calibration dependence of number photoelectrons from average signal amplitudes for PMT

---
Small PMT Hamamatsu R7400U
An alternative is a direct light collection.
Compact photomultiplier Hamamatsu R7400U (the model is often used for RICH-detectors).
16mm outer diameter and weight 5.3g. The leading edge of the signal is less than 1 ns
Quantum efficiency at 425 nm (maximum luminescence spectrum for the used scintillators) is ~20%.
The spectral sensitivity of the R7400 type photomultiplier.

---
t vs A (for LED)
 t vs A (for CFD)
Fig.7 Dependence of response time on signal amplitude for PMT R7400U.
Figure. 7 shows the response signal dependence on the amplitude using the two discriminator : leading edge discriminator (LED) and constant fraction discriminator (CFD).
Since the basic requirement for the hodoscope is a good time resolution on-line, all presented measurements were performed using CFD to minimize the time response dependence on the amplitude of the signal (walk-effect).