## Slide 1: TDAQ Challenges and overview Tuning DAQ tools for the 2014 run
R. Fantechi

## Slide 2: DAQ tools
My feelings
Not dealing with readout stuff
  No TEL62, no CREAMS, etc
  But the auxiliary software needed to run the experiment
After the experience of the dry run, look at what is ready and what is not

## Slide 3: Run Control
General tuning and operation documentation
Handling of configuration files
  Proposal to have files (and not filenames) sent to the detectors
  Preparation/modification of config files left to detector experts
  Run control will have an interface to define a “configuration” as an ensemble of config files
Interaction with DCS for some detectors
  i.e. LAV for threshold settings
Initialization procedure for Straw and GTK still unknown
Definition of parameters for a run database

## Slide 4: PC Farm
Software stable during the Dry run
For 2014:
  Fix the endianity of the CREAM data
  What about data from Straw and GTK?
  L1/L2 code
  Possible work needed to handle the LKR ZS data
    Preparation of a scheme where a second readout of NZS data around ZS seeds is performed
  Settle the question of the PF-Ring driver
    Licenses to be paid?
Provide a backup to Jonas
  For maintenance and new developments
CDR changes foreseen, possible use of EOS
  Followed in the past by Gianluca & Felice

## Slide 5: Service PCs
Available now:
  LKRPN2: DIM, L0TP control, L0TP GUI, etc
  LKRPN0: boot and file server for TEL62s (32 bit OS)
  LKRPN3: Windows, used for firmware development and testing
  PCATD105: timing, on loan from Atlas (PCI-X)
    New PCI express interface to be obtained from D. Gigi, then change
Consolidation needed
  Backup servers
  Moved to better machines (a number available in the barrack from SLM readout)
  Which of them could go upstairs?
    PN0 and PN3 possibly (use the Ethernet Blaster)
    PN2 has (will have?) direct raw Ethernet connections to L0TP
    PCATD105 possibly (check if a single mode fiber is available from EB to 918)
Make a plan for this upgrade

## Slide 6: ELOG
Already available for the past runs
Additional features implemented by Katelyn Fariss (G. Mason Univ.)
  Electronic checklist with a form to be filled and saved to the ELOG data files
  Remote access to run data
    Run Control main screen
    DCS status
    Environment monitor
Additional advertising needed to stimulate people to use ELOG in a productive way

## Slide 7: Run database
To be implemented
No clear proposals up to now

## Slide 8: Event display-Online monitor
First prototype implemented for the technical run
Need someone following it
  Better integration
  Histograms from all detectors
    Physics? Detector performances?
Make it a robust monitor/debugging tool

## Slide 9: EOB summary
TEL 62 boards can handle EOB triggers and transfer to the PC farm data like burst summaries, etc.
A similar mechanism is needed for those systems which are PC based
  LKr calibration, CREAM control PCs, DCS data which must go in the data stream
I have done a protoype system, based on DIM
  A set of C calls for the sender process
  Synchronized with the software SOB/EOB
  C++ code for the collector (i.e. the PC Farm), which receives data from many senders
  The data are merged by the collector in one block with a specific identifier
The communication works, need to be integrated in our environment
  Mainly in the PC Farm

## Slide 10: Message utility
In NA48 we used the old EMU software package to
  Create info/error/fatal messages in the daq programs
  Display them in one (or more) centralized screens
What could be available for NA62?
  A possibility could be to use a feature implemented in the run control interface used i.e. by the TEL62 or the L0TP control
  Namely a call to a DIM function which publishes some info data
  With a collector similar to the EOB one could gather all these messages, format them and make a display on a suitable screen
Pieces are available, need to put them together and test

## Slide 11: Experiment network
Hardware should be bought to complete the network
  Missing switches for the barrack and for the hall
  10 Gb line cards for the router
The logical structure is defined
  Matter of configuring the switches with the required segments
  Do we need specific segments definitions besides the standard 3 (Data,Config, DCS)?
    Example: segments for the CREAM switches
    May be specific needs for the GTK?
Additional little and useful configurations could be done
  Definition of a “generic” node on all the switches, whose MAC could be redefined on the fly to allow the connection of a laptop for tests in the area (but with fixed IP address)
  Definition of a port as a mirror of another, to spy the traffic of a device which cannot run wireshark
    Very useful during the debugging of the CREAM firmware
Application access points to the NA62 network
  As shown during the last meeting, two PCs will be configured to act as application gateways to our network
  Preparation of the work will start middle of September
  Real implementation time is a function of the dry run dates
    It could be possible to do all the configurations before the dry run and then switch and test the result after.

## Slide 12: Configuration files
Proposal by Vlado on a mechanism to use XML
  Could be a little heavy to be used with C
  With C++ it is simpler, a new implementation exists:
    The LKr calibration driver software by Christina Hughes
    It uses an XML file for the calibration sequence definition
For the other users, mainly TEL62
  Need to setup a strategy
  Maybe prototyping needed to modify and test TDSPY
    Validate the goodness of using XML
    Evaluate the possible complexity of the usage of XML and C

## Slide 13: LTU – Clock – SPS timing
LTU HW/SW stable during the dry run
  Need a new crate/new modules for 2014
  Check if all the used fanouts (SOB, EOB, clock) have enough outputs
Clock: possible long term need for the substitution of the old HP clock (Mainz) + the NA48 HW (Vienna)
  Tek AWG good candidate: from the pool? Costs?
SPS timing: possible substitution of the actual NIM crate with the functions of the TALK board
  Start thinking, need firmware development
  It could share the LKr calibration TALK (which anyway needs timing infos)

## Slide 14: Documentation
Improve the efforts to disseminate the information
Twiki, help files, etc
Efficiency of data taking depends
  On the good DAQ tools
  On the way people is able to operate them

## Slide 15: Logistics
Spare parts inventory
  LTU, TTC, clock fanout, CHEF boards, …
  TDCB, TEL62
  Timing stuff, service PCs
  Network equipment
    Either buy an additional switch or agree with IT for a quick replacement policy for the duration of the run
Organization of the control room
  “Detector” area to be better organized
    Allocate areas to individual detectors?
    With some PC installed?
  Avoid storage of material
  Leave “Operator” area free for the experts