## Slide 1: Electronic Systems for Experiments
Visit of CSEM
23 May 2013
Philippe.Farthouat@cern.ch

## Slide 2: The LHC Experiments

## Slide 3: The ESE Group: mandate
Development/qualification of specific technologies required for experiments
  Radiation hard IC Technologies: 250nm, 130nm, 65nm CMOS
  Common building blocks: Optical links, Power conversion, Control/monitoring
  Readout electronics of detectors: from sensors to data storage
  Infrastructure: Crates, Racks, Power supplies
Contribute to specific experiment systems
  E.g. CMS tracker upgrade, ATLAS Central Trigger, ALICE Inner Tracker, LHCb Velo, NA62 Gigatracker, ...
Make general instrumentation available to CERN users and experiments
  Electronics pool
  Procurement and maintenance contracts for crates and power supplies
Electronics coordination
  “Management” in experiments
CERN contributes ~20% to the electronics of the experiments. However more orders can go through CERN

## Slide 4: The ESE Group: composition
55 CERN staffs
  36 engineers or applied physicists
15 Post Docs
7 Doctoral Students
3 Technical Students (undergraduate)

## Slide 5: CERN Electronics Pool
Rental of instrumentation, modular electronics, LV and HV power supplies, crates
  Technical Support
    Systematic verification
    Test benches for each equipment type
  Database (18000 items)
  Logistics (4400 movements in 2011)
  Procurement
    6 Frame contracts
CAEN HV test bench

## Slide 6: Power and Crates (1)
LHC Power supplies and crates, procurement and maintenance
  Frame Contracts (7)
  Database (13k items)
  Logistics (20-30 repairs/month)
  Technical Support
    Verification
    Preventive maintenance
    Test benches
Power distribution to Experiments
CAEN & Wiener equipment under contract
LVPS Test system

## Slide 7: Power and Crates (2)
xTCA evaluation project
  Crates and power supplies
    Test system
    MMC controller
    Load boards
Future bulk power supplies developments
  More radiation tolerance

## Slide 8: System Designs (back-end)
Heavily involved in readout system
  VME or xTCA or PCIxx based designs
  Large use of FPGAs
  Commercial digital optical links
CMS-Preshower DCC
TTC FMC
GLIB
ALICE C-RORC

## Slide 9: System Designs (front-end)
Front-end systems for several detectors and experiments
  NA62: Gigatracker, Straws, LKr Calorimeter
  ATLAS luminosity detector (ALFA)
  ALICE TPC and Pixel
  ...
Front-end development for LHC upgrades
  CMS tracker readout hybrid
  LHCb Velo upgrade
  ...
Developments for future experiments
  E.g. power pulsing for a linear collider experiment

## Slide 10: Two examples of front-end systems
NA62 straw detector
CMS tracker upgrade readout hybrids

## Slide 11: Microelectronics: Technologies
CMOS 65nm
High performance technology for dense Low Power designs.
65nm CMOS
CMOS 8RF-LM
Low cost technology for
Large Digital designs
CMOS 8RF-DM
Low cost technology for
Analog & RF designs
BiCMOS 8WL Cost effective technology for Low Power RF designs
BiCMOS 8HP
High Performance technology for demanding RF designs
CMOS 9SF LP/RF
High performance technology for dense designs
130nm CMOS
90nm CMOS
Legacy technology IBM CMOS6SF (250nm)
  Re-fabrication of old designs
  Small number of new designs
Mainstream technology IBM CMOS8RF-DM (130nm)
  Technical support: CERN compiled Mixed-Signal design kit
  Frequent MPW and Engineering runs
Advance technology IBM CMOS9LP/RF (90nm)
  Limited support: Project specific
Future technology (65nm)
  For LHC upgrade applications
CMOS 6SF
Legacy designs
250nm CMOS

## Slide 12: 130 nm MPW Activity
CERN participates on all MOSIS MPW runs (4 runs/year) and organizes ad-hoc MPWs with the foundry for high volume and/or area demanding prototyping.
CMOS8RF-DM (3-2-3) is the dominant metal stack option.
Prototyping and Engineering run costs are kept the same for the last 2 years.
Chart: CMO8RF (130nm) Prototyping activity
| 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0
Number of designs | 8 | 20 | 32 | 28 | 21
Total Silicon Area (mm2) | 28 | 100 | 277 | 125 | 295
Evolution of the Prototyping activity on CMOS8RF for the last 5 years

## Slide 13: Future Working Model for 65 nm
Transfer of most support activities to IMEC
  PDK co-development
  PDK distribution and maintenance
  User support MPW organization
  Training
TSMC
IMEC
Physics institutes
Cadence VCAD design services
CERN

## Slide 14: Microelectronics: common projects
Evaluation of new technologies
Radiation-hard and magnetic tolerant (up to 4 T) POL DC-DC converters
GigaBit Transceiver (GBT) and the Versatile Link

## Slide 15: DC-DC Converter
28.5mm
13.5mm
“optimized” PCB
Custom inductor
Covering shield
Converter ASIC under the inductor
To be optimized on final application (customization depends on assembly technology, inductor, overall needs in mass and size
Air-core inductor
Radiation hard ASIC developed
Plastic shields with Cu plating and clips: OK for Phase1 applications. Better options are explored for the future
Output voltage 1.2, 1.8, 2.5, 3.3V or selectable
Output current: up to 3A
Input Voltage: nominal 5-10V

## Slide 16: GBT and Versatile Link 4.8 Gbps bidirectional link
On-Detector
Radiation Hard Electronics
Off-Detector
Commercial Off-The-Shelf (COTS)
GBTX
GBTIA
GBLD
PD
LD
Custom ASICs
Timing & Trigger
DAQ
Slow Control
Timing & Trigger
DAQ
Slow Control
FPGA
GBT
GBT
Versatile Link

## Slide 17: Microelectronics: specific designs
Several chips for Medipix applications (medical imaging)
Readout chip for the ATLAS upgrade silicon strip (ABC130)
NA62 GigaTracker TDCPIX
ALICE monolithic pixel
And several others

## Slide 18: Medipix Chips development
 | Timepix3 | Smallpix | CLICpix prototype
Technology | 130nm | 130nm | 65nm
Pixel size | 55x55mm2 | ~40x40mm2 | 25x25mm2
Analog/digital | 730/2300mm2 |  | 350/275mm2
Chip area | 210mm2 | ~400mm2 | 5.4mm2 (pixel array 2.56mm2)
#pixels/chip | 256x256 (65k) | ~250k | 64x64 (4k)
Functionality | TOT 10bit, ToA 14+4bit or ITOT 14bit, PC 10bit | ToA+TOT or PC+ITOT | ToA 4bit, TOT 4bit or PC 4bit (only for calibration)
Clock frequency | 40MHz |  | 100MHz
Readout clock | 160MHz |  | 320MHz
Readout mode | Data Driven or Sequential | Sequential | Sequential
Power pulsing | YES | YES | YES
Data Compression | Per pixel (sparse readout) | Per pixel, per column | Per pixel, per cluster, per column

## Slide 19: ATLAS ABC130
CMOS 130 nm
256 channels
Preamplifier, shaper, discriminator
Complex buffering schemes
Readout at 160 Mbps

## Slide 20: NA62 GTK TDCPIX
CMOS 130nm
Pixel matrix (300x300um); 1800 pixel cells
Hit time measurement
  ~100 ps resolution
Pixel matrix
“South bank”

## Slide 21: ALICE Monolithic Pixels
Technology offers high resistivity epitaxial layer of up to 18 micron thick and a deep Pwell, allowing integration of PMOS and NMOS in the pixel
Can be used to implement a monolithic detector integrating a detector matrix and its readout in one piece of silicon
Deep Pwell
Pwell
P-substrate
Nwell
Nwell Collection Electrode
Pwell
Nwell
P-epitaxial layer
18 micron

## Slide 22: Other Developments
Readout chips for GEM detectors
Amplifier for diamond beam condition monitor detector
Pixel prototype for a linear collider pixel detector (65 nm)

## Slide 23
THANK YOU FOR YOUR ATTENTION