## Slide 1
CSEM – 2013
CSEM, an accelerator for Scientific Instrumentation
Dr Ivar KJELBERG
Senior Project Manager
Precision mechanisms, Systems ivar.kjelberg @ csem.ch

## Slide 2: Outline
CSEM at a glance
Key competencies for Scientific Instrumentation
Scientific Instrumentation project examples
Centre Suisse d’Electronique et de Microtechnique SA

## Slide 3: CSEM at a glance
Our mission: development and transfer of micro-technologies to the industrial sector – in Switzerland, as a priority – in order to reinforce its competitive advantage
Incorporated, not-for-profit Research and Technology Organization (RTO), supported by the Swiss Government
A public-private partnership
  31 % public
  69 % private
Key figures (2010)
  Revenues ~ CHF 70 mio
  Employees ~ 400
16% Swiss Confederation (EPFL)
15% Neuchatel (city and canton)
69% Private organizations
shareholders
Centre Suisse d’Electronique et de Microtechnique SA
Notes: Animated slide -> on click goes to the next paragraph

## Slide 4: CSEM’s positioning
Research
Transfer to industry
Production and commercialization
Development and integration of technologies
Centre Suisse d’Electronique et de Microtechnique SA
European Allies
EMPA, PSI
EPFL, ETHZ
Universities
Industrial partners
Spin-off, Start-ups
Notes: Animated slide -> on click goes to the next paragraph

## Slide 5: Outline
CSEM at a glance
Key competencies for Scientific Instrumentation
Scientific Instrumentation project examples
Centre Suisse d’Electronique et de Microtechnique SA

## Slide 6: Key competences for Scientific Instrumentation
Key competences to support the Scientific instrumentation for in the development of innovative prototypes and product concepts
  Multi-disciplinary team of engineers
  Innovative systems design and multi-physics modeling
  Capability to produce and to tests advanced prototypes
  Perform feasibility studies and small series production
  Follow up quality aspects, space hardware …
Focus on three application domains:
  MacroMems
  Atomic clocks and lasers
  Advanced mechanisms for space applications and astrophysics
Centre Suisse d’Electronique et de Microtechnique SA
Management Systems - ISO 9001:2008

## Slide 7: Outline
CSEM at a glance
Key competencies for Scientific Instrumentation
Scientific Instrumentation project examples
Centre Suisse d’Electronique et de Microtechnique SA

## Slide 8: Technology’s Offer
CSEM Scientific Instrumentation technology’s offer
Atomic clocks
Stabilized lasers
Remote optical sensing
Miniature atomic clock

## Slide 9: Stabilized Lasers
Realization of state-of-the-art stabilized lasers
Full know-how on:
  Optical frequency reference (optical reference cavity, atomic cells)
  Driving and stabilization electronics
  Opto-mechanical systems
  Fiber & nonlinear optics
  Characterization & metrology
  Modeling
CSEM Scientific Instrumentation examples Stabilized lasers
Objectives
System integration

## Slide 10: Stabilized lasers
1-Hz linewidth continuous-wave lasers with <100mHz residual frequency drift
Compact and robust opto-mechanical system
Fully-stabilized 1 micron and 1.5 microns optical frequency combs
Sub-100 attosecond pulse timing jitter of femtosecond lasers at telecom wavelengths
Ultra-low amplitude noise (down to -158 dBc/Hz)
CSEM Scientific Instrumentation examples Stabilized lasers
Results

## Slide 11: Swiss Miniature Atomic Clock (Swiss–MAC)
Concept and realization of a miniature, low-power and low-cost atomic clock
In house manufacturing and integration of the main building blocks:
  miniature atomic vapor cell
  stabilized laser source
  ultra-low power ASIC
  packaging and encapsulation
CSEM Scientific Instrumentation examples Atomic clocks
Objectives
Swiss–MAC
System integration

## Slide 12: Swiss Miniature Atomic Clock (Swiss–MAC)
Versatile prototype assembled and integrated
Prototype currently under full characterization
Target performances
Frequency stability:
  σy < 2∙10-10 @ 1s
  σy < 2∙10-11 @ 1day
Volume < 5 cm3
Power consumption < 100 mW
CSEM Scientific Instrumentation examples Atomic clocks
Results

## Slide 13: Flash Optical Sensor for Terrain Relative Navigation (EU-FOSTERNAV)
  Study multiple beam 3D flash imaging LiDAR for soft-landing and rendezvous applications.
  Develop/build a prototype
  Test the prototype on test benches reproducing missions conditions
CSEM Scientific Instrumentation examples Remote Sensing
Objectives
Landing test bench
Rendezvous test bench

## Slide 14: Miniaturized Imaging LiDAR Systems (MILS)
  Study 3D flash imaging LiDAR for three space applications:
  Develop, build & test a technology demonstrator breadboard
  Provide FM development roadmap for each application
CSEM Scientific Instrumentation examples Remote Sensing
Objectives
Soft-landing
Rover navigation
Sample container
Rendezvous

## Slide 15: Technology’s Offer
CSEM Scientific Instrumentation technology’s offer

## Slide 16: ESA Corner Cube Mechanisms (CCM) on IASI Instrument MetOp
IR interferometer delay line
> 10 years continuous operation at 2.5 Hz
Straight linear motion of optical payload to < 0.5 µm
> ±10 mm stroke at constant 133 mm/s velocity
< 0.2 N exported forces
Fully tested and validated Mechanics and controls law delivered
CSEM Scientific Instrumentation examples Space
Objectives

## Slide 17: ESA Corner Cube Mechanisms (CCM) on IASI Instrument MetOp
ESA Project for Aerospatiale (F)
1st launch 2006 MetOp A
2nd launch 2012 MetOp B
3rd launch, in storage, MetOp C
Follow-up project started for next generation of Meteo satellites with ESA / Thales Alenia
CSEM Scientific Instrumentation examples Space
developed software platform
Picturese w.r.t. costs savings example
Results
www.esa.int

## Slide 18: ESA Compliant mechanism HAFHA flexure
ESA project
Design, produce and test a rotational flexure bearing pivot for high precision rotations
Centre of rotation deviation of < 1µm for ± 15° rotation
For payloads > 1 kg
First payload mode > 100 Hz
To withstand launch loads
Rotational stiffness < 1 N m/rad
CSEM Scientific Instrumentation examples Space
developed software platform
Test bench with Flex pivots
Objectives
www.esa.int

## Slide 19: ESA Compliant mechanism HAFHA flexure
CSEM Scientific Instrumentation examples Space
Tested mechanism
Results

## Slide 20: ESA MERIS calibration Mechanism
Calibration wheel for the Medium Resolution Imaging Spectrometer instrument on the ENVISAT satellite
Soft support for several Spectralon® samples, shutter and baffle aperture
No launch lock, mass balance
Precision repositioning
Initial MOS2 lubrication
Currently Fomblin Z25 lubrication
CSEM Scientific Instrumentation examples Space
Objectives

## Slide 21: ESA MERIS calibration Mechanism
Initial project for Aerospatiale Cannes (now Thales Alenia )
Launched on ENVISAT satellite on 1 March 2002
End of mission April 2012
Follow-up mission: performed bearing delivery to CSL for Sentinel-3 : OLCI CM Calibration Mechanism Launch in 2013
Identical design 15 years later !
CSEM Scientific Instrumentation examples Space
www.esa.Int
Results

## Slide 22: ESA Door Mechanisms for X-ray Multi-Mirror Satellite (XMM)
UHV protection of CCD detectors for XMM
> 2 years ground storage without loosing UHV pressure
Assembly & test in Class-100 clean-room environment
Door opening in space with extremely high reliability
Critical single Point Failure element for X-ray instrument
CSEM Scientific Instrumentation examples Space - Astro
Objectives
Tested mechanism

## Slide 23: ESA Door Mechanisms for X-ray Multi-Mirror Satellite (XMM)
ESA project: Xray telescope for astrophysics (X-rays do not pass through the atmosphere)
Launched in 1999 December 10
Door opening successfully
Mission should last at least 2 years, large success
Telescope is still operational and we are in 2013!
Data processing still ongoing for the
CSEM Scientific Instrumentation examples Space - Astro
Results
www.esa.int

## Slide 24: ESA LISA satellite: Point ahead Mechanism
Highest precision Point ahead mirror mechanism
Angular stroke : ± 412 μrad (mechanical angle)
Scan speed : ± 62.5 prad/s (155 days to cover entire range)
Total Piston error budget below 1.5 pm (0.000 000 001 5 mm) for a 140 nrad rotation (1 nrad = 0.000 000 057 °)
CSEM Scientific Instrumentation examples Space - Astro
Objectives
Tested mechanism

## Slide 25: ESA LISA satellite: Point ahead Mechanism
ESA project performed in collaboration with RUAG Space
Project terminated in 2010
For the LISA satellites for a gravitational wave observatory
Mechanism delivered, tested in vacuum and cryo configuration
Requested specification have been validated
CSEM Scientific Instrumentation examples Space - Astro
developed software platform
Mechanism ready to be tested
Results

## Slide 26: ESA Slit mask for the James Webb space telescope
Backup solution for JWST space telescope NIRSpec instrument
Cryo mechanism at LHe 30 K or (-243°C) temperatures
25 slits of adjustable width
Adjusted to < 5 µm precision
Validate at cryo-temperatures for lifetime and precision
Validate for launch vibration survival with launch locks
CSEM Scientific Instrumentation examples Space - Astro
Objectives
Tested mechanism

## Slide 27: ESA Slit mask for the James Webb space telescope
Designed, developed & tested for ESA as part of NIRSpec, 2004
Tested at Liquid Helium conditions at CERN
Tested successfully twice for launch vibration
Finally the telescope will fly with US produced MEMS slits
Allowed interesting follow up projects for ground astrophysics
CSEM Scientific Instrumentation examples Space - Astro
developed software platform
Artist view of the James Web Telescope
Results
www.esa.int www.nasa.gov

## Slide 28: Keck Telescope 1: Cryo Configurable Slit Mask Unit CSU
Configurable 46 slit mask
Cryo environment LN2 > 10 years continuous operation
267x267 mm filed of view
< 10 µm slit reproducibility and precision
< 1.2 W consumption over 30 min
Mechanics, electronics, control law and software delivered
CSEM Scientific Instrumentation examples Astro
Objectives
Picturese w.r.t. costs savings example

## Slide 29: Keck Telescope 1: MOSFIRE instrument in operation
Testing and support provided at UCLA before delivery in 2011
Arrived at KECK Hawaii on 22 Feb 2012
First light with CSEM Slit Mask on 4 April 2012
First results presented at SPIE meeting Astronomical Telescopes and Instrumentation in Amsterdam July 2012
Successful operation since
CSEM Scientific Instrumentation examples Astro
developed software platform
Picturese w.r.t. costs savings example
Results
www.keckobservatory.org

## Slide 30: SOFIA Secondary Mirror Mechanism
Secondary Mirror tip-tilt
Ø 360 mm SiC aspheric mirror
Hexapod for positioning 3 mm
Active tip tilt with momentum compensation 20 Hz chopping
µrad tip tilt resolution
6 DoF testing and calibration
Mechanics, electronics, control laws & software delivered
FAA certification
CSEM Scientific Instrumentation examples Astro
Objectives
Picturese w.r.t. costs savings example

## Slide 31: SOFIA Secondary Mirror Mechanism
Project for DLR / MAN
System delivered in 2002
First official flight in 2010
105 flight in April 2013
Several projects done since for spare parts and support for DSI / DLR & NASA
New project under definition for full new mechanism
Discussions regarding upgraded new generation SMM
CSEM Scientific Instrumentation examples Astro
developed software platform
SOFIA 747 airplane with 3 m telescope
Results
www.dsi.uni-stuttgart.de www.nasa.gov

## Slide 32: SOFIA Secondary Mirror Mechanism
FAA compliant flight electronics and control laws for SOFIA
PPC604 & RIO 8062 (CES) VME controllers
18 bit DACs
24 bits ADCs
CSEM Scientific Instrumentation examples Astro
Results

## Slide 33: ESO M2 Mechanism for the four AT auxiliary telescopes
High stiffness precision hexapod system for secondary mirror control and positioning
The mobile AT telescope provide reference beams for the VLTI interferometer
> 25 years operation
1 µm positioning precision
> 200 Hz first modal resonance
6 DoF testing and calibration
CSEM Scientific Instrumentation examples Astro
Objectives
Tested mechanism

## Slide 34: ESO M2 Mechanism for the four AT auxiliary telescopes
Project for ESO / AMOS (B)
Four mechanism and one spare delivered, mechanics, electronics, control laws and software
Follow up support, spare parts deliveries, and several training provided also on site at Paranal (Chile)
CSEM Scientific Instrumentation examples Astro
ESA AT telescopes at Cerro Paranal Chile
Results
AT-1, 2 & 3 (4)
www.eso.org

## Slide 35: ESO VLT NAOS Field Selector Units (NACO – Instrument)
Two high precision and high stability Tip tilt piston mirror and control systems
± 6 ° mechanical tip/tilt
< 1 µrad motion resolution
90 mm Ø ultra-flat SiC mirror
Active Piston stabilization
Counter chopping fast response
Delivered: Mechanics, electronics, control laws and software
CSEM Scientific Instrumentation examples Astro
Objectives
Tested mechanism

## Slide 36: ESO VLT NAOS Field Selector Units (NACO – Instrument)
ESO project with LAOG Grenoble and the Observatory of Meudon (Paris)
Key sub-unit for reference star localization of first major Adaptive Optics instrument on VLT-4 Yepun (Paranal - Chile)
In operation since 2002
Provided since support and maintenance and training for ESO Paranal staff
CSEM Scientific Instrumentation examples Astro
www.eso.org
Mechanism ready to be tested
Results

## Slide 37: GTC Secondary Mirror Tip/Tilt & Steering Mechanism
Secondary M2 steering mechanism for GTC telescope
Mechanism design and control laws performed by CSEM
6-DoF Hexapod + fast tip-tilt chopper (100 kg tip-tilt mass)
M2 mirror of 1.1 m in diameter fully compensated to minimize exported momentum
Final delivery, mechanism, electronics, control laws and software
CSEM Scientific Instrumentation examples Astro
Objectives
Tested mechanism

## Slide 38: GTC Secondary Mirror Tip/Tilt & Steering Mechanism
Mounted on GTC 10.8-m astronomical telescope located on the island of La Palma
M2 mechanism made in partnership with NTE (Spain main contractor) and ADS (Italy)
Delivered in 2005
First light in 2007 July 13
Fully operational in May 2009
CSEM Scientific Instrumentation examples Astro
www.gtc.iac.es
Mechanism
Results

## Slide 39: VISTA Telescope Secondary Mirror Steering Mechanism
Secondary M2 steering mechanism for the 4 meter VISTA telescope
Mechanism design and control laws performed by CSEM
6-DoF Hexapod,
M2 mirror of 1.1 m in diameter
Final delivery, mechanism, electronics, control laws and software
CSEM Scientific Instrumentation examples Astro
Objectives
Tested mechanism

## Slide 40: VISTA Telescope Secondary Mirror Steering Mechanism
Mounted on Visible and Infrared Survey Telescope for Astronomy located at Paranal Chile
Made in partnership with NTE (Spain) and ADS (Italy)
Delivered in 2005
First light on 11 December 2009
CSEM Scientific Instrumentation examples Astro
www.eso.org www.vista.ac.uk
Vista Telescope at Paranal Chile
Results

## Slide 41: ESO: ELT-M5 Adaptive Optics Tip/Tilt Steering Mechanism
CSEM Scientific Instrumentation examples Astro
Objectives
Tested mechanism
In collaboration with:
Design of Full opto-mechanical system, FEM modelling, prototype assembly and tests
Analysis and control simulations of a 3x2.5 meter Silicon Carbide (SiC) mirror (450-600 kg) on three High Power Piezo XXL APA® actuators for dynamic control and image stabilisation
Actuator main specification:
  Stroke: > 0.5 mm
  Resolution: < 1 nm
  Nominal load: < 2 kN
  Maximum load: > 15 kN
  Total weight of PZT: 4 kg
  Full actuator weight: 15.5 kg
APA is a trademark of CEDRAT Technologies, France

## Slide 42: ESO: ELT-M5 Adaptive Optics Tip/Tilt Steering Mechanism
The M5 mirror mock-up is here an optical Honeycomb table (450 kg) with representative mirror eigenfrequencies, mounted on a support structure allowing axial rotation for true real-time motion control and validation in closed loop of the specified motion law.
Successful proof of specified requirements obtained
CSEM Scientific Instrumentation examples Astro
Second generation Mechanism
Results
Full scale prototype courtesy NTE/SENER (ES)

## Slide 43: PSI: PRIGO X-ray diffraction analysis goniometer
3 Rotations (Euler Cradle/Arc)
  OMEGA [-inf, +inf]
  CHI [0-90°]
  PHI [-inf, +inf]
Sample Holder Dimension (Vector)
  SHx [-3mm, +3mm]
  SHy [-3mm, +3mm]
  SHz [16mm, 24mm]
TCP Position (Point in space, where beam should hit sample)
  Ox [-2mm, +2mm]
  Oy [-2mm, +2mm]
  Oz [274mm, 276mm]
CSEM Scientific Instrumentation examples Science
Objectives
Tested mechanism

## Slide 44: PSI: PRIGO X-ray diffraction analysis goniometer
Project started by PSI and EPFL
Optimisations of 6 DoF goniometer in collaboration with CSEM
Kinematic modeling
System control laws
Development of calibration procedure
CSEM Scientific Instrumentation examples Science
www.psi.ch
Second generation Mechanism
Results

## Slide 45: Examples of development tools and data exchange
SolidWorks CAD
GibbsCAM CAM (workshop)
COMSOL Multiphysics FEA
Maple & MapleSim (Modelica based) analytical tools
Matlab & Simulink or Octave & SciLab numerical tools
dSpace rapid prototyping of control algorithms and data acquisitions
LabView data acquisition
C+/# programming
Optics and clean-room labs
Micro-vibration shakers and analysis instruments
CSEM Scientific Instrumentation

## Slide 46: FlexTec : Flexure-based mechanisms
CSEM Scientific Instrumentation examples

## Slide 47: Thank you for your attention!