## Slide 1: CATHI Marie Curie Initial Training Network Cryogenics, Accelerators and Targets at HIE-ISOLDE
SERENA CIMMINO(EN-STI/RBS)*
Target Unit Design Study

## Slide 2
Outline
Target Container Optimization
Standard Temperature Calibration
Cold Line – Alternative Cooling Solution Study
Neutron Converter
Design Study
Outlook

## Slide 3
Target Container
Ion Source
Feed-Through
Cold Line
ISOLDE Target Unit
Target Life
Production
Safety
Radioactive Waste
Optimization
Active Cooling
Outlet Temperature: 24-25°C
Pressure: Approx. 5 bars
Flow rate: 180 L/h
Inlet Temperature: 15°C
Vacuum (10 -7 mbar)
Ohmic Heat (2000 °C)
Systems

## Slide 4
Standard Temperature Calibration

## Slide 5: Calibration Chart
Calibration Chart
Preserve the target during operation
Avoid excessive stress
Icont [A] | Vcont [A] | Isource [A] | Tcont [°C] | Tsource [°C]
450 | 3.01 | 270 | 1717 | 1294
500 | 3.38 | 270 | 1740 | 1294
550 | 3.68 | 270 | 1850 | 1294

## Slide 6: Thermal Measures Optimization
Precision
Reproducibility
Intensive Test Campaign
Diagnostic Instrumentation Study
Laboratoire national de métrologie et d’essais
Calibration Cell

## Slide 7: Standard Thermal Calibration
Pyrometer to use
Thermocouple Installation
Measurement Conditions

## Slide 8
Target Container Optimization

## Slide 9
Conventional ISOLDE Container
Uniform Thermal Field
Release Efficiency Increase
Target Container Optimization

## Slide 10
New Graphite Heater Prototype

## Slide 11
New Graphite Heater Prototype
Ohmic Heat / Containement
Thermocouple

## Slide 12
Graphite Prototype Study
Graphite Heater
Tests
Graphite Heater Tests and Simulations
Graphite Heater – Sigratherm Shielding : Tests and Simulations
Total Graphite
Graphite Heater Simulations
Sigratherm Screen Tests
Sigratherm screen Simulations

## Slide 13
Parts Collection

## Slide 14
Prototype

## Slide 15
Cold Line – Alternative Cooling Solution Study

## Slide 16
Water Leaks Investigation
Brazing
Electron Bombardment welding
It resists up to 500 bar

## Slide 17
Alternative Cooling Solutions
No cooling Water
750W to dissipate
Load | 
Container heat | 1370 [W]
Source heat | 1250 [W]
Radiation | 1 enclosure
Film Coefficient Convection | 3500 W/m2
Thermal Contact Flange
Heat Flux Optimization
Heat Pipes Integration

## Slide 18
Heat Flux Optimization
Thickness Increase
Connection Hot-Cold

## Slide 19
Heat Pipes

## Slide 20
Heat Pipes Integration
Material: Copper nickel plated;
Wick Type: Sintered;
Fluid: water;
Active Length: 100mm;
Total Length: 130mm;
Diameter: 10mm;
Heat Transport 65 W;
Thermal Resistance: 0.015 ~ 0.0769.

## Slide 21
Feed Through Solution

## Slide 22
Neutron Converter
Design Study

## Slide 23
Neutron Spallation Source
Z=50, N = 82 double nuclear shell closure (132Sn)
Z=28, N = 50 double nuclear shell closure (78Ni)
Energy Deposition
Neutron Converter
Isobaric Contaminant

## Slide 24
R. Catherall et al., NIMB, 204 (2003) 235.
R. Luis et al., European Physics Journal A, 48 (2012) 90
ISOLDE Conventional Converter
Proton Distribution(p/cm2/μC)
Neutron Distribution(n/cm2/μC)

## Slide 25
Simulation Validation
A. Gottberg et al., to be submitted to NIM B

## Slide 26
Production Comparison

## Slide 27
Production Comparison

## Slide 28
Design Study
Beam Energy: 500 MeV;
Beam Intensity: 100μA;
FWHM: 3mm;
Particles per second: 6.242 E14;
UCx density: 3.63g/cm3

## Slide 29
Production Comparison

## Slide 30
Production Comparison

## Slide 31
Preliminary Thermal Analysis

## Slide 32
Outlook
Calibration Cellule Development
Graphyte Protoptype
Experimental Tests
Design Optimization Test and Simulations
Neutron Converter Design Finalization
Converter Online Tests

## Slide 33
THANK YOU FOR THE ATTENTION