## Slide 1: ISOLDE DUMPS THERMO-MECHANICAL STUDY
Valentina Venturi EN-STI-TCD
Notes: Method:
individual interviews with group leaders based on the April schedule -> to gather bottom-up data,
EN retreat on 1st July -> the aim was to bring the MTP in line with the last schedule & saving requests from the Council in June
ENMB on 26th July -> validate with group leaders the top-down arbitration

## Slide 2: INTRODUCTION
OBJECTIVES
Understand the present state of HRS and GPS dumps from the thermo-mechanical point of view (FEA)
Dumps were designed for a beam of 800 MeV
Check the future situation in case of beam upgrade
Dumps are under-dimensioned
Present the proposed solution

## Slide 3: ISOLDE DUMPS LOCATION
GPS DUMP
HRS
DUMP
HRS core
GPS core

## Slide 4: DUMPS CHARACTERISTICS
Dump material: not fully defined
 carbon steel A36 (S275)
Dimensions (WxHxL) [m]:
-HRS: 0.4x0.4x1
-GPS: 1.6x1.6x2.4
Shielding: concrete blocks
State of contact shielding/dump: unknown
April 1991

## Slide 5: ASSUMPTIONS
Assumptions are necessary:
very bad/no contact  very good contact
Constant temperature around the dumps (22 °C)
Dynamic analysis not considered for pulses
Thermal properties data are available up to 800 °C
simplifications
for
calculations
core
core

## Slide 6: ASSUMPTIONS
A36 thermal properties:
Thermal conductivity
W/(m.K)
Thermal expansion
1/oC
Specific heat
J/(kg.K)
Chart: Temperature [°C]
Chart: Temperature [°C]
Chart: Temperature [°C]
| 19.899999999999999 | 29.9 | 39.9 | 49.9 | 59.9 | 69.900000000000006 | 79.900000000000006 | 89.9 | 99.9 | 109.9 | 119.9 | 129.9 | 139.9 | 149.9 | 159.9 | 169.9 | 179.9 | 189.9 | 199.9 | 209.9 | 219.9 | 229.9 | 239.9 | 249.9 | 259.89999999999998 | 269.89999999999998 | 279.89999999999998 | 289.89999999999998 | 299.89999999999998 | 309.89999999999998 | 319.89999999999998 | 329.9 | 339.9 | 349.9 | 359.9 | 369.9 | 379.9 | 389.9 | 399.9 | 409.9 | 419.9 | 429.9 | 439.9 | 449.9 | 459.9 | 469.9 | 479.9 | 489.9 | 499.9 | 509.9 | 519.9 | 529.9 | 539.9 | 549.9 | 559.9 | 569.9 | 574.9
 | 500.91 | 504.7 | 508.01 | 510.92 | 513.5 | 515.79 | 517.87 | 519.77 | 521.56 | 523.29 | 525 | 526.73 | 528.53 | 530.44 | 532.49 | 534.72 | 537.17 | 539.84 | 542.79 | 546.02 | 549.56 | 553.43 | 557.65 | 562.22 | 567.16 | 572.48 | 578.18 | 584.26 | 590.73 | 597.58 | 604.82 | 612.42 | 620.38 | 628.7 | 637.34 | 646.31 | 655.56 | 665.09 | 674.87 | 684.87 | 695.06 | 705.4 | 715.86 | 726.4 | 736.99 | 747.57 | 758.1 | 768.53 | 778.81 | 788.89 | 798.7 | 808.2 | 817.32 | 825.99 | 834.15 | 841.73 | 845.28

## Slide 7: CASES STUDIED
Beam parameters:
“PS BOOSTER DUMP UPGRADE,
EDMS 1229493”
Case | Intensity [particles/pulse] | Energy/proton [GeV] | Pulse period [s] | Pulse time [µs] | Beam power [kW] | Heat generated in core [kW]
1 Present situation | 3.30E+13 | 1.4 | 2.4 | 0.94 | 3.08 | 2.25 (HRS) 2.32 (GPS)
From FLUKA simulations
3 Higher intensity and energy | 8.00E+13 | 2.0 | 2.4 | 0.94 | 10.68 | 7.57 (HRS) 7.85 (GPS)
2 Higher intensity | 8.00E+13 | 1.4 | 2.4 | 1.96 | 7.46 | 5.45 (HRS) 5.62 (GPS)

## Slide 8: CALCULATIONS
Results of temperatures and stresses
for different boundary conditions:
HRS at 1.4 GeV present state |  |  |  | 
h (Heat transfer coefficient) [W/m2K] | Min Temp [oC] | Max Temp [oC] | Max Comp. Stress [MPa] | Tensile Strength [MPa]*
3 (bad contact) | 356 | 607 | 336 | 159
5 | 218 | 377 | 116 | 391
10 | 111 | 230 | 157 | 440
20 | 60 | 153 | 120 | 441
30 | 43 | 139 | 110 | 441
40 (good contact) | 36 | 113 | 105 | 441
Steady-state temperature
Single pulse temperature
Thermal stresses
Maximum temperature increase for a single pulse: 7 oC
Maximum stress for a single pulse: 19 MPa
*Values corresponding to maximum temperature of the dump for each analysis

## Slide 9: CALCULATIONS
RESULTS
Chart: 
| 19.899999999999999 | 69.900000000000006 | 119.9 | 169.9 | 219.9 | 269.89999999999998 | 319.89999999999998 | 369.9 | 419.9 | 469.9 | 519.9 | 569.9 | 619.9 | 669.9 | 703.9
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Steel properties

## Slide 10: CALCULATIONS
RESULTS
Chart: 
| 19.899999999999999 | 69.900000000000006 | 119.9 | 169.9 | 219.9 | 269.89999999999998 | 319.89999999999998 | 369.9 | 419.9 | 469.9 | 519.9 | 569.9 | 619.9 | 669.9 | 703.9
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Steel properties
Yield stress

## Slide 11: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 19.899999999999999 | 69.900000000000006 | 119.9 | 169.9 | 219.9 | 269.89999999999998 | 319.89999999999998 | 369.9 | 419.9 | 469.9 | 519.9 | 569.9 | 619.9 | 669.9 | 703.9
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Steel properties
Tensile strength
Yield stress

## Slide 12: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 19.899999999999999 | 69.900000000000006 | 119.9 | 169.9 | 219.9 | 269.89999999999998 | 319.89999999999998 | 369.9 | 419.9 | 469.9 | 519.9 | 569.9 | 619.9 | 669.9 | 703.9
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
Steel properties
Tensile strength
Yield stress
Maximum
service
temperature

## Slide 13: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 19.899999999999999 | 69.900000000000006 | 119.9 | 169.9 | 219.9 | 269.89999999999998 | 319.89999999999998 | 369.9 | 419.9 | 469.9 | 519.9 | 569.9 | 619.9 | 669.9 | 703.9
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
Steel properties
Tensile strength
Yield stress
Maximum
service
temperature

## Slide 14: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 19.899999999999999 | 69.900000000000006 | 119.9 | 169.9 | 219.9 | 269.89999999999998 | 319.89999999999998 | 369.9 | 419.9 | 469.9 | 519.9 | 569.9 | 619.9 | 669.9 | 703.9
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
Safe region

## Slide 15: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 19.899999999999999 | 69.900000000000006 | 119.9 | 169.9 | 219.9 | 269.89999999999998 | 319.89999999999998 | 369.9 | 419.9 | 469.9 | 519.9 | 569.9 | 619.9 | 669.9 | 703.9
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
Safe region

## Slide 16: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 19.899999999999999 | 69.900000000000006 | 119.9 | 169.9 | 219.9 | 269.89999999999998 | 319.89999999999998 | 369.9 | 419.9 | 469.9 | 519.9 | 569.9 | 619.9 | 669.9 | 703.9
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
Safe region

## Slide 17: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 19.899999999999999 | 69.900000000000006 | 119.9 | 169.9 | 219.9 | 269.89999999999998 | 319.89999999999998 | 369.9 | 419.9 | 469.9 | 519.9 | 569.9 | 619.9 | 669.9 | 703.9
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000

## Slide 18: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 607 | 377 | 230 | 153 | 139 | 113
HRS 1.4 low I | 336 | 216 | 157 | 120 | 110 | 105
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000

## Slide 19: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 607 | 377 | 230 | 153 | 139 | 113
HRS 1.4 low I | 336 | 216 | 157 | 120 | 110 | 105
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
HRS at 1.4 GeV present state |  |  |  | 
h (Heat transfer coefficient) [W/m2K] | Min Temp [oC] | Max Temp [oC] | Max Comp. Stress [MPa] | Tensile Strength [MPa]*
3 | 356 | 607 | 336 | 159
5 | 218 | 377 | 116 | 391
10 | 111 | 230 | 157 | 440
20 | 60 | 153 | 120 | 441
30 | 43 | 139 | 110 | 441
40 | 36 | 113 | 105 | 441

## Slide 20: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 153 | 127 | 107 | 95 | 89 | 86
GPS 1.4 low I | 117 | 108 | 100 | 95 | 93 | 92
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
h=3 (bad contact)

## Slide 21: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 607 | 377 | 230 | 153 | 139 | 113
HRS 1.4 low I | 336 | 216 | 157 | 120 | 110 | 105
GPS 1.4 low I | 117 | 108 | 100 | 95 | 93 | 92
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
today

## Slide 22: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 607 | 377 | 230 | 153 | 139 | 113
HRS 1.4 low I | 336 | 216 | 157 | 120 | 110 | 105
GPS 1.4 low I | 117 | 108 | 100 | 95 | 93 | 92
GPS 1.4 high I | 508 | 427 | 364 | 325 | 305 | 295
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
today

## Slide 23: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 607 | 377 | 230 | 153 | 139 | 113
HRS 1.4 low I | 336 | 216 | 157 | 120 | 110 | 105
GPS 1.4 low I | 117 | 108 | 100 | 95 | 93 | 92
HRS 1.4 high I | 815 | 807 | 796 | 501 | 424 | 384
GPS 1.4 high I | 508 | 427 | 364 | 325 | 305 | 295
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
today

## Slide 24: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 607 | 377 | 230 | 153 | 139 | 113
HRS 1.4 low I | 336 | 216 | 157 | 120 | 110 | 105
GPS 1.4 low I | 117 | 108 | 100 | 95 | 93 | 92
HRS 1.4 high I | 815 | 807 | 796 | 501 | 424 | 384
GPS 1.4 high I | 508 | 427 | 364 | 325 | 305 | 295
GPS 2.0 | 927 | 721 | 535 | 461 | 431 | 402
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
today

## Slide 25: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 607 | 377 | 230 | 153 | 139 | 113
HRS 1.4 low I | 336 | 216 | 157 | 120 | 110 | 105
GPS 1.4 low I | 117 | 108 | 100 | 95 | 93 | 92
HRS 1.4 high I | 815 | 807 | 796 | 501 | 424 | 384
GPS 1.4 high I | 508 | 427 | 364 | 325 | 305 | 295
HRS 2.0 | 996 | 995 | 934 | 868 | 626 | 548
GPS 2.0 | 927 | 721 | 535 | 461 | 431 | 402
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
today

## Slide 26: CALCULATIONS
RESULTS
Chart: Max temperature [°C]
| 607 | 377 | 230 | 153 | 139 | 113
HRS 1.4 low I | 336 | 216 | 157 | 120 | 110 | 105
GPS 1.4 low I | 117 | 108 | 100 | 95 | 93 | 92
HRS 1.4 high I | 815 | 807 | 796 | 501 | 424 | 384
GPS 1.4 high I | 508 | 427 | 364 | 325 | 305 | 295
HRS 2.0 | 996 | 995 | 934 | 868 | 626 | 548
GPS 2.0 | 927 | 721 | 535 | 461 | 431 | 402
Tensile strength | 441.57 | 441.28 | 440.98 | 440.69 | 440.39 | 439.27 | 425.49 | 397.83 | 359.05 | 311.92 | 259.2 | 203.68 | 148.11 | 95.271 | 62.312
Yield strength | 251.23 | 230.82 | 215.89 | 204.9 | 196.48 | 189.34 | 182.39 | 174.63 | 165.21 | 153.42 | 138.69 | 120.57 | 98.764 | 73.104 | 53.432
Max service temperature | 0 | 2000
today

## Slide 27: CONCLUSIONS FOR CURRENT DUMPS
The present situation seems already critical for the HRS dump
An upgrade of just the beam intensity would be enough lead to a failure of the material if no active cooling is added
PROPOSALS
Replacement (price would be very high)
Reinforcement (possibility of solving thermo-mechanical problems)

## Slide 28: NEW DESIGN
HRS dump is studied
water cooled copper block (CuCrZr) could be placed in front of the existing dumps (length = 0.5 m)
CuCrZr  new PSB dump
Beam parameters:
-high intensity (8 E13 ppp)
-high energy (2.0GeV)
HRS dump

## Slide 29: CFD SIMULATION
85 % of the total power is deposited on the Copper block (6.5 kW)
water flow: 1 m^3/h , 20 oC
water temperature increase: 5 oC
CFD: steady-state temperatures
CFD: water cooling

## Slide 30: CFD SIMULATION
Thermo mechanical study
Steady-state + pulse temperatures on the CuCrZr block
Dynamic stresses analysis
Part | Max temperature increase per pulse [ºC] | Max temperature steady- state [ºC] | Steady-state stresses compressive [MPa] | Dynamic compressive stresses [MPa] | Fatigue: stress amplitude [MPa]
CuCrZr | 27 | 90 | 41 | 149 | 53.8
Steel | 0.2 | 62 | 6.5 | 7 | 0.25

## Slide 31: CONCLUSIONS
All results are based on the beam parameters described on the document:
“PBU-T-ES-0002-00-20, EDMS 1229493”
The placement of a water cooled copper block in front of the dumps seems to be a good option to avoid the replacement of the dumps from the thermo-mechanical point of view
The results of the analysis show that temperatures and stresses remain below the material’s limits in both blocks during commissioning
For further information:
“ISOLDE DUMPS: EVALUATION OF PRESENT AND FUTURE OPERATION , EDMS 1277863 “
“ISOLDE DUMPS DESIGN PROPOSAL: EVALUATION OF FUTURE OPERATION, EDMS 1308217”

## Slide 32
Thank you!