## Slide 1: Muon systems and associated electronics
P. Dupieux (ALICE), A. Cardini (LHCb)
M. Abbrescia, K. Hoepfner, A. Safonov (CMS)
Ch. Amelung, O. Kortner, S. Veneziano (ATLAS)

## Slide 2: Preliminary issues #1
Defined three main “themes” :
  New running conditions and new requirements from physics, consequences for muon detection
  System longevity, upgrades foreseen,new detectors and R&D
  Electronics (front-end and trigger),trigger algorithms, alignment

## Slide 3: Preliminary issues #2
Thinking of splitting theme #2 in two talks:
  2a. Longevity of the muon systems
  2b. Upgrades and new detectors R&D
Agreed with the Tracker PG that MPGD technologies – of interest for both communities - will be dealt here
Dicussion on potential speakers just started
  Premature to propose names – will do it before the end of June
Discussion on talk duration just started (depend on split of theme#2)

## Slide 4: Theme (talk) #1
New running conditions and new requirements from physics, consequences for muon detection
focus on muon detectors requirements from operating conditions after LS2 and the HL-LHC physics program
  final integrated luminosity and accumulated radiation, increased instantaneous luminosity, pile-up, etc.
  predictions for correlated (beam-induced) and uncorrelated (cavern) background
  consequences for detector functioning, required time resolution, and off-line track reconstruction
  adequacy or deficiencies of the existing systems performance (extrapolated), and potential improvements
  new/better signal/track reconstruction algorithms possible with improved detectors

## Slide 5: Theme #2 – one or two talks
System longevity, upgrades foreseen, new detectors and relative R&D
System longevity of the muon systems (talk 2a?)
  Muon detector problems after LS2, actions to keep the performance stable, possible improvements using new detectors
  Chambers reaching rate limits, high occupancy, high dead time;
  Chambers aging due to radiation or accumulated charge
Upgrades with new detectors (talk 2b?)
  Replacing old detectors by new ones
  Extending muon system coverage with new detectors
  R&D for new detector types (including MPGD)
  Experimental facilities needed for this R&D

## Slide 6: Theme #3
Electronics (front-end and trigger), alignment
effect of increased radiation and higher collision rates on front-end electronics and trigger systems
  radiation damage, single-event upsets
  readout electronics bandwidth limitations
  electronics upgrades
  trigger performance, sharpness of trigger threshold, purity
  hitting maximum allowed trigger rates
  increasing the complexity of low-level trigger algorithms – requiring increased trigger latency
  alignment – optical systems and alignment-using-tracks
  radiation damage to sensor electronics

## Slide 7: ATLAS@theme#1
Basic goals of ATLAS:
  Keep muon detection efficiency and momentum resolution at the existing level
  Keep muon trigger rates at acceptable level
Assumptions for run IV (after LS3):
  <L>=5x1034 cm-2s-1, Lpeak=7x1034 cm-2s-1
  Up to 200 pile-up events (with a safety factor of ~1.5)
  Plan to accumulate 3000 fb-1 of pp collision data.

## Slide 8: ATLAS@theme#1
Implications of these operating parameters:
  High cavern background:
    Highest expected rates in the Small Wheels (innermost endcap wheel, 7m from IP): 15 kHz/cm2 (r=100 cm from beam line), 100% occupancy in the MDT chambers, and too high for CSC chambers too.
    For comparison, highest rates in the Big Wheels (middle endcap wheel, 14m from IP): ~250 Hz/cm2, corresponding to ~10% occupancy in the MDT chambers.
  Present level 1 trigger rates would be as high as 140 kHz for single muon trigger with pT>20 GeV at the HL-LHC peak luminosity.
  Frequent buffer overflows of the MDT front-end electronics expected, due to a high trigger rate at high occupancy.

## Slide 9: ATLAS@theme#1
Present upgrade plans - the two major ones:
  Small Wheels will be replaced in phase-1 upgrade by New Small Wheels (NSW), using sTGC and Micromegas chambers. NSW is designed to be able to continue to operate under HL-LHC operating conditions, i.e. until the end of the lifetime of ATLAS.
  Redesign of the complete level 0/1 muon trigger, which entails replacing a large fraction of the electronics chain of precision and trigger chambers.

## Slide 10: CMS@theme1 - Physics context
Muon offline coverage and trigger performance critical independent of physics; e.g. sensitivity to H couplings measurements strongly depends on channels with µ:
  H-> ττ-> µ +X is key for measuring coupling to fermions
  H->ZZ->4µ or 2µ+X is key for coupling to vector bosons
  H->2 µ will be measurable at high luminosity giving new insight on fermion coupling
Substantial gains in LHC reach, if iCMS to extend muon system and possibly triggering capabilities beyond current η=2.4
  A substantial challenge as even maintaining the current envelope may not be easy, given very high rates and limitations arising from complex magnetic field configuration, material.
  Particularly strong motivation for going forward if inner tracking capabilities are extended simultaneously (being considered by CMS)

## Slide 11: CMS@theme2 - Scenarios for moving forward
A 2-prong strategy being pursued:
Work to ensure maintaining the current µ offline and triggering envelope, provide strengthening as required
  Very likely that we will find that it will be necessary as a third of µ coverage 1.6<η<2.4 is in potential jeopardy due to rate increases and trigger bandwidth limitations
A thorough cost-benefit analysis of scenarios extending into the region of up to η=3.5-4.0
  Physics gains substantial, but challenges can be very significant
  The outcome will depend on other sub-system’s plans, especially tracking, but also the calorimeter
  New technologies capable of withstanding high rates are considered (GEM, MPGD, iRPC) including new ideas, e.g. imaging calorimeter with µ tagging
Simulation will be critical to provide the full picture

## Slide 12: CMS#theme1 - Challenges in more detail
Maintaining current envelope:
  All the original complexities for the forward region stay in place: magnetic field, large material budget, high background rates, triggering challenges, shielding concerns given the space constraints
  Rate increase further complicates these old challenges, but also bring new ones (aging)
Enhanced coverage options beyond η=2.4 and up to η=4.0:
  New ideas in the context of physics enhancements due to better triggering, resolution and efficiency, including the broader context of the related detector systems (tracking, calorimetry)
Detector technology choices at very forward region driven by high rates and aging.
  Post-Phase-2: 10s of kHz/cm2 in the region η=1.6-2.4.
  Expect a further rate increase, perhaps up to an order of magnitude on the high eta edge? Even higher abilities to withstand aging needed

## Slide 13: ALICE@theme#1
The plans of the ALICE muon system (MS) upgrades are limited (as compared to CMS/ATLAS ones) because the constraints on the luminosity are much less important
ALICE MS upgrades are fully scheduled to be installed during the LS2, nothing foreseen for LS3.
Operating conditions and requirements. ALICE operating conditions after LS2:
  PbPb 100 kHz (MAX collision rate) => L~10^28 /cm/s (the constraints in pp are expected to be less)
  One order of magnitude above the MS present design.
  Total integrated luminosity in PbPb ~10 nb-1 (goal)

## Slide 14: ALICE@theme#2-3
Detector upgrades
  Existing MS: Angular coverage: 2-9 degrees (one arm only)
  Muon Traking, 10 planes of cathode pad/strip chambers, 1 Mch
  Muon Trigger, 4 planes of single gap RPCs, 20 Kch
  Upgrade Plans: No modification of the existing detectors
Electronics upgrades
  Replacement of the readout electronics of the Muon Tracking and Muon Trigger, towards a dead time free readout => ALICE CRU (Common Readout Units)
  Replacement of the very FE of the Muon Tracking => based on ongoing developements of the S-ALTRO chip essentially
  Replacement of the very FE of the Muon Trigger => very FE with amplification (it is not the case presentely) for operation in genuine avalanche mode (like CMS/ATLAS RPCs) in order to limit the RPC aging => new ASIC (FEERIC) being developped

## Slide 15: LHCb@themes 1-2-3
Upgrade taking place in LS2, like ALICE
Operating conditions and requirements
  After LS2 we will be operating at 2 x 1o33 cm-2-s-1, which is x10 w.r.t. current design, but only x5 w.r.t. to current data taking conditions Plan is to acquire 50 fb-1 in 10 years.
Muon chambers for the upgrades
  Only minor modifications of the existing muon detector (but probably only between LS2 and LS3): some highly irradiated detectors ( MHz/cm2) will be replaced with triple-GEM detectors with pad reaodut
Electronics upgrade - This is the main goal of our upgrade:
  new common readout boards for 40 MHz readout
  new muon off detector electronics boards
  low level muon trigger at 40 MHz used just after LS2, and eventually we will go to NO low level trigger and processing of ALL events by high level trigger with a super PC farm
  new electronics for muon control

## Slide 16: Things to do
Decide if split theme#2 into two talks
Better define talks from #2 on (talk #1 is quite well defined)
Decide speakers and allocate talks